## Slide 1: One Box Gunnery Trainer Interim Design Review
Group 10
Anthony Muller
Gerald Tyberghein
Joshua Wood

## Slide 2
Overview
The Advanced Gunnery Trainer System
  Problem Statement
Product Specifications
Breakdown
Tradeoffs
Concept Design
Tip Analysis
MIL-STD-810
FEM Analysis
Cost Analysis
Future Plans

## Slide 3
Introduction
Figure 1: Lockheed Martin TAGTS
Source(www.lockheedmartin.com)
Figure 2: Pelican-Hardigg case in military use
Source: Pelican-Hardigg Case (www.pelican.com)

## Slide 4
The Advanced Gunnery Trainer System (AGTS)
Compact, cost efficient tabletop system
Used to sustain precision gunnery skills at all levels
Provides training procedures, basic skills, and drills
Can be linked together with other AGTSs

## Slide 5
Product Specifications
Weighs less than 120 lbs
Sights and gunner handle mounted in correct tactical position
Equipment must be safe when being transported
Packing does not interfere with components’ cooling
System must be stable
System must be durable
Easy to set up
Figure 3: Current TAGTS setup
Source: Payne, Jeffrey

## Slide 6
Tabletop vs. Box on Floor Design
Figure : Initial tabletop concept.
Figure 3: Initial B.O.F concept

## Slide 7
Breakdown
Component | Tabletop | Box on Floor
Weight | 102-110 lbs | 110-130 lbs
Handle Linkage | 2 parts | 6 parts
Monitor Linkage | 1 part | 6 parts
Case Durability | High | Medium
Ease of Access | High | Medium
Air Ventilation | High | Low – Medium
User Convenience | Medium | Medium
Manufacturing | Easy | Difficult
Shock Mounting | High | Medium-High
Table 1: Tabletop vs. Box on Floor Properties

## Slide 8
Tradeoff Decision – Main Points
Weight – about 15-20 lbs lighter than Box on Floor.
Shock Mounts – Pelican provided shock mounts will provide better impact force protection compared to a foam insert/sheet metal combination for a box on floor design.
Manufacturing – Easier on large scale to order a Pelican case with internal Mac Rack frame and shock mounts rather than design and manufacture foam inserts and sheet metal for every case.
User Convenience – Easier to access parts for maintenance and repairs. Also, leg room is not an issue.

## Slide 9
Concept
Figure 4 : Case Packed
Position
Figure 5 :
Case Rolling
Figure 6: Side View Inside Case

## Slide 10
Concept
Figure 7: Person Using TAGTS

## Slide 11
Tip Analysis
Figure 8 : Force Distribution of Deployed System

## Slide 12
Tip Analysis
Set left side normal force equal to 0, to assume tipping.
Take moments about right side normal force, and solve for the input force on the handle.
98lbs(10.63in) – F(16.76in) = 0
Maximum applied downward force on handle
F = 62.16 lbs

## Slide 13
MIL-STD-810 Test
“…a generally accepted standard of ruggedisation for testing and compliance for mobile computers and equipment.” (Secure Systems and Technologies)
Mechanical Shock
Random Mechanical Vibration
Altitude

## Slide 14
FEM Analysis
Figure 9 : Stress Distribution of von Mises

## Slide 15
FEM Analysis
Figure 10 : Stress Distribution of the Maximum Principle Stresses

## Slide 16
FEM Analysis
Figure 1 : Stress Distribution of the Maximum Shear Stresses

## Slide 17
Item | End Product Cost | Required for Project | Project Cost
Box | 1800 |  | 0
Monitor Bracket | 700 200 | √ | 0 200
Computer Bracket | 500 65 | √ | 0 65
Keyboard Mount in Lid | 70 25 | √ | 0 25
Mouse | 20 |  | 0
Headset | 300 |  | 0
Handle Bracket USB Interface | Proprietary 150 Proprietary | √ | 0 150 0
Power Strip Mount | 45 5 | √ √ | 45 5
Cable Management | 50 | √ | 50
Total | 3930+ |  | 540+
Cost Analysis

## Slide 18
Future Plans
Currently in “Design Refinement” Phase of Gantt Chart
Attend Interservice/Industry Training, Simulation, and Education Conference (11/29/10-12/02/10)
Order Pelican case from Ms. Daria Boley of Pelican Hardigg
Implement components into case and mount system for testing and analysis

## Slide 19
References
Lockheed Martin. The Advanced Gunnery Trainer System (AGTS) Tabletop Trainer. Lockheed Martin. Www.lockheedmartin.com. Web. 31 Oct. 2010.
Pelican. Pelican Hardigg Cases. Pelican, 2010. Www.pelican.com. Web. 03 Nov 2010.
Secure Systems and Technologies. MIL-STD-810 Overview. Secure Systems and Technologies. http://www.sst.ws/images/downloads/MIL-STD-810%20overview%20iss%205.pdf. Web. 31 Oct. 2010.

## Slide 20
Acknowledgement
Sponsor – Lockheed Martin
- Jeffrey Payne (Mechanical Engineer)
Sponsor – Pelican Hardigg
- Daria Boley (Pelican Hardigg Salesperson)
Advisors –
- Dr. Rob Hovsapian
- Dr. Patrick Hollis
- Dr. Srinivas Kosaraju
- Ms. Shannon Ingersoll
- Mr. Joseph Trpisovsky