## Slide 1: Spring progress report side under ride guard and aerodynamic fairing
Kenji Petrucci
Cody Jones
Sam Murphy

## Slide 2: Introduction
Passenger cabin intrusion, PCI
Severe Injury/fatalities
No requirement to prevent side under ride

## Slide 3: Background
Rear guard
  initially required in 1953 but were highly ineffective; safer guards required in 1998 by NHTSA

## Slide 4: Background
Over 4 million trailers travel on US roads, none with side under ride guards
Approx 226 people die annually due to side under ride
98% of collisions with a trailer result in at least 1 fatality
*all pictures from http://www.crashforensics.com/truckunderride.cfm

## Slide 5: Customer needs
Absorb force of a light duty vehicle (6000lbs) traveling at 35mph and prevent under ride
Cost efficient and easily installed by end user; bolt-on “kit” configuration
Provide aerodynamic qualities
  Offset cost of purchase/installation
  Increase fuel efficiency
  Reduction in total hauling capacity

## Slide 6: Product Specifications
Impulse time of 200ms
Impulse force vs. static force
  Safety factor N = 2
 | English | SI
Mass | 6000lb | 2722kg
Velocity | 35mph | 15.65m/s
Δt | 0.2s | 0.2s
Δv | 35mph | 15.65m/s
Table 1

## Slide 7: Product Specifications
Units of N*s
Factor of safety = 2 means double the impulse force
Nearly 500,000N of force for static load

## Slide 8: Product Specifications
Modular vs. single unit
Impact always on at least 2 sections
  Force per bar approximately 213,000N
    47,884lbs

## Slide 9: Final Design
Aluminum
  1.5in (0.25in wall thickness) square tubing
  0.25in thick brackets for welding
Steel
  2in (0.25in wall thickness) square tubing
  Weld directly to trailer I-beam
6in x 24in x 0.5in aluminum impact bar

## Slide 10: Final Design Aluminum w/brackets

## Slide 11: Final Design Steel

## Slide 12: Stress/Deflection Analysis 6061-Al
Max stress
  100ksi for steel
  85ksi for aluminum
Max stress at joint corners
  Impact bar failure acceptable

## Slide 13: Summary
Aluminum questionable (6061-T6)
  UTS = 45ksi
  Tensile yield strength = 40ksi
  UBS = 88ksi
  Bearing yield strength = 56ksi
Max deflection at ends acceptable, even if failure occurs
Safety factor of 2 realistic and achievable

## Slide 14: Fabrication/Assembly/Testing

## Slide 15: Risks
Time constraints
  Parts/Shipping
  Fabrication
    Welding, machining
  Testing
    Correct material choice

## Slide 16: Acknowledgements
Dr. Hollis
  Faculty advisor
Perry Ponder
  Sponsor
Andrew Magaletti

## Slide 17: References
Çengel, Yunus A., Robert H. Turner, and John M. Cimbala. Fundamentals of Thermal-fluid Sciences. 3rd ed. Boston: McGraw-Hill, 2008. Print.
Wolfson, Richard. Essential University Physics. 1. San Francisco: Pearson Addison Wesley, 2007. Print
www.onlinemetals.com