Microcontroller

In selecting the microcontroller for our robot we eventually had to just pick one because of all the thousands of different models out there to choose from. Most microcontrollers have the same functions built into them. They have timers to perform regular timed actions and for pulse width modulation, UARTs for serial transmission and analog to digital converters to read in analog signals. The important parameters then are speed, number of pins, and cost. With so many to choose from we fortunately had a representative from ARM, a microcontroller company, come to the school and he donated a microcontroller to the project. This ended up being the MCBSTM32, a 32 bit 72MHz cortex M3 based microcontroller. This board comes with a development kit which includes an IDE to develop software for it and a hardware programmer to get the software onto the board. All of this usually goes for about $230 so getting it for free is a huge boon. The board is more than enough for our purposes having 48 pins and being plenty fast. Now especially with the rule changes because it doesn't need to be autonomous so there is much less demand on the microcontroller.

Our Microcontroller MCBSTM32

The first thing needed from the microcontroller is a UART which will be used to connect to the serial to WiFi module. The board has three UARTs and they are all linked to ports on the board which are USB, RS-232 and CAN. Fortunately, the microcontroller and WiFi module both work at 3.3V so they will just be connected directly and the distance between them should be short enough that RS-232 shouldn't be needed. Next are the digital inputs from the two touch sensors. If these output 3.3V as high logic they will simply just be read in by two pins configured as input. If not some voltage drop will be needed to drop the voltage from the sensors to 3.3V. Then there are the analog inputs from the weight sensor, accelerometer and current sensor. These sensors all output an analog voltage ranging from 0 to 3.3v so they can be read in using the analog to digital pins on the microcontroller. Everything will be attached to the pins on the board labeled PA PB and PC. These pins are direct connections to the microcontroller and bypass any built in things on the board.

The programming requirements for the microcontroller are now much simpler because autonomous functions are no longer needed. It's going to be almost completely remote controlled so the microcontroller is only reacting to the commands received over the communication link. Periodically, the microcontroller needs to poll all of its sensors, send the values it reads over the communication link. The sensor data is used by the human operator and not the microcontroller. The microcontroller also needs to listen to the link and receive commands from it, decode the commands, and act on them by driving the right motors.

The motor control for the two main drive motors will be the only complicated programming requirement. The speed of these two motors needs to be controlled more accurately. If the robot wants to go straight, the two motors need to be turning at the same speed or else it will veer off course. The speed modulation of these motors will be done via pulse width modulation. The microcontroller will generate a signal that switches at a few kHz at a certain duty cycle. This will turn the motor on and off so it is only on a fraction of the time. So a 50% duty cycle drives the motor at half speed. This isn't ideal though, and all motors are different so an additional feedback loop will be used to control speed. The speed the hall effect sensors are changing will be used to detect the speed the motors are spinning and a simple PD loop will be used to keep the motors spinning at the desired speed.

The link to the robot isn't perfect and if the competition from this year was any indication it goes down fairly often. The robot then needs some way of coping with losing the connection to the control computer. It could always just keep executing the last command it received but that might be dangerous. There's no telling how long the break will last so it might just smash straight into a wall. The safest method is to just have the robot kill the drive motors when this happens. It's easy to implement but we waste time with the robot not doing anything. The robot could also take over with some autonomous function when this happens but that would be very complex to implement. The link shouldn't go down as much as the 2009 competition as there is now no delay so this will hopefully not be too much of an issue.

Motor Control

The two brushed DC motors that run the conveyor belt and linear actuators are easy to control. The conveyor belt only needs to run in one direction so a half bridge will be enough to run it. The linear actuator needs to run in both directions though, so it will need to be run with a full H bridge. These two should be low enough power that an IC can be used that contains all the drive circuitry. If not, we can get a full circuit board driver that will do everything needed and support higher currents. These will take in two signals, a pulse width modulated signal which controls the speed and a digital signal that controls direction.

The two drive motors however are far more complicated being brushless motors. These motors don't handle commutation automatically so it needs to be done manually. They're essentially AC motors driven with a DC current. The commutation is performed by determining the current position of the rotor of the motor using three hall effect sensors then changing which phases of the motor that are being driven to the next set as seen in the diagram. The full board motor controllers for brushless motors are horribly expensive so we're going to we're building it ourselves. This consists of two parts, the drive circuitry and commutation circuitry. There aren't chips available that do both parts because the current requirements of the motors is too high and they max out at about 2.5A.
Diagram showing motor, and outputs for sensor inputs

The commutation part simplifies down to a 6 state finite state machine for the 6 phase combinations that the motor can be driven in. Each time one of the three position sensors on the motor shaft changes it switches to the next state. For example, if the sensors change and are now 101, phase A now needs to be driven high and B driven low. To go forward it progresses forward through these states and to go backwards it reverses the order. Because the microcontroller isn't going to be used for much anymore, it probably has enough resources left that this can be done in software with a few external interrupts. There are also chips available that perform all of this and also have safety features built in which would work much better. Unfortunately they're all surface mount so it would be a huge pain to make a circuit board to put them on.

The other section of the controller is the drive circuitry. This is the part that actually interfaces with the terminals of the motor and performs the high power switching needed. The motors are going to need far too much power to be able to use a chip to do this so it needs discrete power transistors instead. This will be three half bridge circuits, one for each phase, using MOSFETs. MOSFETs because they are very common for these low voltage applications and their isolated gate makes them easier to drive with a microcontroller compared to a BJT. The driver works by having 6 MOSFETs acting as switches. Turning on one of the high side switches connects that phase of the motor to VCC and turning on a low side switch connects that phase of the motor to ground. So one phase will be high and the other low and current will be driven through the motor. Turning on both high and low of the same phase will short the battery and be a very bad thing to happen so the commutation circuit will need to ensure that never happens.

Three half bridge motor driver for three phase Brushless DC motor.

Entire motor controller subsystem

Communication

With the change to remote control, the communication system has become far more important. Instead of just using it to tell the robot to start and stop operations, the robot now completely depends on remote commands. The old rules had a 2 second delay for all data sent through the network but that delay is now gone so there's not really any point anymore in making the robot autonomous. We can make use of the superior decision making abilities of the operator instead of trying to program all of that ourselves.
Lantronix Matchport Serial to WiFi module

On the robots side of the link, the robot sends commands serially via one of its UARTs to a serial to WiFi module. This module will be a Lantronix Matchport which handles all of the networking automatically and relays all data sent to it over the network. It also has a bunch of other features which might come in handy like a built in web server and telnet access. It will connect to the provided network via a WiFi access point on it. The competition provides us with two IP addresses on their network and this will be using one of them.

The other side of the link will be in the control room where the operator will be. This will be run from one of the member's laptops or some other computer. This computer will connect to the network with a wired Ethernet connection and communicate with the robot via port redirection software that comes with the Matchport. The port redirection software creates a virtual serial port on the computer which redirects data sent to it to a member on the network. Using this, the entire network can be abstracted away and the connection from both ends will just look like a wired serial connection. This is very nice as serial connections are incredibly simple and we don't have to worry at all about the network.

The protocol for the serial connection making the communication link will be a standard 8 bits data, 1 end bit and 1 odd parity bit. The data will be transmitted in bytes as individual ASCII characters. Transmitting 5 bytes for each sensor reading will allow 0 to 99999 to be sent which should be enough to give a good representation of the sensor readings. Each packet sent on the robot's end will be 25 bytes or 250 bits after adding parity and end for each byte. A packet of sensor data will be sent 10 times a second giving a transfer rate of 2500 bits/s, well under our limit.

Accelerometer X	Accelerometer Y	Accelerometer Z	Weight	Current

Packet of data sent by robot. 5 bytes ea.

On the control side of the link, the computer needs to send the speed and direction of the two drive motors and activation of the linear actuator and conveyor belt. The speed of the motor needs one byte which gives 256 divisions of speed, because the joystick used has 256 divisions, enough that the divisions are almost indistinguishable. The direction of the motor though, only needs one bit. 0 is forward and 1 is reverse. The conveyor belt only moves one direction so only one bit is needed. 0 for off and 1 for on. The linear actuator needs two bits, the first being 1 to move it up and the other 1 to move it down. This gives 5 bits for all of this so it can all be sent in one byte. This gives 3 bytes per motor data packet or 30 bits after adding parity and end bits. 25 of these packets will be sent per second for a data rate of 750 bit/s.

Left Motor Speed	Right Motor Speed	Other Motor Info

Packet of data sent by control computer. 1 byte ea.

This bandwidth is much less than the limit from the competition of 5Mbit/s. That is a huge amount though and is about as much data transmission as a DVD movie. The Matchport can transmit data wirelessly at about 1Mbit/s which is still far more than is needed. The real bottleneck is the link though is the link between the microcontroller and the Matchport. That serial connection maxes out at about 115kbit/s. This is still plenty fast for just transmitting the types of simple commands that we're using. To make use of all the extra bandwidth not being used, it was thought to add a network camera that can connect directly to a wireless network to the robot. A first person view from the robot would be useful for control and it would be easy to add. It wouldn't need to interface with the microcontroller at all and could just be controlled completely over the network using the second IP address available to us.

Communications Diagram
WAN
no delay
5Mbit/s Bandwidth
Control Room

Playing Field

Robot
Control
Computer

Control

This is another section that has grown in importance with the change to making the robot remote controlled. This subsection consists of everything on the operator's end before the communication link. This is mainly all the software running on the control computer. First, the control computer needs to open a standard COM port to establish the connection. Then it receives all the data the robot sends it and displays it nicely for the operator. Trying to make sense of lines of text is a pain so one goal here is to make a good user interface for the operator. After that, it reads in the joystick, determines which motors to turn on and sends that data to the robot.

For the actual control of the robot we've come up with two different methods. The first using two joysticks and linking them directly to the two drive motors. Pushing the left joystick forward or backwards would make the left motor turn forward or backwards with the speed determined how hard it's pushed. The right joystick would work the same way. So to go forward, push both forward. Left, push the right forward and left backwards and so on. This is very simple to implement as no processing needs to be done to the signals from the two joysticks but is more complicated for the operator.

The other method is more indirect using one joystick with X and Y axises. The Y axis will control the forward and backwards movement and the X will control left and right movement. This includes combinations of each axis so pushing the joystick forward and to the left will cause the robot to move forward while turning left. This method is a bit more complicated as some processing has to be done on the joystick inputs to calculate the values to send to the robot and it's more dependent on the robot being able to run both drive motors at the same speed accurately. It should be easier on the operator and be simpler to use however. In the end, we decided to implement both methods and give the operator an option to choose between them so we can see which works best.

Direct Vs Indirect control scheme