## Slide 1: NASA Lunabotics Mining Competition Interim Design Presentation
Team 19: Aleks Fedoriw
Duncan Haldane
Arthur Pack
Michael Pearse
Carlos Ruiz

## Slide 2: Chassis
Material:
  Aluminum 6063
    ¾” Square Tubing
    ¼” Plate
Primary Focus:
  Attachment for Motor/Gearbox Assembly
  Attachment for Excavation/Dumping Systems

## Slide 3: Chassis
Additional Constraints:
  1m x .370m Max Dimensions
  Minimize Weight
Mass Calculations (ProEngineer):
  Volume = 3.33e+06 mm3
  Surface Area = 1.33e+06 mm2
  Density = 2.685e-06 kg/mm3
  Total Mass = 8.95 kg

## Slide 4: Walking
Walking using hip actuated leg
Torque at touchdown: 70 Nm @ 1.5 Hz
Motor: 18V (36V) Maxon RE65 with 50:1 gear reduction
  35 A draw for each motor
  Need 105 A capability

## Slide 5: Leg Design
Semi-circular legs 0.297 m in Diameter, 9cm wide
Need Radial Stiffness of 15,905 N/m
  Pseudo Rigid Body Model
    w = 0.09m; t = 0.00518m

## Slide 6: FEA Simulation
For a 1 kN load
  Vertical tip Deflection: 65.93mm
  K = 1000/0.06593 = 15,167 N/m
Vertical Deflection

## Slide 7: Excavator System
Bucket Chain system
Uses lower plate to hold material while scoops push it along
Swivels on a four-bar linkage
Powered by a single motor

## Slide 8: Bucket System
Uses two power screws to lift bucket
Cable connected to frame forces bucket to dump contents
Lid is hinged to allow contents to dump farther away from the bucket
Very lightweight

## Slide 9: Final Design

## Slide 10: System Power Circuit

## Slide 11: Battery Type
Lithium Ion Polymer | 
Packing | 10 pcs High Power Polymer Li-Ion Cell: 3.7V 10 Ah
Voltage | 37V
Capacity | 10 Ah
Max. Discharging Rate | 70A
Weight | 5 Lb.
Cost | $699 .95

## Slide 12: Sensors
Webcam
Weight Sensors
Bump Sensor

## Slide 13: Main Control

## Slide 14: Wireless Aspects

## Slide 15: MCU

## Slide 16: Controls

## Slide 17: Overall design

## Slide 18: Questions?
?