## Slide 1: Integration of experimental propulsion systems in micro air vehicles
Deliverable: Interim Design
November 9, 2010
Team # 3
Erica Cosmutto
Hunter Metzger
Joel Ware
Kristina De Armas
Michael Isaza
Santiago Baus

## Slide 2: OverView
Introduction
EDF vs Propeller
Final Component Selection
IE Update
Calculated Values
Designs
Center of Gravity
Cost and Weight Analysis
Conclusion
Future Work

## Slide 3: Introduction
Integrate an electric ducted fan into the fuselage of a Micro Air Vehicle (MAV)
Focus on:
  Fuselage design
  Air Flow Inlet/Duct design
  Integrating electronics and fan into the fuselage
Constraints:
  10 lb max
  6 in diameter
  32 in length

## Slide 4: EDF VS Propeller fan
Duct reduces losses in thrust caused by tip vortices
The Ducted fan operated at higher velocity
EDF has a smaller diameter
EDFs are quieter and safer

## Slide 5: Final Component Selection
76mm ID, 80mm OD
22.2V
391g
55A
$129.50
TP8000-6S4PL
22.2V
8000mAh
16C
$509.99
Smart Guide ESC
Up to 44.4V
100A
$120.00

## Slide 6: IE Update
Lean Six Sigma Methodology
  DMAIC process
Define Phase Complete
Measure Phase due November 30th
  Define performance standards
  Establish data collection plan
  Validate the measurement system
  Collect necessary data from existing system

## Slide 7: Values Calculated
Maximum Thrust of 2.2 kg =21.6 N
Ideal Inlet Area= 5.643 in2 (FSA, Fan Sweep Area)
Ideal Exit Area=4.3 in2 (75% of FSA)
Maximum Velocity Exiting Fan=52.478 m/s

## Slide 8: Design 1
Design specified by sponsor
Intake from the bottom of the MAV

## Slide 9: Design 2
Intake on top and bottom
Laminar flow off top surface

## Slide 10: Design 3
Maximize flow intake
Simple design

## Slide 11: Design 4
Uses two side ducts
Smooth intake of air

## Slide 12: Center of Gravity
ESC
110g
Battery
932g
Fuselage
3084g
Fan
391g
Desired
CG
Current
CG
1.92 in

## Slide 13: Cost and Weight Analysis
Component | Cost | Weight
EDF | $129.95 | .862 lbs
Battery | $509.99 | 2.05 lbs
Battery Charger | $109.98 | 
Woodworks LipoSack (Storage) | $34.99 | 
ESC | $120.00 | .242 lbs
Transmitter/ Receiver | $179.97 | .033 lbs
Industrial Strength Velcro | $7.00 | 
TOTAL | $1091.88 | 3.187 lbs

## Slide 14: Conclusion
Four fuselage designs
Initial Calculations and Analysis
Calculated Ideal Inlet and Outlet Areas
Center of Gravity Analysis
Final Component Selection
The team has started work at HPMI

## Slide 15: Future Work
Continue work at HPMI
Produce the first mold
Receive Components
Testing in Comsol and wind tunnels
Measurement of Existing Model

## Slide 16: References
Hobbypartz.com
Thunderpowerrc.com
Hobbytown.com
“The Calculation and Design of Ducted Fans”.Wattflyer.com
www2.nlr.nl/public/facilities/AVET-Info/Content/UK/PropBlades.html
www.sterndrive.info/400_800_cobra_propellers.html

## Slide 17
Calculations: