## Slide 1: Gunnery Control Handle
Group 9: Senior Design
Deanna McKenzie Michael D. Brown William Thornton

## Slide 2: Presentation Outline
Background
Project Introduction
Center Body
Handle Attachment
Haptics
Sensors
Cost Analysis
Conclusion
Future Plans

## Slide 3: Background
Armored Vehicles
  Very expensive pieces of equipment
  Pilots cannot always be trained in the field
  Need for simulators to help train drivers
  There are MANY types of vehicles; hence MANY different simulators

## Slide 4: Project Scope
Design a generic simulator handle
  Reduce Weight
  Make handle interchangeable

## Slide 5: Center Body
Design
Aspects
Two shafts = roll and pitch
Accelerometer for roll and pitch sensing
Top and back detachable
Ribbed for support

## Slide 6: Center Body
Handle bar and ball bearings allow for pitch rotation
Center bar and ball bearings allow for yaw rotation
Pitch
Roll

## Slide 7: Handles
Detachable handles from a Generic center body
  Handles can be removed from the center body
  Handles customized to a different vehicle
M2-Bradley
M1-Abrams

## Slide 8: Handles
Properties of each handle:
  Customized buttons and triggers
  Will connect/disconnect with a keyed shaft
Keyed shaft
Torsion spring
M1-Abrams
handle

## Slide 9: Design Selection for Haptic Response
Opposing Clock Spring
  2 springs per handle
  Customized to each handle configuration
  Slide onto keyed shaft
  Attach to peg on center body
  Held in place by handle
  Cap to allow 150˚ full angle

## Slide 10: Concept for Handle Sensing Methods
Accelerometer
2 dimensional sensing
X-plane measures yaw
Y-plane measures pitch
Attached to handle shaft through center
Circuitry Unknown

## Slide 11: Cost Analysis
Part | Quantity | Supplier | Pr ice ($) | Total Cost ($) | Item Number
Shaft | 1 | McMaster-Carr | 11.35 | 11.35 | 88955K261
Bearings | 4 | McMaster-Carr | 8.72 | 34.88 | 57155K338
Shaft | 1 | McMaster-Carr | 16.66 | 16.66 | 87095K621
Torsion Springs | 6 | McMaster-Carr | 7.88 | 47.28 | 9293K31
Accelerometer | 1 | Dimension Engineering | 22.95 | 22.95 | DE-ACCM2G2
Total $133.12 |  |  |  |  | 
Unknowns include: Wiring for circuitry, Plastics, Hardware

## Slide 12: Final Design

## Slide 13: Future Plans
Meet with Sponsor with prototype
Finalize Design
Plastic material testing
Order Materials

## Slide 14: Questions
???