## Slide 1: Gunnery Control Handle
Group 9: Senior Design
Deanna McKenzie Michael D. Brown William Thornton

## Slide 2: Presentation Outline
Introduction
Mechanical System
Computer Interface
Prototype Design
Proposed Improvements

## Slide 3: Intro: Background
Armored Vehicles
  Very expensive pieces of equipment
  Pilots cannot always be trained in the field
  Need for simulators to help train drivers
  There are MANY types of vehicles; hence MANY different simulators

## Slide 4: Intro: Project Scope
Design a generic simulator handle
  Reduce Weight
  Make handle interchangeable

## Slide 5: Mech: Pro/E Assembly

## Slide 6: Mech: Torsion Springs
Counter-opposing
Constant torsion
Difficulty keeping equilibrium position
Recommend combination with cam system

## Slide 7: Mech: Gears and Potentiometers
Each shaft geared to potentiometer
Pots have large full angle (about 290˚)
Gearing gives shafts small full angle (about 150˚) while still utilizing full angle of pots

## Slide 8: Center Body Layout
4 Bearings
2 Shafts
4 Gears
2 Potentiometers
4 Torsion Springs
1 Microcontroller

## Slide 9: Mech: M1A Gunners Handle
2 Triggers
2 contact switches
1 button switch

## Slide 10: Mech: Handle Attachment
Wire Connections
Handle Connector

## Slide 11: Rapid Prototype: Equipment
Can print models up to 10” x 10” x 12”
Prints with ABSplus thermoplastic
  Production grade
  Printed from bottom up
Soluble supports during printing
  Allows for more complex modeling

## Slide 12: Rapid Prototype: Center Body
Material is layered ABS plastic
Weaker than injection molded ABS
Yields quicker along print planes
Only to be used as prototype

## Slide 13: Rapid Prototype: M1A Gunners Handle
Original handle
No measurements
No pictures
Handle design in Pro/E
Produced from first hand experience and assorted pictures online
Final Handle
ABS printed plastic
2 triggers (2 switches)
1 button switch
http://www.armedforces-int.com/suppliers/afv-sim-ltd.html

## Slide 14: Microcontroller
Arduino Uno Microcontroller
  Open source
  Thirteen digital pins plus ground pin
  6 analog to digital converters
  6 power source options
  USB connectivity/power
  Can be powered by adapter, USB or battery

## Slide 15: Microcontroller: Schematic

## Slide 16
330Ω
330Ω
330Ω
330Ω
330Ω
330Ω
left handle
right handle
6 wires
6 wires
3 wires
3 wires

## Slide 17: Handle Wiring
Wiring moves from the connector to switches inside the handle.
Connector allows for detachable handles

## Slide 18: Prototype: Key Problems and Solutions
Problems
Solutions
Accessibility to center shaft springs is inadequate.
Handles will not always return to equilibrium
Difficulty wiring system
Layered ABS is weak along plastic planes
Allow for access through front of center body
Use torsions springs as well as cam system
Design for wiring pathways within body
Fabricate using injection molded ABS

## Slide 19: Prototype: Cam System Proposal
All aspects of handles can be controlled by different cams
Cam defines equilibrium for each handle
Cams can be lined up next to one another for easy switching between handles

## Slide 20: Cost Analysis
Part | Quantity | Pr ice ($) | Total Cost ($)
Shaft | 1 | 20.25 | 20.25
Bearings | 4 | 8.72 | 34.88
Microcontroller | 1 | 29.95 | 29.95
Potentiometers | 2 | 6.35 | 12.70
Pinion Gear | 2 | 13.05 | 26.10
Gear | 2 | 13.56 | 27.12
6-cond. Wire | 15 ft | 0.31/ft | 4.65
4-cond. wire | 15 ft | 0.37/ft | 5.55
Torsion Springs | 8 | 7.88 | 63.04
Buttons | 6 | 6.95 | 41.70
Total $265.94 |  |  | 

## Slide 21: Acknowledgements
Lockheed Martin; Client
Steve Preston; Client Contact
Jeff Payne; Client Contact
Ernie Morrow; General Dynamics Contact
Dr. Rob Hovsapian; Senior Design Professor
Dr. Jonathan Clark; Faculty Advisor

## Slide 22: Questions?