## Slide 1: Gunnery Control Handle
Group 9: Senior Design
Deanna McKenzie Michael D. Brown William Thornton

## Slide 2: Presentation Outline
Project Scope
Pro E Assembly
Rapid Prototyping
  Equipment
  Center Body
Microcontroller
  Specs
  Schematic
Cost Analysis
Future Plans
  Rapid Prototype Handles
  Complete Assembly
  Optimize Assembly/Design
Schedule
Risk Assessment

## Slide 3: Project Scope
Design a generic simulator handle
  Reduce Weight
  Make handle interchangeable

## Slide 4: Pro/E Assembly

## Slide 5: Rapid Prototyping Equipment
Can print models up to 10” x 10” x 12”
Prints with ABSplus thermoplastic
  Production grade
  Printed from bottom up
Soluble supports during printing
  Allows for more complex modeling

## Slide 6: Center Body: Rapid Prototype
Material is layered ABS plastic
Weaker than injection molded ABS
Only to be used as prototype

## Slide 7: Microcontroller
Arduino Uno Microcontroller
  Open source
  Thirteen digital pins plus ground pin
  6 analog to digital converters
  6 power source options
  USB connectivity/power
  Can be powered by adapter, USB or battery

## Slide 8: Microcontroller: Schematic

## Slide 9: Microcontroller Programming
Programming done in C
Have written preliminary programs to show:
Digital pins are working
  When a button is pressed, an LED light will turn on.
Analog pins are working
  When variable resistor passes voltage threshold, an LED light will turn on.
Currently working on using microcontroller in Visual Basic for a more user friendly GUI

## Slide 10: Cost Analysis
Part | Quantity | Unit Price ($) | Total Cost ($)
Shaft | 1 | 20.25 | 20.25
Bearings | 4 | 8.72 | 34.88
Microcontroller | 1 | 29.95 | 29.95
Potentiometers | 2 | 6.35 | 12.70
Pinion Gear | 2 | 13.05 | 26.10
Gear | 2 | 13.56 | 27.12
6-cond. Wire | 15 ft | 0.31/ft | 4.65
4-cond. wire | 15 ft | 0.37/ft | 5.55
Total $161.20 |  |  | 
Part | Quantity | Unit Pr ice ($) | Total Cost ($)
Torsion Springs | 4 | 7.88 | 47.28
Buttons 1 | 4 | 10.92 | 43.68
Buttons 2 | 2 | 10.92 | 21.84
Hardware | - | - | -
Triggers | - | - | -
Total $112.80 |  |  | 
Future Orders
Ordered
We have currently received no pricing information for rapid prototyping material or services

## Slide 11: Rapid Prototype Handles
Using the same method and machining for the center body
Model for handles to evaluate design
  Trigger holes are the right size
  Placement of electronic wiring
  Fits in the hand comparably to M1-Abrams and M2-Bradley Handles

## Slide 12: Assemble Rapid Prototype
Make sure parts fit together according to design
Evaluate size and feel of the handles and center body
Redesign handles if needed

## Slide 13: Optimize Design
Optimize parts and fabricate with injection molded engineering plastic
Find correct torsion spring loading for each handle design
Finalize code for microcontroller

## Slide 14: Schedule
General Dynamics Trip: Feb. 23
Four Aker: Feb. 23
All parts ordered by: Feb. 25
Microcontroller:
  Digital Button Programming Feb. 28
  Analog (potentiometer) Programming March 4
Handles Printed: March 4
Assembly (w/out microcontroller) March 18
Debugging/Comp. Integration March 18
Full Assembly March 25
Operations Manual/Final Reports April 4

## Slide 15: Risk Assessment
Risks
Possible Solutions
Wiring space in shaft
Internal/External springs
Shaft mount strength
Parts don’t arrive on schedule
2-types of wire
May require redesign
Thicken mount
Use time to plan and reschedule
We are a fair amount below budget as well, so we do have options if something goes wrong.

## Slide 16: Questions
???