## Slide 1: Critical Current Probe
Mid-Point Review
Amy Eckerle
Andrew Whittington
Philip Witherspoon
Team 16
NHMFL
Applied Superconductivity Center

## Slide 2: The Project
Modify existing cryostat probe to conserve the amount of liquid helium, $5/liter of liquid He, used during a critical current measurement test.
Current Leads
Helium level
Cryostat
Voltage tap
Magnet
Sample
Voltage tap wire
Stainless Steel Jacket
Notes: Mention what a critical current measurement is

## Slide 3: Constraints
Constraints
  Test 6-8 samples
  Budget of $4000
  Constant casing diameter
  Minimum length to reach center of cryostat

## Slide 4: Solutions
HTS Leads and support
Poor Conductor of heat
Low thermal conductivity with high electrical conductivity
Great reduction in copper surface area
Prevents copper leads from entering liquid helium bath
G10 Support
HTS Lead

## Slide 5: Solutions
Number of Leads
  Leads are major heat leak
  Maintain 8 samples with 6 leads
Current Leads

## Slide 6: Solutions
Jacket Design
Current Leads
Stainless steel portion
G10 portion
  interrupts thermal conduction of the stainless steel tube

## Slide 7: Problems
Re-design was needed for HTS leads protection
Previous design of sample holder was impractical
  New design was made
Ordering Problems

## Slide 8: HTS Section
High Temperature Superconducting
  Eight tapes will be stacked
  Reduce surface area
Most important section
Fragile
Copper Lead
HTS Lead

## Slide 9: HTS Protection
No HTS Protection
Free hanging, fragile wires
Susceptible to twisting and pulling
Low durability
Protection Requirements
Protect HTS leads
Allow for thermal contraction

## Slide 10: HTS Protection
Spacers
Keeps rods from swinging or touching
Have holes drilled for voltage taps, copper leads, and support rods
Will connect to G-10 casing via holes screws

## Slide 11: HTS Protection
G-10 Support Rods
Prevents rods from twisting
Screwed into top spacer
Clamp placed on bottom spacer will allow for upward motion

## Slide 12: HTS Protection
G-10 Casing
Adds durability
Prevents bending

## Slide 13: Sample Holder Redesign
Reduction in leads required new design
New design features
  Avoidance of bending copper
  Using 6 current leads for 8 samples
  Mounting for spiral sample
Need to order copper for sample holder

## Slide 14: Parts en Route
8 ft current leads (qty. 6)
Current connects (qty. 6)
Copper for sample holder
G-10 Rods (qty. 4)
Stycast

## Slide 15: Machining
Parts Needing Machining
Sample holder
Copper leads
Current connects
Parts Undergoing Machining
G-10 top flange
Spacers
Jacket welding
Guide
Connector
Notes: Be more specific on parts being machined

## Slide 16: Machining
Parts Needing Machining
Sample holder
Copper leads
Current connects
Parts Undergoing Machining
G-10 top flange
Spacers
Jacket welding
Guide
Connector
Notes: Be more specific on parts being machined

## Slide 17: Machining
Parts Needing Machining
Sample holder
Copper leads
Current connects
Parts Undergoing Machining
G-10 top flange
Spacers
Jacket welding
Guide
Connector
Notes: Be more specific on parts being machined

## Slide 18: Machining
Parts Needing Machining
Sample holder
Copper leads
Current connects
Parts Undergoing Machining
G-10 top flange
Spacers
Jacket welding
Guide
Connector

## Slide 19: Machining
Parts Needing Machining
Sample holder
Copper leads
Current connects
Parts Undergoing Machining
G-10 top flange
Spacers
Jacket welding
Guide
Connector

## Slide 20: Machining
Parts Needing Machining
Sample holder
Copper leads
Current connects
Parts Undergoing Machining
G-10 top flange
Spacers
Jacket welding
Guide
Connector

## Slide 21: Machining
Parts Needing Machining
Sample holder
Copper leads
Current connects
Parts Undergoing Machining
G-10 top flange
Spacers
Jacket welding
Guide
Connector

## Slide 22: Machining
Parts Needing Machining
Sample holder
Copper leads
Current connects
Parts Undergoing Machining
G-10 top flange
Spacers
Jacket welding
Guide
Connector

## Slide 23: Machining
Parts Needing Machining
Sample holder
Copper leads
Current connects
Parts Undergoing Machining
G-10 top flange
Spacers
Jacket welding
Guide
Connector

## Slide 24: Testing
Testing can only occur when the final design has been completely finished
Place probe in existing cryostat for regular testing
Compare helium losses with the existing design
Comparing weight

## Slide 26: Questions?