## Slide 1: Critical Current Probe
Progress Report
Amy Eckerle
Andrew Whittington
Philip Witherspoon
Team 16
NHMFL
Applied Superconductivity Center

## Slide 2: Scope
No Updates
Needs Assessment
  Liquid helium is a necessity for superconductivity
Background
  Superconductivity
  Multi-sample probe
  Need for liquid helium
  Unable to modify existing probe
Methodology
  Understand existing probe
  Design more efficient probe
  Order parts
  Testing

## Slide 3: Scope (cont.)
Constraints
  Test 6-8 samples
  Budget of $4000
  Constant casing diameter
  Certain probe length to center of magnet
Expected Results
  Working probe to test samples
  Significant reduction in helium consumption

## Slide 4: The Project
Modify existing cryostat probe to conserve the amount of liquid helium used during a critical current measurement test.
Conserve helium
1 spiral sample
Capability to deliver 1000 amps to samples
Durable

## Slide 5: Probe Layout
Current Leads
Helium level
Cryostat
Voltage tap
Magnet
Sample
Voltage tap wire
Stainless Steel Jacket

## Slide 6: Approach
Identify Major Heat Leaks
  Current leads
  Stainless steel jacket
Reduce Heat Conduction
  Optimizing number of leads
  Removing copper leads from helium bath
    Substitute HTS material
  Replacing lower half of stainless steel jacket with G-10 jacket

## Slide 7: Concepts
HTS Leads and support
Number of Leads
Jacket Design
Ways to Reduce Helium Consumption

## Slide 8: Concepts
HTS Leads and support
Number of Leads
Jacket Design
Ways to Reduce Helium Consumption
Problems Encountered
Redesign of support structure
Solder joints
G10 Casing Design
G10 Support
HTS Lead

## Slide 9: Concepts
HTS Leads and support
Number of Leads
Jacket Design
Ways to Reduce Helium Consumption
  Problems Encountered
  Optimized to six leads for eight samples
Current Leads

## Slide 10: Concepts
HTS Leads and support
Number of Leads
Jacket Design
Ways to Reduce Helium Consumption
Current Leads
Stainless steel portion
G10 portion
  Problems Encountered
  None currently

## Slide 11: Status
Checking the ASC Inventory for Usable Parts
Updating CAD Model
  Lead changes
  HTS casing
  Sample holder
Acquiring and Machining all Parts

## Slide 12: Course of Action
Set up Construction Space
Lab Certifications for all Members
Commence First Phase of Construction Process
  Delegating probe responsibilities
Insulate 22 meters of HTS Material

## Slide 13: Project Timeline
Buffer Says for Unforeseen Problems
Estimated Testing Date: March 2

## Slide 14: Summary
Project is on Schedule
No Major Issues or Setbacks
Starting Construction Next Week
Testing by March 2nd