## Slide 1: Team #2 Solar Car Project Senior Design 2011 – 2012
  Electrical Team:
  Shawn Ryster
  Patrick Breslend
  Greg Proctor
  Jordan Eldridge
Mechanical Team:
Valerie Pezzullo
Bradford Burke
Tyler Holes

## Slide 2: Overview of the Current State of the Project
Current Budget: $1600
Estimated cost of the project $3,652
Protection circuits being fabricated by Dante

## Slide 3: Motor
Presented by: Greg Proctor

## Slide 4
Lemco DC Brushed Motor (LEM200-127)
Rated Voltage 48V
Rated Current 215A
High Torque at low speeds
8.55 kW rated power
Will need a new motor controller.
Cost: $1900

## Slide 5
Kelly Motor Controller - KDZ48201
Input voltage range 18V – 60V
Output voltage 24V-48V
Maximum sustained amperage of 80A
Supports regenerative braking.
Cost: $200

## Slide 6: Motor & Motor Controller Budget and Schedule Risks
Budget Risk
Schedule Risk
Cost of the motor exceeds current budget
Outside sponsorship
  Funds from University
  Envision Credit Union
Ordering the motor takes time
Without funds ordering the motor will be pushed into spring.
Mitigated by ordering and installing motor controller

## Slide 7: Maximum Power Point Tracker
Presented by: Shawn Ryster

## Slide 8: Overall Approach
Purchase Pre-existing MPPT
Build our own converter/MPPT
Pros:
Easy Implementation
Cons:
Much more expensive
Pros:
More Experience with design of converter/MPPT
Minimum Cost
Already Have Microcontroller
Cons:
More design of converter/MPPT

## Slide 9: Boost Converter Topology
L
C
Voltage output increases as duty cycle of switch increases.
Ideal case
Components
Inductor (L)
High Frequency Switch: MOSFET
Diode
Capacitor (C)

## Slide 10: MPPT top level

## Slide 11: MPPT algorithm
Perturb and Observe
Incremental Conductance

## Slide 12: Current and Voltage Transducers
Current Transducer
Tamura S22P015S05
-15A to 15 A
5 V supply
$15.88
Voltage Transducer
LEM USA Inc. - LV 20-P
0 -600 V
15 V supply
$36.60

## Slide 13: Inductor and Capacitor Values
Inductor (1 mH)
Wurth Electronics
744824101
10 A max (DC)
$5.62
Capacitor (1.5 mF)
Panasonic
EET-UQ2C152JA
0 -1600 V
3.75 A ripple current
$4.29

## Slide 14: MOSFET and Diode
MOSFET
IXYS
IXTH11P50
11 A max (DC)
500 V drain to source max
$8.58
Schottky Diode
Vishay
8TQ080PBF
8 Amp Max
80 V reverse breakdown voltage
$1.00

## Slide 15
Risk | Chance | Impact | Cost
Backordered Parts | Low | Med | Low
Programming/Testing Issues | Med | High | None
Part Failure | Low | High | High
Actual Cost | 
Components | $71.97
Mounting/PCB | $50.00
Wiring | $20.00
Total | $141.97

## Slide 16: Solar Array
Presented by:
Patrick Breslend & Jordan Eldridge

## Slide 17: PV Array
Design and Implementation

## Slide 18: PT15-300 Solar Module
Parameters
Voltage (oc): 19.0V
Current (sc): 240mA
Rated Operation
Voltage Rating: 15.4V
Current Rating: 200mA
Module Size
Total Size: 270 x 325 mm
Aperture Size: 240 x 300 mm

## Slide 19: Module Connection Design
Protection Circuit Design
Protection Circuit Design Implementation

## Slide 20: Module and Drill Placement Plan
62 total modules
82 drill holes

## Slide 21: PV Array Placement and Drilling

## Slide 22: PV Array Implementation
Solar mounting tape to boarder the array
High-Temperature spray adhesive to secure
the PV array onto the car

## Slide 23: Implementation of wiring system
Color coding and Inserting tabs
into predrilled holes
Color coded tabs to match previous wiring design from the underside of the lid

## Slide 24: End Result of PV Implementation

## Slide 25: PV Array
Simulation

## Slide 26: 2 Module Series Modeling
Simulink Diagram

## Slide 27: 2 module Series Modeling
Simulink Results
P-V Curve
IV Curve

## Slide 28: Modeling of Entire PV System
Simulink Diagram

## Slide 29: Modeling of Entire PV System
Simulink Results

## Slide 30: Modeling of Entire PV System
Simulink Results

## Slide 31: PV Array
Risks

## Slide 32: Technical Risk: Solar Array
Description:
  Improper mounting of solar array could allow them to be exposed to the elements. This includes wind, precipitation and sun damage.
  Current feedback into a module
Probability: low
  The chances of the vehicle being exposed to bad weather at this stage in the project are low. This is due to the vehicle being stored and only removed for testing in acceptable conditions. The vehicle in the next stage will be given a final protective layer to further protect it from potential damage.
Consequences: Moderate
  In the current stage the solar modules will be held by mounting tape so that testing can be done with ease of removal for damaged modules. There would be a loss of power from the damaged modules but this is just a small technical issues that can be easily fixed.
Solution:
  The solar car will only be run in optimal conditions(means sunny and no chance of rain) and kept indoors and a reasonable temperature when not in use
  There is a protection circuit as described previously to keep the modules safe from current feedback.

## Slide 33: Schedule Risks: Solar Array
Risks:
  Printed circuit-board production could be delayed or have a design flaws.
  The delivery of the diodes in the protection circuit could be delayed
  Damaging existing cells
  No risk in implantation of modules themselves
Probability: Low
Consequences: Moderate
  If the PCB’s aren't completed on time or have flaws, or the diodes aren't delivered on schedule the full completion of the PV array will be delayed but will not impede the progress on the rest of the vehicles design.
  If a cell is damaged it will have to be removed from the system and with no extra cells to replace a damaged one the array current will diminish but have a very small effect on the overall design
Solution:
  In order to ensure that all the PCB’s are completed on time and good quality we are ordering a single unit and inspecting that unit then ordering the remainder units before break so we can inspect and reorder any defective units.
  To make sure the diodes arrive on time the ordering process will have to be completed before the end of the week .
  Damaging existing cells can be avoided by taking extra care around the PV array especially in the handling of the top of the vehicle.

## Slide 34: Budget Risks: Solar Array
Description:
  The existing solar array on the vehicle could get damaged and need replacement and with our budget constraints it would be difficult to continue the project
Probability: Very Low
  With the solar array on the vehicle and proper care is being taken when working around the vehicle the chance for damage is minimal. And with he vehicle in a non working state at the moment the weather is not a factor in damaging the vehicle
Consequences: Moderate
  If the solar panels get damaged they will not be able to be replaced with the current budget but the impact on the car for not having them attached would only cause the current to drop by 250mA for every damaged series set.
Strategy
  The only strategy to have to make sure that the panels don’t get damaged and ensure they stay in a working condition.
TOTAL COST OF SOLAR ARRAY/ PROTECTION CIRCUIT: $175.00

## Slide 35: Battery System
Design and Implementation

## Slide 36: Current VS Previous Designs
Previous
Current
30 LiFePO4 in series
  Producing 96V @ 15 A
15 LiFePO4 batteries in series
2 series sets in parallel
  Producing 48 V @ 30 A
TOTAL BATTERY COST: $0.00

## Slide 37
Battery Management System
Re-using the existing system
  Allows for an easy install
  Proven to work in previous system
Eliminate the risk of completely draining any one battery
  Uses red/green led to show if batteries are in a working condition
  Wont allow the series connected system to operate if a single unit is bad

## Slide 38: Latch/Hinge System
Presented by: Valerie Pezzullo

## Slide 39: Latches Considered
Fixed-Rod Multi-Point Latch
Draw Latch
Double Point Remote Release Cable Latch

## Slide 40: Decision Matrices - Latch
Remote Release Cable Latch |  |  | 
Criteria | Weight | Score | Weighted
Low Cost (ranks high) | 20% | 3 | 0.6
Durability | 10% | 7 | 0.7
Ease of Installation | 20% | 7 | 1.4
Ease of Operation | 30% | 10 | 3
Applicability | 20% | 10 | 2
TOTAL | 100% |  | 7.7

## Slide 41: Decision Matrices - Latch
Draw Latch |  |  | 
Criteria | Weight | Score | Weighted
Low Cost (ranks high) | 20% | 10 | 2
Durability | 10% | 7 | 0.7
Ease of Installation | 20% | 7 | 1.4
Ease of Operation | 30% | 7 | 2.1
Applicability | 20% | 2 | 0.4
TOTAL | 100% |  | 6.6

## Slide 42: Decision Matrices - Latch
Fixed-Rod Multi-Point Latch System |  |  | 
Criteria | Weight | Score | Weighted
Low Cost (ranks high) | 20% | 5 | 1
Durability | 10% | 7 | 0.7
Ease of Installation | 20% | 5 | 1
Ease of Operation | 30% | 7 | 2.1
Applicability | 20% | 9 | 1.8
TOTAL | 100% |  | 6.6

## Slide 43: Final Latch Decision
Latch | Score
Remote Release Cable Latch | 7.7
Draw Latch | 6.6
Fixed-Rod Multi-Point Latch | 6.6

## Slide 44: Hinges Considered
Take-off/Lift Apart Hinge
Piano/Continuous Hinge
Or Custom Continuous Hinge

## Slide 45: Decision Matrices – Hinge
Take-Apart/Lift-off Hinge |  |  | 
Criteria | Weight | Score | Weighted
Low Cost (ranks high) | 20% | 10 | 2
Durability | 10% | 8 | 0.8
Ease of Installation | 20% | 9 | 1.8
Ease of Operation | 30% | 7 | 2.1
Applicability | 20% | 3 | 0.6
TOTAL | 100% |  | 7.3

## Slide 46: Decision Matrices – Hinge
Piano/Continuous Hinge |  |  | 
Criteria | Weight | Score | Weighted
Low Cost (ranks high) | 20% | 3 | 0.6
Durability | 10% | 9 | 0.9
Ease of Installation | 20% | 8 | 1.6
Ease of Operation | 30% | 9 | 2.7
Applicability | 20% | 9 | 1.8
TOTAL | 100% |  | 7.6

## Slide 47: Decision Matrices – Hinge
Custom Continuous Hinge |  |  | 
Criteria | Weight | Score | Weighted
Low Cost (ranks high) | 20% | 2 | 0.4
Durability | 10% | 9 | 0.9
Ease of Installation | 20% | 8 | 1.6
Ease of Operation | 30% | 9 | 2.7
Applicability | 20% | 9 | 1.8
TOTAL | 100% |  | 7.4

## Slide 48: Final Hinge Decision
Latch | Score
Take-Apart / Lift-Off Hinge | 7.3
Piano / Continuous Hinge | 7.6
Custom Continuous Hinge | 7.4

## Slide 49: Final Latch and Hinge Decisions
Piano/Continuous Hinge
Or Custom Continuous Hinge
Double Point Remote Release Cable Latch
Cost: $88.84 + shipping
Cost: $69.97 + shipping

## Slide 50: Risks – Latch and Hinge
Budget
  Low risk:
    Relatively inexpensive compared to other components of car
Technical
  Low risk:
    Frame and latch stability
    Materials used in product are rated for extremely high shear stresses
Schedule
  Low risk:
    Delayed delivery or loss of product has low probability of occurring

## Slide 51: Parking Brake
Presented by: Valerie Pezzullo

## Slide 52: Parking Brake Placement

## Slide 53: Parking Brake Caliper
Wilwood single piston floating Mechanical Spot Caliper
Cost: $76.79 + cost of brake cable (~ $30) + cost of actuating handle (~30) + cost of nuts & bolts + shipping

## Slide 54: Risks – Parking Brake
Budget
  High risk:
    High probability that the budget will not allow room for parking brake components
      Lower priority task
Technical
  Low risk:
    Installation and operation
Schedule
  Low risk:
    Delayed delivery or loss of product has low probability of occurring

## Slide 55: Air Ventilation
Presented by: Tyler Holes

## Slide 56: Vents Considered
Solar Vent
Side-panel scoop
Driver centered hood scoop

## Slide 57: Decision Matrices – Solar Vent
Solar Vent |  |  | 
Criteria | Weight | Score | Weighted
Low Cost (ranks high) | 20% | 3 | 0.6
Durability | 10% | 8 | 0.8
Ease of Installation | 10% | 9 | 0.9
Ease of Operation | 30% | 10 | 3
Applicability | 30% | 7 | 2.1
TOTAL | 100% |  | 7.4

## Slide 58: Decision Matrices – Side Scoops
Side Scoop |  |  | 
Criteria | Weight | Score | Weighted
Low Cost (ranks high) | 20% | 10 | 2
Durability | 10% | 9 | 0.9
Ease of Installation | 10% | 7 | 0.7
Ease of Operation | 30% | 10 | 3
Applicability | 30% | 5 | 1.5
TOTAL | 100% |  | 8.1

## Slide 59: Decision Matrices – Hood Scoop
Hood Scoop |  |  | 
Criteria | Weight | Score | Weighted
Low Cost (ranks high) | 20% | 10 | 2
Durability | 10% | 9 | 0.9
Ease of Installation | 10% | 8 | 0.8
Ease of Operation | 30% | 10 | 3
Applicability | 30% | 8 | 2.4
TOTAL | 100% |  | 9.1

## Slide 60: Final Ventilation Decision
Air Ventilation | Score
Solar Vent | 7.4
Side Scoop | 8.1
Hood Scoop | 9.1
Solar vent too expensive
Difficult side scoop installation and airflow routing
Hood scoop allows for simple solution to budget, installation and location

## Slide 61: Hood Scoop Design
Lightweight fiberglass material
Mesh screen to filter incoming air
Easy routing of air ducts due to centered location
20.75in.
27in.
19.25in.
Scoop stands at about 3.5 in. tall
Closable vent during cold temperatures

## Slide 62: Hood Scoop Placement
Fit in space left between solar array
Allows direct airflow to driver and components
Bolted to frame
Centered in front of the bubble

## Slide 63: Risks – Hood Scoop
Budget
  Low risk:
    Design and fabrication done by team
      Relatively low cost of fiberglass
Technical
  Low risk:
    Possible dirt and bugs coming through vent
Schedule
  Low risk:
    Delay in fabrication or material does not affect other components progress

## Slide 64: Rear Arm and Suspension
Presented by
Tyler Holes & Bradford Burke

## Slide 65: Old Rear Arm/Suspension
U-brackets rotated about bolt causing positive camber
Suspension arm designed for the old on-wheel motor
Not set up for convenient removal or installation

## Slide 66: New Rear Arm/ Suspension
New design is similar to rear arm of a motorcycle
Is designed for new motor and for just a wheel attachment
Allows for adjustment of rear wheel to keep tension in chain or belt

## Slide 67: Risks – Rear Suspension
Budget
  Medium Risk:
    Design and fabrication done by team
      Relatively low cost of Aluminum
Technical
  High risk:
    Problems occurring during operation would cause significant damage
Schedule
  Medium risk:
    Problems would delay attending events and trial runs but not other progress on the car

## Slide 68: Driver Encasement
Presented by Bradford Burke

## Slide 69: Projected Designs
Design 2
Design 1
Design 3
Design 4

## Slide 70: Materials and Mounting
30 in. by 26 in. space for bubble to fit
Polycarbonate plastic
    Clear
    Grey Tinted
    48x48 1/8“ - $183.26
Aluminum channel around the hole on the top
Base of bubble will fit into channel and be bolted in place

## Slide 71: Comsol Simulations 2D
Air flow over a circle
Air flow over the 2 Dimensional design
of Bubble 3

## Slide 72: Comsol Simulations 3D
Velocity Magnitude and Streamlines
of air flow over a sphere

## Slide 73: Comsol Simulations 3D Cont.
Velocity Magnitude and Streamlines
of air flow over chosen design of bubble

## Slide 74: Risk Assesment
Budget
  High risk:
    The materials and forming of the bubble are fairly expensive, only have one chance to make it right
      High priority task
Technical
  Low risk:
    Any errors in design or manufacturing of bubble can affect its functionality in completing the car
Schedule
  Low risk:
    Mishandling of bubble or incorrect

## Slide 75: Schedule