## Slide 1: CanSat Interim Presentation
Group Members: Samuel Rustan,Yasmin Belhaj, Andrew Grant, Andrew Guerr, Maxwell Sandler
Faculty Advisor: Dr. Kamal Amin, Dr. Michael Frank
Technical Advisors: Dr. David Cartes, Dr. Victor DeBrunner
Senior Design Team #18
11/14/2012

## Slide 2: Competition Background
American Institute of Aeronautics and Astronautics (AIAA) organize design-build-launch competition
Simulate satellite entering planet atmosphere
Gathers flight data and safely delivers a sensor payload to the planet’s surface
Main Components of CanSat
  Payload that secures the sensor (a hen egg)
  Container that encloses the payload from ascent to initial descent

## Slide 4
Phase 1: Passive Braking, at 670 m, uses streamer or parachute to reduce velocity to 20 m/s
Phase 2: Active Braking autonomously engages at 400 m when payload is released from container
Phase 3: How to secure the “sensor”
Telemetry and communication specifications
Additional requirements
  Weight, mass, shape of CanSat
  Limitations on methods of braking
  Selectable objective (camera v force sensor)

## Slide 5: Previous Gantt Chart

## Slide 6
Round Parachute
Square Parachute
Parasheet
Streamer
Fixed, Rigid
Rotational, Rigid
Rotational, Semi-rigid
Compressed Gas
Electric Motor
Buoyant Neutral Fluid
Dough/Foam Enclosure
Flexible Membrane Clamp
Phase 1
Phase 2
Phase 3
Concept Generation Review
Expense

## Slide 7: Phase 2 Generated Concepts

## Slide 8
Model Concept Development
Image 2

## Slide 9
Outputs:
Accurate prediction of the objects decent
  Verified by experiment
Determines parachute or streamer size, given terminal velocity
Core code will be applied to subsequent phases
Model Application
Decent Prediction
Figure 1

## Slide 10: Phase 1 Experiment “Parachute vs. Streamer”
Phase 1 Decision Matrix |  |  |  |  |  | 
 | Drag Coefficient (0.2) | Small Size (0.1) | Low Wind Drift (0.3) | Low Complexity (0.2) | Low Cost (0.2) | Total
Flat Streamer | 1 | 1 | 5 | 5 | 3 | 3.4
Folded Streamer | 2 | 2 | 4 | 4 | 4 | 3.4
Parasheet | 3 | 3 | 3 | 3 | 5 | 3.4
Round Parachute | 5 | 5 | 1 | 1 | 1 | 2.2
Square Parachute | 4 | 4 | 2 | 2 | 2 | 2.6
Purpose
  Test Model
  Aid in Phase 1 decision

## Slide 11: Phase 1 Experiment “Parachute vs. Streamer”
Independent Variables
  Mass
  Height
  Chute/Streamer
Dependent Variables
  Time
Required Number of People
Iterations

## Slide 12: Parachute Vs. Streamer Results
Model Accuracy
  Parachute: experimental data fit model
  Expected more drag for streamer
    Difficult to determine drag coefficient
Using the model to determine size
  A streamer would be over 5 times larger.
  Decision
Chart: Experimental Data Vs. Model
| 0.292 | 0.292 | 0.292 | 0.292 | 0.292 | 0.292 | 0.292 | 0.292 | 0.292 | 0.292
Parachute 1 | 1.8 | 1.7 | 2.7 | 2.7 | 2.6 | 2.4 | 2.4 | 2.3 | 2.7 | 2.5
Model P1 | 2.46
Parachute 2 | 1.9 | 2 | 1.9 | 1.7 | 2.1 | 1.9 | 1.9 | 1.6 | 1.9 | 2.1
Model P2 | 1.8
Steamer | 1.5 | 1.5 | 1.7 | 1.2 | 1.7 | 1.5 | 1.4 | 1.1
Model S | 1.62

## Slide 13: ECE Systems Design
Microcontroller
Flight Software
XBEE
Tx/Rx
Altimeter
Force Sensor/Accel.
GPS
Audible Locator
Battery
Ground Station
Laptop
Flight Software
XBEE
Rx/Tx

## Slide 14: ECE Component Selection
Description | Range (km) | Power Req. (mW) | Cost ($US) | Configuration
Pro-802.15.4 Series 1 (S1) | 1.6 | 63 | 32 | Point-to-point (easily configured)
DigiMesh Series 2 | 3.2 | 63 | 36 | Mesh Network (more difficult)
ZigBee SMT Series 2 | 3.2 | 100 | 48 | Point-to-point (configuration more complex than S1)
802.15.4 Series 1 meets requirements
  Range requirement
  Ease of implementation/configuration

## Slide 15: ECE Component Selection
Description Priority Factor | Range 4 | Power Req. 3 | Cost 2 | Configuration 1 | Weighted Total
Pro-802.15.4 Series 1 (S1) | 1 | 3 | 3 | 3 | 10
DigiMesh Series 2 | 3 | 3 | 2 | 1 | 6.3
ZigBee SMT Series 2 | 3 | 1 | 1 | 2 | 4.2
XBEE Series 1, Decision Matrix

## Slide 16: Website & File Management
    Website available
    Contains meeting minutes,
    calendar
    deliverables, other information
    http://eng.fsu.edu/me/senior_design/2013/team18/
Group email address set up at fsucansat13@gmail.com
  Emails to this address are forwarded to each team member
  Google docs folder used as central repository for documents
  Google calendar used to keep track of meeting times and deadlines

## Slide 18
Funding
Income and Expenses |  |  |  | 
Sponsor Name | Funds Received | Funds Pending | Equipment Purchased | Cost
ECE Department | 200 | 0 | 2 xbee radios | 84.81
Private Donation | 0 | 750 | 2 rocket parachutes | 4.28
Dr. Shih | 200 | 800 | Can of Oats, Fishing Line, Ribbon | 8.75
State Farm | 0 | 250 | Can of Oats | 3.39
Total Funding | 400 | 1800 | Total Expenses | 101.23
Total Available Funds | 298.77 |  |  | 

## Slide 19: References & Acknowledgements
This source
That source
This person/org
That person/org