## Slide 1
CanSat Competition
Belhaj, Y., Grant, A., Rustan, S., Sandler, M., Guerr, A.
Dr. David Cartes and Dr. Victor DeBrunner
Design a canister satellite to protect a sensor payload
Must weigh 700 g with a tolerance of 10 g
Fit inside the cylindrical rocket compartment with diameter 130 mm and height 250 mm
From deployment at apogee to 400 m, the CanSat must fall at 20 m/s using a parachute
From 400 m, the CanSat deploys an aero-braking structure that will limit the velocity to below 20 m/s
CanSat must telemeter GPS data, altitude, pressure, temperature, battery voltage, flight state and time
Upon ground impact, an impact force measurement is taken and stored for later retrieval
Total cost of final product must be under $1000
Competition Objectives
Launch Configuration
Payload connected to container via separation mechanism
Designed with proper clearance for rocket payload compartment
Container protects payload during launch and release
Bosch™ BMP085 : Press/Temp.
GlobalTop™ FGPMMOPA6C : GPS Module
Analog Devices ADXL326 : Accelerometer
Impact force calculated from the mass and acceleration upon impact (F=ma)
Telemetry Sensor System
GPS Module
Press/Temp
Accelerometer
Microcontroller
XBEE RF Transmitter
(CanSat)
Data
Power
RF Data
Battery
XBEE RF
Receiver (Ground Station)
Ground Control Station (Laptop)
USB/FTDI
2.4 [GHz]
ADC
Pre-Launch
Preflight Briefing
Integrate CanSat into Rocket
Final Systems Check & Power On
CanSat Deployment & Initiate Telemetry
Ground Impact, End Telemetry
Parachute Deployment & Container-Payload Separation
CanSat Recovery
Post Flight Analysis
Data Retrieval
Launch
Post-Launch
Mission Sequence of Events
Separation Mechanism
Separation Mechanism connects container to payload
Consists of a motor, open ring attached to the top of the payload and an eyebolt attached to the inside of the container
At 400m the separation mechanism will activate
Payload will drop out of container
Eye-Bolt
Open Ring
Motor
Aero-Braking Structure
Once activated, will increase effective area by 5 times
The aero-braking structure holds the supports that will absorb most of the impact force
Sensor (egg) protected using polystyrene beads
Supports
Egg
Separation Mechanism
Released Aero-Brake
Flight Software Flow Diagram
Begin Signal Transmission
Received?
Check Altitude
Determine State
Deploy DCS
Read Sensors
Transmit Telemetry
Start Beeper
Altitude 400m And State 3?
2s Since Last Transmission?
Landed
(State 5)?
NO
NO
YES
NO
YES
YES
YES
NO