## Slide 1: CanSat Presentation
Yasmin Belhaj (ME)
Andrew Grant (ME)
Andrew Guerr (CE)
Samuel Rustan (EE)
Maxwell Sandler (ME)
Technical Advisors: Dr. David Cartes, Dr. Victor DeBrunner
Course Instructors: Dr. Kamal Amin, Dr. Michael Frank
ME Senior Design Team #18
April 18, 2013

## Slide 2: Outline
Competition Overview
Design Specifications
Concept Generation and Selection
Final Design
Manufacturing and Assembly
Operation and Reliability
Testing and Results
Conclusion

## Slide 3: Competition Overview and Design Specifications
Belhaj

## Slide 4: Competition Overview
  Design a container/payload system to be launched via rocket and develop autonomous descent control strategy to safely land CanSat
Main objective
  Deliver the payload safely to the ground
Secondary objective
  Collect telemetry data & impact force calculation

## Slide 5: Mission Sequence of Events
Pre-Launch
Preflight Briefing
Integrate CanSat into Rocket
Final Systems Check & Power On
CanSat Deployment & Initiate Telemetry
Ground Impact, End Telemetry
Parachute Deployment & Container-Payload Separation
CanSat Recovery
Post Flight Analysis
Data Retrieval
Launch
Post-Launch

## Slide 6: CanSat Sample Specifications
Mass must be 700 g
Material limitations
Geometric constraints due to rocket bay size
Descent Control Strategies limited
Telemetry
  GPS data
  Altitude
  Air temperature
  Battery voltage
  Flight software state
Deliver detailed presentations to NASA/AIAA representatives

## Slide 7: Concept Generation and Selection
Passive Braking Method
Separation Mechanism
Aero-braking Structure
Sensor Protection
Microcontroller
GPS, Sensors, Radio
Battery
Grant and Rustan

## Slide 8: Descent Control Strategies
Round Parachute
Parasheet (Concept Selected)
Diameter: 7.5in
Streamer
Spring Loaded Rods (Concept Selected)
Deployable Exterior Panels
Telescoping Arms
Passive Braking Criteria
Drag coefficient Wind Drift Potential Stability
Aero-braking Structure Criteria
Reaction time Number of Moving Parts Structural Integrity
Notes: Round Parachute
  Pros: Drag coefficient 1.5 High stability, Compact
  Cons: High wind drift potential
Parasheet (Concept Selected)
Pros: Simple, Compact, Drag Coefficient 0.75
Cons: High wind drift potential, less stable
Streamer
Pros: Low Wind Drift Potential, Simple
Cons: Drag Coefficient 0.14 – 0.4
Spring Loaded Rods (Concept Selected)
Torsional springs open rods/fabric fastened at base.
Pros: Lightweight, Easy deployment
Cons: Structural Integrity
Deployable Exterior Panels
Rigid panels open using motor.
Pros: Durable
Cons: Weight, Power requirement
Telescoping Arms
Fabric connected at center and tips will extend using linear actuator.
Pros: Large area, Max drag
Cons: Complex, Lengthy deployment time

## Slide 9: Container-Payload Separation and Sensor Protection
Linear Release
Rotational Release (Concept Selected)
Trap Door
Memory Foam
Polystyrene Beads (Concept Selected)
Dough
Separation Mechanism Criteria
Reaction time Number of Moving Parts Structural Integrity
Sensor Protection Criteria
Cost Density Efficacy
Notes: Linear Release
Pros: Few parts, easy manufacturability
Cons: Slow reaction time
Rotational Release (Concept Selected)
Pros: Proven technique, Inexpensive
Cons: Slow reaction time, Fabrication considerations
Trap Door
Pros: Provides structural support
Cons: Multiple moving parts, heavy
Memory Foam: costly, high volume, light, poor under heat
Dough: Variable density, cheap, Inconsistent properties
Polystyrene Beads: relatively high density 1050-1120kg/m3, Cheap, light

## Slide 10: Sensor Selection
Telemetry Sensors
Bosch™ BMP085, Pressure/Temperature Sensor Selection criterion:
    Precision: ± 0.25m, ± 2.0 ºC
    Reliability: vetted by many users
    Cost: $20
GlobalTop™ FGPMMOPA6C, NMEA GPS Module Selection criterion:
    Reliability: -165 dBi sensitivity
    Low power: 20 mA current draw
    Cost: $40
Analog Devices™ ADXL-326, Accelerometer
Selection criterion:
    Range of measurement: ±16g
    5v logic ready, via onboard regulator
    cost: $18

## Slide 11: Communication Selection
Data Handling and RF Communications
Xbee Pro™ Series 1, 802.15.4 (Digi Int’l)
Selection criterion:
    Selection restricted by competition
    Series 1 point-to-point communication
    Compatible with Adafruit™ breakout kit
    Advantageous for breadboard proto-typing
Arduino Pro Mini™ Microcontroller
Selection criterion:
    Size: 18x33mm, essential due to size limits
    Handles power demand of all connected devices, ADC, I2C, Serial, Analog, Digital
    Open source platform
    Code is easily migrated from other Arduino environments (Uno, Duo, etc)

## Slide 12: Battery/Voltmeter Selection
Electrical Power System
Energizer 2CR5, 5v, Li/MnO2
Selection criterion:
    High energy density, low weight
    High discharge current current (1500 mA)
    Capacity exceeds need by factor of 3
    Rated voltage output ensures power delivery
1.5 MΩ

## Slide 13: Final Design Configuration
Sandler

## Slide 14: Launch Configuration
Egg Compartment
Electronic
Components
Shelving
Separation
Mechanism
Parachute
Aero-braking
Structure
Container
Payload
Notes: Explain selection of each subsystem:
Container is the entire length of structure. Made of plastic, it is open on the bottom.
Payload is the portion inside that houses the electronic components and the raw egg.
Parachute was selected by conducting an experiment on the braking efficacy and ease of implementation of parachutes and streamers for this application. The diameter of the parachute was calculated to achieve the desired 20 m/s at 400m.
While under descent of parachute, the payload will detach from the container via this separation mechanism. A motor will provide the rotation of this ring to allow the payload to fall from out from the bottom.
The aero-braking structure is secured in its launch configuration, surrounding the payload. Support rods connect the top and bottom portions of the aero-braking structure to the payload.
Electronic components are in the top portion of the payload, and the egg is housed near the bottom.

## Slide 15: Deployed Configuration
Specifications
Mass: 700 g
Height: 220 mm
Width: 110 mm
Parachute: D = 175 mm
Aero-Structure: D = 500 mm
Support rods
Tension Wires
Aero-Braking Structure
Notes: Rocket bay dimensions: 130mmx250mm
Based on diameter of wings: Velocity at ground:

## Slide 16: Manufacturing and Operation
Sandler and Rustan

## Slide 17: CanSat Fabrication
Mechanical Design Criteria
Material/Part Acquisition Lightweight Low Radio Interference Inexpensive

## Slide 18: Payload Fabrication
Aero-braking top and bottom – 3D printed ABS
Payload Envelope – Modified polyethylene bottle
Torsion springs allow quick and reliable opening
Deployed via heating element at 400 m
Structural rods made of wood
Structural rods attached to aero-braking top and bottom with screws
Separation mechanism on top of aero-braking structure

## Slide 19: Electronic Component Fabrication
Components mounted on laser cut acrylic disks using perf-boards
Pressure/Temperature Sensor and Accelerometer
GPS Module
Microcontroller and XBEE
Antenna
Battery

## Slide 20: Integration of Electrical Components
Level 1
Telemetry Sensors
Level 2
Data Handling & Communications
Level 3
Electrical Power System
Notes: -Multi-Level Electronics Arrangement
-Permanently Affixed to Payload Half
-Rigid shelves made of plastic

## Slide 21: System of Operation
Secure Egg Inside Payload Envelope and Assemble Payload
Place in Launch Configuration. Telemetry Data Transfer to Ground Station.
Launch and Eject at Apogee.
Parachute Deployment. 20m/s Decent from 670m.
Altimeter Reads 400m
Separate from Container, Engage Aero-Braking.
Decent Until Impact in which Force of Impact is Recorded.
Retrieve Payload and Force of Impact Data.
Locate Payload through Visual Sight and Audible Noise.

## Slide 22: Subsystems Operation
Bosch™ BMP085 : Press/Temp.
GlobalTop™ FGPMMOPA6C : GPS Module
Analog Devices ADXL326 : Accelerometer
  Impact force calculated from the mass and acceleration upon impact (F=ma)
Telemetry Sensor System
GPS Module
Press/Temp
Accelerometer
Microcontroller
XBEE RF Transmitter
(CanSat)
Data
Power
RF Data
Battery
XBEE RF
Receiver (Ground Station)
Ground Control Station (Laptop)
USB/FTDI
2.4 [GHz]
ADC
Bosch™ BMP085 : Press/Temp.
GlobalTop™ FGPMMOPA6C : GPS Module
Analog Devices ADXL326 : Accelerometer
  Impact force calculated from the mass and acceleration upon impact (F=ma)
Telemetry Sensor System
GPS Module
Press/Temp
Accelerometer
Microcontroller
XBEE RF Transmitter
(CanSat)
Data
Power
RF Data
Battery
XBEE RF
Receiver (Ground Station)
Ground Control Station (Laptop)
USB/FTDI
2.4 [GHz]
ADC
Bosch™ BMP085 : Press/Temp.
GlobalTop™ FGPMMOPA6C : GPS Module
Analog Devices ADXL326 : Accelerometer
  Impact force calculated from the mass and acceleration upon impact (F=ma)
Telemetry Sensor System
GPS Module
Press/Temp
Accelerometer
Microcontroller
XBEE RF Transmitter
(CanSat)
Data
Power
RF Data
Battery
XBEE RF
Receiver (Ground Station)
Ground Control Station (Laptop)
USB/FTDI
2.4 [GHz]
ADC
Bosch™ BMP085 : Press/Temp.
GlobalTop™ FGPMMOPA6C : GPS Module
Analog Devices ADXL326 : Accelerometer
  Impact force calculated from the mass and acceleration upon impact (F=ma)
Telemetry Sensor System
GPS Module
Press/Temp
Accelerometer
Microcontroller
XBEE RF Transmitter
(CanSat)
Data
Power
RF Data
Battery
XBEE RF
Receiver (Ground Station)
Ground Control Station (Laptop)
USB/FTDI
2.4 [GHz]
ADC
GPS Module
Press/Temp
Accelerometer
Microcontroller
XBEE RF Transmitter
(CanSat)
Data
Power
RF Data
Battery
XBEE RF
Receiver (Ground Station)
Ground Control Station (Laptop)
USB/FTDI
2.4 [GHz]
ADC
Audible Locator

## Slide 23: Testing, Results, Reliability
Aero-braking Deployment
Separation Mechanism
Telemetry and Electronics
Flight and Ground Control Software
Rustan and Guerr

## Slide 24: Separation and Deployment
Unable to test in operation conditions
Test individual components
Parachute
  Test confirmed validity of model
Separation Mechanism
  Successfully detached payload from container
Aero-braking
  Manually deployed structure

## Slide 25: Telemetry Testing and Results
Test Result:
OK
Test Result:
Inconclusive
Test Result:
OK
Test Result:
OK
Competition Req
Force Sensor
Accelerometer
100 Hz sample rate
Press./Temp.
GPS Module
XBEE Pro Series 1
Competition Req
Altitude Sensor
Competition Req
GPS NMEA Data
Competition Req
XBEE Series 1 or 2
0.25 m precision
NMEA std. output
2.4 GHz
RF LOS ~1km

## Slide 26: Reliability
Digital Communications (XBEE, RF), Link Margin
Transmitter
18 dBm
Antenna
2.1 dB
Cable
-0.5 dB
Transmission in Air
-100 dB
Antenna
2.1 dB
Cable
Receiver
-100 dBm
-1 dB
XBEE Receiver
Sensitivity: -100 dBm
Received Power: -72.5 dBm
Link Margin: -28 dBm
Software Error Handling
Received Signal
Graphical Display
Output to File
Data Reliability

## Slide 27: Software Testing and Results
CanSat Flight Software
Telemetry Sensors
Flight Software
Serial
I2C
Analog
Telemetry Packet
XBEE RF Transmitter
(CanSat)
Altitude
FSW State
Ground Control Software
Telemetry Packet
Telemetry Packet
XBEE RF
Receiver
USB/FTDI
Ground Station Software
Graphical Display
Output to File
Parsed
Telemetry Data
System Ran for over 1 hour
System Ran for over 1 hour

## Slide 28: Discussion and Conclusions
Belhaj

## Slide 29: Project Budget
Revenue |  | Expenses | 
Funding Source | Funds Received | Procured | Expense Amount
ECE Department | $200.00 | ECE Components (Telemetry) | $300.00
Private Donation | $750.00 | Mechanical & Structural | $175.00
Dr. Shih | $1000.00 | Shipping | $25.00
State Farm | $250.00 |  | 
Total Funds Generated | $2200.00 | Total Procurement Expenditures | $500.00
Total Available Funds Remaining | $1700.00 |  | 

## Slide 30: Competition Benchmarks
Delivered Preliminary Design Review (PDR)
  Feedback: Scored 92% from AIAA/NASA Panel
Scheduled Delivery for Critical Design Review (CDR)
Competition Date: June 8, 2013
Post-Flight Review: June 9, 2013
Notes: It may be smart to set this up so each checklist or check box “Appears” with a separate mouse click. Otherwise big lists like these can be overwhelming to look at.

## Slide 31: Conclusions
Physical prototype manufactured within competition specifications
Telemetry sensors tested and integrated
Flight Software and Ground Station Software completed
Electrical power system and RF communications are operational
Total budget under $600
All competition requirements have been met.