## Slide 1: Team 6: Autonomous Aerial Vehicle
Imaging Processing
Camera
Voltage Regulator
Aileron Servo
GPS
11.1 Voltage DC Battery
Radio Transmitter
Autopilot System
Gimbal Servo
Throttle Servo
Elevator Servo
Rudder Servo
Video Transmitter
Ardupilot Mega 2.5
  3 axis gyro
  Accelerometer
  Magnetometer
  Barometer
  Arduino compatible
3DR Radio Telemetry Kit
  915 MHz
  20dBm transmit power
  250 kbps air data rate
  Adaptive time division multiplexing
  Built in error correcting code
  Approx. 1 mile range
3DR GPS uBlox LEA-6
  5Hz update rate
  3.3V regulator
  I2C EEPROM for configuration storage
Navigation System
4.8 V Battery
  Supplies power to APM and autopilot servos
  Rechargeable
  NiMH
11.1 V Battery
  Supplies power to image processing hardware
  Rechargeable
  Lithium Polymer (Li-Po)
Power System
Mechanical System
Motor/Propeller
  4 Stroke/Single Cylinder Magnum XL Fuel Engine
  15x6” APC Propeller
  16 OZ Fuel Tank + 6 OZ Additional Tank
  1 Damping Square Pad (Firewall Insulation)
Gimbal System
  2 Futaba 180° Standard Servos
  3 Machined and Bended Aluminum Parts (2 U Shape, 1 L Shape, Designed in Pro/e)
  1 Damping Square Pad
  1 Small U Bracket (Holds Camera)
  2 Servo Control Horns
  1 Aluminum Screw Hub
Flight Controllers
  2 Futaba Servos (Elevators Control)
  2 Futaba Servos (Ailerons Control)
  1 Futaba 180° Servo (Throttle Control)
Camera
Transmitter
Transmitter
Receiver
Radio
USB Encoder
Communications Interface
Image Processing Hardware
  Asus Laptop Computer
    Intel core i5 dual core processors
    4 GB ram memory
  Sony KX700-SHQ Camera
    700 TVL resolution
    Total Pixels: 1020x508
Image Processing Software
  OpenCV – Computer Vision Libraries
    C++ Language
    MS Visual Studio Design Environment
Wireless Video Communication
  TX-V584 Transmitter – 5.8GHz
  R5800DX Receiver – 5.8 GHz
  Composite-to-USB converter