## Slide 1: Senior Design : Shape Conformable Battery Pack
Sponsor: Dr.Zheng
Advisor: Dr.Shih
Team Members:
Jenna Pine
Niraj Thakker
Jianchen Yu
David Goss
Roberto Moutran
Brian Rainbeau

## Slide 2: Battery CRASH COURSE

## Slide 3: Project Description
Objective | Constraints
Build a battery that can be integrated into the wing of a UAV system Develop uniquely shaped battery or formable battery The battery must satisfy the power need of the RC plane Battery is to be detachable for charging | Limited project Budget Limited research or experience available Battery must not explode or catch fire Enough power must be supplied for at least a 5 minute flight without switching batteries or recharging
What’s the project about?

## Slide 4: House of Quality

## Slide 5: Introduction
Cathode sheets consist of Lithium Iron Phosphate () spread over an Aluminum Sheet
Anode Sheets consist of graphite spread over a copper sheet
What is a lithium pouch cell battery?

## Slide 6: Design Concept for battery
Create many thin layered batteries and seal them independently
Pros
  Easy to seal
  Making the batteries thin increases their bendability
Cons
  Bending pouches may result in loss of electrolyte conductivity
  Sharp bending angle may impair electrolyte flow
Concept 1: Thin C-Shaped Pouches

## Slide 7: Design Concept for battery
Concept 2: Single Pouch
  Require different size anode and cathode sheets
Pros
  True conformability
Cons
  High risk of shorting the battery
  Vacuum sealing will be difficult due to the shape of the pack.

## Slide 8: Design Concept for battery
Concept 3: Individual Cell Pouches
Make individual batteries and connect them in series/parallel
Pros
  Easiest to manufacture
  No loss of electrolyte conductivity from bending
Cons
  Longer manufacturing time
  Not the most creative design

## Slide 9: Design Concept for Plane
Wing over Body | Wings to the side
Pros More Support for the heavy wings Having a single wing makes the attachment and detachment process easier Conformable battery placement is more flexible Cons Support rods add additional weight, which increase the power requirement Rods will also increase the induced drag | Pros Less induced drag Weigh’s less, since there are no additional support components Cons Attachable/detachable wing will be unstable Less flexibility for placing the conformable battery

## Slide 10: Analysis of the airfoil
Assumptions
  Thin Air Foil (To use Kutta-Condition for coefficient of Lift)
  Laminar Flow
Experimental Analysis
  Placing the airfoil in the wind tunnel
  Computing lift at different angles of attack
Theoretical Analysis
  Use 2-D Finite Element Model for a flow over an airfoil
  Use natural boundary condition to set up the model
How are we going to analyze Lift on the airfoil?

## Slide 11: Selection of battery Material
Two choices : Lithium Ion and Lithium Solid Polymer.
  Light-weight, Rechargeable and High capacity
What kind of Lithium Battery are we going to choose?
Lithium Ion | Lithium Polymer
Pros Commercially available materials Access to battery lab Cons Lower specific energy Less shape conformable | Pros High specific energy Shape conformable Cons Materials are harder to find No production facility available
Since Lithium Ions materials are readily available, Lithium Ion will be selected

## Slide 12: Selection of battery Material
Three Prevalent types of Lithium Ion Battery cathode.
  Lithium-cobalt dioxide (LiCoO2)
  Lithium-manganese oxide (LiMn2O4)
  Lithium iron phosphate (LiFePO4)
Of these three LiCoO2 and LiFePO4 offer higher specific energy, but LiFePO4 is roughly half the cost of LiCoO2 (Iron is more common than cobalt)
Choices for ready made Anode and Electrolyte materials were limited to Graphite and Lithium Salt (Lithium hexafluorophosphate)
Types of Lithium Ion Batteries

## Slide 13: Analysis of battery material
The plane is equipped with a 11.1V, 3200mAh battery which weights 309 g
How much material is needed to produce the required power?
We need 4254cm2 of each electrode and 102.81g of electrolyte
Electrode | Volts | Capacity (mAh/cm2) | material to achieve 3200mAh (cm2) | material to achieve 3200mAh, 11.1V (cm2) | anode + substrate weight per cm2 (g) | cathode + substrate weight per cm2 (g) | Electrode weight needed total(g) | Electrolyte needed total(g) | 3200mAh 11.1V cell weight no package (g)
LiFePO4 | 3.45 | 2.42 | 1322.31 | 4254.40 | 0.03 | 0.02 | 205.63 | 102.81 | 308.44

## Slide 14: Summary
Based on house of quality we choose
For battery housing
  Concept 1: Thin-C shaped Pouches
  Concept 3: Individual Cell Pouches
For plane
  Concept 1: Wing over the body
For battery material(Cathode)
  LiFePo4
What designs did we choose?

## Slide 15: Future Works
Analyzing the power output of each of the battery shape concepts
Analyzing the placement of the battery in the wing
Designing various concepts to attach and detach the wing from the plane
Analyzing different combinations of series and parallel connection to obtain the required output
What’s next?

## Slide 16: References
1Amin, D. (2013, August). EML4551C-Senior Design Project 1 . Retrieved September 22, 2013, from Blackboard: https://campus.fsu.edu/webapps/portal/frameset.jsp?url=%2Fwebapps%2Fblackboard%2Fexecut e%2Flauncher%3Ftype%3DCourse%26id%3D_6389491_1%26url%3D
2Ismail, M. H. (2003). Designing lithium ion batteries for high power applications. PECon 2003 National Proceedings, (pp. 289 – 291).
3Kam, K. C. (2012). Electrode Materials for Lithium Ion Batteries. Material Matters.
4Linden, D. (2002). Handbook of Batteries. New York: McGraw-Hill.
5Server Experts. (2011). LiPo Batteries and Charging for your Model RC Airplane. Retrieved September 21, 2013, from L.I. Foam Flyers: http://www.longislandelectricrcairplanes.com/learnbatteries.php
6Unknown. (2010, October). Learn about Batteries. Retrieved September 21, 2013, from Battery University: http://batteryuniversity.com/learn/article/is_lithium_ion_the_ideal_battery
7Unknown. (2012). BYD Company Limited. Retrieved 10 19, 2013, from http://bydit.com/doce/products/Li-EnergyProducts/
8Unknown. (2013, 10 20). Apprentice S 15e RTF. Retrieved from HobbyZone: http://secure.hobbyzone.com/EFL3100.html
9Zheng, H., Liu, G., Crawford, S., & Battaglia, V. S. (2010). Fabrication Procedure for Lithium-ion Rechargeable Coin Cells. Berkeley: Lawrence Berkeley National Laboratory.

## Slide 17: Questions??