## Slide 1: Senior Design : Shape Conformable Battery Pack
Sponsor: Dr.Zheng
Advisor: Dr.Shih
Team Members:
Jenna Pine
Niraj Thakker
Jianchen Yu
David Goss
Roberto Moutran
Brian Rainbeau

## Slide 2: RECAP
Decided to go with the over the
body style wing design
  Give us most stability
  Keep weight centered
Using lithium ion battery material
  Not able to pursue lithium solid polymer
  Using liquid electrolyte battery

## Slide 3: Battery shape
C-shape battery pouch
  Give conformability to wing
  shape
Foldable battery
  Allow battery to fold into different shapes

## Slide 4: Battery information
Wingspan: 38.6 in (980mm)
Battery: 1000mAh 7.4V Li-Po (included with RTF)
Li-Ion Battery Cathode - Aluminum foil double coated LiFePO4
Li-Ion Battery Anode -Copper foil double side coated CMS Graphite
Electrolyte LiPF6 for LiMn2O4/LiFePO4 Lithium-ion battery

## Slide 5: General process
Secondary Inputs
Primary Inputs
Outputs
Function
Primary Inputs: power requirements of the device
Secondary Inputs: material-specific properties
Outputs: total material required to meet power requirements and overall battery weight

## Slide 6: Excel function
Primary Inputs: desired current (mAh) and voltage (V)
Secondary Inputs: material-specific properties
Outputs: total area, total battery weight, number of cells

## Slide 7: Excel function
Assumptions:
  Weight of separator paper is negligible
  Electrolyte weight is cathode plus anode weight divided by 2
Limitations:
  Cells have to be of the same size
  Cells are connected in series

## Slide 8: Sealing process
Existing sealing process
The flexible packaging is a five-layer film
Before sealing flexible packaging films, the films will be punched into a groove with certain depth to put the lithium battery.
When sealing, The PE and PP layers of two sides of the film will be melted into one.

## Slide 9: Sealing process
With different combinations of batteries, they can fit into different spaces.
Seal along the red dashed lines.

## Slide 10: Battery Properties
Voltage requirement for Plane = 7.4V
LiFePO4 provides 3.45 V
Connect cells in series.
Voltage output = 10.35 V
Will use a resistor to reduce the voltage to 7.4V
Value of resistor can only be found experimentally
Load
V
V
V
R

## Slide 11: Conclusion
Currently waiting for materials
Conformable battery building process
Exploring additional ideas to enhance conformability

## Slide 12: Future Works
Build Battery!
Test battery performance (flat and bent)
Test internal resistance of battery
Learn to fly RC plane
Fly the plane!