## Slide 1: Self-Stabilizing Pool Table
Team 19 Group Members:
Norman Gross & Alexander York
Advisor: Keith Larson
2/13/2014

## Slide 2: Project
Notes: Beyond Innovation has the solution to this problem. A prototype is being developed to reduce the footprint of the pool table by up to 75%. This will give the table a capability of vertically stowing itself in a discrete housing in case the additional space is needed. Along with its storage ability, the table will also have a self-stabilization feature that levels the slate-top to have a perfectly horizontal playing field. The design of this table will have both the look and the feel of a standard slate pool table.

## Slide 3: Project Scope
Reduce the footprint by 75%
Vertically Stowable
Self-Stabilizing
Notes: Beyond Innovation has the solution to this problem. A prototype is being developed to reduce the footprint of the pool table by up to 75%. This will give the table a capability of vertically stowing itself in a discrete housing in case the additional space is needed. Along with its storage ability, the table will also have a self-stabilization feature that levels the slate-top to have a perfectly horizontal playing field. The design of this table will have both the look and the feel of a standard slate pool table.

## Slide 4: Housing Concept
Housing
Internal Frame
  Steel
External Frame
  Wood
Potential Challenges

## Slide 5: Lifting Concept
Lifting Mechanism
Linear Guides
  Seen on elevators
Guide Rails
  Minimize moments
Hooking arms

## Slide 6: Transition Concept
Notes: Show all angles of transition

## Slide 7: Prototype Specs
Engineering Specs
  750lb max weight
  7ft x 3.5ft

## Slide 8: Table Concept
Table
4 linear actuators
4 XY Inclinometer sensors
Microcontroller

## Slide 9
Linear Actuators
Original Setup:
4 DC Motors
  No encoders
  Limited accuracy during leveling
Corrected Setup:
4 “Four Phase NEMA 23” Stepper Motors
  Increased accuracy
  Smaller power consumption
  Higher Hold Torque rating
Each phase draws 1 A at 8.6 V
Holding torque of 14 kg-cm (190 oz-in)
Can be used as a unipolar or bipolar stepper motor
Has a 1.8° step angle 200 steps/rev

## Slide 10
XY Inclinometer
4 XY Inclinometer sensors
  2 pairs each identically oriented on opposite sides of the table; using each other and gravity as reference points
Resistive Sensors
Operates on 5V Logic
Analog Output

## Slide 11
Microcontroller
Micro Dragon Microcontroller
Processing:
16 MHz crystal, 8 MHz default bus speed and up to 25MHz bus speed via PLL
Pre-installed with Serial Monitor for CodeWarrior
91 of MC9S12DG256 I/O pins are accessible on male header connectors for user applications
MCU also includes the following peripherals:
  3 SPIs
  2 SCIs
  2 CANs
  I2C interface
  8 16-bit timers
  8 PWMs
  16-channel 10-bit A/D converter

## Slide 12: Leveling Control

## Slide 13: Current Progress

## Slide 14: Procurement

## Slide 15: Future Plans
Develop leveling system
  Testing
Create table frame
Construct housing and lift assembly
Finalize system controls

## Slide 16: Project Timeline

## Slide 17: Questions

## Slide 18: Citation
http://muller.lbl.gov/teaching/H7B/pages/ElasticModuliTable.htm
http://www.pianoworld.com/faq.htm