## Slide 1: Shell Eco-Marathon FAMU-FSU 2014 Solar Car Milestone #2 Presentation Team #2

## Slide 2: Qualifications
Fritz Jeanty- Responsible for the motor controller. Fritz has taken courses related to motor controller including C++ programming, Digital Logic, electronics, and Microprocessor based system design.
Francois Wolmarans- Responsible for finances, and ergonomic design. In addition to his experience in education and research at HPMI, he has founded 3 start ups (of which 2 have been profitable).
Jose Cardenal- Responsible for safety considerations, and ergonomic design, and manufacturing. His previous job in process improvement and analysis and a research assistant at HPMI allow him to qualify for this task.
Julia Clarke- Responsible for accessory battery. Clarke is currently enrolled in courses relating to batteries and has a great interest in batteries.

## Slide 3
Zachary Barr- Responsible for the DC-DC convertor. His experience in soldering electronics and Multisim qualify him to work this aspect of the project.
Wael Nabulsi- Installations manager. His employment at the Applied Super Conductivity center, in addition to his previous coursework allow him to do this job effectively.
David Joliceur- Responsible for all mechanical designs. He is currently enrolled in energy conversions for sustainability and vehicle design, which complement the project.
James Croasmun- Responsible for front wheel mount system and steering assemblies. He has completed various courses related to his responsibilities.
Qualifications

## Slide 4: Shell Eco-Challenge Marathon
Urban Concept and Prototype
Divisions
FAMU/FSU Participation
Registration
Francois Wolmarans

## Slide 5: Introduction
Acknowledgements
General Problem Statement
General Solution Approach
Operating Environment
Intended Use(s)/User(s)
Assumptions and Limitations
Francois Wolmarans

## Slide 6: Budget Summary
Francois Wolmarans

## Slide 7
Fish Bone Analysis
What:
Team brainstorming approach to determine the voice of the customer
How:
Using required and desired capabilities
Why:
Allows the team to determine the major vehicle components
Jose Cardenal

## Slide 8: House of Quality Results:
Results:
Saftey
Cost
Weight
How it was created:
HOQ What's:
Customer Requirements
HOQ How's:
Vehicle, components, specifications, and major factors
What is the HOQ:
Quality Function Deployment tool
  Helps determine VOC
Allows the team to prioritize tasks and vehicle components
Points out positive and negative correlations
Jose Cardenal

## Slide 9: Comparison Matrix
Design Options | Safety (0.432) | Cost (0.208) | Component Weight (0.187) | Implementation (0.173) | Total
Design 1 | 3 | 3 | 3 | 3 | 3
Optimization Legend:
1 least optimal
2 more optimal
3 most optimal
nth more optimal
Weight Legend:
Safety = 0.432
Cost = 0.208
Weight = 0.187
Implementation = 0.173
Jose Cardenal

## Slide 10: Design Phase Gant Chart
Jose Cardenal

## Slide 11: Front Brake Designs
Design 1
Design 2
James Croasmun

## Slide 12: Steering System Design
Design 1
Design 2
James Croasmun

## Slide 13: Front Wheel Mount & Steering Assembly
Design 1
Design 3
Design 2
James Croasmun

## Slide 14: Front Wheel Mount and Steering Assembly
Design Options | Safety (0.432) | Cost (0.208) | Component Weight (0.187) | Implementation (0.173) | Total
Design 1 | 3 | 3 | 3 | 3 | 3
Design 2 | 2 | 1 | 1 | 1 | 1.432
Design 3 | 1 | 2 | 2 | 2 | 1.568
Design 1
James Croasmun
Design 1

## Slide 15: Seat Designs
Design Considerations
Design 1
David Joliceur

## Slide 16: Solar Panel Placement and Implementation
Design 1
Design 2
Design 3
David Joliceur

## Slide 17: Proposed Design
Design Options | Safety (0.432) | Cost (0.208) | Component Weight (0.187) | Implementation (0.173) | Total
Design 1 | 1 | 2 | 3 | 2 | 1.755
Design 2 | 2 | 3 | 2 | 3 | 2.381
Design 3 | 3 | 1 | 1 | 1 | 1.864
David Joliceur

## Slide 18: Rear Brakes
Design 1
Design 2
Wael Nabulsi

## Slide 19: Component Placement
Component Placement 1
Component Placement 2
Wael Nabulsi

## Slide 20: Roll Bar / Wheel Mount Design
Design 1
Design 2
Design 3
Wael Nabulsi

## Slide 21: Roll Bar Design 3
Design 3
Design Options | Safety (0.432) | Cost (0.208) | Component Weight (0.187) | Implementation (0.173) | Total (1.000)
Design 1 | 1 | 3 | 3 | 1 | 1.963
Design 2 | 2 | 2 | 2 | 2 | 2.000
Design 3 | 3 | 1 | 1 | 3 | 2.210
Wael Nabulsi

## Slide 22: Electrical Component Block Diagram
Electrical Component Placement Diagram
Fritz Jeanty

## Slide 23: Brushless 3-Phase Motor
Motor Specifications
  24Volts
  250-750W
  30A
Single Board Controller options
  RDK-BLDC
  TI MSP430 LAUNCHPAD
  TI TMS320F28
          ATAVRMC100
Driver Gate Options
  IR3230SPBF
  TI DRV8301DCA
Golden Motor Magic Pie Motor
Fritz Jeanty

## Slide 24: Motor Controller
Single Board Controller Comparison Matrix
Advantages
Supports and includes a three phase brushless motor
On board breaking circuit for protection against unsafe current levels
Screw Terminals allow direct input source for the propulsion battery
TI RDK-BLDC Motor Controller
Design Options | Safety (0.432) | Cost (0.208) | Efficiency (0.187) | Implementation (0.173) | Total (1.000)
Design 1 | 3 | 3 | 4 | 4 | 3.36
Design 2 | 1 | 4 | 1 | 1 | 2.296
Design 3 | 2 | 1 | 2 | 2 | 1.56
Design 4 | 4 | 2 | 3 | 3 | 2.776
Fritz Jeanty

## Slide 25
Gate Driver Comparison Matrix
Advantages
Over current protection
Specifically for three phase motor drive applications
Current Shunt amplifiers that support bi-directional current sensing
Gate Driver
Design Options | Safety (0.432) | Cost (0.208) | Efficiency (0.187) | Implementation (0.173) | Total
IR 3230SPBF | 1 | 2 | 1 | 1 | 1.208
TI DRV8301DCA | 2 | 1 | 2 | 2 | 1.792
Fritz Jeanty
TI DRV8301DCA

## Slide 26: IGBT
Operate more efficiently at higher temperatures
Higher Voltage, Current and Power rating
  Motor operate at minimum 250W
Fritz Jeanty

## Slide 27: Accessory Battery
Electrical Engineers have considered using a 12V accessory
A 12V lead acid rechargeable battery with a 20Ah capacity
By forgoing the accessory battery the horn and ventilation system would be hooked up to the primary battery
Adding additional components would make the car less efficient
Julia Clark
Accessory battery

## Slide 28: DC-DC Converter
ISV005V2
Cost: Free
98% Efficiency
Overvoltage, Over current, and Over Temperature Protection
TCDC7001
Cost: $90
80% Efficiency
Over Voltage, Over current Over Temperature, and short circuit recovery
Plastic Insulation
Zachary Barr
ISV005V2
TCDC7001

## Slide 29: DC-DC Converter Test Summary
Zachary Barr
  8-9V
  3-3.5A
  Output from converter: 20V
    Conclusion: Watt meter absorbs 5V
  Output voltage is 24V
  Once connected, voltage drops and battery does not charge

## Slide 30: Circuit Schematics
Zachary Barr

## Slide 31: Micro-Soldering
The Safety/integrity of the board is paramount
Tools:
  Heat Sink
  Helping Hands
Risks
  Entire board could be rendered useless
Zachary Barr
ISV005V2
  Heat Sink
  Helping Hands

## Slide 32: Acknowledgments

## Slide 33: Questions

## Slide 34: References