## Slide 1: “Wear It” Impact Baseball Vest
Garth Fletcher
Kyler Hast
Kyle Meredith
Team Members
Maria Miro
Ryne Wickery
Cecilia Wong
Mechanical Engineering Advisor
Dr. Amin
Industrial Engineering Advisor
Dr. Olawale
Project Sponsor
Gavin Boone
Kyle Meredith

## Slide 2: General Overview
Background
Customer Requirements
Project Scope
Project Overview
    Design Constraints
    Design Considerations
    Material Selection
    Impact Analysis
    Ergonomics
    Safety
Proposed Budget
Future Plans
    Final Design Selection
    Prototype
    Manufacturing
Schedule Update
Kyle Meredith

## Slide 3: Background
Batter may incur severe or painful injuries often from being hit by a baseball in torso/neck region.
These types of injuries deter younger children from continuing to play the game of baseball.
With an effective design of a protective vest, injuries to areas like the spine and neck can be prevented.
No current protection available.
Kyle Meredith

## Slide 4: Customer Requirements
Vest must protect batter from hit by pitch.
Vest must allow for player to retain range of motion.
Vest must be worn over top of the uniform.
Vest should be lightweight.
Vest should be affordable.
Cecilia Wong
Notes: Safety: the vest must protect the players from being hit by a pitch.
Player Performance: the vest must allow for player to maintain freedom of movement.
Functionality: the vest must be worn over the uniform so its easy to take of after batting, or at first base.
Lightweight: the vest must not add significant weight on the player, so his speed is affected.
Cost: vest should be affordable for mid-class families.

## Slide 5: Customer Requirements
Cecilia Wong
Most important:
    Vest size.
    Vest shape.
    Weight
Notes: Form the analysis in our House of Quality: it was taken into consideration the relationship between our customer requirements and the technical requirements. As well as the correlation of the technical requirements. And we found that the most relevant technical requirements that we will have to look into are, vest size, vest shape and weight. This 3 requirements are the ones that will have a “control” over the others in order to have an optimal design that satisfies our customer requirements.

## Slide 6: Scope
Design vest to protect batter when hit by a pitch.
Design a vest that is aesthetically pleasing and therefore marketable.
Design a vest than can be adapted to players of different sizes.
Design a vest that protect without impeding a batter’s motions.
Construct a prototype and develop a manufacturing methodology.
Kyle Meredith

## Slide 7: Project Overview
FALL
    Define Constraints
    Brainstorm Ideas / Design Considerations
    Material Selection
    Impact Analysis
    Ergonomics
    Safety
SPRING
    Design Selection
    Build Prototype
    Devise Manufacturing Method
Kyle Meredith

## Slide 8: Constraints
Must withstand impact force of 100 mph baseball.
Should weigh under 7 pounds.
Name / Number must be visible while wearing vest.
Should achieve quick application/removal.
Should not impair range of motion.
Maria Miro

## Slide 9: Design Considerations
Prevent Damage
    Padding in critical areas only [reduce weight]
    Hard plate to spread out force
    Spring board plates
    Inside Padding
Retain Range of Motion
    Minimal material in moving areas
    Divide padding into small sections
    Minimize collar
    Use of elastic materials
Maria Miro

## Slide 10: Design Considerations
Lightweight
    Lightweight materials
    Remove unnecessary materials
    Minimize thickness
    Minimize padding
Worn Over Uniform
    Quick securing (Velcro/snaps/etc.)
    Transparent material in number area
    Interchangeable numbers (Velcro/pouch/etc.)
    Aesthetically pleasing
Maria Miro

## Slide 11: Material Selection
Kyler Hast

## Slide 12: Material Selection
Chose Carbon Fiber for final plate material selection
Manufacturing Carbon Fiber plates is simpler than processing silicon into desired plates
Kyler Hast

## Slide 13: Impact Analysis
Calculation Assumptions
    1 Dimensional
    Elastic region
    Uniform force
    Constant force
Speed of sound of rubber
    About 60 m/s
    Assumed to be a solid rubber ball
    Used to calculate impact time.
Ryne Wickery

## Slide 14: Impact Analysis
Impact time
    2.455*10-3 sec
Force of ball at 100mph
    2.581 kN (580 lbf)
Surface area of ball compressed
    0.503 in2
Impact Energy = 141 J
ECFRP_absorb. = 2059 J
F.S = 14.5
Ryne Wickery

## Slide 15: Impact Analysis
Ryne Wickery
Rib Plate: Deflection (inches) [left] & Safety Factor [right]

## Slide 16: Impact Analysis
Ryne Wickery
Spine Plate: Deflection (inches) [left] & Safety Factor [right]

## Slide 17: Ergonomics
Collar piece height shouldn’t be the same on the front than at the back of the neck.
The arrangement and size of the padding should follow the form of the muscles underneath.
The arm holes should not cover the shoulder area to allow free range of movement.
The length of the vest shouldn’t exceed the waist of the player.
Cecilia Wong
Notes: Because we are making a product that is going to be wear by our customers, we have to consider ergonomic analysis.
We have to consider the interaction between the human body and the vest.
Our focus the neck. The collar height has to vary from the back to the front, because on the front, the collar must not impede the rotation of the head, plus the ear protection of the helmet.
For a better acceptance of our product we have to consider that the shape of the padding used to protect the body should mimic or by similar to the form of the muscles underneath.
Also, to allow free arm movement, the armholes shouldn’t cover the shoulder area, the entire semi-sphere of the shoulder is not confined and able to move in every direction. The opening would start closer to the neck, and on the bottom, it should go up to under the pectorals, so when the arms are raised the vest doesn’t cause pressure under the armpits.
Because the players bend forward while in a squatting position, and swing to an almost straight position, the vest length should not go over the waist level. the players wont feel discomfort in its lower abdomen, and also on the upper part of the thighs as its squads.

## Slide 18: Safety
Fabric or buffering material should be thick enough to prevent skin injuries from shattered material.
Vest must allow the transfer of body heat to the environment as players performs.
Possible risk analysis.
Cecilia Wong

## Slide 19: Proposed Budget
Carbon fiber fabric 5.7 oz
    $36 per sq. yard
Fiberglass fabric 6 oz
    $7 per sq. yard
Polyester resin
    $24 per quart
Closed cell foam pad
    $12 for 72in x 20in x 3/8in sheet
Kyler Hast

## Slide 20: Future – Design Selection
Collar Dimensions
    1.5” – 2.5” tall
    210o @ 2.5” - 4.5” radius
Spine Plate Dimensions
    3” – 4.5” wide
    16” – 20” tall
Rib Plate Dimension
    6” – 9” tall
    85o @ 3” – 6.5” radius
Kyler Hast

## Slide 21: Possible Design Concepts
Kyler Hast

## Slide 22: Possible Design Concepts
Kyler Hast

## Slide 23: Future – Design Selection
Critical Protection Areas
    Neck
    Spinal Region
    Ribs
    Kidney / Liver / Exposed Organs
More Analysis Required
    Possibly real-world testing of prototype.
Kyler Hast

## Slide 24: Future - Prototype
Prototype will be created for testing next semester
It will allow us to test behavior of carbon fiber plates under impact
We can attched padding material to plates to determine cushioning characteristics
Maria Miro

## Slide 25: Competitive Priorities
Maria Miro
Cost
Quality
Delivery
Flexibility
Performance
Aesthetics
Technical durability
Selling price
Manufacturing cost
Value-addded cost
Price performance
Ability to keep promises
Material quality
Output quality
New product

## Slide 26: Future - Manufacturing
Process choice: Batch Flow
Manufacturing Strategy: Made-to-Stock (MTS)
Choice of machine: Industrial sewing machine
Operations Strategy:
    Order qualifier: Safety
    Order Winning: Quality, Performance & Price
Garth Fletcher

## Slide 27: Future - Quality
Would like to develop a process to achieve 6-sigma production standards (3 defects per million).
Comply with ISO 9000 requirements.
Introduce aftermarket accessories to protect additional areas if time permitting
Coping with changes in demand.
Garth Fletcher

## Slide 28: Updated Schedule
Garth Fletcher
Chart: Team 26 Gantt Chart
| Fall 2013 | Organize project team | Introduction | Select team leaders | Meet with advisors | Design | Get the “voice of customer” from sponsor | Come with design alternatives | Decide design solution | Aim for design optimization | Material | Material research | Material selection | Material purchase | Impact Analysis | Calculate energys and forces by baseball | Implement forces to material selected | 3D Analysis on material | Spring 2014 | Prototype | Prototype construction (Generation I) | Prototype testing | Impact test | Thermal test | Comfortability test | Market test | Needed modifications (small ones only) | Final prototype (Generation II) | Manufacturing | Manufacturing plannification | Aim for lean production (six sigma) | TOTAL
START | 41535 | 41535 | 41535 | 41543 | 41551 | 41562 | 41565 | 41568 | 41582 | 41596 | 41600 | 41610 | 41610
DURATION (days) | 5 | 1 | 1 | 3 | 28 | 7 | 11 | 3 | 7 | 35 | 14 | 14 | 7 | 13 | 10 | 3 | 3

## Slide 29
Questions?

## Slide 30: References
http://www.acs.psu.edu/drussell/bats/nonlinear-ball.html