## Slide 1
“Wear It” Baseball Vest
Garth Fletcher
Maria Miro
Cecilia Wong
Kyler Hast
Kyle Meredith
Ryne Wickery
Advisors
Dr. K. Amin
Dr. D. Olawale
Sponsor
Gavin Boone

## Slide 2
Ages 0-15: 23.9 percent
Ages 16-30: 14.4 percent
Ages 31-45: 6.9 percent
Ages 46-60: 3.8 percent
Ages 61-75: 2.2 percent
Ages 76-98: 0.6 percent
“To enhance a player’s ability on the field, by endorsing confidence through safety”
Kyle Meredith

## Slide 3
Sports equipment development company.
Specialized in athletic protective equipment.
Provision of innovative gear to protect players during sporting events.
Overview
Kyle Meredith

## Slide 4
Sponsor Overview
Kyle Meredith
Mr. Gavin Boone, candidate for an MBA at Florida State University
Currently works as an executive professional of sales at SANOFI, a leading global health care company
Served as Athletic Director at Holy Comforter Episcopal Middle School for 4 years
Has coached for many years at the high school level, specifically at A.C Flora and Duluth High Schools
Notes: The inspiration for this project arose from Mr. Boone seeing a player being struck in the back of the neck during a game.
Mr. Boone recognized there was a need for a protective garment that would protect the neck and other vital areas.

## Slide 5
Kyle Meredith
The inspiration for this project arose from Mr. Boone seeing a batter struck in the back of the neck during a game.
Mr. Boone recognized there was a need for a protective garment that would protect the neck and other vital areas.
Product Need
Notes: The inspiration for this project arose from Mr. Boone seeing a player being struck in the back of the neck during a game.
Mr. Boone recognized there was a need for a protective garment that would protect the neck and other vital areas.

## Slide 6
2009 14,390 neck fractures.
  2,692 were sports related
With an effective protective collar, injuries to the spine and neck can be prevented
No current protection is available for the neck region
Market Opportunity
Ages 0-15 | 23.9 %
Ages 16-30 | 14.4 %
Ages 31-45 | 6.9 %
Ages 46-60 | 3.8 %
Ages 61-75 | 2.2 %
Ages 76-98 | 0.6 %
Kyle Meredith
Notes: Batter may incur severe or painful injuries often from being hit by a baseball in torso/neck region.
These types of injuries deter younger children from continuing to play the game of baseball.
With an effective design of a protective vest, injuries to areas like the spine and neck can be prevented.

## Slide 7
Competition
Direct
None
There is no current market offering of a batting protective collar
Indirect
EvoShield Torso Protection
Cooper Batting Vest
Adams Torso Padding Vest
Garth Fletcher

## Slide 8
Design a collar to prevent injury from baseball impact.
Design the collar so it does not hinder motion/performance.
Design collar to be attached to the vest and/or to the body of the player.
Project Scope
Garth Fletcher

## Slide 9
Customer
Requirements
Garth Fletcher

## Slide 10
Customer Requirements
Garth Fletcher
Technical Requirements
Plate Thickness
Padding Thickness
Collar Size
Collar Shape
Wear ability
Flexibility
Collar Weight
Customer Requirements
Impact Safety
Aesthetics
Lightweight
Cost
Player Performance
Durability
Comfort
Functionality
  486.2
  500.0
   651.7

## Slide 11
Human Factor
Range of Motion of head and neck
Comfort
    Size
      Based on average dimensions
    Weight
      Maximum of 11 oz. (Half of current helmet)
    Conformance to body shape
Garth Fletcher
Notes: Comfort
    Foam will be comfortable to player
Fit
    Thermoplastic, and elastic foam will allow collar to be molded as desired [Retain mobility]
Safety
    Collar will protect player from damage caused by impact
Chemical
    Polyethylene and EVA will not react with skin of player that would cause rash or disturbance.
Range of motion:
Head:
- flexion, bend the head forwards; 40 to 60 degrees.
- extension, tilting the head backwards (like looking at the ceiling) 45 to 70 degrees
rotation, turning of the head to the sides, 60 to 80 degrees
Lateral bending: 45 degrees.
Shoulders:
Abduction: 150 degrees
Forward flex: 180 degrees
Extension: 45-60 degrees
Rotation: external – 90 degrees, internal – 70 to 90 degrees.
Comfort:
Size – maintain a small collar, to avoid impairing the players view and range of motion, based on the average neck height of 95% males. (6ft) from the baseball almanac.
Weight – based on complains from players having to wear a heavier helmet (rawlings 22 oz). Goal, our collar to be 50% lighter than the helmet.

## Slide 12
Garth Fletcher
Body Measurements of Mature Men (in.) | Percentiles |  |  |  | 
 | 1st | 5th | 50th | 95th | 99th
Head Breadth | 5.5 | 5.7 | 6.0 | 6.3 | 6.5
Menton to Back | 6.2 | 6.5 | 7.2 | 7.9 | 8.2
Menton to Top of Head | 8.4 | 8.6 | 9.1 | 9.7 | 10.0
Menton to Sub-Nasal Length | 2.6 | 2.7 | 2.9 | 3.3 | 3.4
Base of Neck to Menton | 3.2 | 3.2 | 3.3 | 3.1 | 3.2
Base of Neck to Hair Line | 5.8 | 5.9 | 6.2 | 6.4 | 6.6
Accurate Fit
  99th percentile of mature male body measurements
Sizing
Notes: Body dimensions:

## Slide 13
Baseball Dynamics
Force of Impact
    2,500 lbf
Surface area of ball compressed
    - 0.50 in2
Impact Energy
    141 J
Pressure of impact at 100mph
    5,000 psi
Ryne Wickery

## Slide 14
Material Selection
Ryne Wickery

## Slide 15
Hard Plate Material
Ryne Wickery
Will be used as an impact surface, to disperse impact load
Last semester carbon fiber was chosen as hard plate material
  Rejected due to degrading mechanical properties upon impact
  Polyester matrix extremely brittle
  If failure occurs, the material could crack / splinter
This semester, a material was chosen based on stiffness, toughness, and strength
  Desired ability to minimize deflection (spread impact load)
  Ability to be molded to desired shape (ex. Thermoplastic)
Notes: Will be used for the hard shell of the collar.
Thermoplastic.
Relatively large strength-to-density ratio.
Currently used in bull riding protection vests, and also in ballistic protection.

## Slide 16
Hard Plate Material
Ryne Wickery
Hard Plate Material Comparison |  |  | 
Property | Polyurethane | HDPE | Kevlar
Density (g/cm^3) | 0.9-1.96 | 0.93-0.97 | 1.44
Tensile strength (MPa) | 35-56 | 40.5-48.3 | 3600-4100
Fracture Toughness (MPa*m1/2) | 1.84-4.97 | 1.44.1.75 | -
Price ($/kg) | 4.10-5.60 | 1.20-1.85 | 35-100
High Density Polyethylene (HDPE)
Notes: Will be used for the hard shell of the collar.
Thermoplastic.
Relatively large strength-to-density ratio.
Currently used in bull riding protection vests, and also in ballistic protection.

## Slide 17
Padding Foam
Ryne Wickery
Will Be used as a backing material to the hard plate.
Hard plate will act to spread the impact load over a larger region and the foam will act to absorb the impact energy
Desired Properties
  Closed cell (minimal water absorption)
  Relatively large elastic deformation (energy absorption)
  Capable of full recovery after impact
  Lightweight
Notes: Padding material for the collar
Used in current protective gear
Water resistant (sweat)
Can be formed to collar shape
Recoverable
Relatively lightweight
Because of the higher tensile strength of the EVA foam, it is stronger than EPE. This is a good thing because
EVA shows a higher elongation @ break. The more it stretches, the more energy it can absorb when the ball hits it.
EVA foam's greater recovery characteristics make it an excellent choice
Stronger
Durable
Lasts longer
Worth the extra money spent
EVA, even it is more expensive, takes the lead in applications where product lifetime and sturdiness is of upmost importance.

## Slide 18
Padding Foam
Ryne Wickery
Padding Material Comparison |  | 
Property | EVA | PE
Density (kg/m3) | 28-33 | 28-33
Thickness (mm) | 3-40 | 3-40
Tensile strength (kPa) | 450 | 350
Elongation @break (%) | 200-250 | 150-200
Compressive strength (kPa) | 30 | 45
Water absorption (g/cm3) | 0.002 | 0.002
Price ($/sheet) | 35.55 | 28.16
Ethylene-Vinyl Acetate (EVA)
Notes: Padding material for the collar
Used in current protective gear
Water resistant (sweat)
Can be formed to collar shape
Recoverable
Relatively lightweight
Because of the higher tensile strength of the EVA foam, it is stronger than EPE. This is a good thing because
EVA shows a higher elongation @ break. The more it stretches, the more energy it can absorb when the ball hits it.
EVA foam's greater recovery characteristics make it an excellent choice
Stronger
Durable
Lasts longer
Worth the extra money spent
EVA, even it is more expensive, takes the lead in applications where product lifetime and sturdiness is of upmost importance.

## Slide 19
Finite Element Analysis
Kyler Hast

## Slide 20
Kyler Hast
FEA – Assumptions
Modeled under the assumption of a flat plate (2” x 4”)
Material constrained from the bottom to emulate the collar being attached to the shoulder
Modeled under worst case scenario (collar touching skin)
Model constructed as a 4 layer combination (HDPE, EVA, Muscle, and Bone)

## Slide 21
Kyler Hast
FEA – Modeling
5 material combinations tested
  all combine to equal ¾“ total thickness
  Compared based on maximum deflection and maximum strain
  ½” Material combinations removed due to nature of failure / minimal padding
5000 psi load (ISSBS)
0.50 in2 impact surface area (Russel, Ph.D.)

## Slide 22
Kyler Hast
FEA - Deflection
Deflection
Deflection provides a relative measure of a materials ability to spread an impact load over a surface
A material with lower deflection (thicker in our case) spreads out the impact load more efficiently

## Slide 23
Kyler Hast
FEA - Strain
Strain
Strain provides a relative measure of a materials ability to absorb impact energy
A sample with a higher strain (of the same material) has stored more impact energy into the molecular structure

## Slide 24
Kyler Hast
NIJ standard for bullet proof vests admit a maximum of 1.73” of backface
signature (deflection).
Thickness (in) HDPE EVA |  | Maximum Deflection (in) | % of NIJ Standard | Maximum Strain (in)
1/8 | 5/8 | 1.60 | 92.5 | 94.2
1/4 | 1/2 | 1.10 | 63.6 | 72.3
3/8 | 3/8 | 0.49 | 28.3 | 32.3
1/2 | 1/4 | 0.26 | 15.0 | 17.2
5/8 | 1/8 | 0.15 | 8.7 | 9.8
3/8” HDPE – 3/8” EVA chosen based on the balance of deflection and strain
    Ability to spread impact load over rear surface (lower deflection)
    Ability to absorb impact energy (higher strain)
Other combinations compromise deflection by absorbing more energy, or compromise energy absorption by decreasing deflection
FEA Results

## Slide 25
Kyler Hast
Hard Plate reduces impact force to acceptable level (89.6% of standard), even before energy absorption of foam and neck muscle is taken into consideration.
Simple Force Analysis

## Slide 26
Kyler Hast
Clay Impact Test

## Slide 27
Collar Design
Cecilia Wong

## Slide 28
Cecilia Wong
Mr. Boone’s Design
Crown Plate
Arched Neck Plate
Flat Plate

## Slide 29
Cecilia Wong
Flat Plate
Evaluation Matrix |  | CONCEPTS |  |  | 
CRITERIA | Importance Rating | Mr. Boone's Design | Crown-like shape | Arched shape | Flat neck shape
Cost | 6 | DATUM | S | + | +
Adjustability | 9 |  | S | - | S
Level of Comfort | 7 |  | - | - | -
Ease of Maintenance | 4 |  | + | + | +
Safety | 10 |  | S | - | +
Aesthetics | 7 |  | S | - | -
Lightweight | 9 |  | + | + | +
Durability | 6 |  | S | - | +
Player Performance | 9 |  | + | - | S
Functionality | 8 |  | S | - | +
Sum of Positives |  | DATUM | 3 | 3 | 6
Sum of Negatives |  |  | 1 | 7 | 2
Sum of Sames |  |  | 6 | 0 | 2
Weigthed Sum of Positives |  |  | 22 | 19 | 43
Weigthed Sum of Negatives |  |  | 7 | 56 | 14
 |  |  | 15 | -37 | 29

## Slide 30
Cecilia Wong
Material Adhesion
Hot Melts
Melding
Double-side tape
Contact cement
Screws & bolts
Contact Cement
  Strong Bonding capabilities
  Waterproof
  Flexible
  Relatively inexpensive

## Slide 31
Cecilia Wong
Body Attachment
Sewing
Velcro
Straps (nylon)
Shoulder padding
Snaps
Straps (nylon)
Lightweight
Strong
Ability to fasten the collar even across front and back
Easily adjustable

## Slide 32
Cecilia Wong
Mr. Boone’s Design
Flat Plate with Shoulder Padding
Flat Plate Design
Final Design

## Slide 33
Cecilia Wong
Description |  | Value (in.)
A | Back Height | 2.25
B | Back/Top Height | 1.50
C | Back/From Height | 2.0
D | Front Height | 1.00
E | Total Back Height | 5.75
F | Back Piece Width | 2.50
G | Shoulder Piece Length | 2.50
H | Shoulder Piece Width | 1.50
I | Collar Diameter | 7.50
J | Strap Hole Width | 1.25
K | Strap Hole Height | 0.125
Dimensions

## Slide 34
Cecilia Wong

## Slide 35: Market Examination
Market Segment
Player Profile
Player Habits
Research and Studies
Maria Miro
Notes: Nowadays, there is a trend in baseball in which players are being instructed to take a pitch for the team because every time this happens, players are allowed to get to first base; hence, increasing their chance to score. The statistics for NCAA baseball for 2013 are showing that there is a very strong correlation between the number of HBP (hit by pitches) each team had, and the team’s win – loss record. For NCAA divisions 1-3, those teams that had the highest HBP, were also usually the teams that had very high winning percentages, whereas the teams with the lowest number of HBP, had the lowest winning percentages with a few exceptions (see Appendix A).
“Catastrophic injuries are rare; yet, most occur when players are struck in the head or chest with a ball or bat.
On average 3 to 4 players (under the age of 15) die each year from baseball-related injuries. As small as this number is, however, baseball still has the highest fatality rate among all common youth sports”
The sporting goods market as whole and the market for baseball equipment are multi-billion and multi-million dollar markets respectively. CAGR: compound annual growth rate

## Slide 36
  Take a pitch
Player Habits
Maria Miro

## Slide 37
  Approximately 500,000 adult Americans play baseball.
  In high school alone, there are 15,000 teams and 450,000+ participants.
  High school, college, major leagues, and minor leagues.
Market Segment
Maria Miro

## Slide 38
  Two Categories
    Youth baseball players
      Teens and high-school players ranging from ages 13-18
    College and major league players
      Adults and ranging from ages 18-45
Player Profile
Market Segment
Player Profile
Maria Miro

## Slide 39
  3 to 4 players (under the age of 15) die each year.
  Baseball has the highest fatality rate among all common youth sports.
  “The U.S. market for sports protective equipment was worth $1.8 billion in 2012. The market increased to nearly $1.9 billion in 2013 and expected to increase to $2.1 billion in 2018, a CAGR of 2.6% between 2013 and 2018”. Source: PR Newswire.
Research and Studies
Maria Miro
Notes: “Catastrophic injuries are rare; yet, most occur when players are struck in the head or chest with a ball or bat. On average 3 to 4 players (under the age of 15) die each year from baseball-related injuries. As small as this number is, however, baseball still has the highest fatality rate among all common youth sports” (Barton). “While the sport may seem safe then, that is little comfort for the parents of children who have been catastrophically injured or died” (R&B Law).
Ages 0-15: 23.9 percent
Ages 16-30: 14.4 percent
Ages 31-45: 6.9 percent
Ages 46-60: 3.8 percent
Ages 61-75: 2.2 percent
Ages 76-98: 0.6 percent

## Slide 40: Marketing Strategy
Exhibits, television, newspaper, and magazines
Product’s website
Individual or corporate sponsorships
License product to current manufacturer
Targeted Media + Public Relations = SUCCESS!
Maria Miro
Notes: This, indeed, is the main mission of this product commercialization.
individual or corporate sponsorships. These will help provide any team or league with the product for no charge to the players.
In addition to individual promotion and sales, there will be an ongoing effort to sell the product to a manufacturer/ marketer of sporting goods, in order to speed the distribution of the collar.
exhibits, television and radio interviews, newspaper and magazine articles, and public speeches will be ongoing parts of the marketing plan for this project. All these will create public awareness of the need to protect youth baseball players from unnecessary pain, suffering, and loss of life (or quality of life).
As an incentive, each contributor to the promotion of “Wear It” will receive a unit for a player of their choice.

## Slide 41: Distribution Plan
Find a buyer with an established distribution channel.
    Ex: Atec, Champro, Easton, Rawlings, Schutt, Wilson, Evoshield, and WSI.
This would help speed the introduction of the product.
Maria Miro
Notes: Find a buyer, with an already established distribution channel, that would be interested in buying the product concept. This would help speed the introduction and access of the product to the baseball community, and potentially save lives and prevent significant injuries sooner. This will be a comparably better alternative than having a Third Party Manufacturer do the work because this will require a capital investor.

## Slide 42: SWOT Analysis
Maria Miro

## Slide 43: Initial Sales
6 collars per team
≈ 16,000 teams
93,750 UNITS
Maria Miro
EVA foam ………………. $3.50
HDPE …………………….. $9.50
Contact Cement ……. $3.00
Straps & Buckle……… $5.00
TOTAL COST $21.00
Cost of Prototype

## Slide 44: Future Work
More Detailed Finite Element Analysis
Impact Testing
    Measured values of Force on neck
Prototype construction
Test collar fit and player mobility
Kyle Meredith

## Slide 45: Conclusion
No current neck protection on the market
    Our product fills this void
Collar exceeds current NIJ deflection standard
Collar effectively reduces shear force applied to neck
3/4” thickness utilized to maximize protection with minimal weight
Kyle Meredith

## Slide 46
Questions?