## Slide 1: Educational Kit for Alkaline Membrane Fuel Cell (AMFC)
Team
------------------------------
Nicole Alvarez
Bryan Anderson
Collin Heiser
Mustafa Nek
James Richardson
Advisor: Juan Ordonez
Sponsor: FSU
Group 10

## Slide 2: Why use Fuel Cells?
Table 1. Fuel Cell Comparisons
Alkaline Membrane Fuel Cells are the most electrically efficient fuel cell technology
Group 10 Bryan Anderson
Slide 2 of 13 Educational Kit of AMFC
Bi-Product of use is water
Completely sustainable, assuming a clean source of hydrogen acquisition
Fuel cells accomplish the same result without the environmental issues
Why Alkaline Membrane?

## Slide 3: Changes from Fall 2014
Fall 2014
Communication
  Brazil  America
Design
  Case Design
  Profitability/Marketing
Spring 2015
Communication
  America
Design
  Functioning Fuel Cell
  Testing FC with kit components
Cost Benefits
Group 10 Mustafa Nek
Slide 3 of 12 Educational Kit of AMFC

## Slide 4: Goal Statement / Objectives
Develop a functioning fuel cell educational kit
  Gather/build components for cell
  Test/experiments with built fuel cell
  Develop a working fuel cell for AME open house
  Obtain necessary materials for kit
  Create safety & operations manual for educational kit
Group 10 Mustafa Nek
Slide 6 of 12 Educational Kit of AMFC
“Deliver a fully functional alkaline membrane fuel cell in a portable case to Florida State University by the end of the spring 2015 semester.”

## Slide 5: Part List and Budget Breakdown
Group 10 Bryan Anderson
Slide 4 of 12 Educational Kit of AMFC
Component | Cost | Notes
Case and padding | $122.84 | May use a cheaper alternative
Membrane | $250.00 | Consumed during process
Tubing/waste container | $8.00 | 
Stainless steel | $52.00 | Needs machining
Compressed gases | $25.00 | Containers are reusable
Power output mechanism | $13.00 | Still in design process
Pressure regulator/guage | $300.00 | Dual stage for steady outlet pressure
Gas leak sensor | $40.00 | Battery operated sensor
Remaining Budget | $189.16 | 
Total | $810.84 | Too high but unpreventable
Chart: 
| Case and padding | Membrane | Tubing/waste water container | Stainless steel | Compressed gases | Power output mechanism | Pressure regulator/guage | Gas leak sensor | Remaining Budget
Case and padding Membrane Tubing/waste water container Stainless steel Compressed gases Power output mechanism Pressure regulator/guage Gas leak sensor Remaining Budget | 122.84 | 250 | 8 | 52 | 25 | 13 | 300 | 40 | 189.16

## Slide 6: Testing Results
6 hour long test with data recorded every 30 minutes
Run with an approximate 40% KOH electrolyte concentration
Relatively pure H2 and O2 fueled the reaction
The power generation was measured using digital multimeters
Chart: 40% KOH Polarization Curve response
| 0 | 6.1600000000000002E-2 | 6.59E-2 | 7.3099999999999998E-2 | 7.7499999999999999E-2 | 8.3099999999999993E-2 | 8.7599999999999997E-2 | 9.2700000000000005E-2 | 0.1011 | 0.11009999999999999 | 0.1215
t = 5 min | 0.94 | 0.55 | 0.53 | 0.48 | 0.46 | 0.42 | 0.39 | 0.36 | 0.31 | 0.26 | 0.19
t = 60 min | 0.95 | 0.49 | 0.46 | 0.43 | 0.42 | 0.38 | 0.37 | 0.34 | 0.29 | 0.24 | 0.16
t = 120 min | 0.95 | 0.54 | 0.5 | 0.46 | 0.44 | 0.4 | 0.38 | 0.33 | 0.31 | 0.23 | 0.18
t = 180 min | 0.95 | 0.56 | 0.51 | 0.5 | 0.47 | 0.42 | 0.39 | 0.33 | 0.3 | 0.25 | 0.18
t = 240 min | 0.95 | 0.52 | 0.49 | 0.47 | 0.44 | 0.42 | 0.39 | 0.34 | 0.3 | 0.24 | 0.16
t = 300 min | 0.87 | 0.37 | 0.36 | 0.34 | 0.33 | 0.3 | 0.29 | 0.26 | 0.23 | 0.17 | 0.13
t = 360 min | 0.8 | 0.44 | 0.4 | 0.38 | 0.36 | 0.35 | 0.31 | 0.28 | 0.25 | 0.19 | 0.12
Figure #. Experimental setup and testing environment in the UFPR LaCelc Lab where the AMFC was tested
Figure #. Sample polarization curves taken from results obtained after 6 hour AMFC test
Group 10 James Richardson
Slide 4 of 12 Educational Kit of AMFC

## Slide 7: Future Considerations
Testing the durability of the platinum electrodes
Formation of possible kit demonstrations
Continuing Collaboration between UFPR-FSU
Figure #. A platinum electrode similar to what is being used in the AMFC kit.
Group 10 James Richardson
Slide 4 of 12 Educational Kit of AMFC

## Slide 8: Gantt Chart
Group 10 Bryan Anderson
Slide 2 of 13 Educational Kit of AMFC

## Slide 9: References
Group 10
Slide 11 of 12 Educational Kit of AMFC
Vargas, J.V C., and J. C. Ordonez. "Alkaline Membrane Fuel Cell (AMFC) Modeling and Experimental Validation." Journal of Power Sources (2012): 1-15.Www.elsevier.com/locate/jpowsour. Elsevier, 11 Apr. 2012. Web. 15 Sept. 2014.
Ordonez, Juan, and Jose Vargas. Design and Development of an Alkaline Membrane Fuel Cell (AMFC) Educational Kit for High School and College Level Laboratory Demonstration. Tallahassee: Florida State Univeristy, n.d. PDF.

## Slide 10: Questions
Group 10
Slide 12 of 12 Educational Kit of AMFC