## Slide 1: Tabletop Torsion Device
Interim Design Review
By: Brendan Keane, Logan McCall, Reggie Scott, Mark Swain
Instructor: Dr. Nikhil Gupta
Sponsor: Mr. Philip Flater (Munitions Directorate Eglin AFB) Advisor: Dr. Simone Hruda

## Slide 2: Overview
Background with Constraints
DIC
Design Overview
  Current Status of Components
Challenges
Budget
Plan of Action
Conclusion
Mark Swain

## Slide 3: Background with Constraints
Maximum torque output: 100Nm
Machine must fit in an area (footprint) of 1m2
Monotonic(one direction) free-end torsion loading
Axial 1 DoF
Compatible with DIC
Budget - $2,000
Existing test hardware at Eglin AFB is not well-suited for characterizing relatively-small test samples that have been fabricated from plate or bar stock
Mark Swain
Figure 2.1: Existing Torsion Machine
Notes: The reason for limited plate thickness is not a matter of cost, however it is a matter of geometry. When the Munitions Directorate is fabricating components of the munitions they use raw stock that is as close to final shape as possible to conserve waste material. In order to properly characterize the materials that end up in a product they have to simply test similar geometry in order the get accurate results.

## Slide 4: DIC (Digital Image Correlation)
“DISTRIBUTION A: Approved for public release, distribution unlimited. (96ABW-2014-1649)”
Figure 3.2 Example DIC use in torsion sample
Figure 3.1 DIC setup at Eglin AFRL
Mark Swain

## Slide 5
Figure 5.1: CAD representation of design
Design Overview
Mark Swain
Steel Shaft
32”
13”

## Slide 6: Load Generation: AC Gearmotor
Vendor: Grainger
Rpm: 18
Gear ratio: 95:1
Max torque: 116 Nm
Weight: 26 lbs
Figure 5.1: AC Gearmotor
Mark Swain

## Slide 7: Motor Control
Vendor: Automation Direct
Single phase input, three phase output
Digital keypad
Forward and reverse
Expandable
Variable Frequency Drive (VFD)
Figure 6.1: VFD keypad
Mark Swain

## Slide 8: Motor Testing
Testing the interface between motor and VFD
Currently capabilities
  Forward and reverse motion by button press
  RPM/Torque control
Desired capabilities
  Set specific shaft rotation
Figure 7.1: Testing of motor and VFD capabilities
Mark Swain

## Slide 9: VFD Parameter Selection
Example: Input motor base RPM
  Select parameter group P0.00 [Program]
  Select setting P0.03[Enter]
  Set motor RPM [Enter]
Figure 8.1: VFD parameter selection flow
Mark Swain

## Slide 10: Load Measurement
Measuring components provided by AFRL
  DIC
  Strain gauges
Coupler material: Al 6061
Shaft properties
  Shear modulus: 26 GPa
  Shear strength: 76 MPa
  Length: 7.6 cm
  Diameter: 1.9 cm
  Expected shear stress for
    Al 2024: 29.5 MPa
    Titanium: 51.5 MPa
Figure 9.1: Stress vs. strain plot showing the shear modulus relationship
Mark Swain
G =

## Slide 11: Load Application: 6-Jaw Chuck
Vendor: LittleMachineShop
Weight: 6.4 lbs
Outer diameter: 3.94 in
Inner diameter: 1.02 in
Figure 10.1: 6 Jaw Chucks holding specimen
Reginald Scott

## Slide 12: Linear Motion: 2 Rail Ball Bearing Guide
Vendor: Grainger
½ inch Steel rails
Slot design to ensure alignment
Figure 11.1: Linear guide system
Reginald Scott

## Slide 13: Housing Design
Steel frame and housing
Shape: hollow square shaped cross-section
Frame dimensions:
  1/8 in inner supports – 304 stainless steel
  1/8 in outer frame - low carbon 1015 steel
Figure 12.1: CAD drawing of frame (bottom view)
Reginald Scott

## Slide 14: Machining Progress
Figure 13.1: Motor shims and connectors
Figure 13.2: Preassembly without welds
Reginald Scott

## Slide 15: Challenges
Budget
Motor Control
  Learning how to use a VFD
Assembly Issues
  Difficulties in machining/assembling
Sponsor Communication
  Scheduling conflicts due to more pressing matters
Delivery of critical components (i.e. coupler material)
Reginald Scott

## Slide 16: Budget
Chart: 
| Load Measurement | Load Generation | Load Application | Linear Motion | Housing | Miscellaneous | Travel
 | 0 | 816.55 | 458.94 | 331.48 | 181.9 | 50 | 0
Budget: $2,000
Spent: $1,839
Net: + $161
Reginald Scott

## Slide 17: Plan of Action
Reginald Scott

## Slide 18: Conclusion
Goal Statement
  Design a more effective way of testing small specimens in free-end torsion.
Next Phase
  Assemble (welding)
  Testing
  Eglin visit for strain gauge placement
Figure 17.1: Design slated for production
Reginald Scott
Notes: Completion of initial design sketches- Preliminary calculations- Design selection for full CAD build- Full CAD build

## Slide 19: Questions?

## Slide 20: References
Carter, B. (2008). Texas Instruments: Op Amp Noise Theory and Applications. Retrieved September 22, 2014
Flater, P. (2014). Tabletop Torsion Test. Eglin, FL: Air Force Research Laboratory.
Ilic, M. (2014, October 11). Clamp for centering. Retrieved from GRABCAD: https://grabcad.com/library/stega-za-centriranje-clamp-for-centering-1
Lathe Chuck. (2014, October 7). Retrieved from GRABCAD: https://grabcad.com/library/lathe-chuck-3
Linear Motion Systems. (2014, September 28). Retrieved from Stock Drive Products: https://sdp-si.com/eStore/coverpg/linearmotion.htm
http://www.centuryspring.com/info/spring_measurement.php - spring picture
Mark Swain

## Slide 21: Specimen Dimensions
Brendan Keane

## Slide 22: Appendix