## Slide 1
Sponsored by
Kim Sash &
The Tall Timbers Research Station and Land Conservancy
In partnership with
Dr. Gupta, Dr. Shih, Dr. Clark, Dr. Harvey, Dr. Frank &
The FAMU-FSU College of Engineering
Presented by
Jane Bartley, ME (team leader)
Bridget Leen, ME
Colin Riley, Lead EE
Also featuring
Jordan Muntain, ME
Lester Nandati, Lead ME
Sina Sharifi-Raini, EE
The Gopher Tortoise Scope

## Slide 2
Background and objectives
Subsystem breakdown
  Specifications
  Integration
  Prototypes
Project management
  Budget overview
  Work to be completed
Presented by Jane Bartley
Overview

## Slide 3
Tall Timbers research focuses on fire dependent ecosystems
One species they study is the gopher tortoise
  They are a keystone species
  Burrows are a maximum of 15m long
  Function of the scope is to take population surveys
Presented by Jane Bartley
Background
Figure 1. Gopher tortoise emerging from his burrow. [1]

## Slide 4
Our objective is to create a design that is:
  Durable
  Capable
  Portable
  Affordable
Presented by Jane Bartley
Objectives and Goals
“The main goal is to design a mechanism that has testing sensors, better durability, and more advanced video capabilities than the current system in order to enhance the surveying process of gopher tortoises.”

## Slide 5
Rover
  Navigates under ground
  Carries camera and sensors
User Interface
  7 inch screen
  Gamepad for controls
  Linux based OS
Battery
Tether
Presented by Bridget Leen
Top Level Design
Rover
User Interface
Battery
Active USB
RCA Video
Data
Power
Above Ground
Below Ground
Notes: Tether weight

## Slide 6
Chassis
Casing
  1/8 inch IR transmitting Plexiglas
  Construction
    Laser cut
    Adhere with silicone sealant
Treads
  Lynxmotion Tracks - Polypropylene/rubber
  Cut width of 2 inch treads in half
Presented by Bridget Leen
Rover Body
Figure 2. CAD drawing of chassis body.

## Slide 7
Simplified design
  Aileron system
  Panning only
Justifications
  Wide angle lens
  Simpler mechanism
  Less space
  Servo motor
Presented by Bridget Leen
Pan Servo
Figure 3. Prototype aileron system.

## Slide 8
Gears and motors are fully enclosed
200:1 gear ratio
High torque - 0.706 N·m
90 degree output
  Easily positioned in the chassis
  Allows shaft to be connected to the axle
Presented by Jane Bartley
Gearmotors
Figure 4. 200:1 Plastic gearmotors (dimensions in mm) [2]
Notes: -Other gearbox was too rudimentary; not enclosed

## Slide 9
Decided to use waterproof connections instead of hand-crafted stops.
Features:
  Kevlar
  50 ft
  3/4 in
  Tensile strength- 440 ksi
Presented by Jane Bartley
Tether
Figure 5. Kevlar expandable braided sheathing. [3]
Notes: -ksi- killa pounds per square inches

## Slide 10
DHTxx sensors measure both temperature and humidity
One wire communication
Code written for the DHT11 is compatible with the DHT22
The DHT22 measures:
  Relative Humidity from 0% to 100% with ±2% accuracy
  Temperatures from -45°C to 125°C with ±0.2°C accuracy
Presented by Colin Riley
Sensors
Figure 6. The DHT11 (blue) and DHT22 (white) temperature/humidity sensors. [4]
Notes: Image source: https://learn.adafruit.com/dht/overview
Content source: http://www.adafruit.com/datasheets/DHT22.pdf

## Slide 11
12 V power is supplied by a buck converter connected to the tether
5 V power is supplied by an output pin on the motor driver
All components share a common ground
Arduino Micro controls all data lines
Presented by Colin Riley
Electrical Schematic

## Slide 12
Main loop of program has been kept as short a possible
Majority of the code is located in functions, which can be called from the main loop
Open-source libraries of code were used instead of custom solutions when possible
Code has been heavily commented to increase readability
Presented by Colin Riley
Rover Programming

## Slide 13
Presented by Colin Riley
Rover Electronics Testing

## Slide 14
Initial prototype
  Built in November
  Off-the-shelf hobby kit
Recent progress
  Laser-cut ABS chassis body and casing
  Custom treads
  Simultaneously controlled motor driver, servo and temp/humidity sensor
Presented by Bridget Leen
Prototypes
Figure 7. Initial prototype (top) and recent prototype (bottom).

## Slide 15
Spent about 54% of total budget
  Two prototypes
  Testing
  New components
Still need:
  Tether connection
  Raw materials
Presented by Bridget Leen
Budget
Figure 8. Budget burn chart.

## Slide 16
Rover
  Solder component connections
  Outdoor testing
  Control testing
  Water resistance
  Fashion axles
  Test durability of the plexiglass
User Interface
  Create a program to read commands from the gamepad
  Build permanent casing
Presented by Colin Riley
Future Work
Notes: Image distortion

## Slide 17
Identified needs and objectives
Integrated components
Began construction of above and below ground subsystems
Completed initial testing
Started construction of a second stage prototype
Presented by Jane Bartley
Summary

## Slide 18
"Gopher Tortoise." Wildlife. Meryman Environmental, n.d. Web. 20 Jan. 2015. <http://merymanenvironmental.com/gopher-tortoise/>.
"Pololu - 200:1 Plastic Gearmotor, 90° Output." Pololu - 200:1 Plastic Gearmotor, 90° Output. Pololu, 2015. Web. 16 Feb. 2015. <https://www.pololu.com/product/1120>.
"Kevlar Expandable Braided Sleeving." Kevlar Expandable Braided Sleeving. Cable Organizer, 2015. Web. 16 Feb. 2015. <http://www.cableorganizer.com/kevlar/#features>.
"DHTxx Sensors." Overview. Adafruit, 29 July 2012. Web. 16 Feb. 2015. <https://learn.adafruit.com/dht/overview>.
Presented by Jane Bartley
References

## Slide 19
Presented by Jane Bartley
Questions?
For more information go to:
eng.fsu.edu/me/senior_design/2015/team21

## Slide 20
Appendix: Gantt Chart