## Slide 1
Sponsored by
Kim Sash &
The Tall Timbers Research and Land Conservancy
In partnership with
Dr. Gupta, Dr. Shih, Dr. Helzer, Dr. Clark, Dr. Harvey, Dr. Frank &
The FAMU-FSU College of Engineering
Presented by
Jane Bartley, ME (Team Leader)
Lester Nandati, Lead ME
Sina Sharifi-Raini, EE
Also featuring
Bridget Leen, ME
Jordan Muntain, ME
Colin Riley, Lead EE
The Gopher Tortoise Scope

## Slide 2
Background
Needs Analysis and Objective
Component Breakdown
Chassis Determination
and Mobility
Prototype Progress
Budget Analysis
Future Challenges
Scheduling
Summary
Presented by Lester Nandati
Overview
Figure 1. Gopher tortoise [1]
Notes: Plexiglass slide
Picture of tortoise: http://blog.safariltd.com/keystone-species-gopher-tortoise/

## Slide 3
Tall Timbers research focuses on fire-dependent ecosystems
One species they study is the gopher tortoise
  Keystone species
  Burrows are a maximum of 15m long
  Function of the scope is to take population surveys
Presented by Jane Bartley
Background
Figure 2. Gopher tortoise burrow [2]

## Slide 4
Current scope design flaws
  Cumbersome and heavy
  Not waterproof or shockproof
  Lack of data acquisition capability
  Poor visibility from mud and dirt
Our device must be:
  Durable
  Capable
  Portable
  Affordable
Presented by Jane Bartley
Needs and Objective
Figure 3. Tall Timbers current gopher tortoise scope
Notes: Scale or description of current scope size

## Slide 5
User Interface
Rover
Battery
  12V 14AH
  5 hour operation
  0.73 kg
Tether
  RCA
  12V power
  Active USB
Presented by Sina Sharifi-Raini
Top Level Design
Rover
User Interface
Battery
Active USB
RCA Video
Data
Power
Above Ground
Below Ground
Notes: Tether weight

## Slide 6
Screen
  7 inch diagonal
  800x480 pixels
  Powered by USB
Microprocessor
  Raspberry Pi B+
  Four USB ports
    Screen
    Arduino
    RCA adaptor
    Gamepad
Presented by Sina Sharifi-Raini
User Interface
Microprocessor
From Battery
USB
RCA from Rover
USB from Rover
Data
Power
HDMI
USB
Notes: cost

## Slide 7
Presented by Sina Sharifi-Raini
Proposed User Interface
Pan/Tilt Motors
Rover Motors
Power Off
Capture Image
Pause Recording
Stop Recording
Start Recording

## Slide 8
IR camera with LEDs
  720x480 pixels
  12V power
Two motor drivers
  Four motors
  12V power input
Data acquisition unit
  Temperature by RTD
  Relative humidity
Microcontroller
  Arduino Micro
  Micro USB port
Presented by Sina Sharifi-Raini
Rover
Microcontroller
Pan/Tilt Motors
Motor Driver
Humidity Sensor
Temperature Sensor
Data
Power
Chassis Motors
From Battery
USB from UI
RCA to UI
From Battery
Notes: Label parts to bullet points?

## Slide 9
Advantage over triangular
  Stability
  Fits in small spaces
  Adjustable height
Advantage over wheeled
  Increased traction
  (51.6 cm2 versus 8.4 cm2)
  Less power needed
    (3W versus 6W)
  Less likely to be rendered immobile
Presented by Lester Nandati
Chassis Determination
Figure 4. CAD assembly and physical prototype [3]
Notes: Pic of cardboard chassis
Better word than jam

## Slide 10
Material structural integrity
  Maximum stress on body: 177.6 kPa
  Yield strength: 110 MPa
  Flexural strength: 115 MPa [6]
Mobility
  Estimated friction: 5.4 N
  Forward force: 35 N
Casing
  Weight
  IR capable
Presented by Lester Nandati
Rover Functionality
Figure 6. Plexiglass initial testing
Figure 5. FEM Von Mises stress distribution on body
177.6 kPa
25.4 kPa
Notes: Overcome friction resistance from tether
Video from plexiglass
Casing dimensions
Camera field of vision
Curved front glass

## Slide 11
Presented by Jane Bartley
Prototype Analysis
Chassis prototype is
  11.4 cm wide
  5.7 cm tall
  0.157 kg
Performed initial tests
  Incline test of 45 degrees
  Confirmed components fit in chassis
Observed obstacles
  Tread durability
  Housing the chassis in plexiglass
Figure 7. Chassis incline test
Notes: Test angle limits
Average rover speed
Tread durability – at 35 deg, rover starts to slip at top

## Slide 12
Presented by Jane Bartley
Prototype Analysis
Further improvements
  Complete chassis body
  Plexiglass housing
  Human-computer interaction
Future testing
  Placing camera and pan and tilt system
  Building a mock burrow
  Subterranean mobility
Figure 8. Chassis prototype with components inside the body
Notes: PIC of fully ‘assembled’ prototype

## Slide 13
Spent about 13% of total budget
  First prototype
  Testing
  Permanent
  components
  Spares
Still needed
  Casing
  Treads
  Tether
  Battery
Presented by Jane Bartley
Budget
Figure 9. Total budget burn chart

## Slide 14
Controller implementation
Video to Raspberry Pi
Casing
Tether
Weatherproofing
Glare mitigation
Reproducibility
Presented by Lester Nandati
Future Challenges
Notes: Image distortion

## Slide 15
Presented by Lester Nandati
Gantt Chart and Scheduling
Notes: Project/task based gantt chart for future work

## Slide 16
Identified problems with current scope design
Analyzed component needs
Determined final design concept
Constructed prototype
Began testing
Established a schedule
Presented by Sina Sharifi-Riani
Summary

## Slide 17
Schurr, Jennifer. "Keystone Species: Gopher Tortoise." Safari Ltd. N.p., 25 Aug. 2014. Web. 19 Nov. 2014. <http://blog.safariltd.com/keystone-species-gopher-tortoise/>.
"Florida Scrub Nature Trail." Florida Scrub Nature Trail. N.p., n.d. Web. 10 Nov. 2014.
"Mini RobotShop Rover Chassis Kit." Mini RobotShop Rover Chassis Kit. RobotShop, 2014. Web. 14 Oct. 2014. <http://www.robotshop.com/en/mini-robotshop-rover-chassis-kit.html>.
"6V DC Motor 340mA 14400RPM." Xump Science Supplies, Toys & Gifts. Xump, 2014. Web. 11 Nov. 2014. http://www.xump.com/science/6V-DC-Motor-340mA-14400RPM.cfm.
"Arduino Micro without Headers - 5V 16MHz ATmega32u4." Adafruit. Adafruit, 2014. Web. 11 Nov. 2014. <http://www.adafruit.com/products/1315>.
"Raspberry Pi B+ Broadcom BCM2835 SoC ARM11 700 MHz Low Power ARM1176JZFS Applications Processor Motherboard/CPU/VGA Combo." Newegg. Newegg, 2014. Web. 10 Nov. 2014. <http://www.newegg.com/Product/Product.aspxItem=N82E16813142003>.
"Properties of PLEXIGLAS," Plexiglas. Evonik Industries. 2010. Web 17 Nov. 2014. <http://www.plexiglas.de/product/plexiglas/en/pages/privacy-policy.aspx>
References
Presented by Sina Sharifi-Riani

## Slide 18
Presented by Sina Sharifi-Riani
Questions?
For more information go to:
www.eng.fsu.edu/me/senior_design/2015/team21/

## Slide 19
Power analysis
Appendix
 | voltage (V) | current (A) | power (W) | Energy (KJ) per hour
rover motors | 3 | 0.9 | 2.7 | 9.72
camera motors | 6 | 2.68 | 16.08 | 57.888
Raspberry pi b+ | 5 | 0.6 | 3 | 10.8
Arduino Micro | 5 | 1 | 5 | 18
IR camera | 12 | 0.13 | 1.56 | 5.616
Gamepad | 5 | 0.5 | 2.5 | 9
Video display | 5 | 0.5 | 2.5 | 9
Total |  | 6.31 | 33.34 | 120.024
Battery: 168 Wh = 605 kJh

## Slide 20
Appendix