## Slide 1
Sponsored by
Kim Sash &
The Tall Timbers Research Station & Land Conservancy
In partnership with
Dr. Gupta, Dr. Shih, Dr. Clark, Dr. Harvey, Dr. Frank &
The FAMU-FSU College of Engineering
Presented by
Jordan Muntain, ME
Bridget Leen, ME
Colin Riley, Lead EE
Jane Bartley, ME (Team Leader)
Lester Nandati, Lead ME
Sina Sharifi-Raini, EE
The Gopher Tortoise Scope

## Slide 2
Background & field research
Design Process
  Component selection
  Final design details
  Initial testing
Project management
  Budget overview
  Work to be completed
Presented by Jane Bartley
Overview

## Slide 3
Sponsor of project: Kim Sash, conservation biologist at Tall Timbers
One species she studies is the gopher tortoise
  Keystone species
  Burrows are an average of 6m long (maximum 15m)
  Function of the scope is to take population surveys
Presented by Jane Bartley
Background
Figure 1. Gopher tortoise emerging from his burrow. [1]

## Slide 4
Design team took a trip to Tall Timbers
Scoped several burrows along with Kim
Able to use the current scope to identify issues and items for improvement
Presented by Jane Bartley
Tall Timbers Expedition
Figure 2. Design team scoping a burrow.

## Slide 5
Current scope design flaws:
  Cumbersome and heavy
  Not waterproof or shockproof
  Lack of data acquisition capability
  Poor visibility from mud and dirt
Presented by Jane Bartley
Current Scope
Figure 3. Tall Timbers current scope.

## Slide 6
Our objective is to create a design that is:
  Durable
  Capable
  Portable
  Affordable
Presented by Bridget Leen
Objectives and Goals
“The main goal is to design a mechanism that has testing sensors, better durability, and more advanced video capabilities than the current system in order to enhance the surveying process of gopher tortoises.”

## Slide 7
  Camera Options
  Wide view color infrared camera (top)
    7 IR bulbs
    Night vision range of 6 meters
  All in one security camera (bottom)
    Already has weatherproof case
    Pan and tilt system built in
Build Pan System
  Adding tilt will be excess due to camera’s wide view range
  Custom fit to camera and chassis
  Smaller than off-the-shelf
Presented by Bridget Leen
Choosing a Camera
Figure 4. Camera designs. [2,3]
Notes: Compare to the all in one system
Get those notes from Sina

## Slide 8
Linear track
  Stability
  Fits in small spaces
  Adjustable height
Advantage over wheeled
  Increased traction
  Less likely to be rendered immobile
Presented by Bridget Leen
Choosing a Chassis
Figure 4. Triangular tracked and linear tracked chassis.
Notes: Hoping Jane can add the triangular track CAD to the bottom of this one

## Slide 9
User Interface
Rover
Battery
  12V
  5 hour operation
  1.5 lbs
Tether
  Video
  12V power
  Data
Presented by Sina Sharifi-raini
Final Design
Rover
User Interface
Battery
Active USB
RCA Video
Data
Power
Above Ground
Below Ground

## Slide 10
Screen
  7 inch display
  Similar in size to the Ipad Mini
Logitech gamepad
Microprocessor
  Raspberry Pi B+
  Runs a Linux OS
  Functions like a computer
Presented by Sina Sharifi-raini
User Interface
Microprocessor
From Battery
USB
RCA from Rover
USB from Rover
Data
Power
HDMI
USB
Notes: cost

## Slide 11
Presented by Sina Sharifi-raini
User Interface
Pan Motors
Rover Motors
Power Off
Capture Image
Pause Recording
Stop Recording
Start Recording

## Slide 12
Infrared camera
  Can see in the dark
  Limits disturbance
Motors and motor drivers
Temperature and humidity sensor
Microcontroller
  Arduino Mircro
  Executes simple instructions sent to it by the microprocessor
Presented by Colin Riley
Rover
Microcontroller
Pan Servo
Motor Driver
Data
Power
Chassis Motors
USB from UI
RCA to UI
Temperature & Humidity Sensor
DC Buck Converter
Power from Battery
Notes: Label parts to bullet points?

## Slide 13
Tether
Electrical wiring
  RCA
  Active USB
  10-gauge speaker wire
Kevlar sheath
  Weather/abrasive contact durable
  Lightweight (0.21 kg for 15 m) [2]
No steel guide wire
  Slack on wires inside body
  Stops on wires and sheath
Presented by Lester Nandati
Figure 3: Tether Tension Solution
Notes: http://www.cableorganizer.com/kevlar/
Diagram of new design

## Slide 14
Camera Movement
Simplified design
  Aileron system
  Panning only
Justifications
  Wide angle lens
  Simpler mechanism
  Less space
  Servo motor
Presented by Lester Nandati
Figure 4: Aileron system
Notes: Pic of aileron

## Slide 15
Materials tested:
  Infrared camera
  Infrared transmitting plexiglass
Confirmed that the camera works in the dark
Discovered that the orientation of the plexiglass is important
Presented by Colin Riley
Camera Testing
Figure 6. Initial testing of camera and plexiglass

## Slide 16
Materials tested:
  Gear box
  Motors
  Treads
Confirmed that the rover can navigate a variety of terrains
Learned that the final design needs wider, more durable treads
Presented by Colin Riley
Mobility Testing
Figure 7. Initial testing of chassis mobility

## Slide 17
Still over 70% of budget available
Spending changes
  Invest in more expensive parts
  Final components
  Allocate 20% to prototype testing
Presented by Lester Nandati
Budget
Figure 6. Budget burn chart.
Chart: Budget Forecast
| 41883 | 41925 | 41930 | 41940 | 41947 | 41950 | 41991 | 42017 | 42088
 | 2000 | 1970.4 | 1930.4 | 1802.36 | 1782.87 | 1730.51 | 1548.97 | 1344.49 | 644.49

## Slide 18
Controller implementation
Video to Raspberry Pi
Casing
Tether
Weatherproofing
Portability
Presented by Jordan Muntain
Work to be completed

## Slide 19
Conducted field research at Tall Timbers
Determined components
Constructed a final design concept
Tested an initial prototype
Established a schedule for future work
Presented by Jordan Muntain
Conclusion

## Slide 20
"Gopher Tortoise." Wildlife. Meryman Environmental, n.d. Web. 20 Jan. 2015. <http://merymanenvironmental.com/gopher-tortoise/>.
"Wide View Color Infra Red Camera with 7 IR LEDs." Wide View Color Infra Red Camera with 7 IR LEDs. SuperDroid Robots, n.d. Web. 14 Oct. 2014.
"Wide View Color Infra Red Camera with 7 IR LEDs." Wide View Color Infra Red Camera with 7 IR LEDs. SuperDroid Robots, n.d. Web. 14 Oct. 2014.
Presented by Jordan Muntain
References

## Slide 21
Questions?
For more information go to: http://www.eng.fsu.edu/me/senior_design/2015/team21/index.html

## Slide 22
Appendix: Gantt Chart