## Slide 1: Pedibus Team 22
Team Members:
Kyle Anderson
Stephen Avery
Alejandro San Segundo
Brett Willenbacher
Team No.22
Slide 1 of 20
Alejandro San Segundo
Midterm II
Sponsor:
Ron Goldstein
Advisor:
Keith Larson
Professors:
Dr. Shih
Dr. Helzer
Dr. Gupta

## Slide 2: Overview
Design Changes
Component Acquisition
  Raw Material
  Powertrain Components
  Rolling Components
Entering Fabrication Phase
  Frame
  Powertrain/Steering
Team No.22
Slide 2 of 20
Alejandro San Segundo
Midterm II

## Slide 3: What is the Pedibus?
Team No.22
Slide 3 of 20
Alejandro San Segundo
Midterm II

## Slide 4: Design Requirements
Team No.22
Slide 4 of 20
Alejandro San Segundo
Midterm II
Pedibus Requirement | Status
10 pedaling passengers | 
Room for extra (non-pedaling) passengers | 
Rolling Chassis must be < 1499 lbs (FL law) | 
Off the Shelf parts | 
Torque output to climb 8° hill grade | 
Able to hold 3000 lbs payload | 
Free weight transportable | 
Reverse gear capability | 
Movable on single rider input | 
Notes: Point 1: 10 Peddlers, 1 driver, 1 “bartender”, and 2 non-peddlers
Point 2: Because of Tallahassee’s hills a crawl gear and cruise gears are recomended

## Slide 5: Chassis Modifications
Eliminated Suspension (torsion axle for towing)
Recumbent Sitting Style
FEA Analysis Concluded Tubing Wall Thickness
A500 Structural Box Steel Construction
Manipulated Dimensions and Angles to Reduce Vehicle Width
Team No.22
Slide 5 of 20
Brett Willenbacher
Midterm II

## Slide 6: Frame Evolution
Team No.22
Slide 6 of 20
Brett Willenbacher
Midterm II
Box Design
Ladder Design w/ Suspension

## Slide 7: Final Frame
Team No.22
Slide 7 of 20
Brett Willenbacher
Midterm II
Final Ladder Frame Design
w/o Integrated Suspension

## Slide 8: Torsion Bar Implementation
Team No.22
Slide 8 of 20
Brett Willenbacher
Midterm II
Eliminates Need for Towing Suspension System
Lockable Steering No Longer Required
Extra Brake Set for Towing Safety

## Slide 9: Frame FEA Testing
Team No.22
Slide 9 of 20
Brett Willenbacher
Midterm II
4500 lb Force on Seat Posts
500 lb Force on Bar Post
1.3 Factor of Safety
Max Deformation of 0.13 in

## Slide 10: Wheels & Brake System
Team No.22
Slide 10 of 20
Brett Willenbacher
Midterm II
Axle | Brakes | Wheels | Tires | Bolt Patterns
Rolling | 12” Hydraulic Disc | 16” | 175/50/R16 185/60/R16 | 5 on 4.5”
Towing | 12” Electric Drum |  |  | 
VS.

## Slide 11: Dual Shaft Design
Team No.22
Slide 11 of 20
Alejandro San Segundo
Midterm II
Eliminates Chain Cross Over
Reduces Torque on Individual Shaft
  Reduce Cost and Weight
Simpler Design for Free Coasting
Peddler Input Design Decision Matrix |  |  |  |  | 
 | Safety | User Comfort | Complexity | Reliability | Weighted Sums
Cross Chained Linkage | 6 | 6 | 7 | 2 | 132
Dual Drive Shaft Chain Drive | 6 | 7 | 4 | 7 | 161
Pump Motion Crankshaft Linkage | 4 | 4 | 1 | 8 | 120
Crossed Chain System
Double Shaft System

## Slide 12: Drivetrain Steering
Peerless 820-040
  Manual Transaxle
  6 speed Including Reverse
Clutch System
  Shift-on-the-Fly
  Belt Friction Clutch (adjustability)
Dual Driveshaft to Single Transaxle Design
Team No.22
Slide 12 of 20
Alejandro San Segundo
Midterm II
No Need for Lockable System
Curb to Curb < 45 ft
  Reasonable U-Turn Diameter
Rack and Pinion
  Easy to Source and Implement

## Slide 13: Ergonomics
Driver Chair
  Pivoting for Easy Access
  Back Support for Reduced Fatigue
Bar Top Positioning
  Height and Width Optimized for Comfort
  Groove Pattern or Handrail for Rider Support
Free Wheeled Driveshaft
  Allows for Individual Cadence
  Prevents Rider Back-Driving
Team No.22
Slide 13 of 20
Alejandro San Segundo
Midterm II

## Slide 14: Peddler Ergonomics
Bench Style Seating
  Relaxed Stands Reduces Back Stress
  Inclined Sitting Ensures 90° Hip Angle
Crank Positioning & Rider Angle
  Comfortably Accommodates 5’1” to 6’4” Peddler
Team No.22
Slide 14 of 20
Alejandro San Segundo
Midterm II
+
=
Compact and Upright Recumbent Stance
Θ ≈ 20°
~20° Incline on bench to ensure proper riding stance

## Slide 15: Safety and Testing
Large Vehicle Footprint
  Increased Stability
  Floorboards to Cover Moving Parts
Pre-Fabrication Frame Analysis
  SolidWorks FEA 
  MATLAB Speed and Force calculations
Post-Fabrication Testing
  Road Testing Prior to Release
Team No.22
Slide 15 of 20
Alejandro San Segundo
Midterm II

## Slide 16: Sourcing and Ordering
Team No.22
Slide 16 of 20
Alejandro San Segundo
Midterm II
Part | Company/Brand | Estimated Cost | Order Date
Frame (Steel) | Metal Fabrication | $400 | 11/19
Transaxle | Peerless | $700 | 11/19
Bicycle Components | Retrospec and Sunlite | $850 | 11/21
Torsion Bars | Northern Tool | $189 | 11/26
Brake System | Wilwood, Jegs, & Tiedown | $950 | 11/26
Wheels and Tires | TBA | TBA | 11/26
Steering | TBA | TBA | TBA
Miscellaneous | TBA | $450 | TBA
** Prices and sourcing subject to change as per sponsor request

## Slide 17: Future Considerations
Adjustable Height Roof
  Fiberglass Hardtop or Canvas T-top
Hitch Mounted Modular Accessories
  Grill, Cooler, or Additional Seating
  Re-evaluation of Electronics
    Digital Advertisement
    LED Lighting
    Sound System
Team No.22
Slide 17 of 20
Brett Willenbacher
Midterm II

## Slide 18: Timeline
Team No.22
Slide 18 of 20
Brett Willenbacher
Midterm II

## Slide 19: Summary
Frame Finalized
Slight Delay Due to Frame Adjustments
Most Components Sourced and Selected
Ordering Starts Tomorrow!
Team No.22
Slide 19 of 20
Brett Willenbacher
Midterm II

## Slide 20
Team No.22
Slide 20 of 20
Alejandro San Segundo
Brett Willenbacher
Midterm II
Questions?