## Slide 1: Midterm 1 Pedibus Team #22
Team Members:
Kyle Anderson
Stephen Avery
Alejandro San Segundo
Brett Willenbacher
Sponsor:
Ron Goldstein
Advisor:
Keith Larson
Professors:
Dr. Shih
Dr. Helzer
Dr. Gupta
Team No.22
Slide 1 of 14
Kyle Anderson
Midterm 1

## Slide 2: Overview
Currently in Design Phase
  Frame Design
  Steering Design
Component Sourcing
  Price vs. Performance
  Availability
  Lead Times
Team No.22
Slide 2 of 14
Stephen Avery
Midterm 1

## Slide 3: Design Requirements
10 -14 person Seating Arrangements
  Bench Seating and Captain’s Chair
Rolling Chassis must be < 1499 lbs
  Towing Legalities
Must be Transportable
“Off the Shelf”
Team No.22
Slide 6 of 14
Stephen Avery
Midterm 1
Notes: Point 1: 10 Peddlers, 1 driver, 1 “bartender”, and 2 non-peddlers
Point 2: Because of Tallahassee’s hills a crawl gear and cruise gears are recomended

## Slide 4: Current Design
Bench Seating
  Increased Seating Capacity
All Steel Construction
Multi-Speed F-N-R Transaxle
Towing Accommodations
Team No.22
Slide 5 of 14
Kyle Anderson
Midterm 1

## Slide 5: Chassis Construction
A500 Structural Box Steel Construction
Main Frame Rails 48” Apart
Ladder Style Frame
Team No.22
Slide 7 of 14
Stephen Avery
Midterm 1
 | Weight: | Price: | Rigidity: | Machinability: | Total:
Decision Weight: | 5 | 3 | 2 | 7 | 17
A500 Steel | 5 | 9 | 9 | 7 | 119
6061 Aluminum | 8 | 6 | 4 | 4 | 94

## Slide 6: Steering Requirements
Tow Ready Steering
  Fully Lockable
  Tow Rated Components
Curb to Curb < 45 ft
  Reasonable U-Turn Diameter
Rack and Pinion
  Easy to Source and Implement
Team No.22
Slide 8 of 14
Kyle Anderson
Midterm 1

## Slide 7: Drivetrain
Peerless 820-040
Clutch System
  “Shift-on-the-Fly”
  Belt Friction Clutch
Team No.22
Slide 9 of 14
Stephen Avery
Midterm 1
 | Durability | Cost | Modularity | User Fatigue | Maintenance | Complexity | Total:
Weight: | 8 | 4 | 2 | 6 | 6 | 2 | 28
Hydrostatic Transaxle: | 2 | 8 | 6 | 6 | 4 | 2 | 124
Manual Transaxle: | 7 | 4 | 8 | 8 | 8 | 3 | 190
Vehicle Axle: | 10 | 6 | 2 | 2 | 7 | 8 | 178

## Slide 8: Wheels and Brakes
Front 13” Disc Brakes
16” Wheel
  Brake Accommodations
5 on 4.5” Bolt Pattern
175/50/R16 – 185/60/R16 size tire
Emergency Brake
Team No.22
Slide 10 of 14
Stephen Avery
Midterm 1

## Slide 9: Ergonomics
Driver’s Chair
  Swiveling for Easy Access
  Seat Back for Reduced Fatigue
Bench Seating
  Narrow Seat for Easy Pedaling
  Seat Back Isolates Passengers
Free Wheeled Driveshaft
  Allows Individual Pace
  Does not Allow Back Driving
Team No.22
Slide 10 of 14
Stephen Avery
Midterm 1

## Slide 10: Safety and Testing
Large Vehicle Footprint
  Increased Stability
Floorboards
Pre-Fabrication Analysis
  SolidWorks FEA
  Matlab Force Calculations
Post-Fabrication Testing
  Road Testing Prior to Release
Team No.22
Slide 10 of 14
Stephen Avery
Midterm 1

## Slide 11: Future Considerations
Roof or Awning
Hitch Mounted Modular Accessories
  Grill, Cooler, or Additional Seating
  Re-evaluation of Electronics
    Digital Advertisement
    LED Lighting
    Sound System
Team No.22
Slide 4 of 14
Kyle Anderson
Midterm 1

## Slide 12: Timeline
  Add Gannt chart
Team No.22
Slide 12 of 14
Kyle Anderson
Midterm 1

## Slide 13: Summary
Significant Progress
  Initial Designs
  Component Selection and Sourcing
Remain on Schedule
Finish Designs
Start Fabrication
Team No.22
Slide 13 of 14
Stephen Avery
Midterm 1

## Slide 14: Questions
Team No.22
Slide 14 of 14
Stephen Avery
Midterm 1