## Slide 1: SoutheastCon Team 1A
Milestone 2 Report: Project Proposal and Statement of Work

## Slide 2: IEEE SoutheastCon Hardware Competition
Team 1A:
  Nils Bjeren
  Donovan Carey
  Christopher Lewis
  Kurt Marsman
  James Pace
  Ryan-David Reyes
  Julian Velasquez
Faculty Advisors:
  Dr. Mike Frank
  Dr. Bruce Harvey
  Dr. Carl Moore
  Dr. Linda DeBrunner
  EEL4911C: Senior Design 1
  Fall 2014
  September 24th

## Slide 3: Requirements
Sense a red LED (start condition)
Navigate according to the white line
Detect the sequence on a Simon Says game
Actuate the correct button sequence on a Simon Says game
Twist both knobs on an Etch-a-Sketch
Twist exactly one row of a Rubik’s Cube
Pick up and carry a single playing card

## Slide 4: Limitations
Robot must be fully autonomous
Robot must fit inside a 1’ by ‘1 by 1’ box at the beginning and end of a run
Robot cannot split into multiple pieces
Robot must contain no flammable liquids, explosives, high pressures, or otherwise dangerous elements
The course must be completed in less than 5 minutes

## Slide 5: Preliminary design
Arduino Mega 2560 is the main controller
Wheels are omnidirectional Mecanum
DC motors with encoders are used for propulsion
Line following subsystem:
  9 IRR Sensors with dedicated Arduino Mini Pro
2 “challenge” subsystems with dedicated microcontrollers:
  Rubik/Simon subsystem
  Etch-a-Sketch/Playing card subsystem

## Slide 6: Project Management
Team Manager: Nils Bjeren
  Coordinates the project as a whole
  Serves as interface between team and ECE faculty
  Is responsible for continued progress being made
Head Programmer/Control Engineer: Ryan-David Reyes
  Oversees and maintains stable versions of all code
  Implements omnidirectional motor control
  Implements communication between subsystems
Head Mechanical Engineer: James Pace
  Has the final say on all mechanical/structural decisions
  Serves as interface between team and ME faculty
  Assures the structural integrity of the chassis

## Slide 7: Project Management
Financial Advisor/Power Engineer: Julian Velasquez
  Maintains budget and purchase record for the team
  Calculates power requirements
  Chooses battery units to satisfy power requirements
Secretary/Systems Engineer: Kurt Marsman
  Creates and maintains meeting minutes and other required documents
  Creates and maintains the system that ensures reliable start
  Assists in development of Rubik/Simon Says subsystem
Systems Engineer: Donovan Carey
  Creates the system-level design of the Etch-a-Sketch/Playing Card subsystem
  Submits software requirements to the Control Engineers
  Performs mechanical testing of the subsystem

## Slide 8: Project Management
Control Engineer: Christopher Lewis
  Works with Etch-a-Sketch/Playing Card systems engineer to establish software requirements
  Writes software for the subsystem
  Mentor and assist other team members with programming

## Slide 9: Concept Generation and Selection
Christopher Lewis
Donovan Carey

## Slide 10: Movement / Line Following Design
Differential Steering vs. Omnidirectional Steering
Infrared Reflective Sensors vs. Camera
Movement Design | Control (0.4) | Flexibility (0.6) | Total
Differential Steering | 4 | 1 | 2.2
Omnidirectional Steering | 3 | 5 | 4.2

## Slide 11: Chassis Design
U-Shaped Chassis
Hole in the Center Chassis
Square Shaped Chassis
Chassis Design | Support of Manipulation (0.4) | Structural Integrity (0.5) | Ease of Manufacture (0.1) | Total
U-Shaped | 4 | 2 | 2 | 2.8
Hole in the Center* | 4 | 3 | 3 | 3.4
Square Shaped | 3 | 5 | 5 | 4.2

## Slide 12: Communication
NO outside communication with the robot.
Communication Protocols
  I2C
    Lower Complexity in wiring
    More difficult to implement
    Communication errors affect entire system
  RS232 (serial)
    Requires Wiring from Mega to each subsystem
    Improved Reliability due to errors only affecting the local subsystem.

## Slide 13: Manipulator Arms
Pros:
Provides a simple means of interface between the autonomous robot and the different challenge
Can minimize the number of manipulators if similarities are found between the challenge games
Cons:
Robot must be perfectly aligned with the toys

## Slide 14: Simon Says/ Rubik’s Cube
Simon Says Implementation
Lower arm over the Simon game
Detect the game sequence using sound detection from a microphone
Analyze the sequence given by the game
Use the servo on the arm move the penetrator to the desired button
Lower the entire arm to press the desired buttons in the sequence given
Rubik’s Cube Implementation
Hold the Rubik’s in place using some type of gripping tool
Lower the arm onto the Rubik’s cube
Use the servo on the arm to turn the top row of the Rubik’s cube an entire 180 degrees
The design for playing the Simon Says game and the Rubik’s cube challenge both require the same circular motion.

## Slide 15
Figure 1: Custom Simon Says/Rubik’s Cube interface

## Slide 16: Etch a Sketch/ Playing Card
Etch a Sketch Implementation
Use a servo to lower the arm onto the game
Align the motors perfectly with the knobs using an adhesive
Use the frictional contact of the adhesive to work with the motors for movement of the knobs
Use the knobs to sketch IEEE into the toy in a timely fashion
Playing Card Implementation
Lower the arm onto the stack of cards
Use adhesive on arm to lift the playing card from the stack
Use the arm to then lift the card
Carry the playing card across the finish line
The design for the etch and sketch arm requires movement in the z-direction which can be used to pick up the playing card using adhesive.

## Slide 17: Power Systems
Propulsion Devices
DC motors with Encoders (x4)
Arduino Mega 2560 microcontroller
Manipulator Devices
Line Following Sensors (x9)
DC motors (x3)
Servos (x2)
Arduino Redboard (x2)
Arduino Mini
We are looking at using two Lithium Polymer(LiPo) for the power distribution to the robot. One of the batteries is intended for the propulsion system while the other will be used to power the manipulator subsystems.

## Slide 18: Alternative Solutions
Power System
Lithium Polymer (LiPo)
Nickel-metal hydride (NiMH)
Simon Says Sequence Detection
Light Detection
Sound Detection (frequency counter vs FFT)
Color Sensor
Simon Says Interface
Four-bar-linkage (single piston)
Four pistons
Etch-a-Sketch Manipulation
Claws
Adhesive between the mounted motors
and knobs
Frictional Contact on the side of the
knob
Rubik’s Cube Rotation
Use motor and adhesive
Servo attached to a manufactured piece
to rotate the row from the outside
Claw rotating around horizontal plane

## Slide 19: Preliminary System-Level Design
Ryan-David Reyes
James Pace

## Slide 20: Block Diagram

## Slide 21: Specifications
Chassis Size:
  Width: 7 in.
  Length: 7 in.
  Height: ½ in. from ground
Propulsion Motors:
  110 oz-in. stall torque
  Encoder: 1920 CPR
  350 RPM
  300 mA free run current
Mecanum Wheels:
  2 in. radius
Master Microcontroller Specs:
  Atmega 2560
  54 DIO, 16 AIO
  4 Serial IO
Batteries:
  2x LiPo 2.3 Ah

## Slide 22: Specifications
Photoresistor (Sense Start)
  5k-100k Ohm variable resistance
Line Following Sensors: IR Reflectivity
  Phototransistor output
  ½ in. effective range
Slave Microcontroller
  Atmega328p
  14 DIO

## Slide 23: Specifications
Rubik’s Cube Arm
Servo 1
  12 oz-in stall torque
  180 degrees of rotation
Servo 2
  93 oz-in stall torque
  360 degrees of rotation
Microphone
  5V Supply
  Requires 500x Output Amplification
Slave Microcontroller
  Atmega328p
  14 DIO

## Slide 24: Specifications
Etch-A-Sketch Arm
DC Motors
  20 oz-in stall torque
  120 RPM
Servo
  12 oz-in stall torque
  180 degrees of rotation
Slave Microcontroller
  Atmega328p
  14 DIO

## Slide 25: Overall Constraints
1 ft. by 1 ft. by 1 ft. size constraint at beginning and end.
Must be able to complete track in 5 minutes.
Robot must not split completely apart.

## Slide 26: Preliminary Overall Design

## Slide 27: Lower Level

## Slide 28: Electronics Level

## Slide 29: Arms

## Slide 30: Budget
Julian Velasquez

## Slide 31: Budget
Category | Cost
Wheels | $80.00
Motors | $300.00
Batteries/Chargers | $150.00
Microcontrollers | $300.00
Electronics | $200.00
Misc. Mechanical Parts | $170.00
Total: | $1,200.00
Budget estimate for milestone 1

## Slide 32: Budget
Purpose | Items | Cost
Simon Frequency Analysis | Miscellaneous Electronics | $11.47
Propulsion | Motor Drivers | $47.95
Battery Charger for Propulsion/Manipulators Batteries | Battery Charger | $40.08
Batteries for Manipulators | Battery | $27.75
Simon/Rubik’s Manipulator | Servo Motor | $19.40
Propulsion | Miscellaneous Equipment | $51.89
Propulsion | Motors for Propulsion | $177.25
Etch-a-sketch manipulator | Gearmounts | $20.35
Etch-a-sketch manipulator | Miscellaneous equipment | $20.11
Mecanum Wheels | Propulsion | $71.76
 | Total: | $508.01
Budget as of 10/17/14

## Slide 33: Budget
Personnel | Total Hours per Semester | Total Hours Worked Both Semesters | Total Base Salary ($30 per hour) | Total Salary + Fringe Rate of (29%)
1 Group Member | 192 | 384 | $11,520 | $14,861
Whole Team (7 Members) | 1,344 | 2,688 | $80,640 | $104,026
Personnel Cost
Direct Cost | Direct Cost + Fringe Rate + Overhead rate (45%) | Direct Cost + Overhead Rate (45%)
$81,148 | $151,574 | $117,665
Direct and Overhead Costs
Overhead costs refers to an ongoing expense of operating a business. I.e. rent, gas, electricity, and labor burden.

## Slide 34: Budget
Category | Expense ($)
Supplies and Small Items (Current) | $508.01
Additional Supplies and Small Items (Projected) | $691.99
Direct Cost + Fringe Rate + Overhead rate (45%) | $151,573.74
Total Project Cost: | $152,773.74
Total Project cost
Fringe rate is the cost of an employee’s benefits divided by the wages paid to an employee for the hours worked.

## Slide 35: Schedule
Julian Velasquez

## Slide 36: Schedule
Event | Date | Individuals Responsible
Simon Arm Prototype Complete | 11/6/2014 | Julian, Nils
Etch-A-Sketch Prototype Complete | 12/16/14 | Donovan, Chris, James
Line Following Complete | 11/4/14 | Nils, Ryan
Final Chassis Built | 2/4/15 | James
Local Competition | Late February | Whole Team

## Slide 37: Risk Assessment
Kurt Marsman

## Slide 38: Budgetary Risks
Design Requirements Not Met
  Buying wrong parts
  Proper planning
Scheduling
  Overall bottom line
  Gantt chart

## Slide 39: Hardware
Voltage and Current Associated with Design
  Motor Drivers
Motors on Robot Breaking
  Double check specs
Solarbotics L298 Compact Motor Driver

## Slide 40: Software
Errors in Code
  Version control
  GIT
No Walls on Track
  Refine code early on
  Have people ready to catch the bot

## Slide 41: Performance Risks
Precision
  Positioning
  Motor Encoder Decoder
Arm Alignment
  Axis of rotation
  Grabber Design
Sideways Movement
  Line following
  Forward motion with turn in place