## Slide 1: SAR Imager
Sponsor Presentation
March 2, 2016

## Slide 2: Team Members
Engineer | Role(s) | Major | School
Luke Baldwin | Main Structure | Mechanical | FSU
Olivier Barbier | Data Processing & Image Formation | Electrical & Computer | FAMU
Jordan Bolduc | Signal Processing | Electrical | FSU
Josh Dennis | ME Project Manager & Procurement | Mechanical | FSU
Scott Nicewonger | EE Project Manager & RF | Electrical | FSU
Kaylen Nollie | Secretary, Risk Management | Mechanical | FAMU
Desmond Pressey | Antenna Hardware & Webmaster | Mechanical | FAMU
Julian Rodriquez | Component Housing | Mechanical | FSU
Kegan Stack | Calibration & Alignment | Mechanical | FSU

## Slide 3: Introduction
Kaylen Nollie

## Slide 4: Outline
Project Scope
1st Generation
SAR Theory
Signal & Data Processing
SAR Structure & Horns
Calibration & Testing
Future Plans
KAYLEN NOLLIE

## Slide 5: SAR Introduction
What is an SAR?
Synthetic Aperture Radar: Typically, a single antenna is attached to an aircraft flying over a target zone capturing several high resolution images to create a single image map.
  Typically for Military
KAYLEN NOLLIE

## Slide 6: Project Scope
Objective:
  Develop a static, multi-antenna Synthetic Aperture Radar (SAR) Imager
    In brief: Giant metal detector
Why?:
  Security – Prevention of guns, knives, or dangerous objects from entering public facilities
    Schools
    Airports
    Office buildings
KAYLEN NOLLIE

## Slide 7: First Generation Goals
Create a Synthetic Aperture Radar:
  Project Features:
    Weapons detection for homeland security
    Multi-Antenna
    Stationary
    Low resolution
    Concealable
    Low Cost
    Relatively mobile
1st Generation Project – Class of 2015
KAYLEN NOLLIE

## Slide 8: Second Generation Goals
Mechanical Engineering
Mobility
Lower Weight
Horn Adjustment
Increase Stability
Minimize Cost
Electrical Engineering
Identify reflector at 20 feet
Standalone functionality
KAYLEN NOLLIE

## Slide 9: Current Status
Task | Design | Prototype | Optimization
Component Testing | ✔ | N/A | ✔
Signal Processing | ✔ | N/A | ○
Data Processing & Image Formation | ✔ | N/A | ○
Structure | ✔ | ✔ | ○
Component Housing | ✔ | ○ | ✘
Horn Holders | ✔ | ✔ | ○
Testing & Calibration Equipment | ✔ | ✔ | ○
Legend
✘ - Not Started
○ - In Progress
✔ - Completed
KAYLEN NOLLIE

## Slide 10: Project Overview & Theory of Operation
Scott Nicewonger, EE Project Manager

## Slide 11: Conventional SAR
SCOTT NICEWONGER

## Slide 12
TX
TX / RX
RX
Real Transmitter
Real
Receiver
Reflective Target
Synthesized Transmitter/Receiver
with Aperture Length d
d
Phase Center
Show wide beamwidths to Narrow BeamWidth
Beamwith, lambda/distance ?
SCOTT NICEWONGER

## Slide 13: Stationary Scanning
Phase Centers are formed at the midpoint between each transmitter/receiver pair
Pulsing a linear array of receivers enables a scan of the target area without any moving parts
Imager consists of linear arrays in X and Y axes to scan the entire scene
TX
RX1
RX2
RX3
RX4
PC 1
PC 3
PC 2
PC 4
TX
RX
RX
RX
RX
RX
RX
RX
RX
TX
RX
RX
RX
RX
TX
RX
RX
RX
RX
TX
Front View
1-D Side View
SCOTT NICEWONGER

## Slide 14: Phase Slope
16 Phase Centers
16 θn ‘s that map to 16 unique regions in the scene
For each θn , a 16-point complex basis function is generated
Received data is convolved (DFT) with basis functions to map energy amplitude VS frequency
Downrange
Scene
θn
d sin(θn)
2d sin(θn)
3d sin(θn)
nd sin(θn)
d
R
R Rcos θ
d = 3λ
θ
SCOTT NICEWONGER

## Slide 15
Image Formation
40 x 40 inch scene
20 [ft] range to scene center
16 - 2.5 inch
1-D Cells in
Azimuth and
Elevation
5 x 5 feet
20nS wide RF
Pulse @ 10 GHz
Antenna Array
Beams are formed
Digitally with Fourier
Transform, 16 in Azimuth
And 16 in Elevation
PC Display
VGA Connection
16 - Azimuth
16 - Elevation
SCOTT NICEWONGER

## Slide 16: Generation II Design Objectives
Implement natively on the FPGA:
  Signal Processing
  System Control & Synchronization
  High-fidelity Pulsing of the Downrange Scene
  Dedicated VGA display
Implement signal processing in Matlab
Implement calibration logic
Demonstrate full-scale RF functionality with FPGA control
Re-design mechanical structure into a serviceable, user-friendly product
SCOTT NICEWONGER

## Slide 17
SCOTT NICEWONGER

## Slide 18: Signal Processing
Jordan Bolduc

## Slide 19: Signal Processing Approach
Reflected signal comes in as two separate components
Amplitude and angle of arrival information is necessary for energy at the scene
A Discrete Fourier Transform (DFT) is necessary
JORDAN BOLDUC

## Slide 20: Goals for Signal Processing
End goal for product is for Signal Processing on the FPGA
Was working towards implementing a Fast Fourier Transform (FFT) algorithm
Decided to move to work towards an initial MATLAB solution
  Ease of coding
  Testing and debugging
  Data Manipulation
  Calibration methods
  Similar to Northrop Grumman development process
  Backbone for future development
JORDAN BOLDUC

## Slide 21: Signal Processing Code
JORDAN BOLDUC

## Slide 22: Moving Forward
Will implement the laptop as part of the signal path
FPGA and MATLAB “talking” with each other
Creating custom Graphical User Interface (GUI)
Expected Challenges:
  Converting 12 bit binary word to decimal
  Accuracy after conversion
  Calibration calculations
JORDAN BOLDUC

## Slide 23: Structure Diagram & Switching Data Processing Image Formation
OLIVIER BARBIER

## Slide 24: SWITCHING
OLIVIER BARBIER

## Slide 25
OLIVIER BARBIER

## Slide 26: SWITCHING
State Diagram
OLIVIER BARBIER

## Slide 27: SWITCHING
OLIVIER BARBIER

## Slide 28: DATA PROCESSING
OLIVIER BARBIER

## Slide 29: DATA PROCESSING
ADC
  Purpose
    Create a 12 bit signal of the DC voltage from the IQ demodulator.
  Victory
    DC voltage can be digitalized.
  Work to be done
    We need to implement a logic circuit to accept negative DC voltage.
Memory
  Purpose
    Read/write 2 bytes of value to/from the onboard memory of the NEXYS3.
  Victory
    Values from the switches was able to be collected and read through Matlab.
    Reading values from the memory.
OLIVIER BARBIER

## Slide 30: DATA PROCESSING
Mathematical calculation
  Parallel work are being done in order to achieve the Discrete Fourier Transform
Matlab
  We were able to get magnitude and phase information using a script.
FPGA
  We are looking into Xilinx own FFT IP core generator.
OLIVIER BARBIER

## Slide 31: IMAGE FORMATION
OLIVIER BARBIER

## Slide 32: IMAGE FORMATION
16 columns showing the magnitude of receiving signal from each antenna.
  No phase information is used in this scenario.
Image formation Possible Alternatives
  Neural Network
  Matlab image processing tool
  SAR processing algorithm (MATLAB)
OLIVIER BARBIER

## Slide 33: RF, Electrical, & Software Summary
Scott Nicewonger, EE Project Manager

## Slide 34: Key Milestones (Electrical)
Completed
Signal Path Testing
VHDL Switching & Timing Logic
  Manual VHDL Switching Verified
Analog/Digital Conversion Logic
MATLAB Signal Processing Logic
Limited Display Functionality
Upcoming
Migrate to New Structure
  Migration Validation Testing
Real-time VHDL Switching
Interface MATLAB & FPGA
Dedicated Display Full-functionality
MATLAB GUI & Display
Calibration Logic
RF Range Testing
JOSH DENNIS

## Slide 35: Structure Design
LUKE BALDWIN

## Slide 36: Initial Design Concepts
Concept 1: 8020 Aluminum Bars
Concept 2: Welded Aluminum Plates
LUKE BALDWIN

## Slide 37: Structure Revision: Version 3
Continuation of 8020
  Change from 1” 10 series to 1.5” 15 series for increased beam strength
Rectangular Base added instead of arbitrary ground
  Caster to be added for relative mobility
  Arms added for ease transportation
Connectors added
  Keeps the structure rigid
  Useful in weight and cost analysis
LUKE BALDWIN

## Slide 38: Structure Revision: Version 3.1
Moment analysis saw potential foreword rotation
Base width extended to 30”
  Increases wheel base for better mobility
  Front of structure supported
LUKE BALDWIN

## Slide 39: Structure Revision: Version 4
Weight analysis of V3.1 was 174 lbs without electrical components
Return to 10 series to reduce weight to 80lb goal
Beam along front removed for potential reflections
Introduction of leveling casters for alignment
Addition of triangle pieces for extra support
Weight reduced to ~55 lbs
66”
67”
30”
LUKE BALDWIN

## Slide 40: Structure Assembly
Physically assembled this version (4hrs)
Some noted challenges
  Leveling casters small 2” plastic wheel
  Slight bend in horizontal beam
  Front and back base beams oscillate independently if shook
LUKE BALDWIN

## Slide 41: Structure Force Analysis
Performed a force analysis to check deflection and find improvements
Application of test force in center of beam with rigid endpoints
Force set to 20 lbs to account for the vertical beam and half of component box
Length set to 62”
LUKE BALDWIN

## Slide 42: Structure Force Analysis Results
Original 1010
New 1020
Total Deflection: 0.0623 In
Total Deflection: 0.0098 In
6x less deformation
LUKE BALDWIN

## Slide 43: New Structure Revision: Version 5
Modification of current structure
  Weight no longer issue
  Goal is for a stable structure
Switch to rubber 4” casters
  No leveling caster presents alignment dilemma
  Solved with foot floor lock (red) and adjustable vibration feet (yellow)
More 45 degree pieces added to resist forward vibration resistance and rotation
Base pieces changed to 1020
1030 piece added to middle of base to join halves
LUKE BALDWIN

## Slide 44: Component Housing
JULIAN RODRIGUEZ

## Slide 45: Component Housing - Final Iteration
Aluminum 6061
Exterior panel mounted connectors
  VGA
  USB x2
  Power
  SMA
24”x17”x5” at 0.09” thickness
Weight: 12.9 lbs
Lockable
JULIAN RODRIGUEZ
Notes: The design philosophy for the box was to first and foremost be accessible for the electrical engineers to conduct their testing as well as being as sealed from the outside environment as much as possible to protect from EMI, in which I will speak about in further detail later. Every input and output to and from the box goes through a panel mounted connection to not only enclose the box but also to make connections as simple as possible. The image above is a view which hides the walls to better show each connector installed into the box. Aluminum 6061 was selected due to its high electrical conductivity, strong weldability, and of course cost. The weight is approximately (12.9 lbs) compared to last year’s weight of (roughly 40lbs) down 67.75%. The latches on the side ensure the enclosure is properly shut when needed, and have the option to install padlocks if need be.

## Slide 46: Component Housing - Final Iteration
JULIAN RODRIGUEZ

## Slide 47: New Thermal Analysis: Component Box
JULIAN RODRIGUEZ
Notes: With the new dimensions for the box, some recalculations had to be made to determine the new thermal analysis. After changing the surface areas and thicknesses within the MatLAB code I created for thermal analysis, again using a Thermal Resistance Network, the total heat dissipation possible actually went up. Previously, the box would have only been able to dissipate approximately (155.37 W) compared to now with a value of (178.08 W). That is up by (14.6%). With this new heat dissipation, this translates to a factor of safety of (5.12).

## Slide 48: Electromagnetic Interference & Shielding
Electromagnetic interference must be minimized when designing an electrical component housing
Methods used to minimize EMI include simplifying circuitry, and shielding via gaskets
  Conductive elastomer
Make every surface sealed with a conductive material
JULIAN RODRIGUEZ
Notes: Electromagnetic interference is emitted by every electrical device and with a high amount of electrical components running there is a lot of potential interference to try and minimize. By enclosing the components from the environment, we are preventing EMI from the outside as well as keeping the components from interfering with outside components. Keeping this in mind, the best way to approach the box design is making sure it is water-tight and any exposed area can be filled with an EMI shielding material: in our case using a conductive elastomer for the top lip that will be opened as well as any excess gaps from holes.

## Slide 49: Horn Holders
DESMOND PRESSEY

## Slide 50: Horn Holder Design
Design Goals
  Independent axis adjustability
  Independent axis locking
  Lightweight
  Ease of adjustability and alignment
  No clearance issues
DESMOND PRESSEY

## Slide 51
DESMOND PRESSEY

## Slide 52
DESMOND PRESSEY

## Slide 53: Final Design Iteration
Removed clearance issues
Moved axis of rotation
Minor dimensional changes
Corrected T-nut series
DESMOND PRESSEY

## Slide 54
DESMOND PRESSEY

## Slide 55: Horn Holder Prototype
Status: Prototype confirmed
  Full scale work order submitted
  Optimize fastening method
Weight: 1.5lb
Cost: $15 per horn holder
What’s left?
  Complete fabrication / install onto frame
4.64”
1”
2.5”
DESMOND PRESSEY

## Slide 56: Calibration & Testing
KEGAN STACK

## Slide 57: Horn Spacing - Jig
Simplest way to ensure exact horn spacing
  Compared to individual measurements
Jig made from 1/8” aluminum 6061
Cut in house with the water jet
  Accurate to within 0.003”
Measures from the intersection of the frame – out
Status: Purchase order submitted
Completion approximately 1 week
Jig
KEGAN STACK

## Slide 58: Horn Calibration – Option 1
KEGAN STACK

## Slide 59: Horn Calibration – Option 2
KEGAN STACK

## Slide 60
Radar Reflectors
Purpose is to create backscatter
  Reflects transmitted RF back to receiving horns
Transmit
Receive
KEGAN STACK

## Slide 61: Room Setup, Budget, & Future Plans
JOSH DENNIS, ME Project Manager

## Slide 62: Room Setup
Considerations:
  Room requirement (30 ‘ x 30’)
  Minimal RF interference
  Easy student access
Anechoic Material
SAR Testing Layout
JOSH DENNIS

## Slide 63: Room Setup
Problem:
  Developing anechoic room would cost $7000+
  No permanent access to a particular room
Solution:
  Create collapsible anechoic arrays
  Cover hotspots of interference
  Cost: $1500
Adhere anechoic material to modular display boards
JOSH DENNIS

## Slide 64: Equipment Storage
Problem:
  Project has support equipment loosely collected in unsecured boxes
    Radar Reflectors
    Tripods
    Anechoic material
    Tools
    Spare parts
Solution (Planned):
  Purchase or build a container
    Lockable
    Shock resistant
JOSH DENNIS

## Slide 65: 2015-2016 Budget
Chart: EE Budget
| COMPONENT HOUSING | ELECTRICAL HARDWARE | TEST EQUIPMENT | REMAINING
 | 690 | 2180 | 20 | 2110
Items yet to be purchased:
Secure case for electrical components
Storage for testing equipment
RF Panel setup
Replacing faulty equipment
Renting testing equipment
Chart: ME Budget
| HORN HOLDER | STRUCTURE | TOOLS | CALIBRATION | TESTING | REMAINING
TOTAL | 410 | 1870 | 120 | 170 | 1370 | 1060
JOSH DENNIS

## Slide 66: Overall Budget (2014-2016)
Chart: 
| ELECTRICAL COMPONENTS | TEST EQUIPMENT | MECHANICAL | CURRENT REMAINING
Total | 33900 | 8500 | 7000 | 3200
JOSH DENNIS

## Slide 67: Remaining Tasks 2016
Mechanical
  Machine shop fabrication
  Modifications to structure
  Anechoic panel setup
JOSH DENNIS
Electrical
  Migrate Electronics to Gen II Structure
  Iterative Testing
  Software Development
  RF Demonstration

## Slide 68: Possibilities for Generation III
Mechanical
Custom Fabrication
Wall-mounted system
Easily collapsible
Improve horn adjustment fidelity
Electrical
Higher resolution
  Enhance array design
“Heat map” display
Weapon Signature Discrimination
  Improve image resolution & display
  Neural network
Automated alert system
  Wireless link to security center
JOSH DENNIS

## Slide 69: Acknowledgements
Mechanical
Instructors:
  Dr. Nikhil Gupta
  Dr. Chiang Shih
Faculty Advisor:
  Dr. Dorr Campbell
Electrical
Instructor:
  Dr. Jerris Hooker
Faculty Advisors:
  Dr. Simon Foo
  Dr. Shonda Bernadin
  Dr. Rajendra Arora
College of engineering
JOSH DENNIS

## Slide 70: Sponsor
Mike Blue
Mechanical Engineer
Mechanical Technology
Pete Stenger
Engineer, RF Microwave Design
RF Devices and Packaging
Northrop Grumman
JOSH DENNIS

## Slide 71: Questions?

## Slide 72: References
http://stores.cumingmicrowave-online-store.com/c-ram-fac-3-x-24-x-24/
http://www.eventfurniturehire.co.nz/catalog/product/gallery/id/99/image/109/
http://www.northerntool.com/shop/tools/product_200377214_200377214

## Slide 73: FRAME
Kegan Stack
3.54”
7.09”
70”
66”
30”

## Slide 74: Structure Examination: V1
8020 Aluminum Beams
  Provide excellent weight to strength ratio
  Easy to assemble
  Light Machining Required
  Joined together by ¼-20 screws and plates
  Recommended to us from Mike Blue
Horns mounted to the front pointing normal to the beam
64”
61”

## Slide 75: Structure Examination: V2
63.65”
Solid Aluminum Beams
  Similar Design as last year’s rendition
  Number of beams reduced
  Welded together for better strength
  Heavy Machining Required
Horns sandwich mounted between two 5” beams
Design ultimately rejected due to machining difficulty
64.55”

## Slide 76
(INCHES)

## Slide 77: Safety
Uses low-powered X-band Radio Frequency (RF) to image objects from a distance (20 feet)
RF Exposure Safety Guidelines
  ANSI/IEEE C95.1-1992
  FCC 47 C.F.R. 1.1307(b), 1.1310, 2.1091, 2.1093
Limit for human exposure: 1 mW/cm2
SAR Peak Transmit: 0.0076 mW/cm2
Scott Nicewonger