## Slide 1: Synthetic Aperture Radar Imager Team 18
Members:
Luke Baldwin
Josh Dennis
Kaylen Nollie
Desmond Pressey
Sponsor: Northrop Grumman
Contact: Mike Blue
Advisor: Dr. dorr Campbell
Instructor: Dr. Nikhil Gupta
Date: 10/22/2015

## Slide 2: Outline
Introduction to SAR
Last Year: Overview
Project Description
Design Concepts
Design Evaluation
Risks and Challenges
Schedule and Future Plans

## Slide 3: SAR Application
[1]

## Slide 4: High-Resolution SAR Image
[2]

## Slide 5: Project Proposal
Create a Synthetic Aperture Radar
  Weapons detection for homeland security
  Stationary
  Low resolution
  Concealable
  Low Cost
  Relatively mobile
[3]

## Slide 6: Imaging Radar Operational Concept
40 x 40 inch scene
20 [ft] range to scene center
16 - 2.5 inch
1-D Cells in
Azimuth and
Elevation
5 x 5 feet
20nS wide RF
Pulse @ 10 GHz
Antenna Array
Beams are formed
Digitally with Fourier
Transform, 16 in Azimuth
And 16 in Elevation
PC Display
VGA Connection
16 - Azimuth
16 - Elevation
[4]

## Slide 7: First Generation: Overview
  Able to produce limited results
  Electrical components and equipment rental consumed most of the budget
  Fabrication issues
    3 week delay
    Poor craftsmanship
    Additional modifications needed
  Needs Improvement:
    Stability
    Weight
    Horn adjustment

## Slide 8: First Generation: Budget
Initial Estimate Final Budget
[5]

## Slide 9: Second Generation: Focus
Mobility
  Attach wheels
Weight
  < 80 lbs
Horn Adjustment
  Aligned within 1ft circle at 20ft away
Stability
  Movement causes artificial phase shift
  Max movement: 1/72 inch
Cost
  Minimize

## Slide 10: Concept Generation
Project was divided into multiple parts:
  Structure
  Horn holders
  Base
  Hardware Box (EE Team)

## Slide 11: Design Concepts – Structure Design A (80-20)

## Slide 12: Design Concepts – Structure Design B (Fabricated Al)

## Slide 13: Concepts Evaluation – Structure Pros
Design A (80-20)
Modularity makes it easy to assemble
Provides limitless translational horn placement along the beam
Simple to order and machine
Lightweight compared to equivalent solid cross section
Design b (Fabricated Al)
Thicker cross section allows more sturdiness and deformation resistance
Larger bolts and hardware can be used in assembly
Larger surface area for ground contact

## Slide 14: Concepts Evaluation – Structure Cons
Design A (80-20)
Fasteners might not carry weight or force well
Offers little waveguide/horn protection to the elements
Component box could deform support beams
Design b (Fabricated Al)
Additional time to manufacture and assemble
More weight than 80-20
Back mount of component box causes additional stress on arms
More expensive

## Slide 15: Design Concepts – Horn Holder Design A (Articulating Arm)

## Slide 16: Design Concepts – Horn Holder Design B (Handle Tilt)

## Slide 17: Design Concepts – Horn Holder Design C (Covered Tilt)

## Slide 18: Concepts Evaluation – Horn Holder Pros
Design A (Articulating Arm)
Simplest of designs
Has proven concept (computer monitor model)
Design b (Handle Tilt)
Cover allows for attachments (laser alignment)
Rotation about the center
Modeled in compatibility with 80/20 structures
Design c (Covered Tilt)
Easy to adjust manually
Rotation one point on the rear

## Slide 19: Concepts Evaluation – Horn Holder Cons
Design A (Articulating Arm)
Design b (Handle Tilt)
Structure is quite complex
Cover may affect antenna readings
Design c (Covered Tilt)
The method of position locking is unclear
Challenging to use handle bars and attach to structure
Pivots are not about the center or in line
Favors mounting to the top of structure bar
Horns on vertical column will be a challenge

## Slide 20: Continued Evaluation
Continue sponsor and ECE team communication
  Optimize structure and horn holder design
  Adding new constraints upon feedback
Cost vs Benefit analysis
Submit final suggestion to sponsor
Base platform concept generation
  Dependent on final structure design
Aluminum Platform Truck:
McMaster-Carr ($450) [6]

## Slide 21: Prioritizing Engineering Characteristics
Customer Requirements | Customer Importance | Engineering Charateristics |  |  |  |  |  |  |  | 
 |  | Structural Thickness | Material Used | Locking Mechanism | Axis Adjustability | Mounting Mechansim | Base size | Height Above Ground | Number of Crossbeams | Weight
Increased Stability | 5 | 9 | 3 | 6 |  | 3 | 9 | 6 | 6 | 
Lower Weight | 5 | 3 | 9 |  |  |  | 6 | 3 | 6 | 9
Good Images | 5 |  |  | 6 | 9 | 9 |  | 3 |  | 
Better Horn Mounting | 5 |  |  | 9 | 9 | 9 |  |  |  | 
Cost | 4 | 3 | 6 | 3 |  | 3 | 3 |  | 3 | 
Hardware Box | 2 | 3 | 6 |  |  |  |  |  |  | 3
Portability | 2 |  | 6 |  |  |  | 9 | 6 |  | 9
Score |  | 18 | 30 | 24 | 18 | 24 | 27 | 18 | 15 | 21
Relative Weight |  | 78 | 108 | 117 | 90 | 117 | 105 | 72 | 72 | 69
Rank |  | 6 | 3 | 1 | 5 | 1 | 4 | 7 | 7 | 9
Most Important EC’s:
1. Mounting Mechanism
1. Locking Mechanism
Material Used
Base Size
Axis Adjustability
Structural Thickness
Height Above Ground
Number of Crossbars
9. Weight

## Slide 22: Schedule

## Slide 23: Future Plans
Regular meetings with group, EE team, and sponsor
Conduct Failure Modes Effects Analysis (FMEA) on designs
Design selection
Propose final design
Make Bill of Materials
Submit Purchase Order

## Slide 24: Summary
Review of SAR
Review of last year’s final product
Project objectives
Generate design concepts
Prioritize engineering characteristics
Proposed course of action for determining final design
Discussed future plans

## Slide 25: References
NASA AirSAR, https://upload.wikimedia.org/wikipedia/commons/a/a6/AirSAR-instrument-on-aircraft.jpg
Radar Tutorial, http://www.radartutorial.eu/20.airborne/pic/sar_principle.print.png
Cammuse, Matthew. “SAR Final Presentation.” http://eng.fsu.edu/me/senior_design/2015/team27/Webpage/presentations/Team%20E%2311_Milestone%20%237%20Presentation_%20Final%20Report.pptx. Web 10/18/2015.
E11 Milestone – Final Report, http://eng.fsu.edu/me/senior_design/2015/team27/
http://www.northropgrumman.com/Photos/pgM_BA-10002_067.jpg
http://www.mcmaster.com/#carts/=zgsvoa