## Slide 1
Purpose
Use Synthetic Aperture Radar (SAR) technology to detect and image metal from a distance for use in the security industry.
Structure Advantages
Extruded Aluminum (80/20) was preferred so the structure could be modified as needed.
  Gives maximum flexibility for adaptation
  Adds strength and stability
  Reduces error in readings
Project Goals
Improve upon aspects of design from previous year’s project:
Lower weight
Improve stability
Make antenna horns more adjustable
Easy to access and set up
ME Team 18: Luke Baldwin, Josh Dennis, Kaylen Nollie, Desmond Pressey
Sponsored by Northrop Grumman: Pete Stenger, Mike Blue
Advisors: Dr. Dorr Campbell
Synthetic Aperture Radar Imager
Design
The antennas are mounted on the structure at predetermined position.
Antennas have 3 degrees of freedom.
Locking mechanism implemented for each degree of freedom.
The structure is light and modular
Function Concept
20 Antennas: 16 Receive – 4 Transmit
EE Team:
FPGA (Signal Processing), Timing, A/D Conversion, and Image Generation
ME Team:
Horn array, mounting and adjusting horns, structure
Holder Advantages
Screw distance compatible with 80/20 rail spacing (3”)
Independent locking and adjustability with wingnuts
Ample space for movement freedom
Keeps assembly stationary
Easy to machine