## Slide 1: Synthetic Aperture Radar Imager Team 18 Spring 2016: Presentation I
Members:
Luke Baldwin
Josh Dennis
Kaylen Nollie
Desmond Pressey
Sponsor: Northrop Grumman
Contact: Mike Blue
Advisor: Dr. dorr Campbell
Instructor: Dr. Nikhil Gupta
Date: 1/19/2016

## Slide 2: Outline
Review of Project Scope
Review Previous Progress
Design Updates
Procurement
Schedule and Future Plans
Luke Baldwin

## Slide 3: Working SAR
[1]
Luke Baldwin

## Slide 4: Imaging Radar Operational Concept
40 x 40 inch scene
20 [ft] range to scene center
16 - 2.5 inch
1-D Cells in
Azimuth and
Elevation
5 x 5 feet
20nS wide RF
Pulse @ 10 GHz
Antenna Array
Beams are formed
Digitally with Fourier
Transform, 16 in Azimuth
And 16 in Elevation
PC Display
VGA Connection
16 - Azimuth
16 - Elevation
[4]
Luke Baldwin

## Slide 5: Project Goals
Create a Synthetic Aperture Radar:
  Project Features:
    Weapons detection for homeland security
    Stationary
    Low resolution
    Concealable
    Low Cost
    Relatively mobile
Luke Baldwin

## Slide 6: Project Organization
ME Team
  Structure
  Horn holders
EE Team
  Hardware Box
  Signal processing
Luke Baldwin

## Slide 7: Second Generation Improvements
Mobility
  Attach wheels
Weight
  < 80 lbs
Horn Adjustment
  Aligned within 1ft circle at 20ft away
Stability
  Movement causes artificial phase shift
  Max movement: 1/72 inch
Cost
  Minimize
1st Generation Project – Class of 2015
Luke Baldwin

## Slide 8: Prioritizing Engineering Characteristics
Customer Requirements | Customer Importance | Engineering Charateristics |  |  |  |  |  |  |  | 
 |  | Structural Thickness | Material Used | Locking Mechanism | Axis Adjustability | Mounting Mechanism | Base size | Height Above Ground | Number of Crossbeams | Weight
Increased Stability | 5 | 9 | 3 | 6 |  | 3 | 9 | 6 | 6 | 
Lower Weight | 5 | 3 | 9 |  |  |  | 6 | 3 | 6 | 9
Good Images | 5 |  |  | 6 | 9 | 9 |  | 3 |  | 
Better Horn Mounting | 5 |  |  | 9 | 9 | 9 |  |  |  | 
Cost | 4 | 3 | 6 | 3 |  | 3 | 3 |  | 3 | 
Hardware Box | 2 | 3 | 6 |  |  |  |  |  |  | 3
Portability | 2 |  | 6 |  |  |  | 9 | 6 |  | 9
Score |  | 18 | 30 | 24 | 18 | 24 | 27 | 18 | 15 | 21
Relative Weight |  | 78 | 108 | 117 | 90 | 117 | 105 | 72 | 72 | 69
Rank |  | 6 | 3 | 1 | 5 | 1 | 4 | 7 | 7 | 9
Most Important EC’s:
1. Mounting Mechanism
1. Locking Mechanism
Material Used
Base Size
Axis Adjustability
Structural Thickness
Height Above Ground
Number of Crossbars
9. Weight
Key:
#1 Important EC
#2 Important EC
#3 Important EC
Luke Baldwin

## Slide 9: Structure: Version 1
  80/20 Design
    Lightweight
    Cheap
    Modular
    Light machining required
Luke Baldwin
Notes: Add words to slide

## Slide 10
Structure: Version 3
Increased cross section width from 1.00” to 1.50”
Added:
  Bottom frame
  Outer Braces
  Brackets
Possible leveling castors
Luke Baldwin
69.50 in
66.00 in
20.00 in

## Slide 11
Structure: Version 4
Increased stability
  Extended horizontal bar on bottom
Luke Baldwin

## Slide 12: Structure: Version 5
Reduced weight
  Change from 1.50” cross section width bar to 1.00”
Fixed possible radar interference
  Removed horizontal bar, kept protruding struts on bottom
Increased stability
  Added braces at some joints
Luke Baldwin

## Slide 13: Horn Holder: Version 1
Compatible with 80/20
Independent locking and adjustability
Compact
Josh Dennis

## Slide 14: Horn Holder: Version 2
Removed box shell
Refined rotation locking
Added 80/20 connection
Josh Dennis

## Slide 15
Horn Holder: Version 3
Clearance
  Moved horn forward in assembly
Standardization
  Small changes in dimensions
Josh Dennis
4.64 in
2.22 in

## Slide 16: Procurement Status
Component | Vendor | Product | Team Member(s) | Price | Purchase Order
Structure | 8020 Inc | 8020 Hardware | Kegan | $920 | Submitted
Horn Holders | OnlineMetal | Aluminum Sheet | Kaylen | $500 | Under review
Fastening Hardware | Local hardware store | Bolts, washers, nuts | Desmond | TBD | TBD
Assembly Tools |  | Wrenches |  | TBD | TBD
Josh Dennis

## Slide 17: Budget
Chart: 
| Structure | Horn Holders | Fastening Hardware (Projected) | Tools (Projected) | Remaining
Budget | 920 | 500 | 100 | 50 | 3430
Josh Dennis

## Slide 18: Schedule
Josh Dennis

## Slide 19: Summary
Review of Project Scope
Review Previous Progress
Design Updates
Procurement
Josh Dennis

## Slide 20: Future Plans
Submit remaining purchase orders
Create operational instructions
Fabrication
Testing & modification
Josh Dennis

## Slide 21: Acknowledgements
Sponsor: Northrop Grumman
  Mike Blue
  Pete Stenger
Senior design instructors:
  Dr. Nikhil Gupta
  Dr. Chiang Shih
Josh Dennis

## Slide 22: References
NASA AirSAR, https://upload.wikimedia.org/wikipedia/commons/a/a6/AirSAR-instrument-on-aircraft.jpg
Radar Tutorial, http://www.radartutorial.eu/20.airborne/pic/sar_principle.print.png
Cammuse, Matthew. “SAR Final Presentation.” http://eng.fsu.edu/me/senior_design/2015/team27/Webpage/presentations/Team%20E%2311_Milestone%20%237%20Presentation_%20Final%20Report.pptx. Web 10/18/2015.
E11 Milestone – Final Report, http://eng.fsu.edu/me/senior_design/2015/team27/
http://www.northropgrumman.com/Photos/pgM_BA-10002_067.jpg

## Slide 23: Questions?

## Slide 24
6in
3in
Structure Version 3
Horn Holder Version 2
Full Assembly

## Slide 25
Full Schedule (including deliverables)