## Slide 1: SAR Imager
Design Review II
March 15, 2016
Josh dennis, Luke Baldwin, Kaylen nollie, desmond pressey

## Slide 2: Outline
Project Scope
1st Generation
SAR Theory
Calibration & Testing
Future Plans
KAYLEN NOLLIE

## Slide 3: SAR Introduction
What is an SAR?
Synthetic Aperture Radar: Typically, a single antenna is attached to an aircraft flying over a target zone capturing several high resolution images to create a single image map.
  Typically for Military
KAYLEN NOLLIE

## Slide 4: Project Scope
Objective:
  Develop a static, multi-antenna Synthetic Aperture Radar (SAR) Imager
    In brief: Giant metal detector
Why?:
  Security – Prevention of guns, knives, or dangerous objects from entering public facilities
    Schools
    Airports
    Office buildings
KAYLEN NOLLIE

## Slide 5: First Generation Goals
Create a Synthetic Aperture Radar:
  Project Features:
    Weapons detection for homeland security
    Multi-Antenna
    Stationary
    Low resolution
    Concealable
    Low Cost
    Relatively mobile
1st Generation Project – Class of 2015
KAYLEN NOLLIE

## Slide 6: Second Generation Goals
Mechanical Engineering
Mobility
Lower Weight
Horn Adjustment
Increase Stability
Minimize Cost
Electrical Engineering
Identify reflector at 20 feet
Standalone functionality
KAYLEN NOLLIE

## Slide 7: Current Status
Task | Design | Prototype | Optimization
Component Testing | ✔ | N/A | ✔
Signal Processing | ✔ | N/A | ○
Data Processing & Image Formation | ✔ | N/A | ○
Structure | ✔ | ✔ | ○
Component Housing | ✔ | ○ | ✘
Horn Holders | ✔ | ✔ | ○
Testing & Calibration Equipment | ✔ | ✔ | ○
Legend
✘ - Not Started
○ - In Progress
✔ - Completed
KAYLEN NOLLIE

## Slide 8: Conventional SAR
KAYLEN NOLLIE

## Slide 9
Image Formation
40 x 40 inch scene
20 [ft] range to scene center
16 - 2.5 inch
1-D Cells in
Azimuth and
Elevation
5 x 5 feet
20nS wide RF
Pulse @ 10 GHz
Antenna Array
Beams are formed
Digitally with Fourier
Transform, 16 in Azimuth
And 16 in Elevation
PC Display
VGA Connection
16 - Azimuth
16 - Elevation
KAYLEN NOLLIE

## Slide 10: Horn Holder Design
Design Goals
  Independent axis adjustability
  Independent axis locking
  Lightweight
  Ease of adjustability and alignment
  No clearance issues
KAYLEN NOLLIE

## Slide 11: Final Design Iteration
Removed clearance issues
Moved axis of rotation
Minor dimensional changes
Corrected T-nut series
KAYLEN NOLLIE

## Slide 12
KAYLEN NOLLIE

## Slide 13: Horn Holder Prototype
Status: Prototype confirmed
  Full scale work order submitted
  Optimize fastening method
Weight: 1.5lb
Cost: $15 per horn holder
What’s left?
  Complete fabrication / install onto frame
4.64”
1”
2.5”
KAYLEN NOLLIE

## Slide 14: Horn Spacing - Jig
Simplest way to ensure exact horn spacing
  Compared to individual measurements
Jig made from 1/8” aluminum 6061
Cut in house with the water jet
  Accurate to within 0.003”
Measures from the intersection of the frame – out
Status: Purchase order submitted
Completion approximately 1 week
Jig
KAYLEN NOLLIE

## Slide 15: Horn Calibration – Option 1
KAYLEN NOLLIE

## Slide 16: Horn Calibration – Option 2
KAYLEN NOLLIE

## Slide 17: Structure Revision: Version 4
Weight analysis of V3.1 was 174 lbs without electrical components
Return to 10 series to reduce weight to 80lb goal
Beam along front removed for potential reflections
Introduction of leveling casters for alignment
Addition of triangle pieces for extra support
Weight reduced to ~55 lbs
66”
67”
30”
LUKE BALDWIN

## Slide 18: Structure Assembly
Physically assembled this version (4hrs)
Some noted challenges
  Leveling casters small 2” plastic wheel
  Slight bend in horizontal beam
  Front and back base beams oscillate independently if shook
LUKE BALDWIN

## Slide 19: Structure Force Analysis
Performed a force analysis to check deflection and find improvements
Application of test force in center of beam with rigid endpoints
Force set to 20 lbs to account for the vertical beam and half of component box
Length set to 62”
LUKE BALDWIN

## Slide 20: Structure Force Analysis Results
Original 1010
New 1020
Total Deflection: 0.0623 In
Total Deflection: 0.0098 In
6x less deformation
LUKE BALDWIN

## Slide 21: New Structure Revision: Version 5
Modification of current structure
  Weight no longer issue
  Goal is for a stable structure
Switch to rubber 4” casters
  No leveling caster presents alignment dilemma
  Solved with foot floor lock (red) and adjustable vibration feet (yellow)
More 45 degree pieces added to resist forward vibration resistance and rotation
Base pieces changed to 1020
1030 piece added to middle of base to join halves
LUKE BALDWIN

## Slide 22: Component Housing
Aluminum 6061
Exterior panel mounted connectors
  VGA
  USB x2
  Power
  SMA
24”x17”x5” at 0.09” thickness
Weight: 12.9 lbs
Lockable
LUKE BALDWIN
Notes: The design philosophy for the box was to first and foremost be accessible for the electrical engineers to conduct their testing as well as being as sealed from the outside environment as much as possible to protect from EMI, in which I will speak about in further detail later. Every input and output to and from the box goes through a panel mounted connection to not only enclose the box but also to make connections as simple as possible. The image above is a view which hides the walls to better show each connector installed into the box. Aluminum 6061 was selected due to its high electrical conductivity, strong weldability, and of course cost. The weight is approximately (12.9 lbs) compared to last year’s weight of (roughly 40lbs) down 67.75%. The latches on the side ensure the enclosure is properly shut when needed, and have the option to install padlocks if need be.

## Slide 23: Component Housing
LUKE BALDWIN

## Slide 24: Electromagnetic Interference & Shielding
Electromagnetic interference must be minimized when designing an electrical component housing
Methods used to minimize EMI include simplifying circuitry, and shielding via gaskets
  Conductive elastomer
Make every surface sealed with a conductive material
LUKE BALDWIN
Notes: Electromagnetic interference is emitted by every electrical device and with a high amount of electrical components running there is a lot of potential interference to try and minimize. By enclosing the components from the environment, we are preventing EMI from the outside as well as keeping the components from interfering with outside components. Keeping this in mind, the best way to approach the box design is making sure it is water-tight and any exposed area can be filled with an EMI shielding material: in our case using a conductive elastomer for the top lip that will be opened as well as any excess gaps from holes.

## Slide 25: Component Housing Migration
Current
Planned
LUKE BALDWIN

## Slide 26
Radar Reflectors
Purpose is to create backscatter
  Reflects transmitted RF back to receiving horns
Transmit
Receive
LUKE BALDWIN

## Slide 27: Room Setup
Considerations:
  Room requirement (30 ‘ x 30’)
  Minimal RF interference
  Easy student access
Anechoic Material
SAR Testing Layout
LUKE BALDWIN

## Slide 28: Room Setup
Problem:
  Developing anechoic room would cost $7000+
  No permanent access to a particular room
Solution:
  Create collapsible anechoic arrays
  Cover hotspots of interference
  Cost: $1500
Adhere anechoic material to modular display boards
LUKE BALDWIN

## Slide 29: 2015-2016 Budget
Chart: EE Budget
| COMPONENT HOUSING | ELECTRICAL HARDWARE | TEST EQUIPMENT | REMAINING
 | 690 | 2180 | 20 | 2110
Items yet to be purchased:
Secure case for electrical components
Storage for testing equipment
RF Panel setup
Replacing faulty equipment
Renting testing equipment
Chart: ME Budget
| HORN HOLDER | STRUCTURE | TOOLS | CALIBRATION | TESTING | REMAINING
TOTAL | 410 | 1870 | 120 | 170 | 1370 | 1060
LUKE BALDWIN

## Slide 30: To Do
Mechanical
  Component housing migration
  Machine shop fabrication
  Modifications to structure
  Anechoic panel setup
LUKE BALDWIN

## Slide 31
2016
2016
Today
03/07
03/11
03/15
03/19
03/23
03/27
03/31
04/04
04/08
04/12
04/16
04/20
Operation Manual & Design Report
4/1/2016
Final Report, Final Webpage, Notebooks
4/8/2016
Final Presentation & Open House
4/14/2016
Gen II Prototype Complete
3/22/2016
Gen II Prototype Verified
4/4/2016
Spring "Break" End
3/13/2016
3 days
3/14/2016 - 3/16/2016
Component Housing Fab & Assembly
4 days
Gen II Migration
1 day
RF Test Range Setup & Alignment
2 days
Delay Line Bench Testing
13 days
RF Range Testing
6 days
3/30/2016 - 4/4/2016
Neural Network Development & Testing (Strech Goal)
4 days
4/5/2016 - 4/8/2016
Data Documentation & Analysis
5 days
4/11/2016 - 4/15/2016
Closure & Gen III Hand-Off Plan
FAMU/FSU COE Synthetic Aperture Radar
Spring 2016 Timeline
LUKE BALDWIN

## Slide 32: Questions?

## Slide 33: References
http://stores.cumingmicrowave-online-store.com/c-ram-fac-3-x-24-x-24/
http://www.eventfurniturehire.co.nz/catalog/product/gallery/id/99/image/109/
http://www.northerntool.com/shop/tools/product_200377214_200377214

## Slide 34: FRAME
Kegan Stack
3.54”
7.09”
70”
66”
30”

## Slide 35: Structure Examination: V1
8020 Aluminum Beams
  Provide excellent weight to strength ratio
  Easy to assemble
  Light Machining Required
  Joined together by ¼-20 screws and plates
  Recommended to us from Mike Blue
Horns mounted to the front pointing normal to the beam
64”
61”

## Slide 36: Structure Examination: V2
63.65”
Solid Aluminum Beams
  Similar Design as last year’s rendition
  Number of beams reduced
  Welded together for better strength
  Heavy Machining Required
Horns sandwich mounted between two 5” beams
Design ultimately rejected due to machining difficulty
64.55”

## Slide 37
(INCHES)

## Slide 38: Safety
Uses low-powered X-band Radio Frequency (RF) to image objects from a distance (20 feet)
RF Exposure Safety Guidelines
  ANSI/IEEE C95.1-1992
  FCC 47 C.F.R. 1.1307(b), 1.1310, 2.1091, 2.1093
Limit for human exposure: 1 mW/cm2
SAR Peak Transmit: 0.0076 mW/cm2
Scott Nicewonger

## Slide 40: New Thermal Analysis: Component Box
LUKE BALDWIN
Notes: With the new dimensions for the box, some recalculations had to be made to determine the new thermal analysis. After changing the surface areas and thicknesses within the MatLAB code I created for thermal analysis, again using a Thermal Resistance Network, the total heat dissipation possible actually went up. Previously, the box would have only been able to dissipate approximately (155.37 W) compared to now with a value of (178.08 W). That is up by (14.6%). With this new heat dissipation, this translates to a factor of safety of (5.12).