## Slide 1: Synthetic Aperture Radar Imager
Final presentation
ece team 11 and ME Team 18
4/14/2016

## Slide 2: Team Members
Engineer | Role(s) | Major | School
Luke Baldwin | Main Structure | Mechanical | FSU
Olivier Barbier | Data Processing & Image Formation | Electrical & Computer | FAMU
Jordan Bolduc | Signal Processing | Electrical | FSU
Josh Dennis | ME Project Manager & Procurement | Mechanical | FSU
Scott Nicewonger | EE Project Manager & RF | Electrical | FSU
Kaylen Nollie | Secretary, Risk Management | Mechanical | FAMU
Desmond Pressey | Antenna Hardware & Webmaster | Mechanical | FAMU
Julian Rodriquez | Component Housing | Mechanical | FSU
Kegan Stack | Calibration & Alignment | Mechanical | FSU

## Slide 3: Introduction
Josh Dennis

## Slide 4: Agenda
Introduction to SAR
1st Generation
Project Goals
ME Team Accomplishments
ECE Team Accomplishments
Future Work

## Slide 5: SAR Introduction
What is SAR?
Synthetic Aperture Radar: Typically, a single antenna is attached to an aircraft flying over a target zone capturing several wide-beam images, and combines them into a single, high-resolution, narrow-beam image.

## Slide 6
Image Formation
40 x 40 inch scene
20 [ft] range to scene center
16 - 2.5 inch
1-D Cells in
Azimuth and
Elevation
5 x 5 feet
20nS wide RF
Pulse @ 10 GHz
Antenna Array
Beams are formed
Digitally with Fourier
Transform, 16 in Azimuth
And 16 in Elevation
PC Display
VGA Connection
16 - Azimuth
16 - Elevation

## Slide 7: Applications
Security industry: protection of high risk areas
Supplemental measure for layered security environments
Primary measure for certain environments
Unique Capabilities
Ranged scanning no apparatus to step into
Discreet placement
Vett the queue before individuals get to Access Control
Concealed Weapon Detection at an Access Control Point

## Slide 8: First Generation Goals
Create a Synthetic Aperture Radar:
  Project Features:
    Weapons detection for homeland security
    Multi-Antenna
    Stationary
    Low resolution
    Concealable
    Low Cost
    Relatively mobile
1st Generation Project – Class of 2015

## Slide 9: Second Generation Goals
Mechanical Engineering
Mobility
Lower Weight
Horn Adjustment
Increase Stability
Minimize Cost
Electrical Engineering
Identify reflector at 20 feet
FPGA System Control
FPGA & MATLAB Signal Processing

## Slide 10: Structure & Component Housing
Luke Baldwin

## Slide 11: Structure Goals
Mobile
Lightweight
Stable
  Movement causes phase error
Modular
Generation I Array

## Slide 12: FRAME V 4.0
Status: Assembled
Weight: 55lbs
Cost $700
What’s left?
  Optimizing for stability & stiffness
    Additional sections, gussets & leveling feet
    Loctite & torque all fasteners
3.54”
7.09”
70”
66”
30”
Leveling castors

## Slide 13: Structure Force Analysis
Issue: bottom beam deflected
  Someone stood on beam
Beam length of 62” only supported at ends
Original 1010
  Deflection of 0.0623(in)
New 1020
  Deflection 0.0098 (in)
  6X less deflection

## Slide 14: Structure Revision: V 4.1
Addition to current structure
Switch to rubber 4” casters
  No leveling caster presents alignment dilemma
  Solved with foot floor lock (red) and adjustable vibration feet (yellow)
Additional gussets to stiffen the structure
Base pieces changed to 1020
1030 piece added to middle of base to unify base
New leveling system not implemented
Gussets
Changed to 1020 series
1030 series

## Slide 15: Component Housing Goals
Easier interface
Secure components
Organized layout
Sufficient heat dissipation
Electromagnetic Interference (EMI) protection
Generation I Component Housing

## Slide 16: Gen II Component Housing
Assembled
  Water jetted
  Welded
  Powder Coated
Machine Shop Error
  Redesign component layout
EMI Shielded
  Conductive gaskets
  Panel-mount interfaces
Weight: 12.9 lbs w/o components
Full Enclosure
Panel Interface & Attenuation Control
Notes: The design philosophy for the box was to first and foremost be accessible for the electrical engineers to conduct their testing as well as being as sealed from the outside environment as much as possible to protect from EMI, in which I will speak about in further detail later. Every input and output to and from the box goes through a panel mounted connection to not only enclose the box but also to make connections as simple as possible. The image above is a view which hides the walls to better show each connector installed into the box. Aluminum 6061 was selected due to its high electrical conductivity, strong weldability, and of course cost. The weight is approximately (12.9 lbs) compared to last year’s weight of (roughly 40lbs) down 67.75%. The latches on the side ensure the enclosure is properly shut when needed, and have the option to install padlocks if need be.

## Slide 17: Installation – Electrical Components
Drop-in tray
  Removable
  Modular
Internal View
  Vibration-dampening
  standoffs
Notes: **Might want to briefly mention RF shielding since you mentioned it in slide 2. Also, we can take a new picture with it wired up now. –Scott ** With the new dimensions for the box, some recalculations had to be made to determine the new thermal analysis. After changing the surface areas and thicknesses within the MatLAB code I created for thermal analysis, again using a Thermal Resistance Network, the total heat dissipation possible actually went up. Previously, the box would have only been able to dissipate approximately (155.37 W) compared to now with a value of (178.08 W). That is up by (14.6%). With this new heat dissipation, this translates to a factor of safety of (5.12).

## Slide 18: Thermal Analysis
Previous temperature rise: 16.65° C (before paint)
Current temperature rise: 9.5° C (after paint)
  Radiant heat transfer efficiency
42% Enclosure temperature decrease
Highest enclosure temperature: 30.5° C
Component maximum operating temperature: 50° C
Notes: Explain chart from Pentair’s (thermal and fluid mgmt. comp) technical document. With the surface area about 10.5ft^2 and total power supplied to components - is 34.8 W. The heat flux is around 3.32. Using the graph one can determine the temperature rise. State previous enclosure before paint, 16.65 increase = 37.65 C, assuming room temperature of 21 C. After paint, only 9.5 C increase = 30.5 C. This is due to an aluminum’s unfinished surface less efficient radiant heat transfer. This translates to 42% decrease on enclosure temperature. Since the most sensitive component’s failure temp is at 50 C, then it is deemed safe by a large amount (19.5 C)

## Slide 19: Horn Holders & Testing
Desmond Pressey

## Slide 20: Horn Holder Design
Design Goals
  Independent axis adjustability
  Independent axis locking
  Lightweight
  Ease of adjustability and alignment
  No clearance issues

## Slide 21: Horn Holders
Tolerance issues
  Expectations: +/- 0.003 inch
  Reality: +/- 0.010 inch
Unable to use star washers
  Reduces locking ability
Successfully utilized in testing
Hardware Cost: $15 per horn holder
4.64”
1”
2.5”
Notes: This is where you could elaborate on how we met the design goals set in slide 2

## Slide 22: Horn Spacing - Jig
Simplest way to ensure exact horn spacing
Cut in house with the water jet
  Accurate to within 0.003”
Repeatable: Measures from the intersection of the frame – out
Jig

## Slide 23: Horn Calibration – 3D Printed Brackets
Align within 5°
Distance: 20 ft
Laser pointer
Issue with laser pointer:
  Laser beam was not centered within laser pointer
  Solved through digital calibration

## Slide 24
Radar Reflectors
Purpose is to create backscatter
  Reflects transmitted RF back to receiving horns
Transmit
Receive
RADAR Corner Reflector

## Slide 25: Room Setup
Considerations:
  Room requirement (30 ‘ x 30’)
  Minimal RF interference
Boresight Angle Alignment
Multipath Fade Point Empirical Determination

## Slide 26: Theory of Operation
Scott Nicewonger

## Slide 27
TX
TX / RX
RX
Real Transmitter
Real
Receiver
Reflective Target
Synthesized Transmitter/Receiver
with Aperture Length d
d
Phase Center

## Slide 28: Stationary Scanning
Phase Centers are formed at the midpoint between each transmitter/receiver pair
Pulsing a linear array of receivers enables a scan of the target area without any moving parts
Imager consists of linear arrays in X and Y axes to scan the entire scene
TX
RX1
RX2
RX3
RX4
PC 1
PC 3
PC 2
PC 4
TX
RX
RX
RX
RX
RX
RX
RX
RX
TX
RX
RX
RX
RX
TX
RX
RX
RX
RX
TX
Front View
1-D Side View

## Slide 29: Phase Slope
16 Phase Centers
16 θn ‘s that map to 16 unique regions in the scene
For each θn , a 16-point complex basis function is generated
Received data is convolved (DFT) with basis functions to map energy amplitude VS frequency
Downrange
Scene
θn
d sin(θn)
2d sin(θn)
3d sin(θn)
nd sin(θn)
d
R
R R cos θ
d = 3λ
θ

## Slide 30: Prototype Design Goals
Electrical Engineering
Identify radar reflector at 20 feet
FPGA signal processing for real-time & standalone functionality
MATLAB signal processing for testing & future development

## Slide 32: System Control
Olivier Barbier

## Slide 33: Xilinx NEXYS 3 FPGA Board
FPGA Controls:
Switching Between Transmit Mode & Receive Mode
Data Processing and Logic
  ADC to Read Voltages from IQ Demodulator
  Read & Write to Memory
VGA output
  16 Columns – Dedicated Display
Olivier Barbier

## Slide 34: Approach
Using board switches to control the Transmit and Receive antennas
  Understand the logic of the switches
Control VGA signal from the FPGA
  Initial goal is to create 16 columns that represent the 16 phase center
Create a fast pulse signal to control the SPDT
Saving data to the memory chip on the FPGA
Olivier Barbier

## Slide 35: Obstacles
Digitalize negative analog voltage
  Added noise for step up circuit
  Solution: Utilization of the 4 Channels from the IQ demodulator
Olivier Barbier

## Slide 36: Obstacles(Continued)
Need clean high speed square wave pulse to drive the SPDT
FPGA Output
MOSFET Switch Design
Solution: High speed MOSFET switch

## Slide 37: Final Program
Created a finite state machine.
  Debug mode : use switches to change antenna
  Real time mode (V1): logic switch antenna every 5 seconds
  Memory: load data to memory, that can be transported to MATLAB
Create VGA output control
Dedicated VGA Display Output

## Slide 38: Signal Processing
Jordan Bolduc

## Slide 39: Signal Processing Approach
Reflected signal comes in as two separate components
Amplitude and angle of arrival information is necessary for energy at the scene
A Discrete Fourier Transform (DFT) is necessary
Phase Information From Target
Spatial
Information
To Display
Notes: You can probably put a little more on this slide

## Slide 40: Goals for Signal Processing
End goal for product is for Signal Processing on the FPGA
Was working towards implementing a Fast Fourier Transform (FFT) algorithm
Decided to move to work towards an initial MATLAB solution
  Data Manipulation
  Testing and debugging

## Slide 41: MATLAB Functions
Discrete Fourier Transform (sarFFT.m)
  Calculates Fourier Transform
Read From FPGA (readI.m & readQ.m)
  Pulls data from FPGA
Calibration
  Corrects for Phase Slope Error

## Slide 42: Image Formation
  Data Visualization in 2D and 3D

## Slide 43: Full-Scale Range Test Results
Jordan Bolduc

## Slide 44
Corner Reflector
RF Absorber
RF Range Testing
Room Top-View
SAR
-5°
Transmitter
Transmitter
Receivers

## Slide 45: MATLAB Simulations

## Slide 46: Simulation VS RF Range Measurements

## Slide 47: Phase Slope Point of View (Boresight)
Chart: Reflector at Boresite (Outdoors)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
 | 21.9911 | 1.7227 | -20.642 | -15.9958 | -24.444 | -62.0205 | 4.2432 | 39.0939 | -29.2914 | 89.2838 | 4.6355 | 68.9625 | -82.3039 | -61.3269 | -72.0127 | 78.6079
Phase
Phase Slope

## Slide 48: Phase Slope Point of View (-5° from Boresight)
Chart: -5° from Boresight (Indoor): Basis Function Prediction VS Field Measurements
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
Basis Function Ideal | -1.2492 | -2.4985 | -3.7477 | -4.9969 | -6.2462 | -7.4954 | -8.7464 | -9.9939 | -11.2431 | -12.4923 | -13.7416 | -14.9908 | -16.24 | -17.4893 | -18.7385 | -19.9877
Actual Measured | -0.10591 | 88.4697 | 11.8166 | -86.8135 | 14.434 | -8.2453 | -9.0163 | 9.8798 | 18.9727 | 2.288 | 27.0297 | -108.5804 | -10.8208 | -104.3061 | -16.0133 | 38.9817

## Slide 49: Error Discussion & Mitigation Strategies
Scott Nicewonger

## Slide 50: Amplitude & Phase Distortion
Chart: Reflector at Boresite (Outdoors)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
 | 21.9911 | 1.7227 | -20.642 | -15.9958 | -24.444 | -62.0205 | 4.2432 | 39.0939 | -29.2914 | 89.2838 | 4.6355 | 68.9625 | -82.3039 | -61.3269 | -72.0127 | 78.6079

## Slide 51
3D Figure: http://www.wipl-d.com/applications.php?cont=antenna-design/aperture-antennas
TX
RX
LNA2
Adjacent Antenna Near Field Effects
Horn Antenna Radiation Pattern
LNA2 still recovering from saturation when receive mode activates
LNA1

## Slide 52
TX
RX
d
RF Absorber (Optional)
RF Isolation Approach 1: Physical Dimensioning
Increase distance to nearest receiver will:
Mitigate bleed-over signal
Change phase center locations
  Re-calculate phase slope
  Modify signal processing logic
LNA2
LNA1

## Slide 53
RF Isolation Method 2: Receive Mode Switch (Design 1)

## Slide 54
RX
TX
…
…
Receiver
Floor
Reflector
RF Absorber
Indoor Phase Distortion
Room Top-View

## Slide 55: Multipath Mitigation
Extensive outdoor testing & data collection
Continue design refinement for outdoor environment
With outdoor baseline data in-hand, test indoors & compare data sets
Investigate mitigation strategies (physical & DSP)

## Slide 56: Timeline & Budget
Scott Nicewonger & Josh Dennis

## Slide 57
2016
2016
Today
03/07
03/11
03/15
03/19
03/23
03/27
03/31
04/04
04/08
04/12
04/16
04/20
Presentation II (Date TBA)
3/25/2016
Operation Manual & Design Report
4/1/2016
Final Report, Final Webpage, Notebooks
4/8/2016
Final Presentation & Open House
4/14/2016
Spring "Break" End
3/13/2016
Gen II Prototype Complete
3/29/2016
Gen II Prototype Verified
4/4/2016
4 days
3/14/2016 - 3/17/2016
Component Housing Fab & Assembly
8 days
3/18/2016 - 3/25/2016
Gen II Migration
5 days
3/21/2016 - 3/25/2016
RF Test Range Setup & Alignment
7 days
3/23/2016 - 3/29/2016
Delay Line Bench Testing
6 days
3/30/2016 - 4/4/2016
RF Range Testing
6 days
3/30/2016 - 4/4/2016
Neural Network Development & Testing (Strech Goal)
4 days
4/5/2016 - 4/8/2016
Data Documentation & Analysis
5 days
4/11/2016 - 4/15/2016
Closure & Gen III Hand-Off Plan
FAMU/FSU COE Synthetic Aperture Radar
Spring 2016 Timeline

## Slide 58: Budget Overview, 2015-2016
Chart: ECE Team, 2015-2016
| Component Box Assembly | Electrical Hardware | Electrical Test Equipment | Remaining
 | 688.97 | 84.79 | 34.86 | 4191.38
Chart: ME Team, 2015-2016
| HORN HOLDER | STRUCTURE | TOOLS | CALIBRATION | RF PANELS | REMAINING
TOTAL | 390 | 1940 | 120 | 170 | 1510 | 870

## Slide 59: Expenditures Overview, 2014-2016
Chart: Expenditures
| GEN 1 TEAM | GEN 2 ME TEAM | GEN 2 EE TEAM
Total | 42530 | 4130 | 810

## Slide 60: Conclusions
SAR can successfully detect RF corner reflector at operational distance
Considerable phase distortion due to:
  Adjacent Tx/Rx near-field effects
  Multipath interference
Can write & read data to FPGA
  Manual Mode operation
  Instantaneous data points (non-real-time)
VHDL Control logic complete
  Need voltage step-up switch circuit
MATLAB signal processing backbone complete
VGA Display logic complete
Gen II Array Structure & Component Housing
  Robust
  Drastic weight reduction
  Modular

## Slide 61: Future Recommendations
Fall 2016 – Spring 2017
New voltage step-up switch circuit for FPGA switching
RF Isolation
  Implement Isolation Switch or Array re-design
Extensive Outdoor Testing to establish baseline, then indoor testing to quantify indoor multipath effects
Real-time data processing (VHDL and/or MATLAB)
Investigate Neural Network implementation
Fall 2016 and Beyond
Patch Antenna Array Re-design
  Collab with HPMI Printed Sensors lab
Phase Slope Simulator
  Coaxial line stretcher & switch to simulate Rx phase slope
Future Project: Phased Array Radar
  Use SAR array backbone
  Drop-in phased array module
  Year 1: Manual beam steering with coaxial line stretchers
  Year 2-3: Digital Beamforming

## Slide 62: Acknowledgements!
Sponsors:
Northrop Grumman
Pete Stenger
Mike Blue
Advisors:
Dr. Simon Foo
Dr. Shonda Bernadin
Dr. Rajendra Arora
Dr. Dorr Campbell
Instructors:
Dr. Jerris Hooker
Dr. Nikhil Gupta

## Slide 63: Questions?

## Slide 64
Existing
SAR Array
Drop-in Phased Array Module
Phase Slope
Detector
COTS Phase Shifters

## Slide 65: ECE Budget Supplement

## Slide 66: Switching Diagram
Olivier Barbier

## Slide 67: Design Overview
Objective
  Develop a static, multi-antenna Synthetic Aperture Radar (SAR) Imager
Specifications
Low resolution proof of concept prototype
10 GHz operating frequency
20 feet range
40” x 40” downrange scene
Safety
RF Exposure Safety Guidelines
  ANSI/IEEE C95.1-1992
  FCC 47 C.F.R. 1.1307(b), 1.1310, 2.1091, 2.1093
Limit for human exposure: 1 mW/cm2
SAR Peak Transmit: 0.0076 mW/cm2

## Slide 68: Obstacles(Continue)
Voltage
Time
MOSFET Circuit Output