## Slide 1: Tesla Pump
Virtual Design Review 1
Patrick Duggan, Eric Goff, Garrett Hart, Tom Kline, Chris Salim
Fall 2017
10/19/2017
Team 12

## Slide 2: Team Members
Chris Salim
Eric Goff
Tom Kline
Garrett Hart
Patrick Duggan
Team Leader
Secretary
Treasurer
Lead ME
Design Coordinator

## Slide 3: Project Brief
Develop Tesla pump for using with in tank propellant mixing and transfer to:
  Distribute heat
  Transfer fluid in/out of a vessel
  Distribute fluid to point of use in vessel
Use of stacked flat disks simplifying:
  Layout
  Manufacturing process
Pump driven by electric motor

## Slide 4: Background Information
Tesla Turbine
  Invented and patented by Nikola Tesla in 1913
  Bladeless turbine
  Series of smooth disks with nozzles spraying fluid
  Incoming fluid flows parallel to disks, exhaust moves out sides
  Has not been successfully commercialized
Figure 1: Basic layout of Tesla Turbine/Pump.[1]

## Slide 5: Background Information
Tesla Pump
  Tesla turbine with reverse functions, effectively a pump
  Fluid flows in perpendicular to discs, exhaust exits parallel
  Commercially available since 1982
  Used to pump rougher, more abrasive fluids than a typical pump
Figure 1: Basic layout of Tesla Turbine/Pump.[1]

## Slide 6: What is a Tesla Pump
The Tesla Pump is a collection of stacked disks
It operates at high RPM
It will be enclosed in housing
The disks have a small specified gap in between each disk
Housing
Stacked Disks
Outlet
Inlet
Figure 2: Depiction of inside a Tesla pump.[2]

## Slide 7: How the Tesla Pump Works
Generate fluid flow by spinning the disks
Thin viscous region created between the disks
  Due to friction between the disks and fluid
    Region is directly related to the boundary layer effect
As revolutions per minute increase, centripetal force expels the fluid through the outlet
Outlet
Closed Outlet
Inlet
Force Vector
Figure 3: Tesla pump fluid flow visual.[3]

## Slide 8: The Boundary Layer Effect
As fluid moves next to surface, velocities of each will theoretically move at the same speed where fluid meets the surface
The boundary layer effect is directly related to:
  Fluid viscosity
  Surface material
With very small gaps between plates in the pump, this effect will be very prevalent
Free Stream Velocity Profile
Boundary Layer
Velocity Profile
Figure 4: Boundary layer illustration with velocity profiles over a flat plate.[4]

## Slide 9: Stakeholders
Sponsor:
NASA – Marshall Space Flight Center (MSFC)
Sponsor:
FAMU – FSU College of Engineering
Engineering Liaison:
James Martin
Engineering Liaison:
James Smith
Project Advisor: Lance Cooley, Ph.D.
Department Advisor: Chiang Shih, Ph.D.
Department Advisor: Shayne McConomy, Ph.D.

## Slide 10: Project Scope
Key Goals
  Minimize number of parts
  Achieve a minimum 5 psi pressure rise
  Achieve 15 gpm flow rate
  Consume least possible amount of power
  Operate at relatively low rpm
  Limit weight
  Operable in a flange
  Meet size constraints
  Design and build testable Tesla pump prototype

## Slide 11: Project Scope Continued
Primary Markets:
  NASA - MSFC
  Other government or private aerospace organizations
Secondary Markets:
  Other government or private industries related to fluid dynamics
  Biomedical industry
Project Assumptions:
  Water is a good fluid choice for operational simulation
  Materials will be liquid nitrogen compatible
  Corrosion and other degradation factors can be mostly ignored
  Vary only disk spacing and not disk size

## Slide 12: Customer Needs
Our team conducted a conference call to gather information on requirements for the design. What we learned includes:
  Fluids being pumped
    Prototype will pump water but model the pump to allow for liquid nitrogen as well
  Preferred RPM
    Pump efficiency is main priority
  Size Constraints
    Design attaches to an 8 inch 304L SS Conflat flange
    Strive to fit through a 4 inch diameter hole
  Weight Constraints
    No set constraint, but excessively heavy parts should be reassessed
  Budget
    Estimated no more than $500

## Slide 13: Functional Decomposition
Table 1: Functional decomposition category and tasks.

## Slide 14: Functional Decomposition
Figure 5: Inside housing functional decomposition. [3]

## Slide 15: Functional Decomposition
Figure 6: Housing and disks functional decomposition. [2]

## Slide 16: References
[1] “Дисковый насос Тесла.” http://www.teslatech.com.ua.
[2] “Tesla Turbine.” TurbineGenerator, TurbineGernerator, 20 Dec. 2016, turbinegenerator.org/tesla-turbine/.
[3] “Designing a 3D Printed Tesla Turbine.” InterPro, InterPro, 2017, interpromodels.com/designing-a-3d-printed-tesla-turbine/.
[4]Guha, Dr. Tufan K. “Pipe Flow: Major and Minor Losses.” Thermal Fluids Lab Class. Thermal Fluids Lab Class, Tallahassee Fl, FAMU-FSU College of Engineering.