## Slide 1
Virtual Design Review 2
Patrick Duggan, Garrett Hart, Thomas Kline
11/09/2017
Tesla Pump
Team 12

## Slide 2
Patrick Duggan
Team Leader
Design Team
Eric Goff
Secretary
Garrett Hart
Treasurer
Thomas Kline
Lead ME
Christopher Salim
Design Coordinator
Project Advisors:
James Martin
James Smith
Faculty Advisors:
Shayne McConomy, PhD
Chiang Shih, PhD
Lance Cooley, PhD

## Slide 3
Tesla Pump Recap
Stacked Disks
Series of flat disks with inner holes that spin due to a motor
Fluid enters around center of disks and centripetally moves outward
The boundary layer effect that occurs between the disks propels the fluid
Increasing rotational speed will increase centripetal force
Figure 1. Tesla Pump System [2]
Thomas Kline

## Slide 4
Tesla Pump Recap
Stacked Disks
Inlet
Series of flat disks with inner holes that spin due to a motor
Fluid enters around center of disks and centripetally moves outward
The boundary layer effect that occurs between the disks propels the fluid
Increasing rotational speed will increase centripetal force
Figure 1. Tesla Pump System [2]
Thomas Kline

## Slide 5
Tesla Pump Recap
Stacked Disks
Outlet
Inlet
Housing
Series of flat disks with inner holes that spin due to a motor
Fluid enters around center of disks and centripetally moves outward
The boundary layer effect that occurs between the disks propels the fluid
Increasing rotational speed will increase centripetal force
Figure 1. Tesla Pump System [2]
Thomas Kline

## Slide 6
Tesla Pump Recap
Used for mixing and transporting cryogenic fluid (Liquid Nitrogen and Oxygen)
Size of tank and type of fluid defines the 15 gpm and 5 psi rise targets
Mixing will help reduce stratification within the fluid as well as disperse thermal energy
Pump shall also be robust and be able to transfer fluid from one tank to another depending on needed application
Figure 2. Propellant Mixing [3]
Thomas Kline

## Slide 7
Target Catalog
Base of major targets
  15 gpm
  5 psi pressure rise
To reach the major targets
  Disk spacing range based on previous studies
  Minimal power and of disks varies based on the provided motor: Bodine 34B4BEBL
Housing dimensions
  Fits on 8 in diameter conflat flange
  Fits through 4 in diameter hole
Table 1. Target Catalog
Thomas Kline

## Slide 8
Concept Generation - Overall Concept 1
Cylindrical Housing
Anchor points at bottom
Two outlets
  Mixing
  Pump out
Inlets at the bottom centered around the shaft
Disks centered in housing
Figure 3. Concept 1
Thomas Kline

## Slide 9
Cylindrical Housing
Anchor points at bottom
Two outlets
  Mixing
  Pump out
Inlets at the bottom centered around the shaft
Disks centered in housing
Concept Generation - Overall Concept 1
Figure 3. Concept 1
Thomas Kline

## Slide 10
Concept Generation - Overall Concept 1
Figure 3. Concept 1
Thomas Kline
Cylindrical Housing
Anchor points at bottom
Two outlets
  Mixing
  Pump out
Inlets at the bottom centered around the shaft
Disks centered in housing

## Slide 11
Cylindrical Housing
Anchor points at bottom
Two outlets
  Mixing
  Pump out
Inlets at the bottom centered around the shaft
Disks centered in housing
Concept Generation - Overall Concept 1
Figure 3. Concept 1
Thomas Kline

## Slide 12
Concept Generation - Overall Concept 1
Figure 3. Concept 1
Thomas Kline
Cylindrical Housing
Anchor points at bottom
Two outlets
  Mixing
  Pump out
Inlets at the bottom centered around the shaft
Disks centered in housing

## Slide 13
Concept Generation - Overall Concept 1
Figure 3. Concept 1
Thomas Kline
Cylindrical Housing
Anchor points at bottom
Two outlets
  Mixing
  Pump out
Inlets at the bottom centered around the shaft
Disks centered in housing

## Slide 14
Presenting Next
Patrick Duggan
Design Concept 2 & Design Components

## Slide 15
Cylindrical divergent housing
  Direct flow to outlet
Solid disk near center of disk stack
  Prevent fluid from traveling farther vertically and direct it outwards
Structural support and mounting at base
  Connect to flange
Concept Generation - Overall Concept 2
Figure 4. Concept 2
Patrick Duggan

## Slide 16
Concept Generation - Overall Concept 2
Figure 4. Concept 2
Patrick Duggan
Cylindrical divergent housing
  Direct flow to outlet
Solid disk near center of disk stack
  Prevent fluid from traveling farther vertically and direct it outwards
Structural support and mounting at base
  Connect to flange

## Slide 17
Concept Generation - Overall Concept 2
Figure 4. Concept 2
Patrick Duggan
Cylindrical divergent housing
  Direct flow to outlet
Solid disk near center of disk stack
  Prevent fluid from traveling farther vertically and direct it outwards
Structural support and mounting at base
  Connect to flange

## Slide 18
Concept Generation - Overall Concept 2
Cantilever style bearings for shaft support
  2 bearings located near base
Two inlets
  Top & bottom
    Permit more fluid to enter
    Top inlet funneled entrance to help guide fluid
One outlet
  Nipple attachment to connect hose
Figure 4. Concept 2
Patrick Duggan

## Slide 19
Cantilever style bearings for shaft support
  2 bearings located near base
Two inlets
  Top & bottom
    Permit more fluid to enter
    Top inlet funneled entrance to help guide fluid
One outlet
  Nipple attachment to connect hose
Concept Generation - Overall Concept 2
Figure 4. Concept 2
Patrick Duggan

## Slide 20
Concept Generation - Overall Concept 2
Cantilever style bearings for shaft support
  2 bearings located near base
Two inlets
  Top & bottom
    Permit more fluid to enter
    Top inlet funneled entrance to help guide fluid
One outlet
  Nipple attachment to connect hose
Figure 4. Concept 2
Patrick Duggan

## Slide 21
Concept Generation - Disk Hole Design
Disk holes directly affect:
  Weight of pump
  Efficiency of fluid flow
  Velocity of fluid
Design can include a combination of multiple hole designs
The housing intakes will also be similar to the disk holes to avoid unneeded stress build up with fluid intake
Figure 6. Disk Hole Concept
Patrick Duggan
(a)
(d)
(b)
(c)

## Slide 22
Concept Generation - Disk Hole Design
The hole shapes in 6a and 6b offer a cheap and simple simple design
  These designs are currently used in a wide range of applications
The teardrop shape in 6c creates a natural vortex in fluid flow pulling it down the length of the shaft
The notches in 6d allow the fluid to be easily channeled about the circumference
  When staggered, the helical shape produces more torque at lower rpm
Figure 6. Disk Hole Concept
Patrick Duggan
Figure 6. Disk Hole Concept
(a)
(d)
(b)
(c)

## Slide 23
Concept Generation - Disk Hole Design
The hole shapes in 6a and 6b offer a cheap and simple simple design
  These designs are currently used in a wide range of applications
The teardrop shape in 6c creates a natural vortex in fluid flow pulling it down the length of the shaft
The notches in 6d allow the fluid to be easily channeled about the circumference
  When staggered, the helical shape produces more torque at lower rpm
Figure 6. Disk Hole Concept
Patrick Duggan
Figure 6. Disk Hole Concept
(a)
(d)
(b)
(c)

## Slide 24
Concept Generation - Disk Hole Design
The hole shapes in 6a and 6b offer a cheap and simple simple design
  These designs are currently used in a wide range of applications
The teardrop shape in 6c creates a natural vortex in fluid flow pulling it down the length of the shaft
The notches in 6d allow the fluid to be easily channeled about the circumference
  When staggered, the helical shape produces more torque at lower rpm
Figure 6. Disk Hole Concept
Patrick Duggan
Figure 6. Disk Hole Concept
(a)
(d)
(b)
(c)

## Slide 25
Concept Generation - Disk Stack
Ending Disk Stack | Spacers | Disks
Figure 7. Disk Stack Concept
“Variable End” Design was generated
Multiple disks are stacked together to form a “variable” disk used on the ends of the stack
The “Variable End” ensures disk spacing can be controlled while keeping overall length constant
For further control the spacers and disks themselves can be made thinner
Patrick Duggan

## Slide 26
Concept Generation - Disk Shaft
Figure 8. Shaft Concepts
Need to:
  Prevent excessive vibration
    Asymmetric vs. Symmetric
  Rigidly attach disks to shaft
    Internal vs. External teeth attachment style
      Location of stress concentrations
  Permit variation of disk spacing
  Feasibility of design
    Can it be manufactured or purchased at a reasonable cost?
Figure 9. Effective Stress Along a Shaft [3]
Patrick Duggan
Stress (Mpa)

## Slide 27
Presenting Next
Garrett Hart
Design Components & Conclusion

## Slide 28
Concept Generation - Outlet Nozzle
Figure 10. a-series
Rectangular cross sectional area nozzle
(a.1)Rectangular tube 90° bend
(a.2)Round tube smooth 90° bend
(a.3)Rectangular tube straight out horizontally
Figure 10. b-series
Round cross sectional area
(b.1)Round tube smooth 90° bend
(b.2)Rectangular tube 90° bend
(b.3)Round tube straight out horizontally
Figure 10. Outlet Nozzle Concepts
Garrett Hart

## Slide 29
Concept Generation - Outlet Nozzle
Figure 10. a-series
Rectangular cross sectional area nozzle
(a.1)Rectangular tube 90° bend
(a.2)Round tube smooth 90° bend
(a.3)Rectangular tube straight out horizontally
Figure 10. b-series
Round cross sectional area nozzle
(b.1)Round tube smooth 90° bend
(b.2)Rectangular tube 90° bend
(b.3)Round tube straight out horizontally
Figure 10-a.1. Outlet Nozzle (a.1) Concept
Garrett Hart

## Slide 30
Concept Generation - Outlet Nozzle
Figure 10. a-series
Rectangular cross sectional area nozzle
(a.1)Rectangular tube 90° bend
(a.2)Round tube smooth 90° bend
(a.3)Rectangular tube straight out horizontally
Figure 10. b-series
Round cross sectional area nozzle
(b.1)Round tube smooth 90° bend
(b.2)Rectangular tube 90° bend
(b.3)Round tube straight out horizontally
Figure 10-a.2. Outlet Nozzle (a.2) Concept
Garrett Hart

## Slide 31
Concept Generation - Outlet Nozzle
Figure 10. a-series
Rectangular cross sectional area nozzle
(a.1)Rectangular tube 90° bend
(a.2)Round tube smooth 90° bend
(a.3)Rectangular tube straight out horizontally
Figure 10. b-series
Round cross sectional area nozzle
(b.1)Round tube smooth 90° bend
(b.2)Rectangular tube 90° bend
(b.3)Round tube straight out horizontally
Figure 10-a.3. Outlet Nozzle (a.3) Concept
Garrett Hart

## Slide 32
Concept Generation - Outlet Nozzle
Figure 10. a-series
Rectangular cross sectional area nozzle
(a.1)Rectangular tube 90° bend
(a.2)Round tube smooth 90° bend
(a.3)Rectangular tube straight out horizontally
Figure 10. b-series
Round cross sectional area nozzle
(b.1)Round tube smooth 90° bend
(b.2)Rectangular tube 90° bend
(b.3)Round tube straight out horizontally
Figure 10-b.1. Outlet Nozzle (b.1) Concept
Garrett Hart

## Slide 33
Concept Generation - Outlet Nozzle
Figure 10. a-series
Rectangular cross sectional area nozzle
(a.1)Rectangular tube 90° bend
(a.2)Round tube smooth 90° bend
(a.3)Rectangular tube straight out horizontally
Figure 10. b-series
Round cross sectional area nozzle
(b.1)Round tube smooth 90° bend
(b.2)Rectangular tube 90° bend
(b.3)Round tube straight out horizontally
Figure 10-b.2. Outlet Nozzle (b.2) Concept
Garrett Hart

## Slide 34
Concept Generation - Outlet Nozzle
Figure 10. a-series
Rectangular cross sectional area nozzle
(a.1)Rectangular tube 90° bend
(a.2)Round tube smooth 90° bend
(a.3)Rectangular tube straight out horizontally
Figure 10. b-series
Round cross sectional area nozzle
(b.1)Round tube smooth 90° bend
(b.2)Rectangular tube 90° bend
(b.3)Round tube straight out horizontally
Figure 10-b3. Outlet Nozzle (b.3) Concept
Garrett Hart

## Slide 35
Concept Generation - Outlet Nozzle
Figure (10-a) a-series
  Rectangular cross sectional area nozzle
Pros
  Promotes better fluid mixing
Cons
  Cost more to produce
  Better fluid mixing = less pressure rise
Garrett Hart
Figure 10-a. Rectangular Outlet Concept

## Slide 36
Concept Generation - Outlet Nozzle
Figure 10-b. Round Nozzle Concept
Garrett Hart
Figure(10-b) b-series
  Round cross sectional area nozzle
Pros
  Generates great fluid Pressure rise
  Easiest to process
  Cheaply made
Cons
  High pressure rise = less efficient
fluid mixing

## Slide 37
Concept Generation - Outlet Nozzle
Garrett Hart
Figure 11. Jet Velocity Gradient [1]

## Slide 38
Concept Generation - Bearings
Garrett Hart
Axial loads are located along the shaft
Radial loads are located perpendicular to the shaft
Figure 12: Bearing Load distribution [4]

## Slide 39
Concept Generation - Bearings
Garrett Hart
Axial loads are located along the shaft
Radial loads are located perpendicular to the shaft
Figure 12: Bearing Load distribution [4]

## Slide 40
Concept Generation - Bearings
Garrett Hart
Axial loads are located along the shaft
Radial loads are located perpendicular to the shaft
Figure 12: Bearing Load distribution [4]

## Slide 41
Concept Generation - Bearings
Figure 13-a. Straight Roller Bearing [3]
Sacrifices axial loads for radial loads
Cylindrical shape spreads out radial stress concentration
Figure 13-b.Tapered Roller Bearing [3]
Better at balancing a combination of axial and radial loads
Figure 13-c. Ball Bearing [3]
Cheapest and easiest to acquire.
Can be prone to deformation
Garrett Hart

## Slide 42
Concept Generation - Bearings
Figure 13-a. Straight Roller Bearing [5]
Sacrifices axial loads for radial loads
Cylindrical shape spreads out radial stress concentration
Figure 13-b.Tapered Roller Bearing [5]
Better at balancing a combination of axial and radial loads
Figure 13-c. Ball Bearing [5]
Cheapest and easiest to acquire.
Can be prone to deformation
Garrett Hart

## Slide 43
Concept Generation - Bearings
Figure 13-a. Straight Roller Bearing [3]
Sacrifices axial loads for radial loads
Cylindrical shape spreads out radial stress concentration
Figure 13-b.Tapered Roller Bearing [3]
Better at balancing a combination of axial and radial loads
Figure 13-c. Ball Bearing [3]
Cheapest and easiest to acquire.
Can be prone to deformation
Garrett Hart

## Slide 44: Questions ?

## Slide 45
References
[1] Dr. Guha, Tufan. “Rectanguar Jet_Lecture Notes.” Thermal Fluids Class. Thermal Fluids Class, Tallahassee, FAMU- FSU College of Engineering.
[2] “Tesla Turbine.” TurbineGenerator, TurbineGernerator, 20 Dec. 2016,
turbinegenerator.org/tesla-turbine/.
[3]“What Is Radial Load and Axial Load?” Quora, Kaydon Bearing Solutions, www.quora.com/What-is-radial-load-and-axial-load.
[4]“Failure Analysis of a Half-Shaft of a Formula SAE Racing Car.” Case Studies in Engineering Failure Analysis, Elsevier, 9 May 2016, www.sciencedirect.com/science/article/pii/S2213290216300086.
[5] “Bearings.” Motion Industries, Motion Industries, www.motionindustries.com/taxonomy/Bearings/browse/en.
Notes: https://www.ksb.com/centrifugal-pump-lexicon/noise-in-pumps-and-systems/191140/