## Slide 1: Team 505: SAE Hybrid Vehicle: Battery Box and BMS
13-Nov-18

## Slide 2: Team Introductions
Thomas O’Neill
ME
Christopher Fishman
EE
William Pisani
ME
Christian Gaya
CPE
Raymond Klouda
ME

## Slide 3: Past Work
William Pisani

## Slide 4: Project Re-Introduction
Objective
  Build a battery box and battery management system (BMS) for the SAE hybrid vehicle competition team
Sponsor
  An American Fortune 500 corporation that designs, manufactures, and distributes engines, filtration, and power generation products.
  Leading innovation in electrified power on numerous applications especially class 8 semi-trucks.
William Pisani

## Slide 5: What was done in VDR1
Project Scope
Project Description
  A small model of the battery box and BMS for the SAE hybrid vehicle will be built. A program will also be created that takes in arbitrary vehicle parameters and outputs the appropriate sizing of the battery system
Key Goals
  Compact battery container integrated into frame of vehicle
  Environmentally sustainable, waterproof, and thermally insulated
  BMS will measure battery charge, control power, and monitor current flow, voltage levels, and temperature
Assumptions
  Vehicle will have enough room for full-scale battery pack and box
  Rulebook will be the same for the year of the competition
  Chassis will remain the same for the year of the competition
William Pisani

## Slide 6: What was done in VDR1 (cont.)
William Pisani
Customer Needs
Interpreted Needs
  A program should take parameters for a battery and output parameters for a battery box and BMS
  The battery box should protect the battery, keep the battery from overheating, and the battery box cannot negatively impact the environment
  A small-scale prototype should be created with proper specifications
  BMS maintains charge control, cell balancing, and monitors power input and output
  Battery system for a momentary high-torque boost should be focal point of the BMS system
  The battery box and BMS must both adhere to SAE competition guidelines

## Slide 7
William Pisani
Battery System
Battery Containment
Battery Management System
Support
Monitor
Integrate
Configure
Control
External Forces
Battery Load
Vehicle Chassis
Battery Layout
Temperature
Control
Charge
Current Flow
Voltage Level
Power Output
Batteries
Temperature
What was done in VDR1 (cont.)
Functional Decomposition

## Slide 8: Targets
William Pisani

## Slide 9
Weight, discharge current, voltage level, power output, G-Force, and input voltage were all chosen in a performance-based perspective
With safety in mind, the impact resistance, box temperature, and cell temperatures were chosen carefully to maintain operation while mitigating risks
William Pisani
Metric | Target | Unit
G-Force | 2 | G’s
Impact Resistant | Yes | N/A
Battery Weight | 8 | Lbs.
Compact | Yes | N/A
Battery Volume | 216 | In3
Internal Box Temperature | <60 | Celsius
Max Discharge Current | 500 | Amps
Battery Pack Voltage Level | 60 | Volts
Battery Cell Temperatures | <60 | Celsius
Power Output | 30 | kW
Input Voltage to Battery | 60 | Volts

## Slide 10: Concept Generation
Chris Fishman

## Slide 11: Methods of Generation
Biomimicry
  Analytically apply our problem to nature and brainstorm nature's own solutions
Anti-Problem
  Project problems were reversed, and possible solutions to these anti-problems were found
Morphological Chart
  Lists functions and various mechanisms that can be used to perform the functions listed
  Includes the ideas we found from biomimicry, anti-problems, and the customer needs
  Lines can be used to connect the rows and columns of the chart. Each line represents a different possible concept
Chris Fishman
Notes: "Next, Anti-problem was used to generate concepts. In this method, the problem was reversed, and possible solutions and problems were created. For example, instead of trying to solve the problem “How will the batteries be cooled” the problem was stated as “How to keep the car from catching fire”. This method allowed us to see simple solutions we were previously missing."
- purpose is to help teams look at a problem in a different way and break out existing patterns.
- how do we keep batteries dry – versus- how do we stop water intrusion. OR, how do we charge the batteries – versus- what is going to be a realistic/feasible power supply.

## Slide 12: Methods of Generation (cont.)
The main functions that were added to the morphological chart derive from the interpreted customer needs
By building a multi-option chart, it is possible to piece together many different combinations of the project functions
Generating a large volume of concepts provides a broad spectrum of options to later narrow down based on a weighted value system in the Concept Selection phase of the project
Chris Fishman

## Slide 13: Morphological Chart
Function | Option 1 | Option 2 | Option 3 | Option 4
Box Shape | Cube | Rectangle | Cross | T-Shape
Box Cooling | Liquid cooling | Air cooling (ventilation) | Fans | 
Box Waterproofing | Rubber seals | Water diversion | Silicon Sealant | Vacuum Sealed
Box Mounting | Integrated into chassis | Bolted into chassis |  | 
Energy Storage Device | Individual ioncells | Purchase off shelf | Capacitor | 
Energy Storage Device Wiring | Series | Parallel | Both series and parallel | 
BMS Measurements | Current | Voltage | Temperature | All measurements
Current Type | AC | DC |  | 
Charging Device | Wall power | Solar | Regeneration | 
Chris Fishman
Function | Option 1 | Option 2 | Option 3 | Option 4
Box Shape | Cube | Rectangle | Cross | T-Shape
Box Cooling | Liquid cooling | Air cooling (ventilation) | Fans | 
Box Waterproofing | Rubber seals | Water diversion | Silicon Sealant | Vacuum Sealed
Box Mounting | Integrated into chassis | Bolted into chassis |  | 
Energy Storage Device | Individual ion-cells | Purchase off shelf | Capacitor | 
Energy Storage Device Wiring | Series | Parallel | Both series and parallel | 
BMS Measurements | Current | Voltage | Temperature | All measurements
Current Type | AC | DC |  | 
Charging Device | Wall power | Solar | Regeneration | 

## Slide 14: Morphological Chart
Function | Option 1 | Option 2 | Option 3 | Option 4
Box Shape | Cube | Rectangle | Cross | T-Shape
Box Cooling | Liquid cooling | Air cooling (ventilation) | Fans | 
Box Waterproofing | Rubber seals | Water diversion | Silicon Sealant | Vacuum Sealed
Box Mounting | Integrated into chassis | Bolted into chassis |  | 
Energy Storage Device | Individual ion-cells | Purchase off shelf | Capacitor | 
Energy Storage Device Wiring | Series | Parallel | Both series and parallel | 
BMS Measurements | Current | Voltage | Temperature | All measurements
Current Type | AC | DC |  | 
Charging Device | Wall power | Solar | Regeneration | 
Chris Fishman

## Slide 15: Concept Selection
Thomas O'Neill

## Slide 16: Comparison Matrix
Thomas O'Neill
Notes: Comparison Matrix allowed us to determine the importance weight factors for each customer requirements to be used in HoQ.

## Slide 17: House of Quality
Thomas O'Neill
Notes: Using importance weight factors, we compared customer requirements to the engineering characteristics and determined how important each customer requirements is to each engineering characteristic. From this, relative weight of each engineering characteristic is found which allows us to find the rank orders.

## Slide 18: Nine-Design Pugh Chart
Thomas O'Neill
Notes: Compared our top 8 chosen design concepts to the selection criteria datum. Each design was rated against each selection criteria and given plus, minus, or satisfactory for each criteria. Everything was summed up and designs 3, 4, 5 scored the lowest and were eliminated.

## Slide 19: Five-Design Pugh Chart
Thomas O'Neill
Notes: The first step was to replace the datum. Here datum 1 was chosen but it didn’t matter which we chose as they all tied. From the results, design 1 seemed to be the best result in regards to number of pluses and minuses.

## Slide 20: Analytical Hierarchy Process
Thomas O'Neill
Notes: Here AHP, a very mathy method, was used to confirm our previous findings from the pugh charts. First we compared each characteristic to themselves and rate accordingly.

## Slide 21: Analytical Hierarchy Process Normalized
Thomas O'Neill
Notes: The vlues from the previous chart were calculated by normalizing each number using the sums from the previous chart. Criteria weights for each characteristic were found.

## Slide 22: Analytical Hierarchy Results
The criteria weights were recorded and used, along with the matrix, in multiple equations
Using these equations, we solved for a consistency ratio
  Aim for a consistency ratio of below 0.1
  Ours was 0.13
  Slight bias towards monitored parameters in BMS
  Crucial for proper operation and safety
Thomas O’Neill

## Slide 23: Analytical Hierarchy Process (cont.)
Thomas O’Neill
Notes: AHP was then done for each characteristic compared to the top 3 designs we found from the pugh charts. Here are two examples, power and weight. The same process was followed as before.

## Slide 24: Analytical Hierarchy Process (cont.)
Thomas O’Neill
Notes: Using criteria weights found for every characteristic, we listed them in a matrix and calculated the alternative values for each design seen at the right. From these it shows that design 1 has the highest value which leads us to believe that design 1 once again is the best slide

## Slide 25: Top Design from AHP and Pugh Charts
Design 1
  Box Shape: Rectangle
  Box Cooling: Liquid Cooling
  Box Waterproofing: Rubber Seals
  Box Mounting: Integrated into Chassis
  Energy Storage Device: Purchase Off Shelf
  Energy Storage Device Wiring: Wiring Included with Purchase
  BMS Measurements: Temperature, Voltage, and Current
  Current Type: DC
  Charging Device: Wall Power
Thomas O'Neill

## Slide 26: References
Motors. (n.d.). Retrieved October 2, 2018, from http://www.evwest.com/catalog/index.php?cPath=8
Fuel Economy Retrieved October 2, 2018, from https://www.fueleconomy.gov/feg/hybridtech.shtml.
800hp Electric Pickup Retrieved October 3, 2018, from https://www.hardworkingtrucks.com/rivian-reveals-chassis-of-800-hp-electric-pickup/
Notes: Not this slide will advance on default after 2 seconds. If you would like to change this then go to the transition tab and under timing change the advance slide settings.

## Slide 27: Questions

## Slide 28
Part # | Part Name | Revision | Description | Specifications | Quantity | Unit of Measure | Unit Cost | Vendor Name | Ordered? | Estimated Delivery | Arrival Date | Maturity | Cost
295B9-3NF0A | Battery | A | Nissan Leaf battery pack to be used with the built battery management system | Single packs that will contain four cells each | 2 | Each | $ 85.00 | Miami hybrid | No | N/A | N/A | 0.38 | $ 170.00
1NYK7 | Aluminum 6061 Sheets | A | Will surround the battery to act as a protective box | 1/4 in x 24 in x 24 in | 3 | Each | $ 191.84 | Grainger | No | N/A | N/A | 0.38 | $ 575.52
8514K74 | Damping Material | A | Prevents damage to internal box components due to shock and vibration | 3/8 in x 24 in x 24 in | 1 | Each | $ 227.31 | McMaster-Carr | No | N/A | N/A | 0.38 | $ 227.31
CL-W019-OS00TR-A | Thermaltake Transparent Hose | A | Carrys the liquid coolant between the battery and the heat exchanger | Inside Diameter: 1/2"(13 mm ) Outside Diameter: 3/4"(19 mm) Length: 6.5' (200 cm) | 1 | m | $ 8.08 | Newegg.com | No | N/A | N/A | 0.38 | $ 8.08
 | Hose Fittings | A | Connect components (battery, heat exchanger, etc.) to hoses |  |  | Each |  | Lowes | No | N/A | N/A | 0.31 | $ -
 | Hose Clamps | A | Firmly retain hoses on hose fittings, prevents leaks |  |  | Each |  | Lowes | No | N/A | N/A | 0.31 | $ -
AF120 | Fan | A | Provides airflow over heat exchanger during low natural air flow conditions |  | 1 | Each |  | Newegg.com | No | N/A | N/A | 0.35 | $ -
 | Heat Exchanger | A | Rids heat from the coolant into the atmosphere |  | 1 | Each |  |  | No | N/A | N/A | 0.27 | $ -
392023004 | Bosch Water Pump | A | Carries coolant through cooling system loop | Auxiliary pump with gaskets and hardwear included | 1 | Each | $ 47.79 | RockAuto | No | N/A | N/A | 0.35 | $ 47.79
9268 | Battery Management System | A | Controls battery input and output prameters to maintain desired performance | Build to order | 1 | Each | $ 168.00 | AA Portable | No | N/A | N/A | 0.35 | $ 168.00
 | Microprocessor | A | Handles the functions of the water pump |  | 1 | Each |  |  | No | N/A | N/A | 0.27 | $ -
 | Wiring | A | Used to connect the microprocessor to batteries, resistors, thermistors, and voltmeters |  |  | Each |  |  | No | N/A | N/A | 0.27 | $ -
 | Resistors | A | Used in the BMS system |  |  | Each |  |  | No | N/A | N/A | 0.27 | $ -
 | Thermistors | A | measure battery temperature to relay to the BMS and ensure safe operating parameters |  |  | Each |  | Grainger | No | N/A | N/A | 0.31 | $ -
10G492 | Rubber Seals | A | Provides water diversion from sensitive electronic components interal to the box | 0.25" W, 25 ft L |  | Each | $ 24.50 | Grainger | No | N/A | N/A | 0.38 | $ -
 | Voltmeter | A | Measures voltage |  | 1 | Each |  |  | No | N/A | N/A | 0.27 | $ -
38HW82 | Esd Mat | A | Protective equipment to be used while working with electrical system | 4ft x 3ft, Thickness: 5/8" | 1 | Each | $ 211.47 | Grainger | No | N/A | N/A | 0.38 | $ 211.47
33525 | High Voltage Tool Kit | A | Protective equipment to be used while working with electrical system | Set of 13 basic insulated hand tools | 1 | Each | $ 926.00 | Grainger | No | N/A | N/A | 0.35 | $ 926.00
53PZ88 | High Voltage Face Mask | A | Protective equipment to be used while working with electrical system | Color: Lime | 2 | Each | $ 21.15 | Grainger | No | N/A | N/A | 0.38 | $ 42.30
4JD54 | High Voltage Gloves | A | Protective equipment to be used while working with electrical system | Class 00 | 1 | Each | $ 64.75 | Grainger | No | N/A | N/A | 0.38 | $ 64.75
 | Totals |  |  |  | 18 |  |  |  |  |  |  |  | $ 2,441.22

## Slide 29: Top Eight Concepts
Concept 1.
Box Shape: Rectangle, Box Cooling: Liquid Cooling, Box Waterproofing: Rubber Seals, Box Mounting: Integrated into Chassis, Energy Storage Device: Purchase Off Shelf, Energy Storage Device Wiring: Wiring Included with Purchase, BMS Measurements: Temperature, Voltage, and Current, Current Type: DC, Charging Device: Wall Power
Concept 2.
Box Shape: Rectangle, Box Cooling: Air Cooling, Box Waterproofing: Rubber Seals, Box Mounting: Integrated into Chassis, Energy Storage Device: Purchase Off Shelf, Energy Storage Device Wiring: Wiring Included with Purchase, BMS Measurements: Temperature, Voltage, and Current, Current Type: DC, Charging Device: Wall Power
Concept 3.
Box Shape: Rectangle, Box Cooling: Liquid Cooling, Box Waterproofing: Rubber Seals, Box Mounting: Bolted into Chassis, Energy Storage Device: Purchase Off Shelf, Energy Storage Device Wiring: Wiring Included with Purchase, BMS Measurements: Temperature, Voltage, and Current, Current Type: DC, Charging Device: Wall Power
Concept 4.
Box Shape: T-Shape, Box Cooling: Liquid Cooling, Box Waterproofing: Rubber Seals, Box Mounting: Integrated into Chassis, Energy Storage Device: Purchase Off Shelf, Energy Storage Device Wiring: Wiring Included with Purchase, BMS Measurements: Temperature, Voltage, and Current, Current Type: DC, Charging Device: Wall Power

## Slide 30: Top Eight Concepts (cont.)
Concept 5.
Box Shape: Cube, Box Cooling: Liquid Cooling, Box Waterproofing: Silicon Sealant, Box Mounting: Integrated into Chassis, Energy Storage Device: Purchase Off Shelf, Energy Storage Device Wiring: Wiring Included with Purchase, BMS Measurements: Temperature, Voltage, and Current, Current Type: DC, Charging Device: Wall Power
Concept 6.
Box Shape: Rectangle, Box Cooling: Liquid Cooling, Box Waterproofing: Silicon Sealant Silicon Sealant, Box Mounting: Integrated into Chassis, Energy Storage Device: Purchase Off Shelf, Energy Storage Device Wiring: Wiring Included with Purchase, BMS Measurements: Temperature, Voltage, and Current, Current Type: DC, Charging Device: Wall Power
Concept 7.
Box Shape: Rectangle, Box Cooling: Liquid Cooling, Box Waterproofing: Rubber Seals, Box Mounting: Integrated into Chassis, Energy Storage Device: Build Using Ion-Cells, Energy Storage Device Wiring: Parallel, BMS Measurements: Temperature, Voltage, and Current, Current Type: DC, Charging Device: Wall Power
Concept 8.
Box Shape: Rectangle, Box Cooling: Liquid Cooling, Box Waterproofing: Rubber Seals, Box Mounting: Integrated into Chassis, Energy Storage Device: Build Using Capacitors, Energy Storage Device Wiring: Parallel, BMS Measurements: Temperature, Voltage, and Current, Current Type: DC, Charging Device: Wall Power

## Slide 31
Question/Prompt | Customer Statement | Interpreted Need
Should we build a battery box specific to the current SAE hybrid vehicle? | I want to be able to provide parameters about the battery that the box is holding and get values returned about the size of the box. | A program should take parameters about a battery and output parameters about a battery box.
Should a physical model of the battery box be built? | The main item I'm looking for is the program that will give me values based on the battery. | The main item I'm looking for is the program that will give me values based on the battery.
What should the battery box protect from? | The container should be waterproof, thermally insulated, and environmentally sustainable. | The battery box protects the battery. The battery box prevents overheating of the battery. The battery box does not negatively impact the environment.
What should the BMS do? | The BMS will maintain charge control and cell balancing of the battery in a safe and efficient manner while also monitoring power input and output. | BMS maintains charge control, cell balancing, and monitors power input and output.
What battery are we using to create a BMS for? | Decide on a series of parallel battery. Whichever work best for the motor that is being used in the vehicle. | Battery system for a momentary high-torque boost should be focal point of the BMS system
Should we investigate building our own battery or buying one off the shelf? | Creating your own battery would be very difficult. I recommend buying one off the shelf and using that to create a BMS. | Battery will be purchased.
Do you think there are any restrictions to the battery box and BMS? | The SAE rulebook for the competition should contain all details about how the vehicles must be built. | The battery box and BMS both must adhere to SAE competition guidelines.

## Slide 32: Backup Slides
Supporting Slides to the content above.

## Slide 34: Standard Shapes
Summary Box
Text box 1
Outlined Text Box

## Slide 35: Approved Logos

## Slide 36: Color Palette

## Slide 37: APA Tables
Category 1 | Category 2 | Category 3 | Category 4 | Category 5
Item 1 |  |  |  | 
Item 2 |  |  |  | 
Item 3 |  |  |  | 
Item 4 |  |  |  | 
 | Category 2 |  |  | Category 3 | 
Category 1 | subcategory 1 | subcategory 2 |  | subcategory 1 | subcategory 2
Item 1 |  |  |  |  | 
Item 2 |  |  |  |  | 
Item 3 |  |  |  |  | 
Item 4 |  |  |  |  |