## Slide 1
Team 501: Powder Recovery for Metal Additive Manufacturing
Arlan Ohrt
Kevin Richter
Vincent Giannetti
Noah Tipton
Joshua Dorfman
April 16th, 2020

## Slide 2: Team Introductions
Arlan Ohrt
Project/Systems Engineer
Kevin Richter
Field
Engineer
Noah Tipton
Design
Engineer
Vincent Giannetti
Manufacturing
Engineer
Joshua Dorfman
Field
Engineer

## Slide 3
Sponsor – Air Force Research Labs (AFRL)
AFRL/RWMW – Ordnance Division, Damage Mechanisms Branch (Eglin Air Force Base)
  A global leader in advancing weapons science and technology
Specific Contact - Dr. Philip Flater
  Lead for the metal additive manufacturing lab at AFRL/RWMW
Vincent Giannetti

## Slide 4
Project Description
The objective of this project is to design a device which increases the amount of recovered steel powder in a metal additive manufacturing process. This device should be compatible with existing hardware and processes while ensuring the safety of the operators.
Vincent Giannetti

## Slide 5
Project Key Goals and Customer Needs
Increase amount of recovered steel powder
Be compatible with existing hardware and processes
Ensure operator’s safety
The objective of this project is to design a device which increases the amount of recovered steel powder in a metal additive manufacturing process. This device should be compatible with existing hardware and processes while ensuring the safety of the operators.
Vincent Giannetti

## Slide 6
Project Background – Metal Additive Manufacturing
Laser Powder Bed Fusion (LPBF):
Powder Distributed in an Even Layer
Laser Traces Layer Path to “Fuse” Material Together
This process results in a large amount of “unfused” powder. This powder should be recycled.
Vincent Giannetti

## Slide 7
Project Background – The Metal Used
17– 4PH Stainless Steel: 17% Chromium, 4% Nickel, Precipitation Hardening
General Info:
Purchased from company that makes the printer
Particle Size: 10 – 15 μm (Paper thickness is ~ 100 μm)
Martensitic Steel (Magnetic)
Vincent Giannetti

## Slide 8
Project Background – Powder Recovery Stages
“Wet Vac Stage”
“Air Powered Stage”
“Built In Stage”
Vincent Giannetti

## Slide 9
Project Background – Powder Recovery Stages
Stage 1 – “Built In Stage”
Built in recovery system
  Vacuum
  Overflow Reservoir
Operation
  Sealed chamber
  Glove to operate vacuum
Substantial Powder Recovery
Stage 2 – “Wet Vac Stage”
Removing the part
  Pass the build plate out
Operation
  Use powered air purifying respirator (PAPR)
  Open door and remove part
  Use Ruwac NA35 Immersion Vacuum
No Powder Recovery
Vincent Giannetti

## Slide 10
Project Background – Powder Recovery Stages
Stage 2 – “Wet Vac Stage”
Removing the part
  Pass the build plate out
Operation
  Use powered air purifying respirator (PAPR)
  Open door and remove part
  Use Ruwac NA35 Immersion Vacuum
No Powder Recovery
Stage 1 – “Built In Stage”
Built in recovery system
  Vacuum
  Overflow Reservoir
Operation
  Sealed chamber
  Glove to operate vacuum
Substantial Powder Recovery
Stage 3 – “Air Powered Stage”
Sandblasting cabinet
Operation
  Place part inside the enclosure
  Use compressed air to remove residual powder
No Powder Recovery
Vincent Giannetti

## Slide 11
Project Background – Powder Recovery Stages
Stage 3 – “Air Powered Stage”
Sandblasting cabinet
Operation
  Place part inside the enclosure
  Use compressed air to remove residual powder
No Powder Recovery
Stage 2 – “Wet Vac Stage”
Removing the part
  Pass the build plate out
Operation
  Use powered air purifying respirator (PAPR)
  Open door and remove part
  Use Ruwac NA35 Immersion Vacuum
No Powder Recovery
Vincent Giannetti

## Slide 12
“Wet Vac Stage”
“Air Powered Stage”
“Built In Stage”
Substantial Powder Recovery
No Powder Recovery
No Powder Recovery
“Our System”
Substantial Powder Recovery
Project Background – Powder Recovery Stages
Vincent Giannetti

## Slide 13
“Wet Vac Stage”
“Air Powered Stage”
“Built In Stage”
Substantial Powder Recovery
No Powder Recovery
No Powder Recovery
“Our System”
Substantial Powder Recovery
Project Background – Powder Recovery Stages
Vincent Giannetti

## Slide 14
Targets and Design
Noah Tipton
Hold the part in the area
Isolate the powder from user
Prevents powder contamination
Build volume: 250 x 250 x 300 mm
Over-estimated weight: 356 N
Passes through 75 μm mesh
Pass Bioenvironmental Engineering Flight (BEF) air test
Function
Target
Separate powder from the part
Transports powder to a container
Greater than 0 grams of separated powder in container
Targets are necessary to contain and direct the project.
We will do various “Target Checks” to show design reasoning.
Impossible to be more specific because of large variation in printed parts.

## Slide 15
Targets
Hold the part in the area
Isolate the powder from user
Prevents powder contamination
Build volume: 250 x 250 x 300 mm
Over-estimated weight: 356 N
Passes through 75 μm mesh
Pass Bioenvironmental Engineering Flight (BEF) air test
Function
Target
Separate powder from the part
Transports powder to a container
Greater than 0 grams of separated powder in container
Targets are necessary to contain and direct the project.
We will do various “Target Checks” to show design reasoning.
Impossible to be more specific because of large variation in printed parts.
Noah Tipton

## Slide 16
Build Plate and Part
Fasteners
Vibrator
New System
Noah Tipton

## Slide 17
New System – Structural Analysis
* CREO Von Mises
σMax* ≈ 315 psi
σy ≈ 40,000 psi
σMax *≈ 915 psi
σy ≈ 40,000 psi
τMax ≈ 157 psi
τFail ≈ τTresca ≈ 20,000 psi
σMax*≈ 300 psi
σy ≈ 47,000 psi
Noah Tipton

## Slide 18
New System – Structural Analysis
* CREO Von Mises
σMax* ≈ 315 psi
σy ≈ 40,000 psi
σMax *≈ 915 psi
σy ≈ 40,000 psi
τMax ≈ 157 psi
τFail ≈ τTresca ≈ 20,000 psi
σMax*≈ 300 psi
σy ≈ 47,000 psi
Noah Tipton
Target Check
Build volume: 250 x 250 x 300 mm
Over-estimated weight: 356 N

## Slide 19
New System – Structural Analysis
What About Powder Containment?
* CREO Von Mises
τMax ≈ 157 psi
τFail ≈ τTresca ≈ 20,000 psi
σMax*≈ 300 psi
σy ≈ 47,000 psi
Noah Tipton
Target Check
Build volume: 250 x 250 x 300 mm
Over-estimated weight: 356 N

## Slide 20
New System
What About Powder Containment?
Noah Tipton

## Slide 21
Barrier Needed to Control Powder
New System
What About Powder Containment?
Noah Tipton

## Slide 22
Chosen Barrier and Operation
Kevin Richter
BADBOY Blaster
Clamshell Design
Fits Design Well
Industrial Quality

## Slide 23
Chosen Barrier
BADBOY Blaster
Clamshell Design
Fits Design Well
Industrial Quality
AFRL is Familiar with BADBOY’s Quality
Kevin Richter

## Slide 24
Chosen Barrier
BADBOY Blaster
Clamshell Design
Fits Design Well
Industrial Quality
AFRL is Familiar with BADBOY’s Quality
Kevin Richter
Target Check
Pass Bioenvironmental Engineering Flight (BEF) air test.

## Slide 25
Chosen Barrier
AFRL is Familiar with BADBOY’s Quality
Kevin Richter
Target Check
Pass Bioenvironmental Engineering Flight (BEF) air test.

## Slide 26
Design Operation
Open blasting cabinet and slide build plate in upside down.
Align threaded holes on build plate with holes shown and fasten.
Kevin Richter

## Slide 27
Design Operation
Align threaded holes on build plate with holes shown and fasten.
Open blasting cabinet and slide build plate in upside down.
Noting that the build plate is fully lifted and secured, close the blasting cabinet.
Kevin Richter

## Slide 28
Design Operation
Noting that the build plate is fully lifted and secured, close the blasting cabinet.
Align threaded holes on build plate with holes shown and fasten.
Raise the tool air pressure until the in-line gauge reads the desired pressure.

## Slide 29
Design Operation
Raise the tool air pressure until the in-line gauge reads the desired pressure.
Noting that the build plate is fully lifted and secured, close the blasting cabinet.
Kevin Richter

## Slide 30
Validation Plan
75 μm Mesh
Scaled 4x
Flour: 25-400 μm
Kevin Richter

## Slide 31
Validation Test and Results
Arlan Ohrt
The Three Polymer Test Prints

## Slide 32
Validation
The Three Polymer Test Prints
Add Flour to Test Print
Arlan Ohrt

## Slide 33
Validation
The Three Polymer Test Prints
Add Flour to Test Print
Remove Bulk Powder
Arlan Ohrt

## Slide 34
Validation
Add Flour to Test Print
Remove Bulk Powder
Adhere to Plate
Mount to Design
Run for 5 Minutes
Arlan Ohrt

## Slide 35
Validation
Remove Bulk Powder
Adhere to Plate
Mount to Design
Run for 5 Minutes
Unofficial Run 4
Ran large cube for 5 minutes, then pounded and blew air. Better results
Arlan Ohrt

## Slide 36
Validation Results
Adhere to Plate
Mount to Design
Run for 5 Minutes
Unofficial Run 4
Ran large cube for 5 minutes, then pounded and blew air on it.
Arlan Ohrt
Target Check
Greater than 0 grams of separated powder in container
Target Check
Passes through 75 μm mesh

## Slide 37
Validation Results
Arlan Ohrt
Target Check
Greater than 0 grams of separated powder in container
Target Check
Passes through 75 μm mesh

## Slide 38
Project Conclusion
Joshua Dorfman
Hold the part in the area
Isolate the powder from user
Prevents powder contamination
Build volume: 250 x 250 x 300 mm
Over-estimated weight: 356 N
Passes through 75 μm mesh
Pass Bioenvironmental Engineering Flight (BEF) air test
Function
Target
Separate powder from the part
Transports powder to a container
Greater than 0 grams of separated powder in container

## Slide 39
Project Results
Hold the part in the area
Isolate the powder from user
Prevents powder contamination
Build volume: 250 x 250 x 300 mm
Over-estimated weight: 356 N
Passes through 75 μm mesh
Pass Bioenvironmental Engineering Flight (BEF) air test
Function
Target
Separate powder from the part
Transports powder to a container
Greater than 0 grams of separated powder in container
Joshua Dorfman

## Slide 40
Budget
Enclosure
$8,000
$4,000
$2,000
$6,000
Design
$2,000
$1,000
$500
$1,500
Joshua Dorfman

## Slide 41
Design
Enclosure
$8,000
$4,000
$2,000
$6,000
Budget
$3,500
$2,000
$1,000
$500
$1,500
$1,100
Joshua Dorfman

## Slide 42
Design Budget
Structure
Build Plate Holder
Pneumatics
Suspension
$2,000
$1,000
$500
$1,500
$220
$243
$292
$345
$1,100
Joshua Dorfman

## Slide 43
Lessons Learned
Joshua Dorfman
Lesson 1
Supplier CAD and drawings may not be accurate.
7/16”
Actual Height
Lesson 2
Machining mistakes can happen, and it helps to communicate efficiently.
Holes machined in incorrect spot, slotted to correct.

## Slide 44
Lessons Learned
Joshua Dorfman
Lesson 2
Machining mistakes can happen, and it helps to communicate efficiently.
Holes machined in incorrect spot, slotted to correct.
Lesson 1
Supplier CAD and drawings may not be accurate.
7/16”
Actual Height
Lesson 3
Time management, frequent communication, and clear roles benefited us greatly.

## Slide 45
Lessons Learned
Joshua Dorfman
Lesson 3
Time management, frequent communication, and clear roles benefited us greatly.
Lesson 2
Machining mistakes can happen, and it helps to communicate efficiently.
Holes machined in incorrect spot, slotted to correct.
Idea
Add a linear actuator to the frame that “beats” the plate like a drum to remove more.
Idea
Add automated compressed air to blow on the plate to remove more.

## Slide 46
Future Concepts
Idea
Add a linear actuator to the frame that “beats” the plate like a drum to remove more.
Joshua Dorfman
Idea
Add automated compressed air to blow on the plate to remove more.
Lesson 3
Time management, frequent communication, and clear roles benefited us greatly.

## Slide 47
Title Slide Background - https://www.materialise.com/en/blog/when-how-and-where-of-metal-3d-printing
Recycle - https://www.recycling.com/wp-content/uploads/recycling%20symbols/black/Black%20Recycling%20Symbol%20%28U%2b267B%29.png
3D Systems – https://www.3dsystems.com/3d-printers/prox-dmp-300/specifications
LPBF Demo GIF - https://thescopepopculturescience.blogspot.com/2015_01_01_archive.html
Stainless Steel Properties - https://www.3dsystems.com/materials/metal
nTopology – https://ntopology.com/
PAPR – https://images-na.ssl-images-amazon.com/images/I/4125zPcBPNL.jpg
Sandblaster - https://badboyblasters.com/product/abrasive-media-sand-blaster-bb1050led-bvr-pr-hv-fl-2/
AFRL Sign - https://news.wfsu.org/post/eglin-air-force-base-ready-adjust-hiring-freeze
Electric Vibrator - https://www.mcmaster.com/5808k61
Dampeners - https://www.mcmaster.com/29895t54 , https://www.mcmaster.com/9241k44
Flour - https://sugarandsparrow.com/homemade-cake-flour-recipe/
Wind - https://icon-icons.com/icon/wind/64274
References

## Slide 48
Team 501: Powder Recovery for Metal Additive Manufacturing
Arlan Ohrt
Kevin Richter
Vincent Giannetti
Noah Tipton
Joshua Dorfman
April 16th, 2020

## Slide 49
Return
Backup Slides
Functional Decomposition
Group Member Contact
nTopology
17- 4PH Material
3D Systems Printer Specs
Validation
Work Breakdown

## Slide 50
Return

## Slide 51
Return

## Slide 52
Group Contact
Return
Arlan Ohrt
ago16b@my.fsu.edu
Kevin Richter
kr15@my.fsu.edu
Noah Tipton
nrt15@my.fsu.edu
Vincent Giannetti
vjg15b@my.fsu.edu
Joshua Dorfman
jd16s@my.fsu.edu

## Slide 53
Group Work Breakdown
Return
Secondary leadership and management
Hands on work
Document refinement
Team leadership and management
Validation runs
Presentations
Validation planning
Hands on work
Always working
Design specific work
Design analysis
CAD
Fiscal documentation and planning
Enclosure analysis and selection
Closing documentation
Team 501
Assignments led
Ideation, concept selection, functional decomp….
Grammar and content checks

## Slide 54
Functional Decomposition
Return
1) Volume
2) Force
Up to Eglin AFB safety standards
Particle Size
1) 250 x 250 x 300 mm
2) 356 N
Passes through 75 μm mesh
Pass Bioenvironmental Engineering Flight (BEF) air test
Metric
Target
Mass
Mass
Greater than 0 grams of separated powder in container
Recover Powder
Manage Powder
Support the Part
Inhibit Powder
Separates powder from the part
Transports powder
to a container
Isolate the powder
from user
Hold the part
in the area
Prevents powder contamination

## Slide 55
17- 4PH Stainless Steel
Return
https://www.3dsystems.com/sites/default/files/2017-06/3D-Systems_17-4_PH_%28B%29_DMP_DATASHEET_US_A4_2017.06.21_WEB.pdf
The strength and hardness of some materials can be increased by the formation of very small particles
This is done through heat treatments
It is called “Precipitation Hardening” because the process results in very small particles, called “Precipitates”
This works because precipitates help block dislocation motion, which is an important aspect of a materials failure and properties
http://www.engineeringenotes.com/metallurgy/age-hardening-treatment/age-hardening-treatment-of-metals-metallurgy/26376

## Slide 56
Validation
Return
Sources for Inconsistencies
Powder and test print size
Underpowered compressor used
Polymer test print surface properties
Flour’s properties other than size
Performed in a backyard with a carboard barrier
 |  | Measured Masses (grams) |  |  |  |  |  |  |  |  | 
 |  | Build Plate | Polymer Test Print | Polymer Test Print + Bulk Powder | Polymer Test Print + Powder Film | Adhesive Used | Polymer Test Print + Powder Film + Adhesive + Build Plate (Before Run) | Powder Catching Platform (Before Run) | Powder Catching Platform + Removed Powder | Polymer Test Print + Powder Film + Adhesive + Build Plate (After Run) | Polymer Test Print + Remaining Powder + Dried Abrasive Residue
 |  | M1 | M2 | M3 | M4 | M5 | M6 | M7 | M8 | M9 | M10
Test Runs | Square Polymer Test Print | 11,340.0 | 611.6 | 1,430.6 | 936.9 | 4.0 | 12,247.0 | 151.5 | 263.1 | 12,247.0 | 752.4
 | Large Cylinder Test Print | x | 402.1 | 815.9 | 440.1 | 5.1 | x | 153.9 | 170.4 | x | 416.1
 | Small Cylinder Test Print | x | 201.4 | 322.0 | 206.9 | 3.9 | x | 152.1 | 153.9 | x | 208.3

## Slide 57
Arlan Ohrt

## Slide 58: Standard Shapes
Summary Box
Text box 1
Outlined Text Box

## Slide 59: Approved Logos

## Slide 60: Color Palette

## Slide 61: APA Tables
Category 1 | Category 2 | Category 3 | Category 4 | Category 5
Item 1 |  |  |  | 
Item 2 |  |  |  | 
Item 3 |  |  |  | 
Item 4 |  |  |  | 
 | Category 2 |  |  | Category 3 | 
Category 1 | subcategory 1 | subcategory 2 |  | subcategory 1 | subcategory 2
Item 1 |  |  |  |  | 
Item 2 |  |  |  |  | 
Item 3 |  |  |  |  | 
Item 4 |  |  |  |  |