## Slide 1: ESD- Vision Impaired Technology
Team 522

## Slide 2: Team Introductions
David Alicea
Field/Test Engineer and Quality Control
Nicolas Garcia
Webmaster, Design Engineer and Resource Manager
Madison Jaffe​
Project Manager and Manufacturing/Controls Engineer
Ethan Saffer
Systems/Design
Engineer
David Alicea

## Slide 3: Advisors
Shayne McConomy
FAMU-FSU College of Engineering
Department of Mechanical Engineering
Michael Devine
Florida State University
Jim Moran College of Entrepreneurship
Jerris Hooker
FAMU-FSU College of Engineering
Department of Electrical Engineering
David Alicea

## Slide 4: Synopsis: Senior Design 1
Key Goals:
  Aids the visually impaired in daily activities.
  Assist people who are visually impaired to become more active.
  Keep the visually impaired safe while executing relatively complex tasks.
Assumptions:
  Users are unaware of objects in new surroundings.
  Users have undergone Orientation and Mobility training/rehabilitation.
  The visually impaired are not fully comfortable in our current society.
David Alicea

## Slide 5: Synopsis: Senior Design 1
David Alicea
Markets:
  Primary market: People with severe visual impairment, rehabilitation and treatment centers.
  Secondary market: Autonomous Systems and State-Local Departments of
  Transportation.

## Slide 6
White Cane
Sunu Band
OrCam MyEye 2
https://athome.medline.com/en/medline-white-cane-for-blind-vision-impaired-1ct-mdswhtcane
https://www.sunu.com/es/index
https://www.orcam.com/en/orcam-faq/
David Alicea
Synopsis: Senior Design 1

## Slide 7: Synopsis: Senior Design 1
David Alicea
1. Helps Avoid Ground Irregularities
2. Allows for Location Awareness
3. Recognizes Surrounding Objects
4. Notify Emergency Contacts
5. Intuitive with O & M Training
6. Identifies and Reads Text
7. Priced for Low-Income Households
Interpreted Customer Needs:

## Slide 8: Critical Functions
Alert of Elevation
Determine Location
Alert of Physical Object
Identify Possible Threats
Interpret Sensory Information
David Alicea

## Slide 9: Concept Generation & Selection
Over 100 ideas were generated through multiple concept generation techniques.
Medium and high-fidelity concepts were chosen to meet our critical function targets.
A House of Quality chart, Pugh Charts, and the Analytical Hierarchy Process were the selection methods used to select a design.
David Alicea

## Slide 10: Final Selection
Our final potential designs were ranked:
  Haptic Smart Cane
  Sensor Pin Chip
  Sensor Watch
#2
Sensor Pin Chip
#1
Haptic Smart Cane
#3
Sensor Watch
David Alicea

## Slide 11
Functions
Madison Jaffe

## Slide 12
The ultrasonic sensor will sense an object up to 3 meters away.
Sense
Functions
Madison Jaffe

## Slide 13
The Raspberry Pi will interpret the sensed information to calculate the proximity to an object.
The ultrasonic sensor will sense an object up to 3 meters away.
Sense
Determine
Functions
Madison Jaffe

## Slide 14
The Raspberry Pi will interpret the sensed information to calculate the proximity to an object.
The ultrasonic sensor will sense an object up to 3 meters away.
Haptic feedback will alert the user with multiple motors with intensity based on distance.
Sense
Determine
Alert
Functions
Madison Jaffe

## Slide 15
The Raspberry Pi will interpret the sensed information to calculate the proximity to an object.
The camera can be activated to scan the desired products.
The ultrasonic sensor will sense an object up to 3 meters away.
Haptic feedback will alert the user with multiple motors with intensity based on distance.
Sense
Determine
Alert
Scan
Functions
Madison Jaffe

## Slide 16
The Raspberry Pi will interpret the sensed information to calculate the proximity to an object.
The camera can be activated to scan the desired products.
The ultrasonic sensor will sense an object up to 3 meters away.
Up to 500 stored products will be in the memory of the Raspberry Pi to identify the product.
Haptic feedback will alert the user with multiple motors with intensity based on distance.
Sense
Determine
Alert
Scan
Identify
Functions
Madison Jaffe

## Slide 17
The Raspberry Pi will interpret the sensed information to calculate the proximity to an object.
The camera can be activated to scan the desired products.
The ultrasonic sensor will sense an object up to 3 meters away.
Up to 500 stored products will be in the memory of the Raspberry Pi to identify the product.
Haptic feedback will alert the user with multiple motors with intensity based on distance.
Haptic feedback will
notify the user when the product has been identified and a speaker will relay the product name.
Sense
Determine
Alert
Scan
Identify
Notify
Functions
Madison Jaffe

## Slide 18: Our Product - HapTac
Scan
The camera can be activated to scan the desired products.
Sense
The ultrasonic sensor will sense an object up to 3 meters away.
Determine
The Raspberry Pi will interpret the sensed information to calculate the proximity to an object.
Notify
Alert
Haptic feedback will alert the user with multiple motors with intensity based on distance.
Identify
Scan
The camera can be activated to scan the desired products.
Sense
The ultrasonic sensor will sense an object up to 3 meters away.
Determine
The Raspberry Pi will interpret the sensed information to calculate the proximity to an object.
Notify
Alert
Haptic feedback will alert the user with multiple motors with intensity based on distance.
Identify
Sense
Sense
Our product attaches to the standard white cane.
Device is perpendicular to retain standard use while also aiming towards components correctly.
Madison Jaffe

## Slide 19: Our Product - HapTac
Scan
The camera can be activated to scan the desired products.
Sense
The ultrasonic sensor will sense an object up to 3 meters away.
Determine
The Raspberry Pi will interpret the sensed information to calculate the proximity to an object.
Notify
Alert
Haptic feedback will alert the user with multiple motors with intensity based on distance.
Identify
Scan
The camera can be activated to scan the desired products.
Sense
The ultrasonic sensor will sense an object up to 3 meters away.
Determine
The Raspberry Pi will interpret the sensed information to calculate the proximity to an object.
Notify
Alert
Haptic feedback will alert the user with multiple motors with intensity based on distance.
Identify
Sense
Sense
Madison Jaffe

## Slide 20: Our Product - HapTac
Housing
Battery Pack
GrovePi+
Raspberry Pi 4
Vibration Motors (3)
Camera
Ultrasonic Sensor
Madison Jaffe

## Slide 21: Device Operational Time
Ultrasonic Sensor
8 mA
Camera
Up to 800 mA
Vibration Motor
58 mA average
100 mA max
Raspberry Pi
3,000 mA
Power Supply
20,000 mAh
Theoretical (Maximum Current Draw) Operation Time: 4.87 Hours
4 hours, 52 minutes and 12 seconds
Madison Jaffe

## Slide 22: Prototype Preparation
Ordering the parts listed in the Bill of Materials
Manufacturing our minimum viable prototype
  Iterating 3D printed housing for the product.
  Overall coding of system.
    Integrating AlexNet
Testing and Validation
  Validate battery usage/ battery life.
  Verify accuracy of various sensors and motors.
Madison Jaffe

## Slide 23: InNOLEvation Challenge
We are one of fifteen projects to advance to the semi-final round of the competition.
Moving forward, we will develop a business pitch and finalize our business model canvas.
Madison Jaffe

## Slide 24: Reference
Madison Jaffe
[1] McConomy, S. (2020, November 11). Engineering Characteristics, Functions, Targets, and Metric. FAMU-FSU College of Engineering.
[2] Queen, K. (2016, June). 7 Ways to Make Communities More Livable for People With Vision or Hearing Impairments. AARP.

## Slide 25
Madison Jaffe
David Alicea
Field/Test Engineer and Quality Control
Daa16@my.fsu.edu
Nicolas Garcia
Webmaster, Design Engineer and Resource Manager
Ng16m@my.fsu.edu
Ethan Saffer
Systems and Design
Engineer
Ers16c@my.fsu.edu
Team 522: Vision Impaired Technology
Madison Jaffe​
Project Manager and Manufacturing/Controls Engineer
Msj16d@my.fsu.edu

## Slide 28
APPENDIX

## Slide 29
8 + 800 + 300 + 3000 = 4108 mA
mAh is mA * (hours operating) = mAh
20000mAh / 5016mA = 4.86855 hours
https://elinux.org/Rpi_Camera_Module
https://static6.arrow.com/aropdfconversion/7ce3c19d47af65a2e4096b327057dad3e30632e1/pgurl_grove-vibration-motor-p-839l.pdf
Sensor 8 mA
Pi: 3A (based on power source)
Camera: up to 800mA
Motor: 58 mA standard, 100 mA at max
Power Supply= 20000 mAh
Therefore: 4.87 Hours of operation at max use

## Slide 30
Function ​ | Target ​ | Metric ​
Alert of Elevation* ​ | 0.25 to 12 inches ​ | Distance ​
Determine Location* ​ | Margin of error of at most 16 feet ​ | Distance ​
Alert of Physical Object* ​ | 65 inches ​ | Distance ​
Identify Possible Threats* ​ | Up to 60 miles per hour ​ | Velocity ​
Access Emergency Contact ​ | 15 seconds ​ | Time ​
Interpret Sensory Information* ​ | 7 seconds ​ | Time ​
Store Frequent Tasks ​ | 1 GB ​ | Memory Allocation ​
Interface with Pre-Existing Skills ​ | 70% ​ | User Satisfaction ​
Compete within Market ​ | 20% ​ | Price Range USD ($) ​
Remain Lightweight ​ | <5 lb ​ | Weight ​
Remain Discrete ​ | 70% ​ | User Approval ​

## Slide 31: Synopsis: Semester 1
Markets:
  Primary market: People with severe visual impairment, rehabilitation and treatment centers.
  Secondary market: Autonomous Systems and State-Local Departments of Transportation.
David Alicea

## Slide 32: Synopsis: Semester 1
David Alicea
1. Helps Avoid Ground Irregularities
2. Allows for Location Awareness
3. Recognizes Surrounding Objects
4. Notify Emergency Contacts
5. Intuitive with O & M Training
6. Identifies and Reads Text
7. Priced for Low-Income Households
Markets:
  Primary market: People with severe visual impairment, rehabilitation and treatment centers.
  Secondary market: Autonomous Systems and State-Local Departments of Transportation.
Interpreted Customer Needs:

## Slide 33: Functional Decomposition
David Alicea

## Slide 34: Targets and Metrics
Function | Target | Metric
Alert of Elevation* | 0.25 to 12 inches | Distance
Determine Location* | ~ 16 feet | Distance
Alert of Physical Object* | 65 inches | Distance
Identify Possible Threats* | Up to 60 miles per hour | Velocity
Access Emergency Contact | 15 seconds | Time
Interpret Sensory Information* | 7 seconds | Time
Store Frequent Tasks | 1 GB | Memory Allocation
Interface with Pre-Existing Skills | 70% | User Satisfaction
Compete within Market | 20% | Price Range USD ($)
Remain Lightweight | < 5.1 lb | Weight
Remain Discrete | 70% | User Approval
David Alicea

## Slide 35: Concept Generation Tools
Biomimicry
Crap Shoot
Morphological Chart
David Alicea
McConomy, S. (2020, November 11). Engineering Characteristics, Functions, Targets, and Metric. FAMU-FSU College of Engineering.

## Slide 36: Morphological Chart
Alert of Elevation | Determine Location | Alert of Physical Object | Inform of Possible Threats | Interpret Sensory Information
Sensor | GPS Through Wi-Fi/Internet Signal | Distance Sensor | Heat | Camera
Cane/Stick | GPS w/ Maps Downloaded | Velocity Sensor | Vibrate | Text Conversion
 | Camera to Read Street Signs and Other Landmarks | Lidar | Noise | Live Imaging Scanned to a PDF Document
 | Memory Storage of Previous Paths |  | Poke | Text to Braille
David Alicea

## Slide 37: Medium Fidelity Concepts
David Alicea
GPS Watch:
- GPS indicate where the user is
- haptic feedback provided through vibration on wrist
Haptic Feedback cane:
- haptic feedback voice-activated
- phone compatible
Smart Glasses:
- sensor and GPS for user location
- Audio feedback through glass-mounted earpiece
Audio Feedback cane:
- audio feedback
- Tactile or voice activation
- Phone compatible
- camera to interpret the environment
GPS app:
- Lidar
- user information through haptics
- computer and GPS track and locate user

## Slide 38: Concept Selection
David Alicea

## Slide 39: Importance Weight Factor
Helps Avoid Ground Irregularities
Recognizes Surrounding Objects
Intuitive with O&M Training
Notify Emergency Contact
Priced for Low-Income Households
Identifies and Reads Text
Allows for Location Detection
Interpreted Customer Needs
Importance Weight Factor
Nicolas Garcia

## Slide 40: House of Quality
Nicolas Garcia

## Slide 41
Interpret Sensory Information
Alert of Elevation
Alert of Physical Objects
Determine Location
Interface with Pre-Existing Skills
Store Frequent Tasks
Inform User of Potential Threats
Access Emergency Contacts
Nicolas Garcia
House of Quality

## Slide 42: Pugh Chart
Nicolas Garcia

## Slide 43: Pugh Chart
Nicolas Garcia

## Slide 44: Second Pugh Chart
Nicolas Garcia

## Slide 45: Second Pugh Chart
Nicolas Garcia

## Slide 46: Analytical Hierarchy Process
Nicolas Garcia
Criteria Comparison Matrix [C] | 
Functions | Criteria Weights{W}
Alert of Elevation | 0.11
Determine Location | 0.13
Interpret Sensory Information | 0.24
Access Emergency Contact | 0.03
Interface With Pre-Existing Skills | 0.11
Store Frequent Tasks | 0.04
Alert of Physical Object | 0.19
Inform User of Possible Threats | 0.15
Sum | 1.00

## Slide 47: Analytical Hierarchy Process
Nicolas Garcia
 | Sensor Pin Chip | Sensor Watch | Haptic Smart Cane
Alert of Elevation | 0.11 | 0.11 | 0.78
Determine Location | 0.16 | 0.19 | 0.66
Interpret Sensory Information | 0.45 | 0.45 | 0.09
Access Emergency Contact | 0.20 | 0.20 | 0.60
Interface with Pre-existing Skills | 0.14 | 0.14 | 0.71
Store Frequent Tasks | 0.33 | 0.33 | 0.33
Alert of a Physical Object | 0.43 | 0.14 | 0.43
Inform User of Possible Threats | 0.33 | 0.33 | 0.33

## Slide 48: Analytical Hierarchy Process
Nicolas Garcia
 | Sensor Pin Chip | Sensor Watch | Haptic Smart Cane
Alert of Elevation | 0.11 | 0.11 | 0.78
Determine Location | 0.16 | 0.19 | 0.66
Interpret Sensory Information | 0.45 | 0.45 | 0.09
Access Emergency Contact | 0.20 | 0.20 | 0.60
Interface with Pre-existing Skills | 0.14 | 0.14 | 0.71
Store Frequent Tasks | 0.33 | 0.33 | 0.33
Alert of a Physical Object | 0.43 | 0.14 | 0.43
Inform User of Possible Threats | 0.33 | 0.33 | 0.33

## Slide 49: Analytical Hierarchy Process
Nicolas Garcia
 | Sensor Pin Chip | Sensor Watch | Haptic Smart Cane
Alert of Elevation | 0.11 | 0.11 | 0.78
Determine Location | 0.16 | 0.19 | 0.66
Interpret Sensory Information | 0.45 | 0.45 | 0.09
Access Emergency Contact | 0.20 | 0.20 | 0.60
Interface with Pre-existing Skills | 0.14 | 0.14 | 0.71
Store Frequent Tasks | 0.33 | 0.33 | 0.33
Alert of a Physical Object | 0.43 | 0.14 | 0.43
Inform User of Possible Threats | 0.33 | 0.33 | 0.33

## Slide 50
Binary Comparison Chart |  |  |  |  |  |  |  | 
Interprted Customer Needs | 1 | 2 | 3 | 4 | 5 | 6 | 7 | Total 1
1. Helps Avoid Ground Irregularities | - | 1 | 0 | 0 | 0 | 0 | 1 | 2
2. Allows for Location Awareness | 0 | - | 0 | 1 | 0 | 1 | 0 | 2
3. Recognizes Surrounding Objects | 1 | 1 | - | 1 | 1 | 1 | 1 | 6
4. Notify Emergency Contacts | 1 | 0 | 0 | - | 1 | 0 | 1 | 3
5. Intuitive with O & M Training | 1 | 1 | 0 | 0 | - | 1 | 1 | 4
6. Identifies and Reads Text | 1 | 0 | 0 | 1 | 0 | - | 0 | 2
7. Priced for low-income households | 0 | 1 | 0 | 1 | 0 | 1 | - | 3
Total: | 4 | 4 | 0 | 4 | 2 | 4 | 4 | 6

## Slide 51: Functional Decomposition
 | Orientation | Mobility | Utility
Alert of Elevation | X | X | 
Determine Location | X | X | 
Alert of Physical Object | X | X | 
Inform User of Possible Threats |  | X | X
Access to Emergency Contact |  |  | X
Interpret Sensory information |  |  | X
Store Frequent Tasks | X |  | X
Interface With Pre-Existing Skills |  |  | X
David Alicea

## Slide 52
Engineering |  | Concepts |  |  |  |  |  |  | 
Characteristics | Oram MyEye2 | Sensor Pin Chip | Pin Matrix Haptics | Sensor Watch | GPS App | GPS Watch | Haptic Smart Cane | Smart Glasses | Audio Feedback Cane
Alert of Elevation | Datum | + | + | + | - | - | + | S | +
Determine Location |  | S | S | + | + | + | + | + | +
Interpret Sensory Information |  | - | - | - | - | + | S | - | S
Access Emergency Contact |  | S | S | S | + | - | + | - | +
Interface With Pre-Existing Skills |  | S | + | + | S | S | + | S | S
Store Frequent Tasks |  | + | S | S | S | - | S | - | +
Alert of Physical Object |  | + | + | + | - | + | - | + | -
Inform User of Possible Threats |  | + | + | + | + | + | - | + | +
# of Pluses |  | 4 | 4 | 5 | 3 | 4 | 4 | 3 | 5
# of Minuses |  | 2 | 1 | 1 | 3 | 3 | 2 | 3 | 1

## Slide 53
Engineering |  | Concepts |  |  |  |  | 
Characteristics | GPS Watch | Sensor Pin Chip | Sensor Watch | GPS App | Haptic Smart Cane | Smart Glasses | Audio Feedback Cane
Alert of Elevation | Datum | + | + | S | + | S | +
Determine Location |  | - | - | S | - | S | -
Interpret Sensory Information |  | + | + | S | + | + | +
Access Emergency Contact |  | S | S | + | S | S | -
Interface With Pre-Existing Skills |  | S | + | + | + | S | +
Store Frequent Tasks |  | + | S | S | S | S | S
Alert of Physical Object |  | + | + | - | + | + | +
Inform User of Possible Threats |  | + | + | - | + | + | +
# of Pluses |  | 5 | 5 | 2 | 5 | 3 | 5
# of Minuses |  | 1 | 1 | 2 | 1 | 0 | 2

## Slide 54
Engineering Concepts |  |  |  |  |  |  |  |  | 
Units |  | Inches | Latitude/Longitude | Seconds | Seconds | Minutes | GB | Seconds | Seconds
Customer Requirements | Importance Weight Factor | Alert of Elevation | Determine Location | Interpret Sensory Information | Access Emergency Contact | Interface With Pre-Existing Skills | Store Frequent Tasks | Alert of Physical Object | Inform User of Possible Threats
1. Helps Avoid Ground Irregularities | 2 | 9 | 5 | 9 | - | 7 | 1 | 7 | 9
2. Allows for Location Awareness | 2 | 9 | 9 | 9 | - | 1 | 1 | 7 | 3
3. Recognizes Surrounding Objects | 6 | 7 | 7 | 9 | - | 3 | 5 | 9 | 3
4. Notify Emergency Contacts | 3 | 1 | 5 | - | 9 | 1 | 3 | 1 | 1
5. Intuitive with O & M Training | 4 | 5 | 5 | 5 | 3 | 9 | 3 | 3 | 1
6. Identifies and Reads Text | 2 | - | - | 5 | 1 | - | 5 | - | -
7. Priced for low-income households | 3 | - | - | - | - | - | - | - | -
Raw Score (629) | N/A | 101 | 85 | 122 | 41 | 73 | 65 | 97 | 43
Relative Weight % |  | 16.1 | 13.5 | 19.4 | 6.5 | 11.6 | 10.3 | 15.4 | 6.8
Rank Order |  | 2 | 4 | 1 | 8 | 5 | 6 | 3 | 7

## Slide 55
Development of Candidate Set of Criteria Weights {W} |  |  |  |  |  |  |  | 
Criteria Comparison Matrix [C] |  |  |  |  |  |  |  | 
 | Alert of Elevation | Determine Location | Interpret Sensory Information | Access Emergency Contact | Interface With Pre-Existing Skills | Store Frequent tasks | Alert of Physical Objects | Inform User of Possible Threats
Alert of Elevation | 1.00 | 1.00 | 0.33 | 5.00 | 1.00 | 3.00 | 0.33 | 1.00
Determine Location | 1.00 | 1.00 | 0.33 | 5.00 | 1.00 | 3.00 | 1.00 | 1.00
Interpret Sensory Information | 3.00 | 3.00 | 1.00 | 5.00 | 3.00 | 5.00 | 1.00 | 1.00
Access Emergency Contact | 0.20 | 0.20 | 0.20 | 1.00 | 0.20 | 1.00 | 0.33 | 0.20
Interface With Pre-Existing Skills | 1.00 | 1.00 | 0.33 | 5.00 | 1.00 | 3.00 | 0.33 | 1.00
Store Frequent Tasks | 0.33 | 0.33 | 0.20 | 1.00 | 0.33 | 1.00 | 0.33 | 0.33
Alert of Physical Object | 3.00 | 1.00 | 1.00 | 3.00 | 3.00 | 3.00 | 1.00 | 1.00
Inform User of Possible Threats | 1.00 | 1.00 | 1.00 | 5.00 | 1.00 | 3.00 | 1.00 | 1.00
Sum | 10.53 | 8.53 | 4.40 | 30.00 | 10.53 | 22.00 | 5.33 | 6.53

## Slide 56
Development of Candidate Set of Criteria Weights {W} |  |  |  |  |  |  |  |  | 
Criteria Comparison Matrix [C] |  |  |  |  |  |  |  |  | 
 | Alert of Elevation | Determine Location | Interpret Sensory Information | Acccess Emergency Contact | Interface With Pre-Existing Skills | Store Fequent tasks | Alert of Physical Objects | Inform User of Possible Threats | Criteria Weights{W}
Alert of Elevation | 0.09 | 0.12 | 0.08 | 0.17 | 0.09 | 0.14 | 0.06 | 0.15 | 0.11
Determine Location | 0.09 | 0.12 | 0.08 | 0.17 | 0.09 | 0.14 | 0.19 | 0.15 | 0.13
Interpret Sensory Information | 0.28 | 0.35 | 0.23 | 0.17 | 0.28 | 0.23 | 0.19 | 0.15 | 0.24
Access Emergency Contact | 0.02 | 0.02 | 0.05 | 0.03 | 0.02 | 0.05 | 0.06 | 0.03 | 0.03
Interface With Pre-Existing Skills | 0.09 | 0.12 | 0.08 | 0.17 | 0.09 | 0.14 | 0.06 | 0.15 | 0.11
Store Frequent Tasks | 0.03 | 0.04 | 0.05 | 0.03 | 0.03 | 0.05 | 0.06 | 0.05 | 0.04
Alert of Physical Object | 0.28 | 0.12 | 0.23 | 0.10 | 0.28 | 0.14 | 0.19 | 0.15 | 0.19
Inform User of Possible Threats | 0.09 | 0.12 | 0.23 | 0.17 | 0.09 | 0.14 | 0.19 | 0.15 | 0.15
Sum | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00

## Slide 57
# of criteria | RI value | Average Consistency | Consistency Index | Consistency Ratio
8.00 | 1.40 | 8.39 | 0.06 | 0.04
Weighted Sum Vector | Criteria Weights{W} | Consistency vector
0.94 | 0.11 | 8.37
1.07 | 0.13 | 8.32
2.02 | 0.24 | 8.57
0.29 | 0.03 | 8.23
0.94 | 0.11 | 8.37
0.35 | 0.04 | 8.32
1.61 | 0.19 | 8.61
1.22 | 0.15 | 8.32

## Slide 58
Development of Candidate Set of Criteria Weights {W} ALERT OF ELEVATION | Alert of Elevation |  | 
Criteria Comparison Matrix [C] |  |  | 
 | Sensor Pin Chip | Sensor Watch | Haptic Smart Cane
Sensor Pin Chip | 1.00 | 1.00 | 0.14
Sensor Watch | 1.00 | 1.00 | 0.14
Haptic Smart Cane | 7.00 | 7.00 | 1.00
Sum | 9.00 | 9.00 | 1.29

## Slide 59: Analytical Hierarchy Process
Nicolas Garcia
Criteria Comparison Matrix [C] |  |  |  |  |  |  |  | 
 | Alert of Elevation | Determine Location | Interpret Sensory Information | Access Emergency Information | Interface with pre-existing skills | Store Frequent Tasks | Alert of Physical Objects | Inform User of Possible Threats
Alert of Elevation | 1.00 | 1.00 | 0.33 | 5.00 | 1.00 | 3.00 | 0.33 | 1.00
Determine Location | 1.00 | 1.00 | 0.33 | 5.00 | 1.00 | 3.00 | 1.00 | 1.00
Interpret Sensory Information | 3.00 | 3.00 | 1.00 | 5.00 | 3.00 | 5.00 | 1.00 | 1.00
Access Emergency Information | 0.20 | 0.20 | 0.20 | 1.00 | 0.20 | 1.00 | 0.33 | 0.20
Interface with Pre-existing Skills | 1.00 | 1.00 | 0.33 | 5.00 | 1.00 | 3.00 | 0.33 | 1.00
Store Frequent Tasks | 0.33 | 0.33 | 0.20 | 1.00 | 0.33 | 1.00 | 0.33 | 0.33
Alert of Physical Objects | 3.00 | 1.00 | 1.00 | 3.00 | 3.00 | 3.00 | 1.00 | 1.00
Inform User of Possible Threats | 1.00 | 1.00 | 1.00 | 5.00 | 1.00 | 3.00 | 1.00 | 1.00
Sum | 10.53 | 8.53 | 4.40 | 30.00 | 10.53 | 22.00 | 5.33 | 6.53

## Slide 60
Development of Candidate Set of Criteria Weights {W} |  |  |  | 
Criteria Comparison Matrix [C] |  |  |  | 
 | Sensor Pin Chip | Sensor Watch | Haptic Smart Cane | Design Alternative Priorities {Pi}
Sensor Pin Chip | 0.11 | 0.11 | 0.11 | 0.11
Sensor Watch | 0.11 | 0.11 | 0.11 | 0.11
Haptic Smart Cane | 0.78 | 0.78 | 0.78 | 0.78
Sum | 1.00 | 1.00 | 1.00 | 1.00

## Slide 61
Weighted Sum Vector | Design Alternative Priorities | Consistency vector
0.33 | 0.11 | 3.00
0.33 | 0.11 | 3.00
2.33 | 0.78 | 3.00
# of criteria | RI value | Average Consistency | Consistency Index | Consistency Ratio
3.00 | 0.52 | 3.00 | 0.00 | 0.00

## Slide 62
Development of Candidate Set of Criteria Weights {W} | Determine Location |  | 
Criteria Comparison Matrix [C] |  |  | 
 | Sensor Pin Chip | Sensor Watch | Haptic Smart Cane
Sensor Pin Chip | 1.00 | 1.00 | 0.20
Sensor Watch | 1.00 | 1.00 | 0.33
Haptic Smart Cane | 5.00 | 3.00 | 1.00
Sum | 7.00 | 5.00 | 1.53

## Slide 63
Development of Candidate Set of Criteria Weights {W} |  |  |  | 
Criteria Comparison Matrix [C] |  |  |  | 
 | Sensor Pin Chip | Sensor Watch | Haptic Smart Cane | Design Alternative Priorities {Pi}
Sensor Pin Chip | 0.14 | 0.20 | 0.13 | 0.16
Sensor Watch | 0.14 | 0.20 | 0.22 | 0.19
Haptic Smart Cane | 0.71 | 0.60 | 0.65 | 0.66
Sum | 1.00 | 1.00 | 1.00 | 1.00

## Slide 64
# of criteria | RI value | Average Consistency | Consistency Index | Consistency Ratio
3.00 | 0.52 | 3.00 | 0.00 | 0.00
Weighted Sum Vector | Design Alternative Priorities | Consistency vector
0.48 | 0.16 | 3.01
0.56 | 0.19 | 3.01
2.00 | 0.66 | 3.06

## Slide 65
Development of Candidate Set of Criteria Weights {W} | Interpret Sensory Information |  | 
Criteria Comparison Matrix [C] |  |  | 
 | Sensor Pin Chip | Sensor Watch | Haptic Smart Cane
Sensor Pin Chip | 1.00 | 1.00 | 5.00
Sensor Watch | 1.00 | 1.00 | 5.00
Haptic Smart Cane | 0.20 | 0.20 | 1.00
Sum | 2.20 | 2.20 | 11.00

## Slide 66
Development of Candidate Set of Criteria Weights {W} |  |  |  | 
Criteria Comparison Matrix [C] |  |  |  | 
 | Sensor Pin Chip | Sensor Watch | Haptic Smart Cane | Design Alternative Priorities {Pi}
Sensor Pin Chip | 0.45 | 0.45 | 0.45 | 0.45
Sensor Watch | 0.45 | 0.45 | 0.45 | 0.45
Haptic Smart Cane | 0.09 | 0.09 | 0.09 | 0.09
Sum | 1.00 | 1.00 | 1.00 | 1.00

## Slide 67
# of criteria | RI value | Average Consistency | Consistency Index | Consistency Ratio
3.00 | 0.52 | 3.00 | 0.00 | 0.00
Weighted Sum Vector | Design Alternative Priorities | Consistency vector
1.36 | 0.45 | 3.00
1.36 | 0.45 | 3.00
0.27 | 0.09 | 3.00

## Slide 68
Development of Candidate Set of Criteria Weights {W} | Access Emergency Contact |  | 
Criteria Comparison Matrix [C] |  |  | 
 | Sensor Pin Chip | Sensor Watch | Haptic Smart Cane
Sensor Pin Chip | 1.00 | 1.00 | 0.33
Sensor Watch | 1.00 | 1.00 | 0.33
Haptic Smart Cane | 3.00 | 3.00 | 1.00
Sum | 5.00 | 5.00 | 1.67

## Slide 69
Development of Candidate Set of Criteria Weights {W} |  |  |  | 
Criteria Comparison Matrix [C] |  |  |  | 
 | Sensor Pin Chip | Sensor Watch | Haptic Smart Cane | Design Alternative Priorities {Pi}
Sensor Pin Chip | 0.20 | 0.20 | 0.20 | 0.20
Sensor Watch | 0.20 | 0.20 | 0.20 | 0.20
Haptic Smart Cane | 0.60 | 0.60 | 0.60 | 0.60
Sum | 1.00 | 1.00 | 1.00 | 1.00

## Slide 70
# of criteria | RI value | Average Consistency | Consistency Index | Consistency Ratio
3.00 | 0.52 | 3.00 | 0.00 | 0.00
Weighted Sum Vector | Design Alternative Priorities | Consistency vector
0.60 | 0.20 | 3.00
0.60 | 0.20 | 3.00
1.80 | 0.60 | 3.00

## Slide 71
Development of Candidate Set of Criteria Weights {W} | Interface With Pre-Existing Skills |  | 
Criteria Comparison Matrix [C] |  |  | 
 | Sensor Pin Chip | Sensor Watch | Haptic Smart Cane
Sensor Pin Chip | 1.00 | 1.00 | 0.20
Sensor Watch | 1.00 | 1.00 | 0.20
Haptic Smart Cane | 5.00 | 5.00 | 1.00
Sum | 7.00 | 7.00 | 1.40

## Slide 72
Development of Candidate Set of Criteria Weights {W} |  |  |  | 
Criteria Comparison Matrix [C] |  |  |  | 
 | Sensor Pin Chip | Sensor Watch | Haptic Smart Cane | Design Alternative Priorities {Pi}
Sensor Pin Chip | 0.14 | 0.14 | 0.14 | 0.14
Sensor Watch | 0.14 | 0.14 | 0.14 | 0.14
Haptic Smart Cane | 0.71 | 0.71 | 0.71 | 0.71
Sum | 1.00 | 1.00 | 1.00 | 1.00

## Slide 73
Weighted Sum Vector | Design Alternative Priorities | Consistency vector
0.43 | 0.14 | 3.00
0.43 | 0.14 | 3.00
2.14 | 0.71 | 3.00
# of criteria | RI value | Average Consistency | Consistency Index | Consistency Ratio
3.00 | 0.52 | 3.00 | 0.00 | 0.00

## Slide 74
Development of Candidate Set of Criteria Weights {W} | Store Frequent Tasks |  | 
Criteria Comparison Matrix [C] |  |  | 
 | Sensor Pin Chip | Sensor Watch | Haptic Smart Cane
Sensor Pin Chip | 1.00 | 1.00 | 1.00
Sensor Watch | 1.00 | 1.00 | 1.00
Haptic Smart Cane | 1.00 | 1.00 | 1.00
Sum | 3.00 | 3.00 | 3.00

## Slide 75
Development of Candidate Set of Criteria Weights {W} |  |  |  | 
Criteria Comparison Matrix [C] |  |  |  | 
 | Sensor Pin Chip | Sensor Watch | Haptic Smart Cane | Design Alternative Priorities {Pi}
Sensor Pin Chip | 0.33 | 0.33 | 0.33 | 0.33
Sensor Watch | 0.33 | 0.33 | 0.33 | 0.33
Haptic Smart Cane | 0.33 | 0.33 | 0.33 | 0.33
Sum | 1.00 | 1.00 | 1.00 | 1.00

## Slide 76
# of criteria | RI value | Average Consistency | Consistency Index | Consistency Ratio
3.00 | 0.52 | 3.00 | 0.00 | 0.00
Weighted Sum Vector | Design Alternative Priorities | Consistency vector
1.00 | 0.33 | 3.00
1.00 | 0.33 | 3.00
1.00 | 0.33 | 3.00

## Slide 77
Development of Candidate Set of Criteria Weights {W} | Alert of Physical Object |  | 
Criteria Comparison Matrix [C] |  |  | 
 | Sensor Pin Chip | Sensor Watch | Haptic Smart Cane
Sensor Pin Chip | 1.00 | 3.00 | 1.00
Sensor Watch | 0.33 | 1.00 | 0.33
Haptic Smart Cane | 1.00 | 3.00 | 1.00
Sum | 2.33 | 7.00 | 2.33

## Slide 78
Development of Candidate Set of Criteria Weights {W} |  |  |  | 
Criteria Comparison Matrix [C] |  |  |  | 
 | Sensor Pin Chip | Sensor Watch | Haptic Smart Cane | Design Alternative Priorities {Pi}
Sensor Pin Chip | 0.43 | 0.43 | 0.43 | 0.43
Sensor Watch | 0.14 | 0.14 | 0.14 | 0.14
Haptic Smart Cane | 0.43 | 0.43 | 0.43 | 0.43
Sum | 1.00 | 1.00 | 1.00 | 1.00

## Slide 79
# of criteria | RI value | Average Consistency | Consistency Index | Consistency Ratio
3.00 | 0.52 | 3.00 | 0.00 | 0.00
Weighted Sum Vector | Design Alternative Priorities | Consistency vector
1.29 | 0.43 | 3.00
0.43 | 0.14 | 3.00
1.29 | 0.43 | 3.00

## Slide 80
Development of Candidate Set of Criteria Weights {W} | Inform User of Possible Threats |  | 
Criteria Comparison Matrix [C] |  |  | 
 | Sensor Pin Chip | Sensor Watch | Haptic Smart Cane
Sensor Pin Chip | 1.00 | 1.00 | 1.00
Sensor Watch | 1.00 | 1.00 | 1.00
Haptic Smart Cane | 1.00 | 1.00 | 1.00
Sum | 3.00 | 3.00 | 3.00

## Slide 81
Development of Candidate Set of Criteria Weights {W} |  |  |  | 
Criteria Comparison Matrix [C] |  |  |  | 
 | Sensor Pin Chip | Sensor Watch | Haptic Smart Cane | Design Alternative Priorities {Pi}
Sensor Pin Chip | 0.33 | 0.33 | 0.33 | 0.33
Sensor Watch | 0.33 | 0.33 | 0.33 | 0.33
Haptic Smart Cane | 0.33 | 0.33 | 0.33 | 0.33
Sum | 1.00 | 1.00 | 1.00 | 1.00

## Slide 82
Weighted Sum Vector | Design Alternative Priorities | Consistency vector
1.00 | 0.33 | 3.00
1.00 | 0.33 | 3.00
1.00 | 0.33 | 3.00
# of criteria | RI value | Average Consistency | Consistency Index | Consistency Ratio
3.00 | 0.52 | 3.00 | 0.00 | 0.00

## Slide 83
 | Sensor Pin Chip | Sensor Watch | Haptic Smart Cane
Alert of Elevation | 0.11 | 0.11 | 0.78
Determine Location | 0.16 | 0.19 | 0.66
Interpret Sensory Information | 0.45 | 0.45 | 0.09
Access Emergency Contact | 0.20 | 0.20 | 0.60
Interface With Pre-Existing Skills | 0.14 | 0.14 | 0.71
Store Frequent Tasks | 0.33 | 0.33 | 0.33
Alert of Physical Object | 0.43 | 0.14 | 0.43
Inform User of Possible Threats | 0.33 | 0.33 | 0.33
Concept | Alternative Value
Sensor Pin Chip | 0.27
Sensor Watch | 0.24
Haptic Smart Cane | 0.49

## Slide 84: Standard Shapes
Summary Box
Text box 1
Outlined Text Box

## Slide 85: Approved Logos

## Slide 86: Color Palette

## Slide 87
Slides to keep:
Intro, Synopsis of VDR1 (Rename), Customer Needs, minimize Concept Gen. & Selection, Final Selection?, What's Next, Last team member slide, Ref.
Slides to add:
Specs of design
BOM/Ordering parts
Our progress in the InNOLEvation challenge?

## Slide 88: APA Tables
Category 1 | Category 2 | Category 3 | Category 4 | Category 5
Item 1 |  |  |  | 
Item 2 |  |  |  | 
Item 3 |  |  |  | 
Item 4 |  |  |  | 
 | Category 2 |  |  | Category 3 | 
Category 1 | subcategory 1 | subcategory 2 |  | subcategory 1 | subcategory 2
Item 1 |  |  |  |  | 
Item 2 |  |  |  |  | 
Item 3 |  |  |  |  | 
Item 4 |  |  |  |  |