## Slide 1: ESD- Vision Impaired Technology
Team 522

## Slide 2: Team Introductions
David Alicea
Field/Test Engineer and Quality Control
Nicolas Garcia
Webmaster, Design Engineer and Resource Manager
Madison Jaffe​
Project Manager and Manufacturing/Controls Engineer
Ethan Saffer
Systems/Design
Engineer
Ethan Saffer

## Slide 3: Advisors
Shayne McConomy
FAMU-FSU College of Engineering
Department of Mechanical Engineering
Michael Devine
Florida State University
Jim Moran College of Entrepreneurship
Jerris Hooker
FAMU-FSU College of Engineering
Department of Electrical Engineering
Ethan Saffer

## Slide 4: Key Goals and Assumptions
Key Goals:
  Aids the visually impaired in daily activities.
  Assist people who are visually impaired to become more active.
  Keep the visually impaired safe while executing relatively complex tasks.
Assumptions:
  Users are unaware of objects in new surroundings.
  Users have undergone Orientation and Mobility training/rehabilitation.
  The visually impaired are not fully comfortable in our current society.
Ethan Saffer

## Slide 5: Markets
Ethan Saffer
  Primary market: People with severe visual impairment, rehabilitation and treatment centers.
  Secondary market: Autonomous Systems and State-Local Departments of Transportation.

## Slide 6: Interpreted Customer Needs
Ethan Saffer
1. Helps Avoid Ground Irregularities
2. Allows for Location Awareness
3. Recognizes Surrounding Objects
4. Notify Emergency Contacts
5. Intuitive with O & M Training
6. Identifies and Reads Text
7. Priced for Low-Income Households

## Slide 7: Critical Functions
Alert of Elevation
Determine Location
Alert of Physical Object
Identify Possible Threats
Interpret Sensory Information
Ethan Saffer

## Slide 8: Medium-High Fidelity Concepts
Ethan Saffer
GPS Watch:
Haptic Feedback cane:
Smart Glasses:
Audio Feedback cane:
GPS app:
Pin Matrix Haptics:
Sensor Watch:
Sensor Pin Chip:

## Slide 9: Concept Generation & Selection
Ethan Saffer
 | Sensor Pin Chip | Sensor Watch | Haptic Smart Cane with Camera
Alert of Elevation | 0.11 | 0.11 | 0.78
Determine Location | 0.16 | 0.19 | 0.66
Interpret Sensory Information | 0.20 | 0.20 | 0.60
Access Emergency Contact | 0.20 | 0.20 | 0.60
Interface with Pre-existing Skills | 0.14 | 0.14 | 0.71
Store Frequent Tasks | 0.33 | 0.33 | 0.33
Alert of a Physical Object | 0.43 | 0.14 | 0.43
Inform User of Possible Threats | 0.33 | 0.33 | 0.33
 | Sensor Pin Chip | Sensor Watch | Haptic Smart Cane
Alert of Elevation | 0.11 | 0.11 | 0.78
Determine Location | 0.16 | 0.19 | 0.66
Interpret Sensory Information | 0.45 | 0.45 | 0.09
Access Emergency Contact | 0.20 | 0.20 | 0.60
Interface with Pre-existing Skills | 0.14 | 0.14 | 0.71
Store Frequent Tasks | 0.33 | 0.33 | 0.33
Alert of a Physical Object | 0.43 | 0.14 | 0.43
Inform User of Possible Threats | 0.33 | 0.33 | 0.33

## Slide 10: Final Selection
Our final potential designs were ranked:
  Haptic Smart Cane
  Sensor Pin Chip
  Sensor Watch
#2
Sensor Pin Chip
#1
Haptic Smart Cane
#3
Sensor Watch
Ethan Saffer

## Slide 11
Functions
Ethan Saffer

## Slide 12
The ultrasonic sensor will sense an object up to 3 meters away.
Sense
Functions
Ethan Saffer

## Slide 13
The Raspberry Pi will interpret the sensed information to calculate the proximity to an object.
The ultrasonic sensor will sense an object up to 3 meters away.
Sense
Determine
Functions
Ethan Saffer

## Slide 14
The Raspberry Pi will interpret the sensed information to calculate the proximity to an object.
The ultrasonic sensor will sense an object up to 3 meters away.
Haptic feedback will alert the user with multiple motors with intensity based on distance.
Sense
Determine
Alert
Functions
Ethan Saffer

## Slide 15
The Raspberry Pi will interpret the sensed information to calculate the proximity to an object.
The camera can be activated to scan the desired products.
The ultrasonic sensor will sense an object up to 3 meters away.
Haptic feedback will alert the user with multiple motors with intensity based on distance.
Sense
Determine
Alert
Scan
Functions
Ethan Saffer

## Slide 16
The Raspberry Pi will interpret the sensed information to calculate the proximity to an object.
The camera can be activated to scan the desired products.
The ultrasonic sensor will sense an object up to 3 meters away.
Up to 500 stored products will be in the memory of the Raspberry Pi to identify the product.
Haptic feedback will alert the user with multiple motors with intensity based on distance.
Sense
Determine
Alert
Scan
Identify
Functions
Ethan Saffer

## Slide 17
The Raspberry Pi will interpret the sensed information to calculate the proximity to an object.
The camera can be activated to scan the desired products.
The ultrasonic sensor will sense an object up to 3 meters away.
Up to 500 stored products will be in the memory of the Raspberry Pi to identify the product.
Haptic feedback will alert the user with multiple motors with intensity based on distance.
Haptic feedback will
notify the user when the product has been identified and a speaker will relay the product name.
Sense
Determine
Alert
Scan
Identify
Notify
Functions
Ethan Saffer

## Slide 18
White Cane
Sunu Band
WeWalk
https://athome.medline.com/en/medline-white-cane-for-blind-vision-impaired-1ct-mdswhtcane
https://www.sunu.com/es/index
https://webrazzi.com/en/2020/05/01/wewalk-investment-750k/
Ethan Saffer
Competitors

## Slide 19: WeWalk
Similar product that incorporates ultrasonic sensors in the format of a smart-cane.
Uses infrared sensors to detect ground irregularities.
Overload of information.
Ethan Saffer

## Slide 20: Competitor Comparison
White Cane | Sunu Band | WeWalk | Our Solution
Senses irregularities below the waist Standard aid for visually impaired | Senses objects nearby Set position on wrist, can discomfort user to "aim" | Infrared Sensor for floor irregularities Ultrasonic sensor for object detection | Senses ground irregularties Notifies user

## Slide 21: Previous Housing & Assembly
Housing
Battery Pack
GrovePi+
Raspberry Pi 4
Vibration Motors (3)
Camera
Ultrasonic Sensor
Nicolas Garcia

## Slide 22: Previous Housing & Assembly
Scan
The camera can be activated to scan the desired products.
Sense
The ultrasonic sensor will sense an object up to 3 meters away.
Determine
The Raspberry Pi will interpret the sensed information to calculate the proximity to an object.
Notify
Alert
Haptic feedback will alert the user with multiple motors with intensity based on distance.
Identify
Scan
The camera can be activated to scan the desired products.
Sense
The ultrasonic sensor will sense an object up to 3 meters away.
Determine
The Raspberry Pi will interpret the sensed information to calculate the proximity to an object.
Notify
Alert
Haptic feedback will alert the user with multiple motors with intensity based on distance.
Identify
Sense
Sense
Nicolas Garcia

## Slide 23: Housing Issues Addressed
Our previous housing design was failing at the cane attachment.
The new design is more capable of handling the stresses that will act on the housing.
Nicolas Garcia

## Slide 24: Updated HapTac Assembly
Nicolas Garcia

## Slide 25: FEA Analysis on Handle
Megapascals (MPa)
The orange on the diagram shows where the stress concentration is highest.
Nicolas Garcia

## Slide 26: Camera Identification - AlexNet
8-layer identification software.
Capable of adding new items to its memory.
Low power drawn enables running on Raspberry Pi.
Nicolas Garcia

## Slide 27: Purchasing Parts
Orders for parts have been placed.
Only one was not successfully ordered by the Mechanical Engineering Department.
An alternate vendor for power source was found.
Nicolas Garcia

## Slide 28: Moving Forwards
Continue iterating 3D printed housing for the product.
Overall coding of system.
Testing and Validation
  Battery
  Sensor
  Camera
  Motors
  Housing
Nicolas Garcia

## Slide 29: Timeline
Retrieve Parts
InNOLEvation Challenge: Finals
Code Software
Testing and Validation
Reiterate Design
Final Product
Order Parts
Print Handle & Housing
Nicolas Garcia

## Slide 30: InNOLEvation Challenge
Selected as one of the eight finalists.
  Executive summary
  Finalize our business model canvas.
Nicolas Garcia

## Slide 31: Reference
Nicolas Garcia
[1] Ebben, J. M., PhD. (n.d.). Wrists at risk: Awkward postures to avoid. Retrieved February 18, 2021, from https://www.iacindustries.com/get-started/ergonomics/wrists-at-risk.asp
[2] González, A., Salgado, D., García Moruno, L., & Sánchez Ríos, A. (2018). An Ergonomic Customized-Tool Handle Design for Precision Tools using Additive Manufacturing: A Case Study. Applied Sciences, 8(7), 1200. doi:10.3390/app8071200
[3] McConomy, S. (2020, November 11). Engineering Characteristics, Functions, Targets, and Metric. FAMU-FSU College of Engineering.
[4] National Federation of The Blind. https://www.nfb.org/resources/blindness-statistics
[5] Queen, K. (2016, June). 7 Ways to Make Communities More Livable for People With Vision or Hearing Impairments. AARP.
[6] Wang, C., & Cai, D. (2020). Hand tool handle size and shape determination based on hand measurements using a contour gauge. Human Factors and Ergonomics in Manufacturing &amp; Service Industries, 30(5), 349-364. doi:10.1002/hfm.20846

## Slide 32
Nicolas Garcia
David Alicea
Field/Test Engineer and Quality Control
Daa16@my.fsu.edu
Nicolas Garcia
Webmaster, Design Engineer and Resource Manager
Ng16m@my.fsu.edu
Ethan Saffer
Systems and Design
Engineer
Ers16c@my.fsu.edu
Team 522: Vision Impaired Technology
Madison Jaffe​
Project Manager and Manufacturing/Controls Engineer
Msj16d@my.fsu.edu

## Slide 35
APPENDIX

## Slide 36: Device Operational Time
Ultrasonic Sensor
8 mA
Camera
Up to 800 mA
Vibration Motor
58 mA average
100 mA max
Raspberry Pi
3,000 mA
Power Supply
20,000 mAh
Theoretical (Maximum Current Draw) Operation Time: 4.87 Hours
4 hours, 52 minutes and 12 seconds
Madison Jaffe

## Slide 37
8 + 800 + 300 + 3000 = 4108 mA
mAh is mA * (hours operating) = mAh
20000mAh / 5016mA = 4.86855 hours
https://elinux.org/Rpi_Camera_Module
https://static6.arrow.com/aropdfconversion/7ce3c19d47af65a2e4096b327057dad3e30632e1/pgurl_grove-vibration-motor-p-839l.pdf
Sensor 8 mA
Pi: 3A (based on power source)
Camera: up to 800mA
Motor: 58 mA standard, 100 mA at max
Power Supply= 20000 mAh
Therefore: 4.87 Hours of operation at max use

## Slide 38
Function ​ | Target ​ | Metric ​
Alert of Elevation* ​ | 0.25 to 12 inches ​ | Distance ​
Determine Location* ​ | Margin of error of at most 16 feet ​ | Distance ​
Alert of Physical Object* ​ | 65 inches ​ | Distance ​
Identify Possible Threats* ​ | Up to 60 miles per hour ​ | Velocity ​
Access Emergency Contact ​ | 15 seconds ​ | Time ​
Interpret Sensory Information* ​ | 7 seconds ​ | Time ​
Store Frequent Tasks ​ | 1 GB ​ | Memory Allocation ​
Interface with Pre-Existing Skills ​ | 70% ​ | User Satisfaction ​
Compete within Market ​ | 20% ​ | Price Range USD ($) ​
Remain Lightweight ​ | <5 lb ​ | Weight ​
Remain Discrete ​ | 70% ​ | User Approval ​

## Slide 39: Synopsis: Semester 1
Markets:
  Primary market: People with severe visual impairment, rehabilitation and treatment centers.
  Secondary market: Autonomous Systems and State-Local Departments of Transportation.
David Alicea

## Slide 40: Synopsis: Semester 1
David Alicea
1. Helps Avoid Ground Irregularities
2. Allows for Location Awareness
3. Recognizes Surrounding Objects
4. Notify Emergency Contacts
5. Intuitive with O & M Training
6. Identifies and Reads Text
7. Priced for Low-Income Households
Markets:
  Primary market: People with severe visual impairment, rehabilitation and treatment centers.
  Secondary market: Autonomous Systems and State-Local Departments of Transportation.
Interpreted Customer Needs:

## Slide 41: Functional Decomposition
David Alicea

## Slide 42: Targets and Metrics
Function | Target | Metric
Alert of Elevation* | 0.25 to 12 inches | Distance
Determine Location* | ~ 16 feet | Distance
Alert of Physical Object* | 65 inches | Distance
Identify Possible Threats* | Up to 60 miles per hour | Velocity
Access Emergency Contact | 15 seconds | Time
Interpret Sensory Information* | 7 seconds | Time
Store Frequent Tasks | 1 GB | Memory Allocation
Interface with Pre-Existing Skills | 70% | User Satisfaction
Compete within Market | 20% | Price Range USD ($)
Remain Lightweight | < 5.1 lb | Weight
Remain Discrete | 70% | User Approval
David Alicea

## Slide 43: Concept Generation Tools
Biomimicry
Crap Shoot
Morphological Chart
David Alicea
McConomy, S. (2020, November 11). Engineering Characteristics, Functions, Targets, and Metric. FAMU-FSU College of Engineering.

## Slide 44: Morphological Chart
Alert of Elevation | Determine Location | Alert of Physical Object | Inform of Possible Threats | Interpret Sensory Information
Sensor | GPS Through Wi-Fi/Internet Signal | Distance Sensor | Heat | Camera
Cane/Stick | GPS w/ Maps Downloaded | Velocity Sensor | Vibrate | Text Conversion
 | Camera to Read Street Signs and Other Landmarks | Lidar | Noise | Live Imaging Scanned to a PDF Document
 | Memory Storage of Previous Paths |  | Poke | Text to Braille
David Alicea

## Slide 45: Medium Fidelity Concepts
David Alicea
GPS Watch:
- GPS indicate where the user is
- haptic feedback provided through vibration on wrist
Haptic Feedback cane:
- haptic feedback voice-activated
- phone compatible
Smart Glasses:
- sensor and GPS for user location
- Audio feedback through glass-mounted earpiece
Audio Feedback cane:
- audio feedback
- Tactile or voice activation
- Phone compatible
- camera to interpret the environment
GPS app:
- Lidar
- user information through haptics
- computer and GPS track and locate user

## Slide 46: Concept Selection
David Alicea

## Slide 47: Importance Weight Factor
Helps Avoid Ground Irregularities
Recognizes Surrounding Objects
Intuitive with O&M Training
Notify Emergency Contact
Priced for Low-Income Households
Identifies and Reads Text
Allows for Location Detection
Interpreted Customer Needs
Importance Weight Factor
Nicolas Garcia

## Slide 48: House of Quality
Nicolas Garcia

## Slide 49
Interpret Sensory Information
Alert of Elevation
Alert of Physical Objects
Determine Location
Interface with Pre-Existing Skills
Store Frequent Tasks
Inform User of Potential Threats
Access Emergency Contacts
Nicolas Garcia
House of Quality

## Slide 50: Pugh Chart
Nicolas Garcia

## Slide 51: Pugh Chart
Nicolas Garcia

## Slide 52: Second Pugh Chart
Nicolas Garcia

## Slide 53: Second Pugh Chart
Nicolas Garcia

## Slide 54: Analytical Hierarchy Process
Nicolas Garcia
Criteria Comparison Matrix [C] | 
Functions | Criteria Weights{W}
Alert of Elevation | 0.11
Determine Location | 0.13
Interpret Sensory Information | 0.24
Access Emergency Contact | 0.03
Interface With Pre-Existing Skills | 0.11
Store Frequent Tasks | 0.04
Alert of Physical Object | 0.19
Inform User of Possible Threats | 0.15
Sum | 1.00

## Slide 55: Analytical Hierarchy Process
Nicolas Garcia
 | Sensor Pin Chip | Sensor Watch | Haptic Smart Cane
Alert of Elevation | 0.11 | 0.11 | 0.78
Determine Location | 0.16 | 0.19 | 0.66
Interpret Sensory Information | 0.45 | 0.45 | 0.09
Access Emergency Contact | 0.20 | 0.20 | 0.60
Interface with Pre-existing Skills | 0.14 | 0.14 | 0.71
Store Frequent Tasks | 0.33 | 0.33 | 0.33
Alert of a Physical Object | 0.43 | 0.14 | 0.43
Inform User of Possible Threats | 0.33 | 0.33 | 0.33

## Slide 56: Analytical Hierarchy Process
Nicolas Garcia
 | Sensor Pin Chip | Sensor Watch | Haptic Smart Cane
Alert of Elevation | 0.11 | 0.11 | 0.78
Determine Location | 0.16 | 0.19 | 0.66
Interpret Sensory Information | 0.45 | 0.45 | 0.09
Access Emergency Contact | 0.20 | 0.20 | 0.60
Interface with Pre-existing Skills | 0.14 | 0.14 | 0.71
Store Frequent Tasks | 0.33 | 0.33 | 0.33
Alert of a Physical Object | 0.43 | 0.14 | 0.43
Inform User of Possible Threats | 0.33 | 0.33 | 0.33

## Slide 57: Analytical Hierarchy Process
Nicolas Garcia
 | Sensor Pin Chip | Sensor Watch | Haptic Smart Cane
Alert of Elevation | 0.11 | 0.11 | 0.78
Determine Location | 0.16 | 0.19 | 0.66
Interpret Sensory Information | 0.45 | 0.45 | 0.09
Access Emergency Contact | 0.20 | 0.20 | 0.60
Interface with Pre-existing Skills | 0.14 | 0.14 | 0.71
Store Frequent Tasks | 0.33 | 0.33 | 0.33
Alert of a Physical Object | 0.43 | 0.14 | 0.43
Inform User of Possible Threats | 0.33 | 0.33 | 0.33

## Slide 58
Binary Comparison Chart |  |  |  |  |  |  |  | 
Interprted Customer Needs | 1 | 2 | 3 | 4 | 5 | 6 | 7 | Total 1
1. Helps Avoid Ground Irregularities | - | 1 | 0 | 0 | 0 | 0 | 1 | 2
2. Allows for Location Awareness | 0 | - | 0 | 1 | 0 | 1 | 0 | 2
3. Recognizes Surrounding Objects | 1 | 1 | - | 1 | 1 | 1 | 1 | 6
4. Notify Emergency Contacts | 1 | 0 | 0 | - | 1 | 0 | 1 | 3
5. Intuitive with O & M Training | 1 | 1 | 0 | 0 | - | 1 | 1 | 4
6. Identifies and Reads Text | 1 | 0 | 0 | 1 | 0 | - | 0 | 2
7. Priced for low-income households | 0 | 1 | 0 | 1 | 0 | 1 | - | 3
Total: | 4 | 4 | 0 | 4 | 2 | 4 | 4 | 6

## Slide 59: Functional Decomposition
 | Orientation | Mobility | Utility
Alert of Elevation | X | X | 
Determine Location | X | X | 
Alert of Physical Object | X | X | 
Inform User of Possible Threats |  | X | X
Access to Emergency Contact |  |  | X
Interpret Sensory information |  |  | X
Store Frequent Tasks | X |  | X
Interface With Pre-Existing Skills |  |  | X
David Alicea

## Slide 60
Engineering |  | Concepts |  |  |  |  |  |  | 
Characteristics | Oram MyEye2 | Sensor Pin Chip | Pin Matrix Haptics | Sensor Watch | GPS App | GPS Watch | Haptic Smart Cane | Smart Glasses | Audio Feedback Cane
Alert of Elevation | Datum | + | + | + | - | - | + | S | +
Determine Location |  | S | S | + | + | + | + | + | +
Interpret Sensory Information |  | - | - | - | - | + | S | - | S
Access Emergency Contact |  | S | S | S | + | - | + | - | +
Interface With Pre-Existing Skills |  | S | + | + | S | S | + | S | S
Store Frequent Tasks |  | + | S | S | S | - | S | - | +
Alert of Physical Object |  | + | + | + | - | + | - | + | -
Inform User of Possible Threats |  | + | + | + | + | + | - | + | +
# of Pluses |  | 4 | 4 | 5 | 3 | 4 | 4 | 3 | 5
# of Minuses |  | 2 | 1 | 1 | 3 | 3 | 2 | 3 | 1

## Slide 61
Engineering |  | Concepts |  |  |  |  | 
Characteristics | GPS Watch | Sensor Pin Chip | Sensor Watch | GPS App | Haptic Smart Cane | Smart Glasses | Audio Feedback Cane
Alert of Elevation | Datum | + | + | S | + | S | +
Determine Location |  | - | - | S | - | S | -
Interpret Sensory Information |  | + | + | S | + | + | +
Access Emergency Contact |  | S | S | + | S | S | -
Interface With Pre-Existing Skills |  | S | + | + | + | S | +
Store Frequent Tasks |  | + | S | S | S | S | S
Alert of Physical Object |  | + | + | - | + | + | +
Inform User of Possible Threats |  | + | + | - | + | + | +
# of Pluses |  | 5 | 5 | 2 | 5 | 3 | 5
# of Minuses |  | 1 | 1 | 2 | 1 | 0 | 2

## Slide 62
Engineering Concepts |  |  |  |  |  |  |  |  | 
Units |  | Inches | Latitude/Longitude | Seconds | Seconds | Minutes | GB | Seconds | Seconds
Customer Requirements | Importance Weight Factor | Alert of Elevation | Determine Location | Interpret Sensory Information | Access Emergency Contact | Interface With Pre-Existing Skills | Store Frequent Tasks | Alert of Physical Object | Inform User of Possible Threats
1. Helps Avoid Ground Irregularities | 2 | 9 | 5 | 9 | - | 7 | 1 | 7 | 9
2. Allows for Location Awareness | 2 | 9 | 9 | 9 | - | 1 | 1 | 7 | 3
3. Recognizes Surrounding Objects | 6 | 7 | 7 | 9 | - | 3 | 5 | 9 | 3
4. Notify Emergency Contacts | 3 | 1 | 5 | - | 9 | 1 | 3 | 1 | 1
5. Intuitive with O & M Training | 4 | 5 | 5 | 5 | 3 | 9 | 3 | 3 | 1
6. Identifies and Reads Text | 2 | - | - | 5 | 1 | - | 5 | - | -
7. Priced for low-income households | 3 | - | - | - | - | - | - | - | -
Raw Score (629) | N/A | 101 | 85 | 122 | 41 | 73 | 65 | 97 | 43
Relative Weight % |  | 16.1 | 13.5 | 19.4 | 6.5 | 11.6 | 10.3 | 15.4 | 6.8
Rank Order |  | 2 | 4 | 1 | 8 | 5 | 6 | 3 | 7

## Slide 63
Development of Candidate Set of Criteria Weights {W} |  |  |  |  |  |  |  | 
Criteria Comparison Matrix [C] |  |  |  |  |  |  |  | 
 | Alert of Elevation | Determine Location | Interpret Sensory Information | Access Emergency Contact | Interface With Pre-Existing Skills | Store Frequent tasks | Alert of Physical Objects | Inform User of Possible Threats
Alert of Elevation | 1.00 | 1.00 | 0.33 | 5.00 | 1.00 | 3.00 | 0.33 | 1.00
Determine Location | 1.00 | 1.00 | 0.33 | 5.00 | 1.00 | 3.00 | 1.00 | 1.00
Interpret Sensory Information | 3.00 | 3.00 | 1.00 | 5.00 | 3.00 | 5.00 | 1.00 | 1.00
Access Emergency Contact | 0.20 | 0.20 | 0.20 | 1.00 | 0.20 | 1.00 | 0.33 | 0.20
Interface With Pre-Existing Skills | 1.00 | 1.00 | 0.33 | 5.00 | 1.00 | 3.00 | 0.33 | 1.00
Store Frequent Tasks | 0.33 | 0.33 | 0.20 | 1.00 | 0.33 | 1.00 | 0.33 | 0.33
Alert of Physical Object | 3.00 | 1.00 | 1.00 | 3.00 | 3.00 | 3.00 | 1.00 | 1.00
Inform User of Possible Threats | 1.00 | 1.00 | 1.00 | 5.00 | 1.00 | 3.00 | 1.00 | 1.00
Sum | 10.53 | 8.53 | 4.40 | 30.00 | 10.53 | 22.00 | 5.33 | 6.53

## Slide 64
Development of Candidate Set of Criteria Weights {W} |  |  |  |  |  |  |  |  | 
Criteria Comparison Matrix [C] |  |  |  |  |  |  |  |  | 
 | Alert of Elevation | Determine Location | Interpret Sensory Information | Acccess Emergency Contact | Interface With Pre-Existing Skills | Store Fequent tasks | Alert of Physical Objects | Inform User of Possible Threats | Criteria Weights{W}
Alert of Elevation | 0.09 | 0.12 | 0.08 | 0.17 | 0.09 | 0.14 | 0.06 | 0.15 | 0.11
Determine Location | 0.09 | 0.12 | 0.08 | 0.17 | 0.09 | 0.14 | 0.19 | 0.15 | 0.13
Interpret Sensory Information | 0.28 | 0.35 | 0.23 | 0.17 | 0.28 | 0.23 | 0.19 | 0.15 | 0.24
Access Emergency Contact | 0.02 | 0.02 | 0.05 | 0.03 | 0.02 | 0.05 | 0.06 | 0.03 | 0.03
Interface With Pre-Existing Skills | 0.09 | 0.12 | 0.08 | 0.17 | 0.09 | 0.14 | 0.06 | 0.15 | 0.11
Store Frequent Tasks | 0.03 | 0.04 | 0.05 | 0.03 | 0.03 | 0.05 | 0.06 | 0.05 | 0.04
Alert of Physical Object | 0.28 | 0.12 | 0.23 | 0.10 | 0.28 | 0.14 | 0.19 | 0.15 | 0.19
Inform User of Possible Threats | 0.09 | 0.12 | 0.23 | 0.17 | 0.09 | 0.14 | 0.19 | 0.15 | 0.15
Sum | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00

## Slide 65
# of criteria | RI value | Average Consistency | Consistency Index | Consistency Ratio
8.00 | 1.40 | 8.39 | 0.06 | 0.04
Weighted Sum Vector | Criteria Weights{W} | Consistency vector
0.94 | 0.11 | 8.37
1.07 | 0.13 | 8.32
2.02 | 0.24 | 8.57
0.29 | 0.03 | 8.23
0.94 | 0.11 | 8.37
0.35 | 0.04 | 8.32
1.61 | 0.19 | 8.61
1.22 | 0.15 | 8.32

## Slide 66
Development of Candidate Set of Criteria Weights {W} ALERT OF ELEVATION | Alert of Elevation |  | 
Criteria Comparison Matrix [C] |  |  | 
 | Sensor Pin Chip | Sensor Watch | Haptic Smart Cane
Sensor Pin Chip | 1.00 | 1.00 | 0.14
Sensor Watch | 1.00 | 1.00 | 0.14
Haptic Smart Cane | 7.00 | 7.00 | 1.00
Sum | 9.00 | 9.00 | 1.29

## Slide 67: Analytical Hierarchy Process
Nicolas Garcia
Criteria Comparison Matrix [C] |  |  |  |  |  |  |  | 
 | Alert of Elevation | Determine Location | Interpret Sensory Information | Access Emergency Information | Interface with pre-existing skills | Store Frequent Tasks | Alert of Physical Objects | Inform User of Possible Threats
Alert of Elevation | 1.00 | 1.00 | 0.33 | 5.00 | 1.00 | 3.00 | 0.33 | 1.00
Determine Location | 1.00 | 1.00 | 0.33 | 5.00 | 1.00 | 3.00 | 1.00 | 1.00
Interpret Sensory Information | 3.00 | 3.00 | 1.00 | 5.00 | 3.00 | 5.00 | 1.00 | 1.00
Access Emergency Information | 0.20 | 0.20 | 0.20 | 1.00 | 0.20 | 1.00 | 0.33 | 0.20
Interface with Pre-existing Skills | 1.00 | 1.00 | 0.33 | 5.00 | 1.00 | 3.00 | 0.33 | 1.00
Store Frequent Tasks | 0.33 | 0.33 | 0.20 | 1.00 | 0.33 | 1.00 | 0.33 | 0.33
Alert of Physical Objects | 3.00 | 1.00 | 1.00 | 3.00 | 3.00 | 3.00 | 1.00 | 1.00
Inform User of Possible Threats | 1.00 | 1.00 | 1.00 | 5.00 | 1.00 | 3.00 | 1.00 | 1.00
Sum | 10.53 | 8.53 | 4.40 | 30.00 | 10.53 | 22.00 | 5.33 | 6.53

## Slide 68
Development of Candidate Set of Criteria Weights {W} |  |  |  | 
Criteria Comparison Matrix [C] |  |  |  | 
 | Sensor Pin Chip | Sensor Watch | Haptic Smart Cane | Design Alternative Priorities {Pi}
Sensor Pin Chip | 0.11 | 0.11 | 0.11 | 0.11
Sensor Watch | 0.11 | 0.11 | 0.11 | 0.11
Haptic Smart Cane | 0.78 | 0.78 | 0.78 | 0.78
Sum | 1.00 | 1.00 | 1.00 | 1.00

## Slide 69
Weighted Sum Vector | Design Alternative Priorities | Consistency vector
0.33 | 0.11 | 3.00
0.33 | 0.11 | 3.00
2.33 | 0.78 | 3.00
# of criteria | RI value | Average Consistency | Consistency Index | Consistency Ratio
3.00 | 0.52 | 3.00 | 0.00 | 0.00

## Slide 70
Development of Candidate Set of Criteria Weights {W} | Determine Location |  | 
Criteria Comparison Matrix [C] |  |  | 
 | Sensor Pin Chip | Sensor Watch | Haptic Smart Cane
Sensor Pin Chip | 1.00 | 1.00 | 0.20
Sensor Watch | 1.00 | 1.00 | 0.33
Haptic Smart Cane | 5.00 | 3.00 | 1.00
Sum | 7.00 | 5.00 | 1.53

## Slide 71
Development of Candidate Set of Criteria Weights {W} |  |  |  | 
Criteria Comparison Matrix [C] |  |  |  | 
 | Sensor Pin Chip | Sensor Watch | Haptic Smart Cane | Design Alternative Priorities {Pi}
Sensor Pin Chip | 0.14 | 0.20 | 0.13 | 0.16
Sensor Watch | 0.14 | 0.20 | 0.22 | 0.19
Haptic Smart Cane | 0.71 | 0.60 | 0.65 | 0.66
Sum | 1.00 | 1.00 | 1.00 | 1.00

## Slide 72
# of criteria | RI value | Average Consistency | Consistency Index | Consistency Ratio
3.00 | 0.52 | 3.00 | 0.00 | 0.00
Weighted Sum Vector | Design Alternative Priorities | Consistency vector
0.48 | 0.16 | 3.01
0.56 | 0.19 | 3.01
2.00 | 0.66 | 3.06

## Slide 73
Development of Candidate Set of Criteria Weights {W} | Interpret Sensory Information |  | 
Criteria Comparison Matrix [C] |  |  | 
 | Sensor Pin Chip | Sensor Watch | Haptic Smart Cane
Sensor Pin Chip | 1.00 | 1.00 | 5.00
Sensor Watch | 1.00 | 1.00 | 5.00
Haptic Smart Cane | 0.20 | 0.20 | 1.00
Sum | 2.20 | 2.20 | 11.00

## Slide 74
Development of Candidate Set of Criteria Weights {W} |  |  |  | 
Criteria Comparison Matrix [C] |  |  |  | 
 | Sensor Pin Chip | Sensor Watch | Haptic Smart Cane | Design Alternative Priorities {Pi}
Sensor Pin Chip | 0.45 | 0.45 | 0.45 | 0.45
Sensor Watch | 0.45 | 0.45 | 0.45 | 0.45
Haptic Smart Cane | 0.09 | 0.09 | 0.09 | 0.09
Sum | 1.00 | 1.00 | 1.00 | 1.00

## Slide 75
# of criteria | RI value | Average Consistency | Consistency Index | Consistency Ratio
3.00 | 0.52 | 3.00 | 0.00 | 0.00
Weighted Sum Vector | Design Alternative Priorities | Consistency vector
1.36 | 0.45 | 3.00
1.36 | 0.45 | 3.00
0.27 | 0.09 | 3.00

## Slide 76
Development of Candidate Set of Criteria Weights {W} | Access Emergency Contact |  | 
Criteria Comparison Matrix [C] |  |  | 
 | Sensor Pin Chip | Sensor Watch | Haptic Smart Cane
Sensor Pin Chip | 1.00 | 1.00 | 0.33
Sensor Watch | 1.00 | 1.00 | 0.33
Haptic Smart Cane | 3.00 | 3.00 | 1.00
Sum | 5.00 | 5.00 | 1.67

## Slide 77
Development of Candidate Set of Criteria Weights {W} |  |  |  | 
Criteria Comparison Matrix [C] |  |  |  | 
 | Sensor Pin Chip | Sensor Watch | Haptic Smart Cane | Design Alternative Priorities {Pi}
Sensor Pin Chip | 0.20 | 0.20 | 0.20 | 0.20
Sensor Watch | 0.20 | 0.20 | 0.20 | 0.20
Haptic Smart Cane | 0.60 | 0.60 | 0.60 | 0.60
Sum | 1.00 | 1.00 | 1.00 | 1.00

## Slide 78
# of criteria | RI value | Average Consistency | Consistency Index | Consistency Ratio
3.00 | 0.52 | 3.00 | 0.00 | 0.00
Weighted Sum Vector | Design Alternative Priorities | Consistency vector
0.60 | 0.20 | 3.00
0.60 | 0.20 | 3.00
1.80 | 0.60 | 3.00

## Slide 79
Development of Candidate Set of Criteria Weights {W} | Interface With Pre-Existing Skills |  | 
Criteria Comparison Matrix [C] |  |  | 
 | Sensor Pin Chip | Sensor Watch | Haptic Smart Cane
Sensor Pin Chip | 1.00 | 1.00 | 0.20
Sensor Watch | 1.00 | 1.00 | 0.20
Haptic Smart Cane | 5.00 | 5.00 | 1.00
Sum | 7.00 | 7.00 | 1.40

## Slide 80
Development of Candidate Set of Criteria Weights {W} |  |  |  | 
Criteria Comparison Matrix [C] |  |  |  | 
 | Sensor Pin Chip | Sensor Watch | Haptic Smart Cane | Design Alternative Priorities {Pi}
Sensor Pin Chip | 0.14 | 0.14 | 0.14 | 0.14
Sensor Watch | 0.14 | 0.14 | 0.14 | 0.14
Haptic Smart Cane | 0.71 | 0.71 | 0.71 | 0.71
Sum | 1.00 | 1.00 | 1.00 | 1.00

## Slide 81
Weighted Sum Vector | Design Alternative Priorities | Consistency vector
0.43 | 0.14 | 3.00
0.43 | 0.14 | 3.00
2.14 | 0.71 | 3.00
# of criteria | RI value | Average Consistency | Consistency Index | Consistency Ratio
3.00 | 0.52 | 3.00 | 0.00 | 0.00

## Slide 82
Development of Candidate Set of Criteria Weights {W} | Store Frequent Tasks |  | 
Criteria Comparison Matrix [C] |  |  | 
 | Sensor Pin Chip | Sensor Watch | Haptic Smart Cane
Sensor Pin Chip | 1.00 | 1.00 | 1.00
Sensor Watch | 1.00 | 1.00 | 1.00
Haptic Smart Cane | 1.00 | 1.00 | 1.00
Sum | 3.00 | 3.00 | 3.00

## Slide 83
Development of Candidate Set of Criteria Weights {W} |  |  |  | 
Criteria Comparison Matrix [C] |  |  |  | 
 | Sensor Pin Chip | Sensor Watch | Haptic Smart Cane | Design Alternative Priorities {Pi}
Sensor Pin Chip | 0.33 | 0.33 | 0.33 | 0.33
Sensor Watch | 0.33 | 0.33 | 0.33 | 0.33
Haptic Smart Cane | 0.33 | 0.33 | 0.33 | 0.33
Sum | 1.00 | 1.00 | 1.00 | 1.00

## Slide 84
# of criteria | RI value | Average Consistency | Consistency Index | Consistency Ratio
3.00 | 0.52 | 3.00 | 0.00 | 0.00
Weighted Sum Vector | Design Alternative Priorities | Consistency vector
1.00 | 0.33 | 3.00
1.00 | 0.33 | 3.00
1.00 | 0.33 | 3.00

## Slide 85
Development of Candidate Set of Criteria Weights {W} | Alert of Physical Object |  | 
Criteria Comparison Matrix [C] |  |  | 
 | Sensor Pin Chip | Sensor Watch | Haptic Smart Cane
Sensor Pin Chip | 1.00 | 3.00 | 1.00
Sensor Watch | 0.33 | 1.00 | 0.33
Haptic Smart Cane | 1.00 | 3.00 | 1.00
Sum | 2.33 | 7.00 | 2.33

## Slide 86
Development of Candidate Set of Criteria Weights {W} |  |  |  | 
Criteria Comparison Matrix [C] |  |  |  | 
 | Sensor Pin Chip | Sensor Watch | Haptic Smart Cane | Design Alternative Priorities {Pi}
Sensor Pin Chip | 0.43 | 0.43 | 0.43 | 0.43
Sensor Watch | 0.14 | 0.14 | 0.14 | 0.14
Haptic Smart Cane | 0.43 | 0.43 | 0.43 | 0.43
Sum | 1.00 | 1.00 | 1.00 | 1.00

## Slide 87
# of criteria | RI value | Average Consistency | Consistency Index | Consistency Ratio
3.00 | 0.52 | 3.00 | 0.00 | 0.00
Weighted Sum Vector | Design Alternative Priorities | Consistency vector
1.29 | 0.43 | 3.00
0.43 | 0.14 | 3.00
1.29 | 0.43 | 3.00

## Slide 88
Development of Candidate Set of Criteria Weights {W} | Inform User of Possible Threats |  | 
Criteria Comparison Matrix [C] |  |  | 
 | Sensor Pin Chip | Sensor Watch | Haptic Smart Cane
Sensor Pin Chip | 1.00 | 1.00 | 1.00
Sensor Watch | 1.00 | 1.00 | 1.00
Haptic Smart Cane | 1.00 | 1.00 | 1.00
Sum | 3.00 | 3.00 | 3.00

## Slide 89
Development of Candidate Set of Criteria Weights {W} |  |  |  | 
Criteria Comparison Matrix [C] |  |  |  | 
 | Sensor Pin Chip | Sensor Watch | Haptic Smart Cane | Design Alternative Priorities {Pi}
Sensor Pin Chip | 0.33 | 0.33 | 0.33 | 0.33
Sensor Watch | 0.33 | 0.33 | 0.33 | 0.33
Haptic Smart Cane | 0.33 | 0.33 | 0.33 | 0.33
Sum | 1.00 | 1.00 | 1.00 | 1.00

## Slide 90
Weighted Sum Vector | Design Alternative Priorities | Consistency vector
1.00 | 0.33 | 3.00
1.00 | 0.33 | 3.00
1.00 | 0.33 | 3.00
# of criteria | RI value | Average Consistency | Consistency Index | Consistency Ratio
3.00 | 0.52 | 3.00 | 0.00 | 0.00

## Slide 91
 | Sensor Pin Chip | Sensor Watch | Haptic Smart Cane
Alert of Elevation | 0.11 | 0.11 | 0.78
Determine Location | 0.16 | 0.19 | 0.66
Interpret Sensory Information | 0.45 | 0.45 | 0.09
Access Emergency Contact | 0.20 | 0.20 | 0.60
Interface With Pre-Existing Skills | 0.14 | 0.14 | 0.71
Store Frequent Tasks | 0.33 | 0.33 | 0.33
Alert of Physical Object | 0.43 | 0.14 | 0.43
Inform User of Possible Threats | 0.33 | 0.33 | 0.33
Concept | Alternative Value
Sensor Pin Chip | 0.27
Sensor Watch | 0.24
Haptic Smart Cane | 0.49

## Slide 92: Standard Shapes
Summary Box
Text box 1
Outlined Text Box

## Slide 93: Approved Logos

## Slide 94: Color Palette

## Slide 95
Slides to keep:
Intro, Synopsis of VDR1 (Rename), Customer Needs, minimize Concept Gen. & Selection, Final Selection?, What's Next, Last team member slide, Ref.
Slides to add:
Specs of design
BOM/Ordering parts
Our progress in the InNOLEvation challenge?

## Slide 96: APA Tables
Category 1 | Category 2 | Category 3 | Category 4 | Category 5
Item 1 |  |  |  | 
Item 2 |  |  |  | 
Item 3 |  |  |  | 
Item 4 |  |  |  | 
 | Category 2 |  |  | Category 3 | 
Category 1 | subcategory 1 | subcategory 2 |  | subcategory 1 | subcategory 2
Item 1 |  |  |  |  | 
Item 2 |  |  |  |  | 
Item 3 |  |  |  |  | 
Item 4 |  |  |  |  |