## Slide 1: RE-RASSOR ARM
Grace Busch | Evaline Cantarero | Jackson Davis | David Nowicki
TEAM 505
Notes: evaline

## Slide 2: Meet Team 505
Evaline Cantarero
Grace Busch
Dynamic System
Engineer
David Nowicki
Design
Engineer
Evaline Cantarero
Mechatronics
Engineer
Jackson Davis
Materials Engineer

## Slide 3: Sponsor and Advisor
Engineering Mentor
Mike Conroy
Florida Space Institute
Academic Advisor
Dr. Patrick Hollis
FAMU-FSU College of Engineering
Evaline Cantarero

## Slide 4: Project Background
Florida Space Institute in collaboration with NASA's Swamp Works has asked us to improve the RE-RASSOR
RE-RASSOR is an educational, mainly 3D printed, open-source platform
The solution we produce will be deployed on the educational version, and some ideas may be used by NASA on the full size RASSOR
Evaline Cantarero

## Slide 5: Project Scope
Shoulder
Drives the system
Gearbox
Motor
Arm
Connects the shoulder to the drum
Supports the drum in all operations
Evaline Cantarero

## Slide 6: Project Objective
Redesign the shoulder, arm, and drive components using parts printed out of PLA
Improve durability and cost through innovative technologies and 3D printing processes
19.05 cm
41.59 cm
Evaline Cantarero

## Slide 7: Customer Needs & Assumptions
Customer Needs
  3D printed PLA parts
  Total cost < $60
  Range of motion and load
Assumptions
  Provided 12 V @ 1.2 A
  Used in earth environment
  Only needs to pivot
Evaline Cantarero

## Slide 8: Market & Functional Decomposition
Market
  NASA, Swamp Works, Florida Space Institute
  STEM Education
  Space/Mining Companies
Functional Decomposition
  Source Power
  Support Arm
  Create Motion
Evaline Cantarero

## Slide 9: Targets & Metrics
Motion
  Rotates 270 degrees
Power
  12 Volts and 1.2 Amps
Support
  Lift 2x 10-kilogram drums per arm
Evaline Cantarero

## Slide 10: Concept Generation
Brain Stroming
Morphological Chart
Biomimicry
Forced Analogy
Evaline Cantarero

## Slide 11: High Fidelity
High Fidelity Concept 1
High Fidelity Concept 2
High Fidelity Concept 3
Stepper motor
Cycloidal drive
transmission
Cylindrical arm
Twin stepper motors
Electromagnetic
brake
Harmonic gearbox
Cylindrical tube
Stepper motor
Worm gearbox
Cylindrical arm
Dowel pin supports
Evaline Cantarero

## Slide 12: Concept Selection
Stepper Motor
PLA filament
RAMPS driver
Hybrid gearbox
Tapered cylindrical arm
Evaline Cantarero

## Slide 13: Initial Design
Name
1
2
3
4
5
8
7
6
2
1. T-Joint
2. Shoulder Blade
3. Arm Flange
4. Arm
5. Arm Knuckle
6. Stepper Motor
7. Motor Mount
8. Gearbox
Jackson Davis

## Slide 14
Gearbox
Nema 23 Motor
T-Joint
Should Blade
Jackson Davis

## Slide 15: Gearbox Design
Our Designs:
Harmonic
Planetary
Harmonic Planetary Hybrid
Cycloidal
Worm Gear
Jackson Davis

## Slide 16
Hybrid Gearbox
Mix between planetary and harmonic
Huge reduction ratio of 155:1
Name
10.05 cm
Design 1
Jackson Davis

## Slide 17
Cycloidal Gearbox
Lower friction and less wear on the tooth flanks
Good torsional stiffness and capacity to withstand shocks
48:1 reduction
Name
Design 2
Jackson Davis

## Slide 18
Planetary Gearbox
Coaxially aligned input and output shafts make it compact
High torque and low backlash
Capable of high gear ratios with compound gear trains
Current: 3.67:1
5.34 cm
4.25 cm
Design 3
Jackson Davis

## Slide 19: Gearbox Testing
Designing Gearbox
Design testing apparatus
Add weight to apparatus till failure
Ideal Gear Ratio: 50:1
Test motor shaft and gearbox coupler
Jackson Davis

## Slide 20
10 kg
10 kg
Jackson Davis

## Slide 21: Stepper Motor
Nema 23: 1.2Nm, 3Nm
50mm vs 100mm
Jackson Davis

## Slide 22: Motor Testing
1.2 Amps, 12 Volts
Provides 0.2 N*m
Jackson Davis

## Slide 23: Arm
Design testing apparatus
Mount the arm to the apparatus
Add weight to arm until failure
Insert a bar into arm knuckle
Add weight to bar until failure
Jackson Davis

## Slide 24
Jackson Davis

## Slide 25: Determine Specs
Determining Specs
Voltage &
Current
Weight of Components
Weight of Loaded Drum
Gear Ratio
Torque
Evaline Cantarero

## Slide 26: Future Work
Determine Specs
Rapid Prototyping
Failure Testing
Torque Analysis
Evaline Cantarero

## Slide 27: References
Showcase, A. P. (2021, August 6). 2020 RE-RASSOR ARM. Florida Space Institute. Retrieved September 13, 2021, from https://fsi.ucf.edu/2020re-rassorarm/.
Showcase, A. P. (2021, August 6). 2020 RE-RASSOR Gold team. Florida Space Institute. Retrieved September 13, 2021, from https://fsi.ucf.edu/2020goldteam/.

## Slide 28: Backup Slides

## Slide 29: Concept Selection

## Slide 30: Embodiment
Upcoming Presenter’s Name

## Slide 32: Manufacturing
Upcoming Presenter’s Name

## Slide 34: Testing
Upcoming Presenter’s Name

## Slide 36: Project Management

## Slide 38: # Most Important Points
The quick brown fox jumps over the lazy dog.
The quick brown fox jumps over the lazy dog.
The quick brown fox jumps over the lazy dog.
The quick brown fox jumps over the lazy dog.
The quick brown fox jumps over the lazy dog.
The quick brown fox jumps over the lazy dog.

## Slide 39: Lessons Learned
Don’t make these start earlier test earlier and so on.

## Slide 40: Questions (be sure to design your own)

## Slide 44: College of Engineering Color Palette
Pantone
2239 C
2239 C
Color Values:
RGB 0 207 180
Hex/HTML #00CFB4
CMYK 59 0 39 0
Pantone
2199 C
2199 C
Color Values:
RGB 0 187 220
Hex/HTML #00BBDC
CMYK 77 0 16 0
Pantone
1788 C
1788 C
Color Values:
RGB 238 39 55
Hex/HTML #EE2737
CMYK 0 88 82 0
Pantone
647 C
647 C
Color Values:
RGB 35 97 146
Hex/HTML #236192
CMYK 96 54 5 27
Pantone
2299 C
2299 C
Color Values:
RGB 164 210 51
Hex/HTML #A4D233
CMYK 41 0 84 0
Pantone
7535 C
7535 C
Color Values:
RGB 183 176 156
Hex/HTML #B7B09C
CMYK 10 11 23 19
CoE Dk Gray
75% Black
Color Values:
RGB 64 64 64
Hex/HTML #404040
CMYK 0 0 0 75
CoE Md Gray
50% Black
Color Values:
RGB 128 128 128
Hex/HTML #808080
CMYK 0 0 0 50
CoE Lt Gray
25% Black
Color Values:
RGB 191 191 191
Hex/HTML #bfbfbf
CMYK 0 0 0 25
Notes: Theses are the official color palettes of the college of engineering.

## Slide 45: PowerPoint Color Theme
Accent6
Pantone
2299 C
2299 C
Color Values:
RGB 164 210 51
Hex/HTML #A4D233
CMYK 41 0 84 0
Accent5
Pantone
7535 C
7535 C
Color Values:
RGB 183 176 156
Hex/HTML #B7B09C
CMYK 10 11 23 19
Accent4
Pantone
2239 C
2239 C
Color Values:
RGB 0 207 180
Hex/HTML #00CFB4
CMYK 59 0 39 0
Accent3
Pantone
1788 C
1788 C
Color Values:
RGB 238 39 55
Hex/HTML #EE2737
CMYK 0 88 82 0
Accent 2
Pantone
2199 C
2199 C
Color Values:
RGB 0 187 220
Hex/HTML #00BBDC
CMYK 77 0 16 0
Accent1
Pantone
647 C
647 C
Color Values:
RGB 35 97 146
Hex/HTML #236192
CMYK 96 54 5 27
Dark 2
CoE Dk Gray
75 % Black
Color Values:
RGB 64 64 64
Hex/HTML #404040
CMYK 0 0 0 75
Dark 1
Black
100% Black
Color Values:
RGB 0 0 0
Hex/HTML #000000
CMYK 0 0 0 100
Light 2
CoE Lt Gray
25% Black
Color Values:
RGB 191 191 191
Hex/HTML #bfbfbf
CMYK 0 0 0 25
Light 1
White
White
Color Values:
RGB 255 255 255
Hex/HTML #FFFFFF
CMYK 0 0 0 0
Notes: These are the college colors as prioritized within this PowerPoint Template

## Slide 46
Notes: This slide has the rule of third layout tool. The rule thirds layout helps with the sizing of elements.

## Slide 47
Notes: This slide has the rule of third layout tool. The rule thirds layout helps with the sizing of elements.