## Slide 1
Additive Manufacturing in Aerospace
Team 508:
David Jay Michael Nalovic Sofia Rodriguez Tristan Wahl
Notes: Don’t assume what is already done, further explain

## Slide 2
Additive Manufacturing in Aerospace
Team 508:
David Jay Michael Nalovic Sofia Rodriguez Tristan Wahl

## Slide 3: Meet Team 508
David Jay
Manufacturing Engineer
Tristan Wahl
Design Engineer
Michael Nalovic
Controls Engineer
Sofia Rodriguez
Aeronautics Engineer
Tristan Wahl

## Slide 4: Sponsors and Advisor
Dr. Yousuf Ali
Teaching Faculty II
Florida Space Grant Consortium
Seminole
RC Club
Tristan Wahl

## Slide 5: Project Objective
Design and manufacture an airplane capable of competing in the SAE Aero Design Competition.
Tristan Wahl
Notes: Try to stop

## Slide 6
01
AHERE TO SAE
GUIDELINES
Follow SAE competition rules and restrictions
Sponsor Needs
02
INNOVATION
Create a new and different design
03
3D PRINTED
PLANE
Majority of the plane must be made of 3D printed material
Tristan Wahl
Notes: Our primary customer for this project is our Senior Design Professor, Dr. McConomy. He gave us 3 primary needs:
-of course we need to comply with SAE competition guidelines
-We need to be innovative in some way or another. Incorporating new ideas wherever possible
-Finally, Dr. McConomy has specified that our plane must be 3D printed. This means that the majority of structural components must be 3D printed.

## Slide 7
01
AHERE TO SAE
GUIDELINES
Follow SAE competition rules and restrictions
Sponsor Needs
02
INNOVATION
Create a new and different design
03
3D PRINTED
PLANE
Majority of the plane must be made of 3D printed material
Tristan Wahl
Notes: Our primary customer for this project is our Senior Design Professor, Dr. McConomy. He gave us 3 primary needs:
-of course we need to comply with SAE competition guidelines
-We need to be innovative in some way or another. Incorporating new ideas wherever possible
-Finally, Dr. McConomy has specified that our plane must be 3D printed. This means that the majority of structural components must be 3D printed.

## Slide 8
01
AHERE TO SAE
GUIDELINES
Follow SAE competition rules and restrictions
Sponsor Needs
02
INNOVATION
Create a new and different design
03
3D PRINTED
PLANE
Majority of the plane must be made of 3D printed material
Tristan Wahl
Notes: Our primary customer for this project is our Senior Design Professor, Dr. McConomy. He gave us 3 primary needs:
-of course we need to comply with SAE competition guidelines
-We need to be innovative in some way or another. Incorporating new ideas wherever possible
-Finally, Dr. McConomy has specified that our plane must be 3D printed. This means that the majority of structural components must be 3D printed.

## Slide 9
01
AHERE TO SAE
GUIDELINES
Follow SAE competition rules and restrictions
Sponsor Needs
02
INNOVATION
Create a new and different design
03
3D PRINTED
PLANE
Majority of the plane must be made of 3D printed material
Tristan Wahl
Notes: Our primary customer for this project is our Senior Design Professor, Dr. McConomy. He gave us 3 primary needs:
-of course we need to comply with SAE competition guidelines
-We need to be innovative in some way or another. Incorporating new ideas wherever possible
-Finally, Dr. McConomy has specified that our plane must be 3D printed. This means that the majority of structural components must be 3D printed.

## Slide 10
Key Goals
Tristan Wahl

## Slide 11: Airplane Controls
Ailerons – Control Roll
1
Elevator – Controls Pitch
2
Rudder – Controls Yaw
4
Throttle – Controls Motor Thrust
3
Tristan Wahl
Notes: Change this to our plane
RC aircraft generally have at least the first 4, HOWEVER, some configurations can get away with only 3.

## Slide 12
Major Functions
Takeoff
Carry Payload
Flight Controls
Landing
Michael Nalovic
Notes: Animate this to go in a specific order
And correct the alignment

## Slide 13
Targets and Metrics
Takeoff Distance
Less than 100ft
Metric
Target
Control Surface Deflection
At least 25°
Metric
Target
Thrust Force
Greater than 10lbs
Metric
Target
Rise Time of Motor Speed
4 seconds
Metric
Target
Wing Area
Greater than 6 ft
Metric
Target
Static Margin
5%– 15%
Metric
Target
Takeoff
Flight Control
2
Michael Nalovic
Notes: Our team allowed the fuselage group to determine their own targets and metrics for the payload and landing gear, while we focused more on takeoff and controlling the plane. Here we have displayed some of the most important metrics that contribute to the aerodynamic success of the airplane.
Our takeoff distance was predefined by the competition guidelines. Using this metric, we made some initial estimates to calculated a required thrust force for the plane based on a wing with a 6ft^2 planform area. The only reason a minimum planform area is defined as a metric is because our calculations all began with that minimum assumption.
For control, the first metric we placed was a minimum control surface deflection. Typically control surfaces lose effectiveness past 20deg, so we design for a larger deflection that can be turned down on the transmitter. In addition, we also require that the motor selected has a minimum rise time of 4 seconds. This will ensure that the pilot has ample throttle control to get out of potentially dangerous situations. Finally, we have set a target for the static margin of the airplane. The static margin is an indicator of the airplanes pitch stability and should be between 5% and 15%

## Slide 14
Targets and Metrics
Securing
Motion Prevented
Metric
Target
Mechanical Taxi
Rudderless Control
Metric
Target
Load/Unload
Under 1 Minute
Metric
Target
Landing Distance
Less than 400 feet
Metric
Target
Geometrical Shell
Fully Encapsulated
Metric
Target
Shock Absorption
Intact Fuselage
Metric
Target
Carry Payload
Landing
Michael Nalovic
Notes: Our team allowed the fuselage group to determine their own targets and metrics for the payload and landing gear, while we focused more on takeoff and controlling the plane. Here we have displayed some of the most important metrics that contribute to the aerodynamic success of the airplane.
Our takeoff distance was predefined by the competition guidelines. Using this metric, we made some initial estimates to calculated a required thrust force for the plane based on a wing with a 6ft^2 planform area. The only reason a minimum planform area is defined as a metric is because our calculations all began with that minimum assumption.
For control, the first metric we placed was a minimum control surface deflection. Typically control surfaces lose effectiveness past 20deg, so we design for a larger deflection that can be turned down on the transmitter. In addition, we also require that the motor selected has a minimum rise time of 4 seconds. This will ensure that the pilot has ample throttle control to get out of potentially dangerous situations. Finally, we have set a target for the static margin of the airplane. The static margin is an indicator of the airplanes pitch stability and should be between 5% and 15%

## Slide 15
Analytical Validation
Michael Nalovic
Servicing and Repair
Fitment
Full System Integration
Control Surface Actuation
Finish
Adhesion Effectiveness
Weight
Meets Target Metric
Stable Static Margin
Notes: Static margin
Moving of soccer ball

## Slide 16
Flight Validation
Michael Nalovic
Reusability
Flight
Stability During Climb
Maneuverability for Flight Pattern
Landing
Durability During Impact
Responsiveness of Control Surfaces
Shock Distribution
Take Off
Mechanical Taxi
Propellor Clearance
High Lift
Notes: Static margin
Moving of soccer ball

## Slide 17: Material Selection
Lightweight PLA
Uses active foaming technology
  PLA + blowing agent the filament produces gasses when heated to 230 degrees Celsius
Reduces the weight of printed parts up to 65% compared to regular PLA
David Jay
Notes: big portion of our project is 3D printing since our sponsor required that 90% of our project be made of 3D printed material

## Slide 18: Material Selection
David Jay
our options
Notes: What Our options are

## Slide 19: Infill
Infill is the structure inside the piece that holds the model together
It is used to give strength to the printed model with the minimal use of material
It can be printed in varying degrees of hollowness known as infill density
David Jay
Notes: What

## Slide 20: Light Weighting
David Jay
Notes: Grow left one to emphasize cross section and do the same with the right one
4 step animation

## Slide 21: Weight Estimation
David Jay

## Slide 22: Concepts
Guppy
Dolphin
Whale
Sofia Rodriguez

## Slide 23: Whale Fuselage Design
Sofia Rodriguez

## Slide 24: Wing Design
Eppler 423 Airfoil
Low Wing
Hoerner Wing Tips
Tapered Wings
Sofia Rodriguez

## Slide 25: Tail Design
Conventional Tail
Cross Connection to Fuselage
Tail Dragger Landing Gear
Sofia Rodriguez

## Slide 26: Static Margin
Static margin is used to determine stability of the plane
Calculated from Center of Gravity to the neutral point
Ideal static margin would be between 5-15%
Sofia Rodriguez
Notes: Change the view to be side vide no tilt
Tilt one way

## Slide 27: Wings
Sofia Rodriguez
Airfoil selection: explain what is important
Sections separated
Should what the taper ratio indicates
Dihedral
Wingtips
Eppler 423 Airfoil
High lift coefficient due to the highly cambered profile
Designed for lower speeds
Smoother small due to the high lift coefficient

## Slide 28: Wings
Sofia Rodriguez
Airfoil selection: explain what is important
Sections separated
Should what the taper ratio indicates
Dihedral
Wingtips
Hoerner Wing Tips
Effective wingspan increases without increasing the geometric wingspan, therefore decreasing drag
Reduces distance required for take-off
Increases overall stability
Notes: https://www.myplane.nl/cherrydocs/THEORETICAL_ASPECTS_AND_PRACTICAL_US_AGE.pdf

## Slide 29: Wings
Sofia Rodriguez
Dihedral
Upward angle of aircraft’s wing, increases stability by causing the lower wing to fly at higher angle of attack compared to a high wing
5° Angle the wing makes with the horizonal
Provides the plane with roll stability
Notes: https://www.myplane.nl/cherrydocs/THEORETICAL_ASPECTS_AND_PRACTICAL_US_AGE.pdf
Taper and measurement

## Slide 30: Spar Selection and Connection
36
Sofia Rodriguez
Aluminum 6061
Lightweight
High Strength Characteristics
Higher Strength than circular spar
Spars will be connected by a bracket within the fuselage
6
Notes: Explain why we made these decisions
From where
Why

## Slide 31: Assembly Method
I-Beams were selected to hold the spars
Reduce and resist shear stress
Flanges act to prevent any bending or vibration that could occur during flight
Web securely hold the spars
Sofia Rodriguez
Notes: Show I beam bending, vibrating
Vibration – certain mass and stiffness selected to prevent vibrations
Bend – strength of I beam should accommodate yield stress
Buckling – flanges chosen to prevent buckling locally, sideways, or torsionally
Tension – web thickness that wont fail, buckle ,or ripple
Take out circle

## Slide 32: Manufacturing Wings
Figure 1: Top View of Wing
Figure 2: Bottom View
Sofia Rodriguez
Aileron
Control Surface
Landing Gear
Servo
Housing
and
Linkage
Notes: Include view of airfoil

## Slide 33: Tail
Tristan Wahl
Primary job of tail is to add stability to aircraft
  Compared with a T-tail and cruciform, the conventional tail was the simplest solution for achieving both structural and aerodynamic needs
  Knowing the span and planform area of the main wing, the areas of both vertical and horizontal sections could be calculated
Figure 3: T-tail, Cruciform and conventional tail setups

## Slide 34: Aero Design of Tail
Tristan Wahl
Figure 4: Tail Assembly
  Airfoil: NACA 0012
  Horizontal taper ratio: 0.50
  Vertical taper ratio: 0.33
  Horizontal area: 221.4 in2
  Vertical area: 86.4 in2
  20° of rudder and elevator actuation is ideal for low-speed aircraft

## Slide 35: Horizontal Tail
Entire airfoil held under tension with aluminum spar running through front part of sections
Elevator will be held by 2" aluminum pins and actuated by servo on underside of airfoil
20° of actuation in both directions
Tristan Wahl
Figure 5: Underside of Horizontal tail assembly
Notes: Add figure #s
Maybe split into two slides

## Slide 36: Vertical Tail
3D printed pins for rudder instead of aluminum
Connections to fuselage in front with cross style connection and in back with elliptical pin to allow for servo wiring
Tristan Wahl
Figure 6: Vertical Tail Assembly
Figure 7: Bottom view of vertical assembly
Notes: Add figure #s
Maybe split into two slides

## Slide 37: Tail Connections
Connection to the main fuselage using the horizontal spar
Cross style connection to provide vertical and horizontal stability
1
Tristan Wahl
Figure 8: Vertical Connector
Figure 9: Detail of Top View
Notes: Figure #

## Slide 38
CAD
SLICER
PRINTER
Manufacturing
David Jay
Notes: Although our concept selection process deemed the SR-22 best for our project, this design lacked in the major aspect of innovation. For the "Final" concept our team will be moving forward with, we decided to use the general layout of the SR-22 design with a new, more innovative fuselage that is better suited for our application.

## Slide 39
CAD
Design for 3D Printing
Design for 3D printing begins in the CAD software
Designers need to consider:
  Size limitations
  Print orientation
  Minimizing overhangs and bridges
  Tolerances
  Raster Orientation
David Jay
Notes: Make gears rotate and have plane appear

## Slide 40
SLICER
Slicing the Part
Slicing software converts CAD models into G-code
G-code files control all aspects of the print from nozzle temperature to movement speeds
Users must tune a variety of slicer settings to get strong and accurate prints
David Jay
Notes: Although our concept selection process deemed the SR-22 best for our project, this design lacked in the major aspect of innovation. For the "Final" concept our team will be moving forward with, we decided to use the general layout of the SR-22 design with a new, more innovative fuselage that is better suited for our application.

## Slide 41
PRINTER
Printing
FDM 3D Printers Work by depositing melted plastic onto a build plate
It can take several hours for the plastic layers to build up into a full part
Failures occur frequently and in many different forms
Proper G-code slicing and regular printer maintenance help to ensure higher print success rates
David Jay
Notes: Although our concept selection process deemed the SR-22 best for our project, this design lacked in the major aspect of innovation. For the "Final" concept our team will be moving forward with, we decided to use the general layout of the SR-22 design with a new, more innovative fuselage that is better suited for our application.

## Slide 42: Manufacturing Trials
Figure 10: Side view of layer Shift
Figure 11: Top view of layer shift
Figure 12: Example of Thermal Runaway
David Jay

## Slide 43: Finish Optimization
Michael Nalovic
Figure 13: Various sanding methods
Figure 14: Spray paint finish
Figure 15: Painting with epoxy finish
Notes: Put graphics

## Slide 44: Controls
Michael Nalovic
Servomotor Selection
Required Torque
Range of Motion
Fitment and Scale
Linkage Design
Four Bar analysis
Control Surface Integration
Weight Balance

## Slide 45: Thrust Test
Achieved approximately 9.5 lbs of thrust which correlates to about 42.3 Newtons
  Required force for liftoff: 10 N
Results for 2 Blade Propeller
Michael Nalovic

## Slide 46: Thrust Test
Achieved approximately 9.2 lbs of thrust which correlates to about 40.9 Newtons
  Required force for liftoff: 10 N
Results for 3 Blade Propeller
Michael Nalovic

## Slide 47: Comparison and Trade-offs
Michael Nalovic
Efficiency
Vibration
Clearance
Higher thrust to drag ratio for two blade
Less pulse per revolution for three blade
Similar thrust with extra clearance for three blade
Primary Selection
Secondary Selection

## Slide 48: Test Flight
Sofia Rodriguez
Location of Flight
Insurance Certificate
Weight of Plane
Pilot
Notes: Present or future?

## Slide 49
01
02
03
FILE SHARING
Use a collaborative file sharing program
PROJECT
METHODOLOGY
Improve the team’s methodology on deliverables
PROJECT
MANAGEMENT
Improve the team’s organization by continuing the use of the task manager
Lessons Learned
Sofia Rodriguez
Notes: Our primary customer for this project is our Senior Design Professor, Dr. McConomy. He gave us 3 primary needs:
-of course we need to comply with SAE competition guidelines
-We need to be innovative in some way or another. Incorporating new ideas wherever possible
-Finally, Dr. McConomy has specified that our plane must be 3D printed. This means that the majority of structural components must be 3D printed.

## Slide 50
Incomplete Work
01
02
03
Submit Test Flight
Request
Sofia Rodriguez
Conduct Test Flight
Final Assembly: Painting, Wiring,
and Gluing

## Slide 51
Summary
September
October
November
Finalize Goals and Functions
Begin Research and Concept Generation
Finalize Airfoil, Taper, and Wingtips Design
Select Final
Design
Build Thrust Test
Print
Prototypes
Sofia Rodriguez
Notes: Should this be included?

## Slide 52
Summary
December
January
February
Begin Tolerance Testing and Wing Printing
Finalize Tail
Design
Finish Wing Assembly
Submit Purchase Requests
Sofia Rodriguez
Size
Control Surfaces
Integration between
Team 507 and 508
Notes: Should this be included?

## Slide 53
Summary
February
March
April 7, 2022
Begin
Printing
the Tail
Finalize Tail
Attachment
Finish Tail
and
Begin Wiring
Final
Assembly
Test Flight
Buy
Wing Spars
Sofia Rodriguez
Notes: Should this be included?

## Slide 54
References
Dr. McConomy, S. (2021). Customer Needs.
“2022 SAE Aero Design Rules.” SAE Aero Design, www.saeaerodesign.com/cdsweb/gen/DocumentResources.aspx.
Raymer, D. P. (1992). Aircraft design: A conceptual approach.
Hermann, Stefan. “Colorfabb LW-Pla - Testing Foaming Pla.” CNC Kitchen, CNC Kitchen, 15 Feb. 2020, https://www.cnckitchen.com/blog/colorfabb-lw-pla-testing-foaming-pla.

## Slide 55
TEAM 508
David Jay
dmj17b@my.fsu.edu
Michael Nalovic
msn15@my.fsu.edu
Sofia Rodriguez
smr16n@my.fsu.edu
Tristan Wahl
trw17c@my.fsu.edu
Project Website

## Slide 56: Static Margin
Neutral point behind the CG, static margin is positive
Ideal, would be %
Blank Blank
Notes: Change the view to be side vide no tilt
Tilt one way

## Slide 57: Static Margin
Neutral point forward of the CG, static margin is negative
How is it determined
Ideal, would be %
Blank Blank
Notes: Change the view to be side vide no tilt
Tilt one way

## Slide 58: Determining CG
David Jay
Photoshop me later
Notes: Put graphics

## Slide 59: TEAM 508 COLORS
Accent6
Pantone
2299 C
2299 C
Color Values:
RGB 164 210 51
Hex/HTML #A4D233
CMYK 41 0 84 0
Accent5
Pantone
7535 C
7535 C
Color Values:
RGB 183 176 156
Hex/HTML #B7B09C
CMYK 10 11 23 19
Accent4
Pantone
2239 C
2239 C
Color Values:
RGB 0 207 180
Hex/HTML #00CFB4
CMYK 59 0 39 0
Accent3
Pantone
1788 C
1788 C
Color Values:
RGB 238 39 55
Hex/HTML #EE2737
CMYK 0 88 82 0
Accent 2
Pantone
2199 C
2199 C
Color Values:
RGB 0 187 220
Hex/HTML #00BBDC
CMYK 77 0 16 0
Accent1
Pantone
647 C
647 C
Color Values:
RGB 35 97 146
Hex/HTML #236192
CMYK 96 54 5 27
Dark 2
CoE Dk Gray
75 % Black
Color Values:
RGB 64 64 64
Hex/HTML #404040
CMYK 0 0 0 75
Dark 1
Black
100% Black
Color Values:
RGB 0 0 0
Hex/HTML #000000
CMYK 0 0 0 100
Light 2
CoE Lt Gray
25% Black
Color Values:
RGB 191 191 191
Hex/HTML #bfbfbf
CMYK 0 0 0 25
Light 1
White
White
Color Values:
RGB 255 255 255
Hex/HTML #FFFFFF
CMYK 0 0 0 0
Notes: These are the college colors as prioritized within this PowerPoint Template

## Slide 60: Horizontal Tail
Elevator will increase by 5" to account for fuselage connection
Elevator will be held by 2" aluminum pins and actuated by servo on underside of airfoil
20° of actuation in both directions
Figure 5: Horizontal Tail Assembly
Tristan Wahl

## Slide 61: SERVO

## Slide 62: LWPLA more info
Notes: CNC kitchen data

## Slide 63: Tolerance Testing Data

## Slide 65: Concept Generation
Fuselage Type
Airfoil
Wing Placement
Landing Gear
Tail
Wing Tips
"Guppy"
"Dolphin"
"Whale"
E-423
S-1223
High Wing
Mid Wing
Low Wing
Tricycle
Tail Dragger
Standard
T-Tail
V-Tail
Cutoff
Hoerner
Upswept
Tristan Wahl
Notes: In order to come up with multiple concept ideas, we started with a morphological chart with our initial design ideas.
We decided the 3 fuselage concepts from our prototypes, the airfoils from their data and earlier research, the wing placements and their various tradeoffs, the 2 landing gear setups, types of tails and eventually wingtips to help with our innovation requirement
http://www.zenithair.com/stolch801/design/design.html

## Slide 66: Medium Fidelity Concepts
Concept 1
  Air Tractor AT-502B
Concept 2
  Cessna 208B
Concept 3
  Cirrus SR-22
Concept 4
  Vans Aircraft RV-14
Fig.1 Air Tractor
Fig. 2 Cessna 208B
Fig. 3 Cirrus SR-22
Fig. 4 Vans Aircraft RV-14
Tristan Wahl
Notes: Talking Points: Wing Placement, Fuselage design, Landing Gear Configuration. They all meet certain criteria of our morphological chart and would be easier to scale down a version than to create an altogether original design. We list them as medium fidelity concepts because scaling down an existing design is not very innovative
Reference: https://www.texascooppower.com/texas-stories/life-arts/the-building-of-a-bird
https://en.wikipedia.org/wiki/Cessna_208_Caravan

## Slide 67: Concept Selection
Customer needs were broken down into engineering characteristics
Importance weight factor calculated for each engineering characteristic to determine which are most vital to success
David Jay
Customer Needs
Comply with SAE guidelines
Engineering Characteristics
Weight
Control Surface Deflection
Static Margin
Thrust Force
Resistance to stress
Innovate
3D Printed
Notes: Most of our engineering characteristics come from the SAE competition guidelines. 5 of the most important engineering characteristics are listed here.
We want to:
-Decrease Weight
-Constrain control surface deflection
-Constrain static margin
-Increase Thrust force
-Increase resistance to stress (make sure the plane doesn’t break under loading)

## Slide 68: Concept Selection
0.524
0.476
Cirrus SR-22
Vans Aircraft RV-14
Alternative Values Calculated from Selection Process
David Jay
Notes: After going through multiple iterations of the concept selection process, we narrowed it down to two candidates. In the end, the Cirrus SR-22 won by a small margin against the Vans RV-14. Both concepts are extremely similar, which makes sense why they are so close in selection values.
One thing to note is that concept selection for an entire airplane is not a trivial task. Almost every decision affects the aerodynamics of the plane and there are thousands of decisions that could be made. Our team used this concept selection process to decide on a final layout of the plane rather than specific details. In addition, nothing scales perfectly, so it’s very likely that our final design differs as we iterate and reanalyze.
If we were to do this project again, we may consider doing a concept selection process for each aspect of the plane, rather than the entire design.

## Slide 69: SAE Guidelines

## Slide 70: Lift/Velocity Estimations
Thrust Force (Ft)
Drag Force
Equations of Motion: