## Slide 1: Team 114
Notes: Customize your title slide to be appealing to the audience. This is the first thing they see apply some graphic design elements that may summarize your presentation.

## Slide 2: Team Members
Valeria Aguilera
Ethan Corey
William Crittenden
Matthew Mohammed
Alexandra Nowzamani
Nickolas Wolniewicz

## Slide 3: Sponsor and Advisors
Project Sponsor Tom Vanasse, Director of Engineering, Exactech
Academic Advisor Stephen Arce, Ph.D.
Professor, FAMU – FSU Engineering
Academic Advisor Shayne McConomy, Ph.D.
Professor, FAMU – FSU Engineering

## Slide 4: Project Objective
The objective of this project is to design a stemless reverse shoulder prosthetic to reduce micromotion and formulate a series of tests to appropriately evaluate the design.

## Slide 5: Total Shoulder Replacement
Purpose:
To reduce shoulder pain and restore mobility and range of motion by replacing portions of the shoulder joint with an artificial implant.

## Slide 6: Key Goals
Induces no immune response.
Implant has Young's modulus approximately: 10-30 GPa.
Pore sizes approximately: 600 µm.
Neck-shaft angle: 135° to 145°.
Humeral Head radius between 20-25 mm.
Insertion requires less than: 1 MPa.
Maximum Length of design: 70 mm.
Glenosphere size: 40-42 mm.

## Slide 7: Customer Needs
Prevents lever out
Prevents micromotion
No device failure
No bone fracture
Easy revision
Immune response
Ease of implantation

## Slide 8: Types of Implants
Stemless Implant
Stemmed Implant

## Slide 9: Stemless Shoulder Implant
Benefits:
More Anatomic.
Reduces Stress Shielding.
Less Bone Removal.
Good Mid to Long-Term Results.

## Slide 10: Inlay vs. Onlay
Inlay - the lowest point of the humeral tray sits at or below the humeral cut.
Onlay - the lowest point of the humeral tray sits above the humeral cut.
Inlay
Onlay

## Slide 11: Reverse Stemless Shoulder Implant
Potential Benefits:
Prevents rotator cuff damage.
Better mechanics for your rotator cuff.
Uses mainly the deltoid instead.

## Slide 12: Research Update
Interview with Mr. Thomas Vanasse
Toured Exactech Facility in Gainsville, FL

## Slide 13: Research Update Cont'd

## Slide 14
Primary Characteristics
  Biomechanics
  Manufacturability
  Marketability
  Surgery
  Biocompatibility
  Implant Design
Mind Map

## Slide 15
Cold Shoulders
Attachment
Manufacturability
Surgery
Screws
Fins
Insertion Technique
Impaction (press-fit)
Compression
Biocompatibility
Single Linked Joint
Biomaterials
Immune response
Sizes
Elastomeric polyamide
Polyethylene
Ceramics
Composites
Metals
Polymers
Implant Design
Anchor
Vitamin E
Hydroxyapatite
Surface Coatings
CoCrMo
Ti-6Al-4V
Modifications
Unlinked joint
“Hinge”
Inlay
Cup
Humeral Tray
Surface porosity
Onlay
Cage
Hemisphere
Autograft
Pegged
Keeled
Augmented
Glenoid Component
Glenosphere
Porosity
Facilitated Bone growth
Short time
Increased Lateral Offset
Minimal bone removal
Recovery
Sphere
Bone
On-growth
Bone Ingrowth
Peripheral Screws
Increased angle of insertion
Increase range of motion
Decreased micromotion
Biomechanics
Surface Coating
Cage
Marketability
Neck-shaft angle
FDA
Improved quality of life
Decreasing Lateral Offset
Increased Diameter or Length
Irregular
Practicality
Cost
Adaptability
Equipment
Regulations
Molding
3D printing
Casting
New
Already owned
Methods
Short Surgery time
Easier revision
Made with Exactech parts
Landscape
Review
IDE
510(k)
ISO 104933
Patents
Forging
Universal
All types
Dual Design
Reverse Stemless
Single design
Bone stability
Painless arm usage
Increased range of motion
Versatility
Anatomical Stemless
Reverse stemless

## Slide 16: Concept Generation
Crapshoot Method:
Allows for concepts to be quickly generated.
Concepts are capable of being creative.
Many concepts may be difficult to implement.
Forced Analogy:
Allows for concepts to be derived from only 2 words.
Creates concepts without previous bias.
Concepts are usually unrealistic.

## Slide 17: Crapshoot Method Examples:
A ratcheting system to secure glenoid component.
A spring component to reduce dislocation.
Coating the base to increase native tissue affinity.

## Slide 18: Forced Analogy Method Examples:
Increasing or decreasing the cage radius.
Parabolic-shaped glenoid or head component.
Modular head or adjustable glenoid during surgery.

## Slide 19: Concepts
Pugh Chart
Exactech Design
Twist/Screw
T-Shaped
Rigid
Anchor

## Slide 20: Concept Selection
Generated
Concepts
House of Quality
Pugh Chart

## Slide 21: House of Quality

## Slide 22: Pugh Chart Part 1

## Slide 23: Pugh Chart Part 2

## Slide 24: Pugh Chart Part 3

## Slide 25: Pugh Chart Part 4

## Slide 26: Next Steps
Build CAD models.
Build and test PLA prototypes.
Build and test aluminum prototypes.