## Slide 1: Smart Projectile
Jack Corbin | Prosley Dorcely | Emily Groth
Deepkumar Patel | Aaron Weingarten

## Slide 2
Prosley Dorcely
Hardware Engineer
Jack Corbin
Fin Engineer
Emily Groth
Assembly Engineer
Deepkumar Patel
Design Engineer
Aaron Weingarten
Systems Engineer
Team 509
Deepkumar Patel

## Slide 3
Dr. Rajan Kumar
Sponsor
Dr. Jonas Gustavsson
Advisor
Robert Smith
Advisor
Sponsor and Advisor
Deepkumar Patel

## Slide 4: Objective
The objective of the project is to create a scale model of a projectile with an articulating nose cone and deflectable fins for subsonic wind tunnel testing.
Deepkumar Patel
Deepkumar Patel

## Slide 5: FCAAP Existing Model
Previous project just dealt with nose deflection.
Deepkumar Patel
Excess weight caused sagging
Fins are not deflectable​
​
Excess current lead to overheating and reduced test time​
Vibration from articulation mechanism​

## Slide 6
Critical Targets and Metrics
θ
Nose deflection between 0 to 5 degrees with resolution ±0.1
Dynamic deflectable fins between 0 to 30 degrees
Time constant optimized to less than 0.5 seconds
Deepkumar Patel

## Slide 7: Assumptions
Assumption 1
Assumption 2
Gravitational force will be far greater than the aerodynamic forces.
Assumption 3
No shockwaves will be produced (subsonic and incompressible)
Model has access to an outside power supply and controls.
Deepkumar Patel

## Slide 8: Nose Cone Light Weighting
Original Model:
Weight: 270g
Simple light weighting can be machined in house
Sintering Light Weight Model:
Weight: 148g
Complex geometries require a method of additive manufacturing
Deepkumar Patel

## Slide 9: Motor Housing
The motors must fit between the support shaft and the inner wall of the outer body
Requirements:
5 grams or less
Under 0.65 in Diameter
Diameter of support shaft is 0.5 inches
Inner diameter of outer body is 1.8 inches
Jack Corbin

## Slide 10: Motor Selection
Specially modified to provide access to the feedback potentiometer through a fourth (green) wire, allowing you to directly measure the position of the output.
FEETECH Sub-Micro Servo FS0403-FB
Specs:
5 Grams
0.79 x 0.76 x 0.33 in
Positional Feed back
Jack Corbin

## Slide 11: Gear Selection
Plastic Miter Gears
18 teeth
Nylon plastic
Gear pitch: 48
Jack Corbin

## Slide 12: Fin Attachment
Method 1
Weld a large short shaft to end of fin
Brittle connection
Possible manufacturing problem when cleaning up connection surface
Method 2
Drill hole in each fin and insert a smaller shaft inside
Might be weaker and compromise the fin
Shaft would fail from bending
Jack Corbin

## Slide 13: Fin Attachment
Jack Corbin
Fins
Attachment
Back Body
Hole is drilled....

## Slide 14: Gear Connections
Jack Corbin
Fins
Attachment
Back Body
Shaft connects gears to Servo

## Slide 15: Fin Assembly
Jack Corbin
Fins
Attachment
Back Body
Hole is drilled....

## Slide 16
Right Side View
Back View
Prosley Dorcely
Fin Motor Configuration
Prosley Dorcely

## Slide 17: Motor Configuration
CAD model for the motors and gears configuration
Angled View
Back View
Prosley Dorcely

## Slide 18: Parts that Need to be Machined Again
Back fin body
Frontal Motor Mount
Frontal Deflecting Surface
Rear Deflecting Surface
Mounting Hub
Prosley Dorcely

## Slide 19: Budget
Item​ | Price​
6 FEETECH sub-micro servo FS0307​ | $39.00​
2 FEETECH sub-micro servo fs0403-fb with position feedback​ | $20.50​
10 plastic miter gears​ | $79.90​
Xometry​ for the Nose Cone | $1000.00​
Prosley Dorcely
Budget | $2000.00
Spent | $1138.90
Left | $861.10

## Slide 20: Next Steps
March
Machining
Assembly
Testing
Update Code
Prosley Dorcely
April
Final Testing
Senior Design Day
Celebration

## Slide 21
Thanks for listening
Jack
Corbin
Prosley Dorcely
Deepkumar Patel
Aaron
Weingarten
Emily
Groth
Prosley Dorcely

## Slide 22: Markets and Stakeholders
Air Force
Boeing
Raytheon
Lockheed Martin
General Dynamics
College of Engineering
Dr. Jonas Gustavsson
Dr. Rajan Kumar
Dr. Shayne McConomy
Dr. Suvranu De
FCAAP
Emily Groth

## Slide 23: Fin Deflection
Implement four small motors to control each individual fin
Lack of space in the rear portion of the model
Need to find motors that are small enough to fit in body and have high precision
Aaron Weingarten

## Slide 24: Fin Motor Configuration 1 (Update with new CAD)
Right Side View
Back View
Prosley Dorcely

## Slide 25: Nose Cone Light Weighting (Update on Sintering?)
Original Model:
Weight: 270g
Simple light weighting can be machined in house
Alternative Drilling Model:
Weight: 260g
Small weight reduction not worth extra complexity
Emily Groth

## Slide 26: Future Work
Prosley Dorcely

## Slide 27: Customer Needs Backup

## Slide 28: Markets Backup
Primary Market
  FCAAP (Florida Center for Advanced Aero Propulsion)
Secondary Markets
  Air Force Office of Scientific Research (AFOSR)
  Air Force Research Laboratory (AFRL)
  Lockheed Martin
  General Dynamics
  Raytheon Technologies
  Boeing
  Northrop Grumman

## Slide 29: Stakeholders Backup
Florida Center for Advanced Aero Propulsion
FAMU-FSU College of Engineering
Dr. Rajan Kumar
Dr. Jonas Gustavsson
Dr. Shayne McConomy
Dr. Suvranu De

## Slide 30: Standard Shapes
Summary Box
Text box 1
Outlined Text Box

## Slide 31: Approved Logos

## Slide 32: Color Palette

## Slide 33: APA Tables
Category 1 | Category 2 | Category 3 | Category 4 | Category 5
Item 1 |  |  |  | 
Item 2 |  |  |  | 
Item 3 |  |  |  | 
Item 4 |  |  |  | 
 | Category 2 |  |  | Category 3 | 
Category 1 | subcategory 1 | subcategory 2 |  | subcategory 1 | subcategory 2
Item 1 |  |  |  |  | 
Item 2 |  |  |  |  | 
Item 3 |  |  |  |  | 
Item 4 |  |  |  |  |