## Slide 1: Team 502
NASA Student Launch
Virtual Design Review (VDR) 2

## Slide 2: Team Introductions
Nicholas Hux
Airframe Design Engineer
Connor Zhou
Controls Engineer
Jacob Miller
Avionics/Software Engineer
Jacob Schmitt
Systems Engineer
Atzimba Avellaneda Fabrication Engineer
Everyone

## Slide 3: Sponsors and Advisor
Sponsor
Shayne McConomy, Ph.D.
Professor
Academic Advisor
Chiang Shih, Ph.D.
Professor
Sponsor
William Oates, Ph.D.
ME Dept. Chair
Connor Zhou

## Slide 4: Objective
The objective of this project is to design, fabricate, and fly a high-powered rocket for competition in the 2024 NASA Student Launch. The vehicle will deliver a payload to a specified altitude, deploy it, and then be recovered safely.
Connor Zhou

## Slide 5: Project Background
Research-based and competitive challenge that supports NASA Space Launch System and Artemis mission.
Student teams across the U.S. design, build, test, and launch a high-powered rocket with an engineering payload.
Connor Zhou

## Slide 6: Key Goals
Demonstrate a successful sub-scale & full-scale flight.
Assemble and launch the vehicle at the official competition in Huntsville, Alabama.
Engage students to interact with STEM activities.
Complete all reports and ensure they are turned in before their due date or on their due date.
Connor Zhou

## Slide 7: Functional Decomposition
Rocket
Propulsion
Avionics
Structure
Aerodynamics
Structural integrity
Payload
Deployment
Control
Retention
Propulsion
Detach payload from vehicle
Reduce vibrations
Accelerates vehicle
Sensing
Secure STEMnauts throughout flight
Allow for ingress/egress after landing
Stabilization
Generate thrust
Dissipation
Dissipate kinetic energy during payload descent
Stabilize payload during flight
Land in desired orientation
Minimize kinetic energy upon landing
Recovery
Deploy drogue parachute at apogee
Deploy main parachute at appropriate height
Measure vehicle altitude and velocity
Store flight data
Receive signal
Decelerate vehicle
Generate gravity opposing force
Minimize aerodynamic stresses
Reduce drag forces
Generate force for stage separation
Location tracking
Launch Vehicle
Recieves launch signal
Ignites propellant
Expels matter
Measure location data
Transmit location data
Secures parachutes to vehicle
Recieve deployment signal
Recieve deployment signal
Keep stages together on ascent
Resist Yaw
Resist Pitch
Connor Zhou

## Slide 8: Functional Decomposition
Rocket
Propulsion
Avionics
Structure
Aerodynamics
Structural integrity
Reduce vibrations
Accelerates vehicle
Sensing
Generate thrust
Recovery
Deploy drogue parachute at apogee
Deploy main parachute at appropriate height
Measure vehicle altitude and velocity
Store flight data
Minimize aerodynamic stresses
Reduce drag forces
Generate force for stage separation
Location tracking
Launch Vehicle
Recieves launch signal
Ignites propellant
Expels matter
Measure location data
Transmit location data
Secures parachutes to vehicle
Recieve deployment signal
Recieve deployment signal
Keep stages together on ascent
Resist Yaw
Resist Pitch
Connor Zhou

## Slide 9: Functional Decomposition
Rocket
Payload
Deployment
Control
Retention
Propulsion
Detach payload from vehicle
Secure STEMnauts throughout flight
Allow for ingress/egress after landing
Stabilization
Dissipation
Dissipate kinetic energy during payload descent
Stabilize payload during flight
Land in desired orientation
Minimize kinetic energy upon landing
Receive signal
Decelerate vehicle
Generate gravity opposing force
Connor Zhou

## Slide 10: Senior Design Deliverable Updates
Targets &
Metrics
Concept
Generation
Concept
Selection
Connor Zhou

## Slide 11: Targets & Metrics
Function | Target | Metric
Generate thrust. | <5120 Ns | Impulse
Measure vehicle altitude and velocity. | 20 Hz | Frequency
Store flight data. | 1 MB | Memory
Deploy drogue chute. | 1491 m | Altitude
Deploy main chute. | 167 m | Altitude
Minimize aerodynamic stress. | 340 Ma | Yield strength
Reduce drag. | 0.29 | Drag coefficient
Reduce excess vibrations. | 0.8 Ns/m | Coefficient of damping
Detach payload from vehicle. | 120-240 m | Altitude
Secure STEMnauts in payload flight. | 2 mm | Positional margin
Connor Zhou

## Slide 12: Concept Generation
Biomimicry
Crap Shoot
Forced Analogy
Battle of Perspectives
Morphological Chart
Nick Hux

## Slide 13: Concept Generation - Medium Fidelity
Solid propellant motor, ogive nose cone, parabolic tail cone, blue tube structure, dual-stage deployment, and off-the-shelf altimeters for flight control.
Solid propellant motor, a conic nose cone, conic tail cone, an aluminum structure, three-stage deployment, and an assortment of sensors.
Solid propellant motor, parabolic nose cone, parabolic tail cone, Blue Tube body, single-stage deployment, and off-the-shelf altimeter.
Nick Hux

## Slide 14: Concept Generation - High Fidelity
Dual deployment rocket with an elliptical nose cone and conic tail cone. Solid propellant motor with G12 fiberglass body structure.
Dual deployment rocket with an Ogive nose cone and parabolic tail cone. Solid propellant motor with G12 fiberglass body structure.
Dual deployment rocket with Haack series nose cone and parabolic tail cone. Solid propellant motor with Blue Tube body structure.
Nick Hux

## Slide 15: Design Feature Pictures
Ogive Nosecone
Elliptical Nosecone
Haack Series Nosecone
Conical Tailcone

## Slide 16: Concept Selection
Pairwise Comparison
House of Quality
Pugh Chart
Analytical Hierarchy
Nick Hux

## Slide 17: Pairwise Comparison Output
Customer Needs | IWF | Customer Needs | IWF
Can withstand flight stresses. | 16 | Prioritize aspects neglected in previous years. | 9
Has correct licenses and permits. | 13 | Payload deploys between 400ft - 800ft. | 9
Can track and store flight data. | 13 | Vehicle reaches specified altitude. | 6
Minimizes danger to surroundings. | 12 | STEMnauts land safely without parachute. | 6
Vehicle/Payload recovered safely. | 12 | Detailed design reports are submitted. | 5
NRA/TRA certified ascent. | 11 | Landing velocity of < 25 ft/s. | 4
All components function intentionally. | 11 | Mass distribution tracked. | 2
Operates up to 5280ft altitude. | 10 | Materials and parts tracked. | 2
Trackable after flight. | 10 | No size requirements. | 2
Customer Needs
Comparison
Importance Weight Factor
Nick Hux

## Slide 18: House of Quality Output
Engineering Characteristics to Pugh Chart
Measure vehicle altitude and velocity.
Generate thrust.
Deploy drogue parachute.
Deploy main parachute.
Minimize aerodynamic stress.
Secure STEMnauts in payload flight.
Customer Needs
Engineering Characteristics
Nick Hux

## Slide 19: Pugh Chart Outputs
Concepts
2 stage powered ascent.
Concepts – Pugh 1
Blue Tube body, Ogive features.
Concepts – Pugh 2
Blue Tube body, Ogive features.
Aluminum body, conic features.
Blue Tube body, Ogive features.
Blue Tube body, parabolic features,
Fiberglass body, elliptical features.
Blue Tube and ASA body, Haack series features.
Fiberglass and PETG body, Ogive features.
Blue Tube body, parabolic features.
Hollowed out components.
Blue Tube and ASA body, Haack series features.
Fiberglass and PETG body, Ogive features.
Blue Tube body, parabolic features.
Fiberglass and PETG body, Ogive features.
Hollowed out components.
Nick Hux

## Slide 20: AHP Output
Criteria Weights
Design Alternate Priority
Alternate Value
Final Selection
Jake Miller

## Slide 21: Concept Selection
Rocket
The selected vehicle concept is a dual-deployment design.
L class solid propellant motor.
G12 fiberglass body with ASA 3D-printed parabolic tail cone and Ogive nose cone.
Payload
Thrust-vectoring monocopter design.
Servo-actuated fins to control descent.
Jake Miller

## Slide 22: NASA Deliverable Updates
Preliminary Design Review.
Sub-scale vehicle.
Critical Design Review.
Jake Miller

## Slide 23: Preliminary Design Review (PDR)
PDR report, presentation, and flysheet were completed and turned in on October 26th.
PDR was presented to NASA on November 15th.
Jake Miller

## Slide 24: Sub-scale Vehicle Overview
Parts, Fabrication, and Testing
Bill of materials finalized for subscale vehicle, recovery, and avionics.
Parts sent to Pro Hruda and are currently arriving.
Fabrication and testing with Zenith team has begun.
Flight Schedule
Subscale flight scheduled December 9th.
Backup subscale flight date set for December 16th.
Successful subscale flight deadline January 8th.
Jake Miller

## Slide 25: Sub-scale Vehicle Design
Airframe
G12 fiberglass body material.
PETG 3D-printed Ogive nose cone.
PETG 3D-printed parabolic tail cone.
Recovery
Dual deployment stage separation.
Separation achieved with black powder and CO2.
Avionics
Off-the-shelf AIM3 and TeleMetrum altimeters.
Jake Miller

## Slide 26: Critical Design Review (CDR)
CDR report, presentation, and flysheet due on January 8th.
Contains sub-scale flight data analysis, iteration on payload, and full-scale vehicles.
Jake Miller

## Slide 27: Future Work
Payload fabrication, testing, and iteration.
Sub-scale launch and possible backup launch.
Spring Project Plan.
Full-scale fabrication and test launches.
Critical Design Review (CDR).
Flight Readiness Review (FRR).
Team Semester Review.
Jake Miller

## Slide 28: Questions?
Thank you!

## Slide 29: Backup Slides

## Slide 31
This is 10-point
This is 15–point Times
This is 20–point
This is 25–point
This is 30–point
This is 35–point
This is 40–point
This is 50–point
This is 60–point
This is 72–point
Notes: Use at least 20-point font in Room A105, B134, and B136
Use at least 25-point font in Room B135

## Slide 32: College of Engineering Color Palette
Fang
Orange
RGB: 238, 118, 36
Hex: #EE7624
CMYK:2, 66, 99, 0
1 2 3 4
1 2 3 4
White
Pantone: PMS 000C
RGB: 255, 255, 255
Hex: #FFFFFF
CMYK: 0, 0, 0, 0
1 2 3 4
Black
Pantone: Black C
RGB: 0, 0, 0
Hex: #000000
CMYK:0, 0, 0, 100
Garnet
Pantone: PMS 195 C
RGB: 120, 47, 64
Hex: #782F40
CMYK:19, 90, 50, 55
1 2 3 4
Notes: Avoid 75% Black in B135

## Slide 33: Accent Color Palette
1 2 3 4
Tardis Blue
RGB: 0, 59, 111
Hex: #003B6F
CMYK:
1 2 3 4
Turquoise
RGB: 64, 224, 208
Hex: #40E0D0
CMYK:
1 2 3 4
American Orange
RGB: 255, 139, 0
Hex: #FF8B00
CMYK:
Rubine Red
RGB: 206, 0, 88
Hex: #CE0058
CMYK: 0, 100, 43, 12
1 2 3 4
1 2 3 4
Asagi-iro
RGB: 72, 146, 155
Hex: #48929b
CMYK:
1 2 3 4
Gainsboro
RGB: 220, 220, 220
Hex: #DCDCDC
CMYK:
1 2 3 4
Corn
RGB: 251, 236, 93
Hex: #FBEC5D
CMYK:
1 2 3 4
Timberwolf
RGB: 219, 215, 210
Hex: #DBD7D2
CMYK:
Imperial
RGB: 104, 40, 96
Hex: #682860
CMYK:
1 2 3 4
1 2 3 4
Tardis Blue
RGB: 0, 59, 111
Hex: #003B6F
CMYK:
Rubine Red
RGB: 206, 0, 88
Hex: #CE0058
CMYK: 0, 100, 43, 12
1 2 3 4
1 2 3 4
Corn
RGB: 251, 236, 93
Hex: #FBEC5D
CMYK:
1 2 3 4
Timberwolf
RGB: 219, 215, 210
Hex: #DBD7D2
CMYK:
Notes: Remove American orange add hyperlink grey
Make corn the last for b135
All work in 134 imperial move later
Tardis doesn’t work in b136

## Slide 34
https://color.adobe.com/create/color-wheel
Analogous
F7AB19
D67F15
EE7624
D64615
F73119
Monochromatic
6E3610
F0A16C
EE7624
6E4931
BASB1C
Triad
A14508
4BED3B
EE7624
250CED
2010A1
Complementary
FF8C40
EE7624
0098A1
24E2ED
A1470C
Split Complementary
28A164
2FED8D
EE7624
0848A1
1871ED
Double Split Complementary
3BED93
EE7624
0C6AED
ED2F18
EDAC2F
Square
C7ED3B
EE7624
0CE1ED
A418ED
ED660C
Compound
87724A
EE7624
60EFCF
09BA61
BA7E09
Shades
6E3610
EE7624
FA7625
D46820
AD551A
Notes: These are the variants that work well with Fang Orange. The bolded items show well on the projectors.

## Slide 35
https://color.adobe.com/create/color-wheel
Analogous
85412D
8F3831
782f40
8F3176
792D85
Monochromatic
C44D69
8E626D
782F40
C48796
451B25
Triad
C43959
78743B
782F40
236178
43A2C4
Complementary
C46078
782F40
25C43D
2F783A
C43959
Split Complementary
93C460
577835
782F40
39C49D
297861
Double Split Complementary
5A783B
782F40
237860
6E2978
784435
Square
78683b
782F40
237830
293978
782337
Compound
DEBAAF
782F40
5D8555
70AB32
AB4D32
Shades
C44D69
782F40
853447
5E2532
38161E

## Slide 36
B135 Stage Right
A105
A105
B135 Stage Left
B135
B134, A105
B136