## Slide 1: Full-Scale Flight 3
Launched again on March 9th.
Epoxied broken fin from last flight.
Parachute lines resized.
Atzimba Avellaneda

## Slide 2: Flight 3 – Launch
Stable flight profile.
Launch angle: 5˚.
Wind speed: 16-mph.
Burn time: 2.27-s.
Atzimba Avellaneda
Notes: This is a convience slide, I broke the video into takeoff, drogue deploy, main deploy, and landing

## Slide 3: Flight 3 – Drogue Chute Deployment
Drogue parachute deployed at apogee.
Descent rate: 85-ft/s.
  Predicted rate: 97-ft/s.
Atzimba Avellaneda
Notes: This is a convience slide, I broke the video into takeoff, drogue deploy, main deploy, and landing

## Slide 4: Flight 3 – Main Chute Deployment
Main parachute deployed above 500-ft.
Descent rate: 11-ft/s.
  Predicted rate: 13-ft/s.
Atzimba Avellaneda
Notes: This is a convenience slide, I broke the video into takeoff, drogue deploy, main deploy, and landing

## Slide 5: Flight 3 – Landing
Landed softly in tall grass. Kinetic energy of 45 ft-lbf.
No damage to launch vehicle or parachutes.
Atzimba Avellaneda
Notes: This is a convience slide, I broke the video into takeoff, drogue deploy, main deploy, and landing

## Slide 6: Full Scale Flight 3 - Analysis
Solved the parachute packing problem.
Fixed Cord length.
Flight was complete success.
Atzimba Avellaneda