## Slide 1: Virtual Design Review 2
Team 513
Automated Shaft Flux Measurement Device

## Slide 2: Team Introductions
Andrew Atallah
Hardware Engineer
Liora Louis
Materials &
Test Engineer
Sean Hemstreet
Design Engineer
Joshua Huls
Systems Engineer
Andrew Atallah

## Slide 3: Sponsor and Advisor
Engineering Mentor
Cole Gray
Mechanical Design Engineer
Academic Advisor
Dr. Shayne McConomy
Senior Design Professor
Engineering Mentor
William Bilbow
Director of Technology & Project Manager
Andrew Atallah

## Slide 4: Objective
The objective of this project is to design a device that will be capable of fully measuring and recording the magnetic flux of compressor shafts in an automated way that allows for accurate measurements, repeatability, and less overall firsthand work for the operator.
Andrew Atallah

## Slide 5: Danfoss VT Series Shaft
Perimeter: 314 mm
Axial Length: 174 mm
5 mm Increments
~63 Measurements
~35 Measurements
2,200 Entries Per Test!
Andrew Atallah

## Slide 6: Fluxmeter
Andrew Atallah

## Slide 7: Primary Market
Andrew Atallah

## Slide 8: Secondary Market
Competing Companies
Research Facilities
Andrew Atallah

## Slide 9: Key Goals
Automation
Consistency
Adaptability
Accuracy
Andrew Atallah

## Slide 10: Assumptions
Device is used over a period of 3 months per year.
MATLAB or an open-source software.
Given one working fluxmeter and sensor.
Testing will be performed at Danfoss.
Operator will be able to lift the shaft onto device.
Andrew Atallah

## Slide 11: Functional Decomposition
AFM
Human Interaction
System
Controls
Andrew Atallah

## Slide 12: Targets and Metrics
Secures Sample
Repeatability
Structural Durability
Data Transfer
Resolution (5mm)
Andrew Atallah

## Slide 13: Targets and Metrics
Secures Sample
Repeatability
Structural Durability
Data Transfer
Resolution (5mm)
Andrew Atallah

## Slide 14: Targets and Metrics
Secures Sample
Repeatability
Structural Durability
Data Transfer
Resolution (5mm)
Andrew Atallah

## Slide 15: Targets and Metrics
Secures Sample
Repeatability
Structural Durability
Data Transfer
Resolution (5mm)
Andrew Atallah

## Slide 16: Targets and Metrics
Secures Sample
Repeatability
Structural Durability
Data Transfer
Resolution (5mm)
Andrew Atallah

## Slide 17: Targets and Metrics
Secures Sample
Repeatability
Structural Durability
Data Transfer
Resolution (5mm)
Andrew Atallah

## Slide 18: Concept Generation
An in-depth process involving multiple team meetings in which team members produced design ideas together and discussed individuals' ideas as a team to compile a list of wildly varying designs.
Anti-Problem
Biomimicry
Brainstorming
Crapshoot
Forced Analogy
Andrew Atallah

## Slide 19: Concept Generation
An in-depth process involving multiple team meetings in which team members produced design ideas together and discussed individuals' ideas as a team to compile a list of wildly varying designs.
Anti-Problem
Biomimicry
Brainstorming
Crapshoot
Forced Analogy
Andrew Atallah

## Slide 20: Medium Fidelity Concepts
5
4
3
2
1
5
Helical Cage Device
4
Typewriter Rail System Device
3
Robotic Arm Device
2
Roller Conveyor Belt Device
1
Vertical Lathe Device
Sean Hemstreet

## Slide 21
5
4
3
2
1
Vertical Lathe Device
Motors
Lathe Chuck Head
Motorized Sensor Track
Lazy Susan Slot
Sean Hemstreet
Secured using a chuck system
Rests on spinning platform
Flux meter sensor is on a vertical motorized track

## Slide 22
5
4
3
2
1
Roller Conveyor Belt Device
Sean Hemstreet
A conveyor belt of rollers is used to spin the shaft
A motor will drive the rollers to turn the shaft precisely
Will have consistent contact pressure on the shaft

## Slide 23
5
4
3
2
1
Robotic Arm Device
Sean Hemstreet
Six degrees of freedom of movement
Suspended shaft with no rotation
Arm can move sensor probe to predetermined locations on shaft

## Slide 24
5
4
3
2
1
Typewriter Rail System Device
= Cam & Follower
= Power Supply, Wires, etc.
Sean Hemstreet
Shaft remains stationary during entire process
The device orbits around the shaft
The device is driven by a servo motor

## Slide 25
5
4
3
2
1
Helical Cage System
Sean Hemstreet
The shaft is mounted vertically during the measuring process
The helical cage is only around the magnetic portion of the shaft
The flux meter probe rides along the helical track and takes measurements

## Slide 26: High Fidelity Concepts
3
2
1
1
Horizontal Lathe Device
3
Lean and Peck Sensor Probe Device
2
Horizontal Roller Bearings Device
Sean Hemstreet

## Slide 27: Horizontal Lathe Device
3
2
1
Lathe Chuck Head
Motors
Table Plate Slot
Live Center
Sensor
Sean Hemstreet

## Slide 28: Roller Bearings Device
3
2
1
Sean Hemstreet

## Slide 29: Lean and Peck Device
3
2
1
Servo Motor
Worm Gear and Track
Two Stepper Motors
Tapered End Fitting with Bearing
Sean Hemstreet

## Slide 30: Concept Selection
Sean Hemstreet
Process of narrowing down all medium and high fidelity concepts into a list of a few designs ranked according to the customer’s design requirements.
Binary Pairwise Comparison and HoQ
Analytical Hierarchy Process
Final Selection
Pugh Charts

## Slide 31: House of Quality
Measures entire magnetic region of the shaft
3
Levels sample
4
Secures sample
5
Consistent measurements
2
Provides reliable measurement feedback
1
Sean Hemstreet

## Slide 32: Pugh Chart: First Iteration
Sean Hemstreet

## Slide 33: Pugh Chart: First Iteration
Sean Hemstreet

## Slide 34: Pugh Chart: Second Iteration
Sean Hemstreet

## Slide 35: Pugh Chart: Second Iteration
Sean Hemstreet

## Slide 36: Pugh Chart: Final Iteration
Sean Hemstreet

## Slide 37: Pugh Chart: Final Iteration
Sean Hemstreet

## Slide 38: Analytical Hierarchy Process
Concept | Alternative Value
Horizontal Lathe | 0.389
Vertical Lathe | 0.275
Typewriter System | 0.336
Sean Hemstreet

## Slide 39: Final Selection
Reliable Measurement Feedback
Consistent Measurements
Measures Entire Region
Secures and Levels Samples
Adaptable
Sean Hemstreet
Horizontal Lathe

## Slide 40: Future Work
Research
Purchasing
Prototyping
Testing
Sean Hemstreet

## Slide 41: Backup Slides

## Slide 42: Pugh Charts
Concepts were compared with one another, with ones that score poorly by comparison being eliminated narrowing selection.
Sean Hemstreet

## Slide 43: Current flux measurement system

## Slide 44
This is 10-point
This is 15–point Times
This is 20–point
This is 25–point
This is 30–point
This is 35–point
This is 40–point
This is 50–point
This is 60–point
This is 72–point
Notes: Use at least 20-point font in Room A105, B134, and B136
Use at least 25-point font in Room B135

## Slide 45: College of Engineering Color Palette
Fang
Orange
RGB: 238, 118, 36
Hex: #EE7624
CMYK:2, 66, 99, 0
1 2 3 4
1 2 3 4
White
Pantone: PMS 000C
RGB: 255, 255, 255
Hex: #FFFFFF
CMYK: 0, 0, 0, 0
1 2 3 4
Black
Pantone: Black C
RGB: 0, 0, 0
Hex: #000000
CMYK:0, 0, 0, 100
Garnet
Pantone: PMS 195 C
RGB: 120, 47, 64
Hex: #782F40
CMYK:19, 90, 50, 55
1 2 3 4
Notes: Avoid 75% Black in B135

## Slide 46: Accent Color Palette
1 2 3 4
Tardis Blue
RGB: 0, 59, 111
Hex: #003B6F
CMYK:
1 2 3 4
Turquoise
RGB: 64, 224, 208
Hex: #40E0D0
CMYK:
1 2 3 4
American Orange
RGB: 255, 139, 0
Hex: #FF8B00
CMYK:
Rubine Red
RGB: 206, 0, 88
Hex: #CE0058
CMYK: 0, 100, 43, 12
1 2 3 4
1 2 3 4
Asagi-iro
RGB: 72, 146, 155
Hex: #48929b
CMYK:
1 2 3 4
Gainsboro
RGB: 220, 220, 220
Hex: #DCDCDC
CMYK:
1 2 3 4
Corn
RGB: 251, 236, 93
Hex: #FBEC5D
CMYK:
1 2 3 4
Timberwolf
RGB: 219, 215, 210
Hex: #DBD7D2
CMYK:
Imperial
RGB: 104, 40, 96
Hex: #682860
CMYK:
1 2 3 4
1 2 3 4
Tardis Blue
RGB: 0, 59, 111
Hex: #003B6F
CMYK:
Rubine Red
RGB: 206, 0, 88
Hex: #CE0058
CMYK: 0, 100, 43, 12
1 2 3 4
1 2 3 4
Corn
RGB: 251, 236, 93
Hex: #FBEC5D
CMYK:
1 2 3 4
Timberwolf
RGB: 219, 215, 210
Hex: #DBD7D2
CMYK:
Notes: Remove American orange add hyperlink grey
Make corn the last for b135
All work in 134 imperial move later
Tardis doesn’t work in b136

## Slide 47
https://color.adobe.com/create/color-wheel
Analogous
F7AB19
D67F15
EE7624
D64615
F73119
Monochromatic
6E3610
F0A16C
EE7624
6E4931
BASB1C
Triad
A14508
4BED3B
EE7624
250CED
2010A1
Complementary
FF8C40
EE7624
0098A1
24E2ED
A1470C
Split Complementary
28A164
2FED8D
EE7624
0848A1
1871ED
Double Split Complementary
3BED93
EE7624
0C6AED
ED2F18
EDAC2F
Square
C7ED3B
EE7624
0CE1ED
A418ED
ED660C
Compound
87724A
EE7624
60EFCF
09BA61
BA7E09
Shades
6E3610
EE7624
FA7625
D46820
AD551A
Notes: These are the variants that work well with Fang Orange. The bolded items show well on the projectors.

## Slide 48
https://color.adobe.com/create/color-wheel
Analogous
85412D
8F3831
782f40
8F3176
792D85
Monochromatic
C44D69
8E626D
782F40
C48796
451B25
Triad
C43959
78743B
782F40
236178
43A2C4
Complementary
C46078
782F40
25C43D
2F783A
C43959
Split Complementary
93C460
577835
782F40
39C49D
297861
Double Split Complementary
5A783B
782F40
237860
6E2978
784435
Square
78683b
782F40
237830
293978
782337
Compound
DEBAAF
782F40
5D8555
70AB32
AB4D32
Shades
C44D69
782F40
853447
5E2532
38161E

## Slide 49
B135 Stage Right
A105
A105
B135 Stage Left
B135
B134, A105
B136