## Slide 1: Team 520: NASA-MSFC Actively Sealed Cryogenic Coupler
Jason Goldstein, Lauren Roche, Sean Rodney,
Valerie Rodriguez, Nicolas Sgammato
Virtual Design Review 4

## Slide 2: Team 520
Nicolas Sgammato
Design Engineer
Jason Goldstein
Materials Engineer
Lauren Roche
Cryogenics Engineer
Sean Rodney
Test Engineer
Valerie Rodriguez
Valerie Rodriguez
Thermal-Fluids Engineer
Department of Mechanical Engineering
2

## Slide 3: Sponsors
James C. Buzzell
Propulsion Systems Engineer,
NASA MSFC
Marvin W. Barnes
Advanced Propulsion Research and Development,
NASA MSFC
Valerie Rodriguez
Department of Mechanical Engineering
3

## Slide 4: Objective
The objective of this project is to design,
build, and test an actively sealed coupler
that prevents the leakage of cryogenic fuel
during the transfer from depot to vessel for future
deep space NASA missions.
Valerie Rodriguez
Department of Mechanical Engineering
4

## Slide 5: Background
Cryogenic Fuel Transfer
Mechanical Connection
Force Held
Sean Rodney
Department of Mechanical Engineering
5

## Slide 6: Key Goals
Effective Sealing
90-Day Lunar Mission
Prevent and Monitor
Leaks
Sean Rodney
Department of Mechanical Engineering
6

## Slide 7: Sponsor Updates:
Insulation negligible for testing
SOFI: Smooth Exterior for future implementation
Flow rate should be low enough during fueling for pressure drop to be negligible.
Lubricant: Dry-film lube
Assume pressure in tanks is equalized.
Department of Mechanical Engineering
7
Sean Rodney

## Slide 8: Fall Design
Force-held
lock
Encapsulated seals
Double-poppet actuator​
F
Department of Mechanical Engineering
8
Valerie Rodriguez

## Slide 9
Department of Mechanical Engineering
9
Initial Concept
Valerie Rodriguez

## Slide 10
Department of Mechanical Engineering
10
Initial Concept
Valerie Rodriguez

## Slide 11: Initial Design Flaws
Department of Mechanical Engineering
11
Valerie Rodriguez

## Slide 12
Department of Mechanical Engineering
12
Flow Channel Misalignment and Size
Insertion Relief Port
Difficult Seal Location and Manufacturing
Valerie Rodriguez

## Slide 13: Updated Design
Department of Mechanical Engineering
13
Sean Rodney
Receiver
Probe

## Slide 14: Receiving Half
Department of Mechanical Engineering
14
Sean Rodney
Static PTFE O-Rings
Stainless Steel Spring
Spring-Energized PTFE Seals
Actuator

## Slide 15: Probe Half
Department of Mechanical Engineering
15
Sean Rodney
Static PTFE O-Rings
Stainless Steel Spring
Actuator
Spring-Energized PTFE Seals

## Slide 16: Updated Sealing
Spring-energized seal
Implements a circular spring to exert outward pressure
Encapsulated by PTFE (Teflon) due to excellent performance in cryogenic applications
Seals translating cylindrical bodies
Static and low speed applications
Department of Mechanical Engineering
16
Sean Rodney
103A Omniseal​®
Note: Image for illustrative purposes only: The depicted seal is for stylization and a similar seal from McMaster-Carr will be implemented.

## Slide 17: Manufacturing
Department of Mechanical Engineering
17
Main components of probe and receiver will be CNC machined by the FAMU-FSU COE machine shop
Springs and seals will be ready to install from the manufacturer
Assembly of the coupler will be completed by the design team
Sean Rodney

## Slide 18
Department of Mechanical Engineering
18
Testing
Leakage
Status:
In Progress
Status:
Approved
Status:
Pending Approval
Status:
Approved
Cryogenic
Flow Rate
Durability
Sean Rodney

## Slide 19: Leakage Testing
Calculate leakage rates and use Nasa environment correction factors to obtain target rates
Identify design conflicts/areas of improvement
Apply calculated rates and developed solutions to improve design before cryogenic testing
Department of Mechanical Engineering
19
Sean Rodney

## Slide 20
Department of Mechanical Engineering
20
Sean Rodney
Initiation of NHMFL
on-boarding and training
KF fitting for compatibility with NHMFL equipment
Material-safety check with Dr. Wei Guo
Cryogenic Testing

## Slide 21: Flow Rate Testing
PIV testing will be conducted at the Florida Center For Advanced Aero-Propulsions
(FCAAP)
The design is to be sliced and placed in the low-speed wind tunnel to test flow rates
Particle Imaging Velocimetry will be used to analyze the flow inside the coupler
Department of Mechanical Engineering
21
Valerie Rodriguez

## Slide 22: Durability Testing
Department of Mechanical Engineering
22
Durability must be tested to identify any possible vulnerabilities in the design
The parts will be brushed with paint and tested at different forces
The paint will chip away exposing areas experiencing the most force
Leakage test will be preformed again to check for cracks and if design is reusable
Valerie Rodriguez

## Slide 23: Testing Validation
Department of Mechanical Engineering
23
Valerie Rodriguez
Leakage
Cryogenic
Flow Rate
Durability
External leakage: Less than 50 SCIM liquid nitrogen at 5 and 50 psig internal pressure
Internal leakage: Less than 500 SCIM liquid nitrogen at 15 and 50 psid while demated
Stainless steel springs can endure at least 10 N of force to keep tightly sealed connection
The valve can endure minimum 80 K temperatures
Less than 5% plastic deformation

## Slide 24: Testing Validation
Department of Mechanical Engineering
24
Valerie Rodriguez
Leakage
Cryogenic
Flow Rate
Durability
External leakage: Less than 50 SCIM liquid nitrogen at 5 and 50 psig internal pressure
Internal leakage: Less than 500 SCIM liquid nitrogen at 15 and 50 psid while demated
Stainless steel springs can endure at least 10 N of force to keep tightly sealed connection
The valve can endure minimum 80 K temperatures
Less than 5% plastic deformation

## Slide 25
Department of Mechanical Engineering
25
Future Work
Finish calculations, order parts, build prototype and refine design
Conduct all
testing methods
Manufacture final design at machine shop
Analyze and Interpret
data from testing
Valerie Rodriguez

## Slide 26: Thank You.
Jason Goldstein, Lauren Roche, Sean Rodney,
Valerie Rodriguez, Nicolas Sgammato
520: NASA Actively sealed Cryogenic Coupler

## Slide 27: Backup Slides

## Slide 28: Flow Rate Testing
In the case testing at the FCAAP lab is denied, fluid dynamics will be simulated in COMSOL.
Testing using PIV would be ideal but main concerns can still be analyzed using this software.
Department of Mechanical Engineering
28
Valerie Rodriguez

## Slide 29: Lunar Refueling Depot
Reduced Cost
Increased Safety
Extended Mission Capabilities

## Slide 30: Problems with Current Designs
Sealing and Leakage
Thermal Radiation
Contamination

## Slide 31: Actively Sealed Coupler
Seals when the two halves make contact

## Slide 32: Background
Cryogenic Fuel Transfer
Deep Space Mission
Lunar Base Fuel Depot
Lauren Roche
Department of Mechanical Engineering
32

## Slide 33: Customer Needs
Extend the life of the cryogenic fuel storage in space
Minimize the leakage rate of fuels during the transfer process
Seal activation upon contact of coupler halves
Limit boil-off of fuel due to heat transfer
Protect system from foreign particulate matter
Valerie Rodriguez

## Slide 34: Customer Needs
Extend life of the cryogenic fuel
Minimize the leakage rate
Seal activation upon contact of coupler halves
Limit Boil Off
System Protection
Valerie Rodriguez

## Slide 35: Customer Needs
Valerie Rodriguez
Minimize the leakage rate
Extend life of the cryogenic fuel
Seal activation upon contact of coupler halves
Limit boil off
System protection

## Slide 36: Functional Decomposition
Coupling System
Durability
Connection
Fueling
Disconnection
Valerie Rodriguez

## Slide 37: Functional Decomposition
Coupling System
Durability
Connection
Fueling
Disconnection
Major Function
Endure Solar Radiation
Mitigate Particulates
Minimize Heat Transfer
Tolerate Vehicle Misalignment
Uphold Structural Durability
Protect Electrical Components
Minor Function
Valerie Rodriguez

## Slide 38: Functional Decomposition
Coupling System
Durability
Connection
Fueling
Disconnection
Major Function
Check Pressure Difference
Level Pressure
Lock two Halves Together
Seal the Connection
Minor Function
Valerie Rodriguez

## Slide 39: Functional Decomposition
Coupling System
Durability
Connection
Fueling
Disconnection
Major Function
Open Pipe Valve
Minimize Fuel Leakage
Close Pipe Valve
Minor Function
Valerie Rodriguez

## Slide 40: Functional Decomposition
Coupling System
Durability
Connection
Fueling
Disconnection
Major Function
Disconnect Both Halves
Purge Excess Fuel
Minor Function
Valerie Rodriguez

## Slide 41
Status Update
Name
Department of Mechanical Engineering
41
Research on materials, locks, insulation, existing designs
Wrapping up concept generation and concept selection
Contact sponsor to get feedback on our top designs

## Slide 42
Department of Mechanical Engineering
42
Fuel Leakage
Measured Using Venturi Flowmeter at the National High Magnetic Field Laboratory (NHMFL)
Target From Critical Targets Table Provided by Sponsor
For Internal Leakage:
≤ 500 SCIM LN2 at 15 and 50 PSID While De-mated
For External Leakage:
≤ 50 SCIM LN2 at 5 and 50 PSIG Internal Pressure
Nicolas Sgammato

## Slide 43
Department of Mechanical Engineering
43
Heat Transfer
Measured Using a Thermocouple in Coupler Interior
Target Derived From Boiling Point of Liquid Nitrogen
Coupler Interior Temperature
≤ 80 K
Nicolas Sgammato

## Slide 44
Department of Mechanical Engineering
44
Coupler Connection
Measured using a Force Transducer Attached to One Half of Coupler
Connection/
Disconnection Force:
≤ 250 LBF
Target Derived From Previous NASA Coupler
Jason Goldstein

## Slide 45
Department of Mechanical Engineering
45
Concept Generation Tactics
Crap Shoot
1
1
1
2
2
2
3
3
3
C
A
B
Biomimicry
Morphological Chart
1
2
3
4
5
A
B
C
D
E
Jason Goldstein

## Slide 46
Seals​
Insulation
Locks
Valves
Department of Mechanical Engineering
46
Terminology
Lauren Roche
Encapsulated O-ring
Teflon Seal
MLI
SOFI
Double vacuum wall
Double poppet valve
Force held
Collet Lock

## Slide 47
Department of Mechanical Engineering
47
High Fidelity Concepts
Concept #33
Force held double poppet actuator, sealed with encapsulated O-rings, insulated by a double vacuum wall structure and Multi-Layered Insulation
Lauren Roche

## Slide 48
Department of Mechanical Engineering
48
High Fidelity Concepts
Concept #98
Force held double poppet actuator, sealed with encapsulated O-rings, insulated by a double vacuum wall structure and Spray-On Foam Insulation (SOFI)
Lauren Roche

## Slide 49
Department of Mechanical Engineering
49
High Fidelity Concepts
Concept #100
Force held double poppet actuator, sealed with Teflon, insulated by a double vacuum wall structure and Multi-Layered Insulation (MLI)
Nicolas Sgammato

## Slide 50
Department of Mechanical Engineering
50
Medium Fidelity Concepts
Nicolas Sgammato
#79
#81
#80
#82
#99

## Slide 51
Double Poppet
Force held lock
Double vacuum & SOFI
Teflon Seals
#99
Department of Mechanical Engineering
51
Medium Fidelity Concepts
Nicolas Sgammato

## Slide 52
Double Poppet
Collet lock
Double vacuum & MLI
Encapsulated Seals
#82
Department of Mechanical Engineering
52
Medium Fidelity Concepts
Jason Goldstein

## Slide 53
Department of Mechanical Engineering
53
Medium Fidelity Concepts
Jason Goldstein
Double Poppet
Collet Lock
Double vacuum & SOFI
Encapsulated Seals
#81

## Slide 54
Pugh Charts- Second Iteration
Concept #100
Selection Criteria
Leakage
Lifetime
Seal
Resilience
Size
Cost
-
S
-
-
S
+
Department of Mechanical Engineering
54
Datum: Concept #33
Force held double poppet actuator, sealed with Teflon, insulated by a double vacuum wall structure and Multi-Layered Insulation (MLI)
Jason Goldstein

## Slide 55
Seals​
Encapsulated O-ring seal​
Teflon Seal
Insulation
MLI
SOFI
Double vacuum wall
Locks
Force held
Collet Lock
Valves
Double poppet valve
Department of Mechanical Engineering
55
Terminology

## Slide 56
Top Concepts
Name
Department of Mechanical Engineering
56
Force held lock with double poppet valve, encapsulated seals, double vacuum and MLI (multi-layered insulation)
Force held lock with double poppet valve, encapsulated seals, double vacuum and SOFI (spray-on foam insulation)
Collet lock with double poppet valve, encapsulated seals, double vacuum and MLI
Collet lock with double poppet valve, encapsulated seal, double vacuum and SOFI

## Slide 57
Department of Mechanical Engineering
57
Pugh Charts- Second Iteration
Selection Criteria
Leakage
Lifetime
Seal
Resilience
Size
Cost
Nicolas Sgammato
Concept #98
S
-
S
-
+
+
Force held double poppet actuator, sealed with encapsulated O-rings, insulated by a double vacuum wall structure and Spray-On Foam Insulation (SOFI)
Datum: Concept #33

## Slide 58
Department of Mechanical Engineering
58
Pugh Charts- Second Iteration
Selection Criteria
Leakage
Lifetime
Seal
Resilience
Size
Cost
Jason Goldstein
Concept #99
-
-
-
-
+
+
Force held double poppet actuator, sealed with Teflon, double vacuum wall structure and Spray-On Foam Insulation (SOFI)
Datum: Concept #33

## Slide 59
Department of Mechanical Engineering
59
Analytical Hierarchy Process
Concept #33
Concept #98
Concept #100
Alternative Value:
0.466
Alternative Value:
0.632
Alternative Value:
1.032
Jason Goldstein

## Slide 60
Department of Mechanical Engineering
60
Targets and Metrics
Fuel Leakage Heat Transfer Coupler Connection Structure Integrity
Fuel Leakage Rate from Flowmeter
Interior Temperature from Thermocouple
Connection Force from Transducer
Material Yielding from Tensile Test
Nicolas Sgammato

## Slide 61
Department of Mechanical Engineering
61
High Fidelity Concepts
Force held double – poppet actuator with double vacuum wall insulation structure paired with:
#33:
Encapsulated
O-ring seals and MLI
#48:
#50

## Slide 62
Department of Mechanical Engineering
62
Medium Fidelity Concepts
Double-poppet valve and double vacuum wall
#49 | Force-held lock Teflon seals SOFI
#32 | Collet lock encapsulated O-ring seals MLI
#31 | Collet lock encapsulated O-ring seals SOFI
#30 | Collet lock Teflon seals MLI
Jason Goldstein

## Slide 63
Department of Mechanical Engineering
63
Medium Fidelity Concepts
Jason Goldstein
Double Poppet
Collet Lock
Double vacuum & MLI
Teflon Seals
#80

## Slide 64
Department of Mechanical Engineering
64
Medium Fidelity Concepts
Lauren Roche
Double Poppet
Collet Lock
Double vacuum & SOFI
Teflon Seals
#79

## Slide 65
Department of Mechanical Engineering
65
Concept Selection
Binary Pairwise Comparison
House of Quality
Pugh Charts
Analytical Hierarchy Process
Final Selection
Lauren Roche

## Slide 66
Department of Mechanical Engineering
66
Binary Pairwise Comparison
Compares Customer Needs to Each Other to Determine Relative Importance
Customer Needs | Score
Fluid Loss Prevention | 6
Active Seal | 6
Maintains Pressure | 6
Effective Coupling | 6
Heat Transfer Protection | 5
Particulate Mitigation | 4
Life-Span | 3
Cost | 3
Sizing Parameters | 3
Material Resilience | 2
Reusability | 1
Lauren Roche

## Slide 67
Department of Mechanical Engineering
67
Structural Integrity
Measured using Tensile Testing on Selected Material
Safe Range was Chosen Due to Material Not Yet Being Selected
Plastic Deformation of Chosen Material:
≤ 5%
Jason Goldstein

## Slide 68
Department of Mechanical Engineering
68
House of Quality
Customer Requirements
Life-span
Fluid Loss
Active Seal
Material Resilience
Reusability
Maintains Pressure
Effective Coupling
Heat Transfer
Particulate Mitigation
Channel Sizing Parameters
Cost
Ranked Engineering Characteristics
1. Fuel Leakage
2. Seal
3. Heat Transfer
4. Durability
5. Weight
6. Cost
Nicolas Sgammato

## Slide 69
Pugh Charts- First Iteration
#82
#81
#80
#33
#98
#100
#99
-2
-2
-2
1
1
1
1
Department of Mechanical Engineering
69
Selection Criteria
Leakage
Lifetime
Seal
Resilience
Size
Cost
Datum: NASA Low Separation Force Quick Disconnect
Nicolas Sgammato

## Slide 70
Department of Mechanical Engineering
70
Medium Fidelity Concepts
#49
Force held double poppet actuator, sealed with Teflon, double vacuum wall structure and Spray-On Foam Insulation (SOFI)
Nicolas Sgammato

## Slide 71
Department of Mechanical Engineering
71
Medium Fidelity Concepts
#32
Double poppet actuator with collet lock, sealed with encapsulated O-rings, double vacuum wall structure and Multi-Layer Insulation (MLI)
Nicolas Sgammato

## Slide 72
Department of Mechanical Engineering
72
Medium Fidelity Concepts
#31
Collet locked double poppet actuator, sealed with encapsulated O-rings, double vacuum wall structure and Spray-On Foam Insulation
Jason Goldstein

## Slide 73
Department of Mechanical Engineering
73
Medium Fidelity Concepts
#30
Double poppet-actuator with collet lock, Teflon seals, double vacuum wall structure and Multi-Layer Insulation
Jason Goldstein

## Slide 74
Department of Mechanical Engineering
74
Medium Fidelity Concepts
#29
Double poppet-actuator with collet lock, Teflon seals, double vacuum wall structure and Spray on Foam Insulation
Jason Goldstein

## Slide 75
Department of Mechanical Engineering
75
High Fidelity Concepts
Concept #33
Concept #48
Concept #50

## Slide 76
Department of Mechanical Engineering
76
High Fidelity Concepts
Force-held lock with double-poppet valve
and double vacuum wall
#33 | Encapsulated O-ring seals MLI
#48 | Encapsulated O-ring seals SOFI
#50 | Teflon seals MLI
Lauren Roche

## Slide 77
Department of Mechanical Engineering
77
Final Concept Selection
Force-held lock with double-poppet valve
and double vacuum wall
#33 | encapsulated O-ring seals MLI
Nicolas Sgammato

## Slide 78: Fall Design
Double poppet actuator and force held lock, seal with encapsulated seals, insulated by double vacuum wall and Multi-Layer Insulation (MLI) blanket

## Slide 79
Department of Mechanical Engineering
79
Final Concept Selection
Lauren Roche
Concept #33: Double poppet actuator and force held lock, seal with encapsulated seals, insulated by double vacuum wall and Multi-Layer Insulation (MLI) blanket

## Slide 80
Department of Mechanical Engineering
80
Concept #33
Lauren Roche

## Slide 81
Department of Mechanical Engineering
81
Concept #33
Lauren Roche

## Slide 82
Department of Mechanical Engineering
82
Concept #33
Lauren Roche

## Slide 83: Probe Half
Department of Mechanical Engineering
83
Sean Rodney
Static PTFE O-Rings
Stainless Steel Spring
Actuator
Spring-Energized PTFE Seals

## Slide 84
This is 10-point
This is 15–point Times
This is 20–point
This is 25–point
This is 30–point
This is 35–point
This is 40–point
This is 50–point
This is 60–point
This is 72–point
Notes: Use at least 20-point font in Room A105, B134, and B136
Use at least 25-point font in Room B135

## Slide 85: College of Engineering Color Palette
Fang
Orange
RGB: 238, 118, 36
Hex: #EE7624
CMYK:2, 66, 99, 0
1 2 3 4
1 2 3 4
White
Pantone: PMS 000C
RGB: 255, 255, 255
Hex: #FFFFFF
CMYK: 0, 0, 0, 0
1 2 3 4
Black
Pantone: Black C
RGB: 0, 0, 0
Hex: #000000
CMYK:0, 0, 0, 100
Garnet
Pantone: PMS 195 C
RGB: 120, 47, 64
Hex: #782F40
CMYK:19, 90, 50, 55
1 2 3 4
Notes: Avoid 75% Black in B135

## Slide 86: Accent Color Palette
1 2 3 4
Tardis Blue
RGB: 0, 59, 111
Hex: #003B6F
CMYK:
1 2 3 4
Turquoise
RGB: 64, 224, 208
Hex: #40E0D0
CMYK:
1 2 3 4
American Orange
RGB: 255, 139, 0
Hex: #FF8B00
CMYK:
Rubine Red
RGB: 206, 0, 88
Hex: #CE0058
CMYK: 0, 100, 43, 12
1 2 3 4
1 2 3 4
Asagi-iro
RGB: 72, 146, 155
Hex: #48929b
CMYK:
1 2 3 4
Gainsboro
RGB: 220, 220, 220
Hex: #DCDCDC
CMYK:
1 2 3 4
Corn
RGB: 251, 236, 93
Hex: #FBEC5D
CMYK:
1 2 3 4
Timberwolf
RGB: 219, 215, 210
Hex: #DBD7D2
CMYK:
Imperial
RGB: 104, 40, 96
Hex: #682860
CMYK:
1 2 3 4
1 2 3 4
Tardis Blue
RGB: 0, 59, 111
Hex: #003B6F
CMYK:
Rubine Red
RGB: 206, 0, 88
Hex: #CE0058
CMYK: 0, 100, 43, 12
1 2 3 4
1 2 3 4
Corn
RGB: 251, 236, 93
Hex: #FBEC5D
CMYK:
1 2 3 4
Timberwolf
RGB: 219, 215, 210
Hex: #DBD7D2
CMYK:
Notes: Remove American orange add hyperlink grey
Make corn the last for b135
All work in 134 imperial move later
Tardis doesn’t work in b136

## Slide 87
https://color.adobe.com/create/color-wheel
Analogous
F7AB19
D67F15
EE7624
D64615
F73119
Monochromatic
6E3610
F0A16C
EE7624
6E4931
BASB1C
Triad
A14508
4BED3B
EE7624
250CED
2010A1
Complementary
FF8C40
EE7624
0098A1
24E2ED
A1470C
Split Complementary
28A164
2FED8D
EE7624
0848A1
1871ED
Double Split Complementary
3BED93
EE7624
0C6AED
ED2F18
EDAC2F
Square
C7ED3B
EE7624
0CE1ED
A418ED
ED660C
Compound
87724A
EE7624
60EFCF
09BA61
BA7E09
Shades
6E3610
EE7624
FA7625
D46820
AD551A
Notes: These are the variants that work well with Fang Orange. The bolded items show well on the projectors.

## Slide 88
https://color.adobe.com/create/color-wheel
Analogous
85412D
8F3831
782f40
8F3176
792D85
Monochromatic
C44D69
8E626D
782F40
C48796
451B25
Triad
C43959
78743B
782F40
236178
43A2C4
Complementary
C46078
782F40
25C43D
2F783A
C43959
Split Complementary
93C460
577835
782F40
39C49D
297861
Double Split Complementary
5A783B
782F40
237860
6E2978
784435
Square
78683b
782F40
237830
293978
782337
Compound
DEBAAF
782F40
5D8555
70AB32
AB4D32
Shades
C44D69
782F40
853447
5E2532
38161E

## Slide 89
B135 Stage Right
A105
A105
B135 Stage Left
B135
B134, A105
B136