## Slide 1: SAFE CNC MACHINE
Design Review V
Samuel Byers, Amanda Garcia-Menocal, Shelby Gerlt, Malik Grant, Carlton Walker
February 18, 2025

## Slide 2: Team 514
Shelby Gerlt
Samuel Byers
Amanda Garcia-Menocal
Malik Grant
Carlton Walker
Supply Chain Engineer
Structural Engineer
Test Engineer
Electrical Engineer
Design Engineer
Malik Grant

## Slide 3: Guidance and Sponsorship
Dr. Eric Hellstrom
Advisor
Dr. Shayne McConomy
Sponsor
Malik Grant

## Slide 4: Project Objective
The objective of this project is to design safeguards for the Senior Design Lab’s CNC router to protect students and staff from hazards and mitigate the need for PPE.
Shapeoko 3 CNC Router
Malik Grant
Notes: The objective of this project is to make the Senior Design Labs CNC router safe for student use without requiring additional supervision. This will be achieved by developing machine safeguards that limit the need for Personal Protective Equipment (PPE) in the room while the machine is in operation.

## Slide 5: Previous Work
Identified hazards in current condition
Designed risk reduction safety features
Completed CAD model
Finalized design and material selection
Selected suppliers for materials
Design Review 5
Malik Grant
Notes: Going to begin with a recap of work done last semester and up to this point, then talk about our current design, and finally plans for this semester as we come to design review 5

## Slide 6: Hazards
Moving Parts
Projectiles
Impalement
Particles
Malik Grant
Notes: The objective of this project is to make the Senior Design Labs CNC router safe for student use without requiring additional supervision. This will be achieved by developing machine safeguards that eliminate the need for Personal Protective Equipment (PPE) in the room while the machine is in operation.

## Slide 7: Critical Targets and Metrics
Function
Halt Projectiles
Limit access while running
Create no interference
Target
<= 4,000 N
Fully Operable
2 ± 0.2mm
Metric
Impact Force
Clearance
User observation
Malik Grant

## Slide 8: Assessed Hazards
Moving Parts
Projectiles
Impalement
Particles
Amanda Garcia-Menocal
Notes: The objective of this project is to make the Senior Design Labs CNC router safe for student use without requiring additional supervision. This will be achieved by developing machine safeguards that eliminate the need for Personal Protective Equipment (PPE) in the room while the machine is in operation.

## Slide 9: Implemented Safety Functions
Moving Parts
Projectiles
Impalement
Particles
Enclosure
Amanda Garcia-Menocal
Notes: The objective of this project is to make the Senior Design Labs CNC router safe for student use without requiring additional supervision. This will be achieved by developing machine safeguards that eliminate the need for Personal Protective Equipment (PPE) in the room while the machine is in operation.

## Slide 10: Implemented Safety Functions
Moving Parts
Projectiles
Impalement
Particles
Enclosure
Emergency Shutoff
Automatic Shutoff
Amanda Garcia-Menocal
Notes: The objective of this project is to make the Senior Design Labs CNC router safe for student use without requiring additional supervision. This will be achieved by developing machine safeguards that eliminate the need for Personal Protective Equipment (PPE) in the room while the machine is in operation.

## Slide 11: Implemented Safety Functions
Moving Parts
Projectiles
Impalement
Particles
Enclosure
Emergency Shutoff
Automatic Shutoff
Amanda Garcia-Menocal
Notes: The objective of this project is to make the Senior Design Labs CNC router safe for student use without requiring additional supervision. This will be achieved by developing machine safeguards that eliminate the need for Personal Protective Equipment (PPE) in the room while the machine is in operation.

## Slide 12: Enclosure Design
Amanda Garcia-Menocal

## Slide 13: Enclosure Design
Front view:
Side view:
Amanda Garcia-Menocal

## Slide 14: Electrical Design
Power Source
Breaks Series
Amanda Garcia-Menocal
Breaks Series
Notes: The way the system would be powered is displayed in this diagram with the essential parts including limit switches on the doors, power source relay on/off switch, and emergency shut off button. The doors will have two limit switches on each side of the door to ensure for contact with the frame. The limit switches will be powered directly from the power source of the machine which is being powered from the room outlet. If the door is not fully in tack then the machine will not be powered. But now if the machine wants to be in use while the doors are open that is when you would use the power source relay on/off button to send the current directly to the machine. And finally, the emergency stop button will cut all power through the series of wire for the whole machine. We are using 12 gauge wiring to feed the current throughout the system

## Slide 15: Door Design
Amanda Garcia-Menocal

## Slide 16: Door Design
Amanda Garcia-Menocal

## Slide 17: Vacuum Collection Design
Dust Separator
Dust Collector
Dust Sweep Attachment
Amanda Garcia-Menocal

## Slide 18: Vacuum Collection Design
Dust Separator
Dust Collector
Dust Sweep Attachment
Amanda Garcia-Menocal

## Slide 19: Vacuum Collection Design
Dust Separator
Dust Collector
Dust Sweep Attachment
Dust
Particles
Amanda Garcia-Menocal

## Slide 20: Projected Costs
Projected costs have considered:
Taxes
Shipping
Cutting & Assembly
Chart: 
| Budget | Spent | Remaining
 | 2000 | 1624.779 | 375.221
Samuel Byers
Notes: Can talk about use of software

## Slide 21: Materials Budget Breakdown
Chart: 
| Electrical | Base | Polycarbonate | Metal | Other
 | 60 | 59.0382 | 428.2317 | 700.2684 | 437.2407
4%
3%
Electrical
$60.00
Chart: 
| Electrical | Base | Polycarbonate | Metal | Other
 | 60 | 59.0382 | 428.2317 | 700.2684 | 437.2407
Base
$59.04
Metal
$700.27
Miscellaneous
$437.24
Polycarbonate
$428.23
Samuel Byers

## Slide 22: Aluminum Extrusion Material Selection
Modular
Good strength-to-weight ratio
Long-term solution
Simple assembly
Corrosion resistant
1.50”
1.50”
Samuel Byers

## Slide 23: Polycarbonate Material Selection
Pros
Impact resistance
Durability
Heat tolerance
Samuel Byers

## Slide 24: Polycarbonate Material Selection
Pros
Impact resistance
Durability
Heat tolerance
Cons
Scratch sensitivity
UV degradation
Chemical sensitivity
Samuel Byers

## Slide 25: Future Work
Finish ordering all materials
Design Review 5
Assemble enclosure
Install and level enclosure
Install vacuum hose
Complete electrical wiring
Test design and verify risk reduction
Samuel Byers
Notes: Figure out how to add attachements
Modify base platform (vibration)
Emergency shut off (figure out)
Verify parts and suppliers

## Slide 26: Project Objective
Implement safeguards for the CNC router to:
Mitigate the need for PPE
Protect students and staff from hazards
Shapeoko 3 CNC Router
Shelby Gerlt
Notes: The objective of this project is to make the Senior Design Labs CNC router safe for student use without requiring additional supervision. This will be achieved by developing machine safeguards that limit the need for Personal Protective Equipment (PPE) in the room while the machine is in operation.

## Slide 27: Stakeholders
FAMU-FSU COE
Tripp Lappalainen
Jacob Schmitt
Elias Haase
FAMU-FSU COE
Shelby Gerlt

## Slide 28: Critical Target: Halt Projectiles
Target | 3000 N
Metric | Impact force
Testing | Impact test
Shelby Gerlt
Notes: To test the ability of a selected barrier to halt projectiles, an impact test will be performed.

## Slide 29: Critical Target: Create No Interference
Target | Pass
Metric | Pass/Fail
Testing | Observation
Shelby Gerlt
Notes: To test whether the design creates no interference, the machine will be tested with the safeguards in place to check that it can successfully complete a cycle.

## Slide 30: Critical Target: Limit Access When On
Target | True
Metric | Pass/Fail
Testing | Observation
Shelby Gerlt
Notes: To test whether the machine prevents the user from accessing it, the machine will be turned on and a subject will attempt to access it. In the case that the access is overridden, the machine will have a limit switch to shut it down.

## Slide 31: Hierarchy of Functions
CNC Safeguard
Protection
Non-mechanical hazards
Mechanical hazards
Interface
Communication
Control
Collect dust
Dampen noise
Halt projectiles
Prevent contact with point of operation
Prevent contact with power transmission
Create no interference
Communicates hazards
Communicates proper use
Stops use of incorrect materials
Limit machine access when running
Shelby Gerlt
Notes: Hierarchy of functions outlines the goals we have for our design. The primary functions are to halt projectiles, create no interference, and limit machine access while running

## Slide 32: Hierarchy of Functions
CNC
Protection
Non hazards
M hazards
Interface
Comm
Control
Collect
Dampen
Halt
Prevent
Prevent
Create
Comm
Comm
Stops
Limit
Non-mechanical hazards
Mechanical hazards
Collect dust
Dampen noise
Halt projectiles
Prevent contact with point of operation
Prevent contact with power transmission
Create no interference
Protection
CNC Safeguard
Shelby Gerlt
Notes: One of the main hazards is projectiles, in case of this our design has to be able to counter or stop projectiles from hitting anyone near the machine.
The safeguard design must also not prevent the machine from functioning as intended.

## Slide 33: Hierarchy of Functions
Interface
Communication
Control
Communicates hazards
Communicates proper use
Stops use of incorrect materials
Limit machine access when running
CNC Safeguard
CNC
Protection
Non hazards
M hazards
Interface
Comm
Control
Collect
Dampen
Halt
Prevent
Prevent
Create
Comm
Comm
Stops
Limit
Shelby Gerlt
Notes: Final critical target, the design will prevent anyone from accessing the router while it is on. This means the user will not be able to come into contact with the machine at all while it is running.

## Slide 34: Targets: Mechanical
Samuel Byers
Function | Target | Metric
Prevent contact w/ point of operation | Particle levels < 5 mg/m3 | Clearance
Prevent contact w/ power transmission | Noise levels < 85 dB | Clearance

## Slide 35: Targets: Non-Mechanical
Samuel Byers
Function | Target | Metric
Collect Dust | Particle levels < 5 mg/m3 | Particulates
Dampen Noise | Noise levels < 85 dB | Decibel

## Slide 36: Targets: Interface
Samuel Byers
Function | Target | Metric
Prevent use of incorrect materials | Customer uses proper materials | User opinion

## Slide 37: Targets: Beyond the Functions
Samuel Byers
Function | Target | Metric
Manage Cables | Visibility of wires/aesthetics | Sponsor opinion
Disassemble Quickly | < 1 day | Time
Limit Vibrations | 5 ± 0.5 mm | Displacement

## Slide 38: Assumptions to Guide the Design
The user will understand how to use the machine
The machine will be properly maintained
The user will not be using PPE
Only compatible materials will be used in the machine
Samuel Byers

## Slide 39: Medium Fidelity Concepts
Malik Grant
Horizontal sliding door
Vertical sliding door
Double sliding door
Top-hinge door
Bifold door
Notes: For our concept selection, we first started with generating 100 different ideas centered around our critical targets. After developing these ideas from each member of the team we came together to narrow down our concepts to 5 medium fidelity concepts and 3 high fidelity concepts. We used different processes to rank these concepts. For our 5 medium fidelity concepts, we were able to get real life comparisons and were able to pull different features that would be best for our prototype.

## Slide 40: High Fidelity Concepts
Malik Grant
Roll cover
Hatch
Oven door
Notes: Here is our 3 high fidelity concepts,

## Slide 41: Concept Selection
Samuel Byers
Concepts

## Slide 42: Concept Selection
Samuel Byers
Impact force
Clearance
Limited access
Disassembly time
Displacement due to vibration
Characteristics
Concepts

## Slide 43: Concept Selection
Samuel Byers
Selection
Impact force
Clearance
Limited access
Disassembly time
Displacement due to vibration
Characteristics
Concepts

## Slide 44: Final Selection
Samuel Byers
Horizontal sliding door
Vertical sliding door
Double sliding door
Top-hinge door
Bifold door

## Slide 45: Changes from Initial Concepts
Carlton Walker
Front Opening Doors
Auto-Off Hinge
Back Door
Preliminary Designs CAD
Updated Design